## Slide 1: Views on Rel-19 Ambient IoT
3GPP RAN-Release 19 workshop
Taipei, June 15 - June 16, 2023
RWS-2300342
Agenda Item: RWS, 5
Source: OPPO
Document for: Discussion

## Slide 2: Outline
Motivation and design target of Ambient IoT
Summary and proposals
Important aspects for ambient IoT

## Slide 3: Motivation on supporting Ambient IoT
  An ambient power-enabled Internet of Things device is an IoT device powered by energy harvesting ( e.g. from radio waves, light (solar), motion, heat etc.), being either battery-less or with limited energy storage capability (e.g. using a capacitor).
  Ambient IoT provides a promising scheme to fulfil the service requirements that can’t be met using the existing IoT technologies(e.g. NB-IoT/MTC etc.).
    Under extreme conditions, e.g., high pressure, extremely high/low temperature, humid etc..
    Where Ultra-low cost, very smaller form factor, maintenance-free and longer life cycle are required.
…
…

## Slide 4: Design principle of Ambient IoT
  The distinguished characteristics of ambient IoT includes:
    Maintenance-free device
    Battery-less device
    Ultra-low cost
    Small size
    Long life span etc.
  From the perspective of both technique design and the target use case, Ambient IoT needs to be complementary to existing 3GPP IoT technologies.
    Overlapping of the target market with existing 3GPP IoT technologies needs to be avoided.
    An ultra-low complexity and ultra-low power consumption communication technology which has obvious difference with the existing technologies shall be targeted for ambient IoT.

## Slide 5: Ambient IoT device capability
  When setting the design target for ambient IoT device capability, the differentiation with existing 3GPP
    technologies and even non-3GPP technologies shall be pursued.
    For example, the coverage (for direct mode) can be relaxed compared with that legacy 3GPP technologies
    For example, the power consumption shall be lower enough to support using ambient power with extremely low power density. Meanwhile, Aspects such as the 3GPP system efficiency, coexistence with the existing 3GPP system(e.g. In-band deployment) deployed in licensed frequency band etc. shall be considered.
  Therefore, It is proposed that Ambient IoT device has a higher capability than that of RFID device and much lower capability than that of existing 3GPP IoT devices.
 | RFID | Ambient IoT | Existing IoT
Coverage | <10 m | 10m~30m (RF power); Up to 200m(other ambient power) | >=1000m
Power Source | RF power only | Various ambient power（RF sensitivity ~35dBm） | Conventional Battery
Techniques | Backscattering | Backscattering(x~10x uW)/Active transmitter（200~500 uW） Ultralow-power receiver （10x~100x uW） Enhanced power saving | OFDM Narrow bandwidth Relaxed processing eDRX PSM, etc.
Power Consumption | 1uw~10uw | <1mw | 100x mw
Device Cost (Relatively) | Low | Medium | High
Maintenance/operation cost | Need labor cost for operation | Maintenance-free and Automated operation | Automated operation but need to replace/recharge the battery

## Slide 6: Potential Ambient IoT architecture
  With direct mode, the network has limited coverage and it is suitable for dedicated deployment for verticals.
  With indirect mode, using relay node (e.g. intermediate node/ a UE), the coverage of ambient IoT can be significantly extended and it can support ambient IoT using the existing network deployment topologies.
  Many To-C applications can be enabled with indirect mode.
  Therefore, it is proposed to study to support both direct mode and indirect mode for ambient IoT in Rel-19.
Operation mode | Coverage | Device power consumption | Device complexity and cost | Data rate | Positioning | Speed
Direct mode | few 10 meters indoor; up to 200 meters outdoor; New base stations are needed | High | High | few kbps | Base station is positioning anchor | low
Indirect mode | few 100 meters or kilo meters by reusing existing infrastruture | Low because of A-IoT device is close to smart phone usually | Low due to low power consumption | few 10 kbps | smart phone is positioning anchor | Could be very high as long as relative speed to smart phone is low

## Slide 7: Active transmitter vs Backscatter
  Both devices type with backscatter and active transmitter has been discussed and agreed to be studied.
  It is beneficial to achieve ultra-low power consumption (e.g. several to tens of uW for uplink) for Ambient IoT devices with an backscatter but it will introduce self-interference issue for mono-static deployment (i.e. topologies 1/2/4 agreed in RAN study).
    Bio-static deployment topology (i.e. topologies 3 agreed in RAN study) can relieve the self-interference issue but it complicates the deployment
    The co-existence with existing 3GPP system also needs to be considered.
  It is also feasible to support ultra-low power active transmitter for ambient IoT device[1][2][3] . Although with slightly higher power consumption (e.g. 100x uW), it can significantly simplify the receiver implementation of the gNB or the Relay UE.
  Therefore, it is proposed to study both backscatter and active transmitter for ambient IoT device.

## Slide 8: Supported functionalities
  Based on the use case study in SA1[4], 4 important functionalities are required for ambient IoT:
    Inventory
    Sensor
    Positioning
    Actuator
  All the 4 functionalities are important. We propose to study to support all these functionalities in Rel-19.
    Ambien IoT positioning is discussed in our companion contribution[5] [6]
  If there shall be a priority, We propose the following priority:
    Inventory and positioning>Sensor>Actuator

## Slide 9: Security
  When support ambient IoT in 5G system, the network security shall be guaranteed.
  In addition, the user privacy needs to be protected for most of the identified use cases.
  On the other hand, it needs to consider the ultra-low complexity and ultra-low power constraint(e.g. peak power consumption less than 1mW) of ambient IoT devices.
  Therefore, it is proposed to study ambient IoT security mechanisms (e.g. Physical layer security) considering the ultra-low complexity and ultra-low power constraint(e.g. peak power consumption less than 1mW) of ambient IoT devices in Rel-19.

## Slide 10: Summary
  Based on the discussion, we proposed to study ambient IoT in Rel-19 and have the following proposals:
    Ambient IoT needs to be complementary to existing 3GPP IoT technologies and overlapping of the target market and the network/device capability with the existing 3GPP IoT technologies shall be avoided.
    Study both direct mode and indirect mode for ambient IoT in Rel-19.
    study both backscatter and active transmitter for ambient IoT device.
    Study to support all 4 identified functionalities(i.e. inventory, sensor, positioning and actuator) in Rel-19.
    study suitable ambient IoT security mechanisms (e.g. Physical layer security) considering the ultra-low complexity and ultra-low power constraint(e.g. peak power consumption less than 1mW) of ambient IoT devices in Rel-19.

## Slide 11: Reference
K. Tang et al., "A 75.3 pJ/b Ultra-Low Power MEMS-Based FSK Transmitter in ISM-915 MHz Band for Pico-IoT Applications," 2021 IEEE International Symposium on Circuits and Systems (ISCAS), 2021, pp. 1-4, doi: 10.1109/ISCAS51556.2021.9401715
M. S. Jahan, J. Langford and J. Holleman, "A low-power FSK/OOK transmitter for 915 MHz ISM band," 2015 IEEE Radio Frequency Integrated Circuits Symposium (RFIC), 2015, pp. 163-166, doi: 10.1109/RFIC.2015.7337730.
J. Bae and H. Yoo, "A low energy injection-locked FSK transceiver with frequency-to-amplitude conversion for body sensor applications," 2010 Symposium on VLSI Circuits, 2010, pp. 133-134, doi: 10.1109/VLSIC.2010.5560325.
S1-231333 TR 22.840v1.2.0 Study on Ambient power-enabled Internet of Things OPPO
RWS_230317 Positioning technologies for Rel-19 Ambient IoT OPPO
RWS_230316 Views on positioning enhancement in Rel-19 OPPO