## Slide 1
Initial views on Rel-19 RAN4
OTA topics
Source: CAICT
Document for: Discussion
Agenda Item: 6
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - 16, 2023
RWS-230359

## Slide 2: Background of NR MIMO OTA
From Rel-11 to Rel-18, 3GPP methodologies for measuring multi-antenna reception performance of UEs have been pursuing
test conditions more closely resembling the realistic channel environment, and
support for more advanced technologies/UE features/frequencies.
HSPA and LTE MIMO OTA
  A set of comparable methodologies were defined in TR 37.977.
  One of the objectives in the WID “the utilization of Variable Reference Channels and other-cell interference shall also be studied at a later stage”, however, is unfinished.
NR MIMO OTA
  In Rel-16, measurement methodologies were defined for FR1 and FR2 UEs in TR 38.827. One of the objectives in the SID “MIMO throughput under dynamic geometry environment”, however, is unfinished.
  In Rel-17, performance requirements for bands n41 and n78 were defined in TS 38.151.
  In Rel-18, the measurement methodologies and performance requirements are being enhanced.

## Slide 3: Potential NR MIMO OTA enhancements in Rel-19
Legacy MIMO OTA test plans only specified stationary channel models, i.e., the large scale channel characteristics in the test zone is fixed during testing.
Existing test plan only applicable to UEs with sizes less than 20cm, free-space scenarios, FR1 and FR2-1.
In Rel-18, enhancements for scenarios with body phantoms are being investigated, but are likely to be leftovers.
Potential Rel-19 objectives:
  Test methodology enhancement
    further optimization on test methodology (reuse the legacy system configuration as much as possible.)
      introduce “dynamic” channel models
      implement a future-proof quite/test zone size
    potential Rel-18 leftovers
      phantom-based test methodology
  MIMO OTA requirements
    FR1 and FR2 requirements for new bands based on operators' interest
    FR1 and FR2 unfinished bands in Rel-18 (if any)

## Slide 4: Potential FR1 TRP TRS enhancement in R19
For the leftovers of Rel-18, as well as some new important features, UE types can be further considered as part of new R19 WI.
Potential Rel-19 objectives：
TRP TRS requirement
  potential R18 leftovers
    any unfinished R18 bands for 1Tx
    PC2 requirement for 2Tx
  more FR1 bands for handheld UE based on operators’interest
  Redcap UE requirements
  PC1.5 requirement for 2Tx
  CA requirements
  Test methodology enhancement
    more UE types, e.g., XR, NTN UE...
    new phantoms
      new phantoms for XR
      new phantoms for wearable Redcap UE other than forearm phantom
    CA to support more UL/DL configurations
    futher optimization on test methodology
      2Tx test methodology
      other test time reduction solutions

## Slide 5: Potential FR2 OTA enhancement in R19
RAN4 is discussing the requirements for multi-Tx , the corresponding test method can be considered in Rel-19.
Potential Rel-19 objectives:
  Test methodology enhancement
    RF/RRM/Demod test methodology to support simultaneous transmission with multi-panel
    any leftovers on multi-Rx test methodology in Rel-18