## Slide 1
Huawei, HiSilicon
Network energy savings enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230364
Taipei, June 15 - 16, 2023

## Slide 2
Motivation for further network energy saving
Energy consumption composition according to SI
Dynamic power by power amplifier (PA) and part of TRX chain
Static power by baseband (BB) and part of TRX chain
    Depending on micro/light/deep sleep mode
R18 NES WI mainly focuses on UE-specific signals/channels
Spatial and power domain techniques are applicable for UE specific PDSCH only, as required by Rel-18 WID
Although a group common PDCCH is introduced for cell DTX/DRX, it does not affect common signals/channels (e.g. no impact on SSB as also required by Rel-18 WID)
Power
Reduced Pstatic as hardware evolves
Pdynamic for common signal/channel
t
Adaptation of common signals/channels are beneficial, as observed/concluded in Rel-18 NES SI, but only SSB-less for CA case is within Rel-18 NES WI
Techniques that enables reduced SIB/Paging etc. were extensively evaluated with benefits shown, however, were not included in Rel-18 WI scope due to limited TU
As the static power consumption decreases due to hardware efficiency improvements, reduction on dynamic power consumption can be critical. However, dynamic power due to common signals/channels is not fully resolved in Rel-18 WI.
R19 key observation: Dynamic power consumption of common signals/channels will become the bottleneck as the static power consumption decreases due to hardware efficiency improvements.
R19 proposal: Enable reduced transmission of common signals/channels for single/multi-carrier scenarios for further network energy saving.

## Slide 3
Further network energy saving: Common signal/channel adaption
Multi-carrier scenario: SIB1/paging-less for non-anchor cells, with SIB1/paging provided from an anchor cell
Anchor cell: Idle camping (SSB/SIB/Paging), broadcasting SIB/paging of non-anchor cell(s)
Non-anchor cell: SIB1/paging is not needed, while RACH can be transmitted
  SSB/DRS for sync or SSB-less (for applicable bands)
  UE: temporally DL sync to a non-anchor cell before RACH transmission, to avoid dual-cell sync issue
  Latency reduction compared to handover/CA procedures, or longer SIB1 periodicity
Single-carrier scenario: on-demand SSB/SIB1 triggered by UE WUS
UE WUS to wake up BS from dormancy state
  WUS configuration and transmission procedure
  Used for band(s) that have not been (largely) deployed, e.g., new band or FR2, etc.
  Longer camping and access delay compared to SIB1-less
  NES gain can be achieved when SSB/SIB1 is not transmitted (i.e., not triggered by UE WUS), typically in the light load cases
SIB1/paging-less
On-demand SSB/SIB1
NES gain for SIB1-less compared with baseline with different SIB1 periods

## Slide 4
Summary
R19 NES objectives: Focusing on common signal/channel reduction/adaptation for IDLE UE
SIB1/paging-less for multi-carrier non-CA scenario
  SIB1 from non-anchor cell(s) carried on anchor cell
  Paging is only transmitted on an anchor cell and omitted in non-anchor cell(s)
  Note: the above proposals can be considered regardless whether SSB or DRS are transmitted on the non-anchor cell(s)
On-demand SSB/SIB1 triggered by UE WUS
  UE WUS to wake up BS from dormancy
  WUS configuration and WUS transmission procedure
  Other NES schemes with smaller NES gain can be considered with low priority, if the spec impact is also marginal, e.g. longer periodicity for common signals/channels