## Slide 1: Multi-carrier enhancements in Rel-19
3GPP TSG RAN Release 19 workshop
Taipei, June 15-16, 2023
RWS-230366
Agenda Item: 5
Source: Lenovo
Document for: Discussion

## Slide 2: CA evolution in 3GPP
Same basic framework as LTE
Self-scheduling
Cross-carrier scheduling with same SCS
Type-1 HARQ-ACK CB
Type-2 HARQ-ACK CB
R15 NR
R16 NR
R17 NR
R18 NR
R19 NR
Cross-carrier scheduling with different SCS on scheduling cell and scheduled cell
FR1 only
Cross-carrier scheduling from SCell to PCell
DL 2-cell joint scheduling
Multi-cell joint scheduling
UL Tx switching
??
Newly introduced in LTE for increasing data rate
Self-scheduling
Cross-carrier scheduling
Single PUCCH on PCell for all scheduled DL cells
PUCCH format 2
PUCCH channel selection
R10 LTE
R11 LTE
R12 LTE
R13 LTE
R14 LTE
TDD inter-band CA with different UL/DL configurations on different cells
TDD-FDD CA
FDD-TDD CA
Dynamic TDD UL/DL configurations on different cells in CA
DL licensed-unlicensed CA
LAA
UL licensed-unlicensed CA
eLAA

## Slide 3: R18: Standardization outcome
In R18 multi-cell scheduling,
  Up to 4 cells can be co-scheduled by one DCI
  At most one PDSCH or PUSCH per scheduled cell
Many important issues are down-scoped in R18 due to limited TU
  Different SCS among co-scheduled cells
  Different carrier types (licensed/unlicensed, FR1/FR2/FR2-2) among co-scheduled cells
  More than one scheduling cell for each scheduled cell
  Simultaneous configuration of CBG-based transmission and multi-cell scheduling
  Simultaneous configuration of multi-PDSCH scheduling and multi-cell scheduling
  Simultaneous configuration of multi-PUSCH scheduling and multi-cell scheduling
  Enhancement of unlicensed spectrum
Two codewords can’t be supported in case of more than 2 cells scheduled by one DCI
Using a single DCI to schedule up to 4 cells with one PXSCH per cell

## Slide 4: R18: DCI size
Fields of DCI format 1_X | Single-cell (bits) | Field type | 2-cell (bits) | 3-cell (bits) | 4-cell (bits)
Identifier for DCI formats | 1 | Type-1A | 1 | 1 | 1
Indicator of co-scheduled cells | 3 | Type-1A | 3 | 3 | 3
BWP indicator | 2 | Type-1A | 2 | 2 | 2
FDRA (RA Type 0, RBG size 16) | 18 | Type-2 | 36 | 54 | 72
TDRA | 4 | Type-1B | 5 | 5 | 5
VRB-to-PRB mapping | 1 | Type-1A | 1 | 1 | 1
PRB bundling size indicator | 1 | Type-1A | 1 | 1 | 1
Rate matching indicator | 2 | Type-1B | 4 | 4 | 4
ZP CSI-RS trigger | 2 | Type-1B | 3 | 3 | 3
MCS for TB1 | 5 | Type-2 | 10 | 15 | 20
NDI for TB1 | 1 | Type-2 | 2 | 3 | 4
RV for TB1 | 2 | Type-2 | 4 | 6 | 8
MCS for TB2 (if configured) | 5 | Type-2 | 10 | 15 | 20
NDI for TB2 (if configured) | 1 | Type-2 | 2 | 3 | 4
RV for TB2 (if configured) | 2 | Type-2 | 4 | 6 | 8
HARQ process number | 4 | Type-2 | 8 | 12 | 16
DAI | 4 | Type-1A | 4 | 4 | 4
TPC for scheduled PUCCH | 2 | Type-1A | 2 | 2 | 2
PUCCH resource indicator | 3 | Type-1A | 3 | 3 | 3
HARQ timing indicator | 3 | Type-1A | 3 | 3 | 3
Antenna port(s) | 4 | Type-3 | 8 | 12 | 16
TCI | 3 | Type-1B | 4 | 4 | 4
SRS request | 2 | Type-1B | 4 | 4 | 4
SRS offset indicator | 2 | Type-1B | 3 | 3 | 3
DMRS sequence initialization | 1 | Type-1A | 1 | 1 | 1
Priority indicator | 1 | Type-1A | 1 | 1 | 1
ChannelAccess-CPext | 2 | Type-1A | 2 | 2 | 2
Total size excluding CRC | 72 |  | 132 | 174 | 216
Table 1. Size of DCI format 1-3 (4 cells scheduled and 275 PRBs assumed per cell)
Two codewords can’t be supported in case of more than 2 cells scheduled, which greatly degrades performance.
Below fields are not considered in Table 1.
One-shot HARQ-ACK request: 1 bit
Enhanced Type 3 codebook indicator: 1~3 bits
HARQ-ACK retransmission: 1 bit
Minimum applicable scheduling offset indicator: 1 bit
SCell dormancy indication: 0~5 bits
PDCCH monitoring adaptation indication: 0~2 bits
PUCCH Cell indicator: 1 bit
PDSCH group index: 1 bit
New feedback indicator: 0~2 bits
Number of requested groups: 1 bit
CBGTI: 2/4/6/8 bits

## Slide 5: R19: Two-stage DCI
Two-stage SCI is specified since R16 V2Xand further enhanced in R17/R18:
  1st-stage SCI on PSCCH for scheduling PSSCH and 2nd -stage SCI
  2nd-stage SCI on PSSCH for decoding PSSCH, indicating HARQ operation, and providing IUC info
If two-stage DCI is supported in R19,
  Total payload is split into two parts with each part not exceeding limitation of max 140 bits
  1st-stage DCI is transmitted in legacy DCI format for scheduling one of co-scheduled cells, providing common information for all co-scheduled cells, and information for decoding the 2nd-stage DCI
  2nd-stage DCI provides cell-specific scheduling information for each of remaining co-scheduled cells
  With two-stage DCI, below cases can be supported:
  up to 4 cells with max two CWs per cell can be co-scheduled
  up to 8 cells with max one CW per cell can be co-scheduled
  Combination of multi-PDSCH/PUSCH scheduling and multi-cell scheduling
  CBG-based transmission with multi-cell scheduling
Two-stage DCI scheduling up to 2 CWs per PDSCH per cell
Two-stage DCI scheduling with one or multiple PDSCHs per cell

## Slide 6: R19: Objectives
Study and specify two-stage DCI for providing larger payload size to support below cases:
  Max 4 cells co-scheduled by one DCI with up to 2 codewords per cell
  Max 8 cells co-scheduled by one DCI with up to 1 codeword per cell
  Max 4 cells co-scheduled by one DCI with up to 8 PDSCHs or PUSCHs per cell
  Optimize single-stage DCI size alignment procedure
Other potential enhancements
  Support of different SCS among co-scheduled cells
  Support of different carrier types (licensed/unlicensed, FR1/FR2/FR2-2) among co-scheduled cells
  Support more than one scheduling cell for each scheduled cell
  HARQ-ACK codebook enhancement to support simultaneous configuration of multi-PDSCH scheduling and multi-cell scheduling
  HARQ-ACK codebook enhancement to support simultaneous configuration of CBG-based transmission and multi-cell scheduling
  Enhancement of unlicensed spectrum

## Slide 7: Thanks
thanks