## Slide 1: 5G-MAG views on Media related topics for Rel-19 Radio Access Network (RAN)
5G MEDIA ACTION GROUP (5G-MAG)
www.5g-mag.com

## Slide 2: MEDIA + ICT + COLLABORATION
5G-MAG fosters collaboration and consensus towards the adoption of global Internet and 5G-based access technologies for Media.
These are our most recent ACTIVITIES and current AREAS OF WORK
As 3GPP Market Representation Partner, we:
  Inform the industry on technologies and features relevant for media
  Provide insight into specs towards development/implementation
  Foster industry engagement into applications and services
  Profile relevant standards to lower the entry barrier to complex technologies
  Support the 5G-MAG Reference Tools Development Programme
  Provide technical feedback to 3GPP and bring specifications to life

## Slide 3: 5G-MAG Reference Tools
5G-MAG is running the 5G-MAG Reference Tools Development Program
An OPEN PLATFORM to support the development of 3GPP media technologies
  Beyond the contributions announced under the Target 2023 roadmap, the successful progress allows us to announce the kick-off of an open-source XR Platform in the next few months.
We invite 3GPP members to join 5G-MAG and the 5G-MAG Reference Tools to add additional features and foster the 5G Media ecosystem
  https://developer.5g-mag.com

## Slide 4: Outline
The views towards 3GPP Release-19 work led by RAN are described in slides 5-7 covering 4 key topics (in no specific priority order) on:
  LTE-based 5G Broadcast & DTT coexistence
  LTE-based 5G Broadcast & Unicast coexistence
  XR & Metaverse enhancements
  MBS capacity enhancements
  MBS via NTN

## Slide 5: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead WG | SA dependencies | WG dependencies
1 | LTE-based 5G Broadcast & DTT coexistence | Due to regulatory constraints and lack of spectrum, there is at least interest in the US to deploy both Digital Terrestrial TV (DTT) ATSC 3.0 and 5G Broadcast in the same carrier. However, the frame structures of these two technologies are not compatible. Key objectives include: Definition of additional periodicity patterns for cell acquisition subframes to allow TDM operation between 5G broadcast and non-3GPP DTT (e.g., ATSC 3.0 and DVB-T2) frame structures. |  | RAN1 | None | None
2 | LTE-based 5G Broadcast & Unicast coexistence | Rel-18 RAN4 WI on “New bands and bandwidth allocation for 5G terrestrial broadcast - part 2” specifies bands and requirements for MBMS-dedicated cells. However, this WI does not address coexistence aspects for the reception of LTE-based 5G Broadcast and unicast in the same UE, which is a key requirement for the deployment of LTE-based 5G Broadcast services. Key objectives include: Base Station and/or UE requirements to allow the reception of LTE-based 5G Broadcast and unicast in the same UE. |  | RAN4 | None | None

## Slide 6: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead WG | SA dependencies | WG dependencies
3 | XR & Metaverse enhancements | Enhancements to optimise XR awareness, capacity, power saving and latency Key objectives include: Capacity enhancements RRM measurements and scheduling restrictions (measurement quality vs. latency) Carrier aggregation (capacity vs. power) High speed packetization CSI enhancements including CBG-based transmission Power saving Further DRX and PDCCH enhancements XR awareness Uplink application awareness to support for very high UE data rates Latency: Congestion-aware RAN (L4S in RAN) to help trim buffer lengths for latency-sensitive applications |  | RAN2 | SA2 | 

## Slide 7: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead WG | SA dependencies | WG dependencies
4 | MBS capacity enhancements | Advanced RAN techniques to further enhance spectral efficiency of 5G MBS Key objectives include: Study of non-orthogonal multiple access techniques to enhance the spectral efficiency of joint broadcast/multicast and unicast transmissions Broadcast/Multicast and Unicast Superposition Transmission (BMUST) and Rate-Splitting Multiple Access (RSMA) techniques |  | RAN1 | None | None
5 | MBS via NTN | Support of Multicast and Broadcast Services via NTN Key objectives include: Broadcast communication service Study NTN enhancements to support NGSO mobile base stations and broadcast to a specific geographical area addressing the discrepancy with beam footprints (e.g., satellite beams spanning over larger areas than the coverage of the targeted area of the broadcast service) Multicast communication service NTN enhancements to support multicast in connected mode in NGSO, addressing mobility issues including hand-over in particular NTN enhancements on the HARQ feedback/retransmission which can be applied to both PTP and PTM transmission NTN enhancements to support multicast over a downlink only NTN combined with a terrestrial network cell. Study the need for architectural enhancements for 5G multicast-broadcast services via NTN |  | RAN2 | SA2 | RAN1 RAN3

## Slide 8: Summary
In general, 5G-MAG supports work aimed at enhancing:
  Coverage (of services from all MNOs)
  Capacity (sufficient capacity both in High Density Demand areas and rural areas)
  Adoption (reducing barriers to uptake for consumers and MNOs -through widespread feature support, features that can be used across multiple services/verticals, cost reduction and a complete and supportive standards-based ecosystem, backwards compatibility)
  Environmental sustainability (through design, measurement and reducing impact)

## Slide 9: Thank you!
5G Media Action Group (5G-MAG)
www.5g-mag.com
  Activity Hub
  https://hub.5g-mag.com
  Developer Space
  https://developer.5g-mag.com
  Publications
  https://pub.5g-mag.com
  Academy
  https://academy.5g-mag.com
  Join our open communities Follow us