## Slide 1: Study on distributed AI for NG-RAN in Rel-19
June 15, 2023
RWS-230390
3GPP TSG RAN Release 19 workshop
Taipei, June 15-16, 2023
Agenda Item: 5
Source: Lenovo
Document for: Discussion

## Slide 2: Motivations
R18 AI for NG-RAN:
  focused on three use cases, i.e., load balancing, network energy saving, and mobility optimization;
  NOT support multi-vendor operability w.r.t. model training/transfer deployment;
  NOT support AI/ML capability at gNB DU;
  NOT support collaboration with CN.
A separate R19 SI can be helpful to address:
  Multi-vendor operability w.r.t model training/transfer/deployment, especially using distributed learning method;
  AI/ML capability at gNB DU;
  Collaboration with CN;
  Possible new use cases.

## Slide 3: Rel19 Distributed AI SI - Overview
Some studies can be carried out in R19 for Distributed AI for NG-RAN:
  Objective 1: Study network functionality and interface procedures in NG-RAN split architecture to support
    AI/ML training/inference at gNB-DU;
    gNB-CU and gNB-DU collaboration for AI/ML training/inference:
      AI/ML training at gNB-CU and inference at gNB-DU;
      Distributed/Federated training among gNB-CU and gNB-DU.
  Objective 2: Study network functionality and interface procedures between different NGRAN nodes to support
    Distributed/Federated training among NG-RAN nodes.
  Objective 3: Study integration and collaboration with 5GC to reach global optimization:
    Input/feedback from 5GC for model training/inference;
    Distributed/Federated training among NWDAF and NGRAN.
  Note: The following aspects can be studied when applicable in Objective 1, 2, 3:
    AI/ML model transfer
    Large size training data set transfer
  Objective 4: Study new use cases for NG-RAN (e.g., AI/ML for slicing, AI/ML for QoE, and other potential use cases) taking the outcome of R18 WI as baseline. [Note: Could also be Included in a separate AI for NG-RAN WI ]

## Slide 4: Rel19 Distributed AI SI (1)
Objective 1: Study network functionality and interface procedures in NG-RAN split architecture to support:
  AI/ML training/inference at gNB-DU;
  gNB-CU and gNB-DU collaboration for AI/ML training/inference:
      AI/ML training at gNB-CU and inference at gNB-DU;
      Distributed/Federated training among gNB-CU and gNB-DU.
CU
DU
DU
Training/Inference Input
gNB-CU/gNB-DU collaboration considering gNB-DU AI/ML capability
Inference output

## Slide 5: Rel19 Distributed AI SI (2)
Objective 2: Study network functionality and interface procedures between different NGRAN nodes to support:
  Distributed/Federated training among NGRAN nodes.
gNB
Model Training/Update Collaboration w/o Training Data exchange
Distributed/Federated training among NG RAN nodes
gNB
gNB

## Slide 6: Rel19 Distributed AI SI (3)
Objective 3: Study integration and collaboration with 5GC to reach global optimization:
  Input/feedback from 5GC for model training/inference;
  Distributed/Federated training among NWDAF and NGRAN.
NWDAF
gNB
gNB
CN
gNB
gNB
System performance
System performance
Model Training/Update
Model Performance Feedback
Feedback from CN to NG RAN
Distributed/Federated training among NWDAF and NG RAN

## Slide 7: Thanks
thanks