## Slide 1
0
2023-06
Further enhancements on network energy saving
CMCC
3GPP TSG RAN R19 Workshop RWS-230423
Taipei, June 15 - 16, 2023
Agenda Item: 5
Source: CMCC

## Slide 2
Backgroud
During R18 SI, NES techniques in time, frequency, spatial and power domain has been studied and evaluated, the description of candidate schemes, power saving gain and performance impact, and specification impact are analyzed and captured in TR38.864
Among the candidate schemes studied in SI, the following are further specified in R18 NES WI
  Time domain: Cell DTX/DRX
  Frequency domain: SSB-less SCell
  Spatial domain: Adaption of spatial elements
  Power domain: Adaption of transmission power for PDSCH
  Higher layer power saving schemes including prevent legacy UEs camping on NES cells, CHO procedure enhancement(s), paging enhancement, RRM/RF core requirements
Techniques specified in WI for time, frequency, spatial, power domain are mainly related to CONNECTED mode operation, impact to IDLE/INACTIVE UEs should be avoided
However, when there is no traffic or no UEs, the transmission of periodic common signals/channels prevent gNB going to deep sleep, enhancement to reduce transmisson of such channels while maintain in time response to UE is needed
Observation: Further enhancement to faciliate reduced transmisson of common signals/channels of gNB while maintain in time response to UE is needed

## Slide 3
Motivation of further NES for common signals/channels
Indoor office scenarios has the following characteristics
  The number of UEs served has obvious time varing characteristics. When there are no users, periodic broadcast signals brings a lot of meaningless energy consumption to the network
      Adaption of common signals/channels for power saving, gNB can adapt the periodicity or pattern of commmon signals/channels
  While even in non-working hours, UEs will occasionally enter the service area, the base station needs to be woken up in time
    Wake up signals from UE to wake up gNB for normal common signals/channels transmission
UE comes, it wakes up gNB
No UE, reduced common signals/chanels
Indoor office scenario
Proposal : Adaption of common signals/channels and UE waking up gNB are supported for R19 NES at least for indoor scenario

## Slide 4
Network power saving benefit
According to TR 38.864, the power saving performance of above two techniques has been studied during R18 SI are as following
Technique A-1 Adapting transmission/reception of common channels/signals “Technique A-1 adapts the transmission pattern (when applicable) of downlink common and broadcast signals, such as SSB/SI/paging/cell common PDCCH, and/or the transmission pattern/availability of uplink random access opportunities. Adaptation of the transmission pattern includes changes to periodicity, time resource locations, and omitting of specific signals/channels. The transmission pattern can be adapted semi-statically or dynamically.” | -4 sources show technique A-1-1 of simplified SSB without PBCH or with partial PBCH could achieve BS energy savings by 0.7%~30.49% in range, with no observed impact on UPT due to empty load. -9 sources show technique A-1-3 of statically adapting the periodicity of SSB longer than 20ms up to 1280ms (with current maximum periodicity being 160ms) could achieve BS energy savings by 0.9%~84.8% in range, meanwhile when traffic occurs and load increases, the UPT significantly decreases and the latency/access delay/UE power consumption increases proportionally as the periodicity of SSB/SIB increases compared to a corresponding baseline
Technique A-3 UE wake up signal (WUS) for gNB “Technique A-3 enables the UE to send an uplink wake-up signal to request transitioning of a cell from no or reduced transmission/reception activity to active transmission or reception of a channel/signal. The technique can be applied to UEs in one or more RRC states. The UE wake up signal (WUS) by technique A-3-1 may be used to trigger the SSB/SIB transmission. It can be used to trigger SSB/SIB1 transmissions with technique A-5. It can also be used to trigger gNB to wake up with technique A-4. | -5 sources show technique A-3-1 of UE WUS triggering gNB for SSB/SIB/RACH, with the assumption of ideal detection of UE WUS, could achieve BS energy savings by 6.2%~80.7% in range with UPT loss by 0%~24.2%, while 1 source shows technique A-3-2 of UE WUS triggering gNB to wake up in case of uplink traffic arrival could achieve BS energy savings by 25.7%~93% in range, with latency reduction of 0%~45.5% depending on the SR periodicity assumed in the baseline, -Note technique A-3-2 of UE WUS triggering gNB to wake up in case of uplink traffic arrival assumes that gNB can detect WUS during sleep state.

## Slide 5
Potential objectives
Specify adaptation of common channels/signals
  At least adaption of SSB, including simplified SSB without PBCH, and SSB periodicity adaption
Specify enhancement on waking up a cell from no or reduced transmission/reception activity to active transmission or reception of channels/signals including SSB/SIB1
  Design and configuration of wake-up signal/channel
  Conditions for triggering WUS
  Mechanisms for DL synchronization and UE measurements needed prior to WUS transmission
  UE behavior/procedure after transmitting WUS
  Mechanism on how the UE can be informed about cell activity or lack of activity

## Slide 6
Thank you!