## Slide 1
0
Study on UE collaboration in R19
3GPP TSG RAN R19 Workshop RWS-230425
Taipei, Jun. 15th-16th, 2023
CMCC
2023-06

## Slide 2
Scenarios for UE backup
  To ensure various scenarios which requires different manners of UE co-ordiantion via a quasi-unified scheme, including synchronization and coordination for multi-flow of single UE/multiple UEs, and support of high reliability of data delivery for URLLC services:
  One important objective of 5G is to enable connected industries, where the scenarios are
    Motion control
    Control-to-control communication for industrial controller
    High data rate video for monitoring/ diagnostics
  This scenarios prevalently exist in
    Factory automation
    Transport industry
    Electrical power distribution automotive
Scenarios
PLC
Freight Forwarding
AGV
  To ensure various scenarios which requires different manners of UE co-ordiantion via a quasi-unified scheme, including synchronization and coordination for multi-flow of single UE/multiple UEs, and support of high reliability of data delivery for URLLC services

## Slide 3
Use Cases
  For example, terminal 1 and terminal 2 are deployed as real-time backup to each other
    The UEs can determine whether to take over or start/activate the data/signalling transmitted/received by associated UE for backup
      Depending on the associated terminal’s state
        i.e. whether the data/signalling can be still successfully received by the associated terminal or not
    Under normal circumstances, terminal 1 and terminal 2 are responsible for different services respectively
    If the data/signalling can not be successfully received by the terminal 1, then the subsequent associated terminal 2’s action is that the terminal2 is to take over or start/activate the service(s) of the terminal1 declaring in abnormal state
  In this case, how to ensure the minimal UP interruption and rapid completion of data forwarding between terminals and reduce the transmission overhead will become an issue to be addressed
Scenarios
Real time multiple-UE backup in normal case
Real time multiple-UE backup in abnormal case

## Slide 4
Scenarios for multi-modalities
  New use cases/scenarios, e.g., the multi-modality environment, multiple UEs collaborate to constructively conduct a task poses new requirements on the 5G network on multi-UE coordination which requires coordinated parallel transmission of multiple modality representations on UE device(s).
  Multiple modalities can be transmitted at the same time to multiple application servers for further processing in a coordinated manner, in terms of QoS coordination, traffic synchronization, etc.
  Additional use cases for Multi-modality can also be found in [TR 22.847] and include:
    Immersive Multi-modal Virtual Reality application
    Remote control robot,
    Immersive VR games
    Haptic feedback for a personal exclusion zone in dangerous remote environments
    Live Event Selective Immersion
Scenarios
  Mobile Metaverse for Immersive ; Gaming and Live Shows [TR22.856]

## Slide 5
Motivations
  To ensure various scenarios which requires different manners of UE co-ordiantion via a quasi-unified scheme, including synchronization and coordination for multi-flow of single UE/multiple UEs, and support of high reliability of data delivery for URLLC services:
    In current URLLC mechanism, RAN or the UE always transmits duplication data through radio links to the target side simultaneously or within the delay-tolerant time range; However, the issues are as follows
      Duplication transmission is not resource-efficient in air interface for network capability
      It face the challenge of failing to meet the high reliability depends on the successful reception just relying on only one terminal in real scenarios
    Therefore, actually, more than one terminal is deployed and utilized to receive repetitive content to ensure the reliability as backup,resulting in high cost of existing backup mechanism for high reliability
        e.g. battery consumption, radio resource, transport resource, processing resource and redundant signalling/data overhead
    For XR, in a resource restricted environment, it is hard to guarantee that the multi-modality services can always acquire all the inputs with the requested QoS:
      Hence, when one target QoS of one UE device can’t be guaranteed, the QoS of other UE devices will also be impacted or adjusted.
      Thus, the 5G system shall support a mechanism for coordination QoS for flows of multiple UEs associated with an application.
Motivations

## Slide 6
  Quasi-unified scheme for Collaborative UEs
  Quasi-unified scheme for Collaborative UEs
Various Scenarios
Various
co-ordination manners among UEs
UE service switching
UE service
Sync.
UE backup
Enable fast service switching across UEs for URLLC senarios to fulfil super high reliability and low latency
Multi-modality
Synchronization and coordination for multi-flow of single UE/multiple UEs
CN
RAN
Collaborative UEs
Shared Rdio Resource
Prior to Switching
After Switching
unicast Rdio Resource
Prior to Switching
After Switching

## Slide 7
Potential Objectives
To investigate the mechanism of different manners of UE co-ordiantion via a quasi-unified scheme
    Study the use cases and benefits of UE co-ordiantion, e.g.,multi-modalities, real-time multiple-UE backup [RAN2, RAN3]
      UE device(s) associated with the same end user under the same/different cell(s)
      real-time multiple-UE backup
    Study necessary procedures and/or information to support for UE co-ordiantion of data/signalling delivery and reception without data disorder or data duplication [RAN1,RAN2, RAN3]
    Coordinated/Group scheduling and synchronized transmission for multiple UEs [RAN1, RAN2]
    Study the support for basic mobility with service continuity [RAN2, RAN3]
Potential Objectives

## Slide 8
THANK YOU !