## Slide 1
0
CMCC
2023-06
NR NTN evolution in R19
3GPP TSG RAN R19 Workshop RWS-230428
Taipei, Jun. 15th-16th, 2023

## Slide 2
Motivations
In R17&R18, only transparent payload is considered. However, regenerative architecture can bring the following benefits:
  propagation delay reduction in Uu
  data communication could use ISL(inter-satellite link), which is even applied to less NTN Gateway scenarios
  regenerative architecture networking is more flexible and easier forward compatibility
Regenerative payload with ISL
Support regenerative payload to reduce propagation delay
  study Full gNB on board
  study only DU on board （ be de-prioritize）
Potential Objectives
Field of view of the satellite (or UAS platform)
Satellite
(or UAS platform)
Satellite
(or UAS platform)
Feeder link
(mandatory if no ISL)
Feeder link
Fig. Non-terrestrial network typical scenario and network architecture with regenerative payload

## Slide 3
Motivations
Rel-18 only focus on UL channel coverage enancements for NTN scenarios to support commercial smartphones services
Considering the NTN characteristics including large propagation delay and potential limited DL transmit power, potential issues and enhancements of DL coverage should be further studied and identified.
DL coverage enhancement
Study NR NTN-specific DL coverage enhancements
  Coverage performance evaluation:
    It should be discussed whether to reuse Rel-18 evaluation results to identify the coverage gap of channels, or additional evaluations are needed
      If additional evaluations are needed, identify simulation assumptions and performance requirements of the target services
    Identify the DL coverage limited physical channels and the gap of the coverage
  Study NTN-specific enhancements for the relevant DL channels
    DL beam enhancements, repetition, and others
Potential Objectives
During Rel-18 NTN, DL coverage performance of PDSCH (for VoIP, low data rate, Msg2, Msg4), PDCCH, SSB have been evaluated.
  DL coverage limitations was observed during the evaluations, e.g. Msg4 PDSCH (2.2~2.8dB gap) in the LEO scenarios, PDCCH without repetition (1.9~2.6dB gap) in the NLOS scenarios for LEO.
DL coverage will be significantly restricted if the satellite transmission power is limited.
Potential issues

## Slide 4
Motivations
The satellite (or UAS platform) typically generates several beams over a given service area：
  Considering a small difference in signal strength between two beams in a region of overlap, a new triggering for beam switching can be studied
  Considering the large cell size of NTN, many devices may be served within a single beam. Depending on constellation assumptions (e.g. propagation delay and satellite speed) and UE density, many UEs may need to perform beam switching at a given time, a possible group beam switching command can be studied to reduce signalling overhead
Considerging the coverage area of NTN is much larger than that of TN, resulting in the beam number within one satellite will be increased, while not all area can be coverred simulateneously due to the limitation of gNB transmission power
Beam Management in NTN
    Support beam management and BWP operation enhancement
  Study beam switching enhancement, e.g. location/time-based (group) beam switching
  Considering both future proof and signalling overhead, study on the SSB number extension
Potential Objectives
Fig. a) same PCI for several satellite beams and b) one PCI per satellite beam

## Slide 5
Motivations
In R18, PCI unchanged for hard satellite switching in quasi-earth fixed cell case has been supported.
While for soft satellite switching in quasi-earth fixed cell case, it is not pursued in R18 due to limited time
In addition, considering the HO case of TN to NTN which less touched in R17/R18, mobility enhancements for this need to be further discussed
Mobility enhancements
Mobility enhancements
  study PCI unchanged for soft satellite switching in quasi-earth fixed cell case
  study mobility enhancements for some new cases, e.g., TN-NTN mobility with QoS adaptation(e.g. PDB relax due to long RTT)
Potential Objectives

## Slide 6
Motivations
In R18, regarding network verified UE location, we focus on single satellite and existing LCS framework for verification.
For R19, we could further consider multiple satellites case to purse more accurate UE positioning calculation considering the positioning inaccuracy issue due to long propagation delay in single satellite case of NTN system.
Network verified UE location enhancements
Support network verified UE location enhancements
  study multiple satellites for network verified UE location (e.g., sattelite-specific assistant information to LMF)
Potential Objectives

## Slide 7
THANK YOU !