## Slide 1
0
2023-06
Further Enhancements of SONMDT in Rel-19
CMCC
3GPP TSG RAN R19 Workshop RWS-230429
Taipei, Jun. 15th-16th, 2023

## Slide 2
General Introduction
Rel-18 SON/MDT
  SHR and SPR
  MRO for CPC and CPA, the fast MCG recovery, inter-system handover for voice fallback
  RACH Enhancements, including RACH partitioning, RACH report retrieval and SN RACH report in MR-DC
  SON/MDT Enhancements for Non-Public Networks, NR-U
Potential objectives for Rel-19 data collection for SON/MDT and AI/ML
  Support the new use cases based on the new features introduced in Rel-17/Rel-18
    SON/MDT enhancements for R18 NR mobility enhancements, Network Slicing, MR-DC (SCG activate/deactivate), MBS, ...
  Specify data collection mechanism(s) for the use cases indentified in AI/ML for air interface and NG-RAN
    SON/MDT enhancements based on the legacy framework
    RAN-initiated data collection
    New entity introduced for AI/ML to meet the requirements of computing capability for model trainning and storage in NG-RAN
  Specify the leftover issues of Rel-18 SON/MDT, if any

## Slide 3
High priority cases in Rel-19 SON/MDT
High priority cases for SON/MDT enhancements considered for the scope of Rel-19 WI
L1/L2 triggered mobility (LTM)
Specify UE reporting for the root cause analysis of LTM failure, near failure case, too late LTM, too early LTM and LTM to wrong cell for L1/L2 mobility optimization
Network Slicing
Specify UE reporting for slice unavailablity or interruption, while UE still in the coverage of radio signalling, which can be used by the operator for network planning of slice deployment
MR-DC
Enhance UE Mobility information to identify SCG activate/deactivate introduced in Rel-17
SDT
Enhance SON to allow SDT failure analysis and configuration optimization

## Slide 4
Rel-19 SON/MDT Enhancements WI Proposal
  Support of the new use cases for SON/MDT Enhancement
  Rel-18 LTM
  Network Slicing
  MR-DC (SCG activate/deactivate)
  MBS, UAV, XR, Sidelink Relay (if needed)
  Support of the data collection mechanism(s) for AI/ML
  SON/MDT enhancements based on the legacy framework
  RAN-initiated data collection
  New entity introduced for AI/ML
  Support of the leftovers in Rel-18 SON/MDT
Data Collection
Model Training
Management
Inference
Training Data
Monitoring Data
Inference Data
Model transfer/
delivery request
Monitoring Output
Performance feedback/
Retraining request
Model selection/
(de)activation/
switching/
fallback
Model Storage
Trained/updated Model
Model transfer/delivery

## Slide 5
Thank you!