## Slide 1
0
Views on Ambient IoT
CMCC
2023-06
3GPP TSG RAN R19 Workshop RWS-230433
Taipei, Jun. 15th-16th, 2023

## Slide 2
Background and general observations
Use case for R19 SI
Device categories for R19 SI
Frequency band and positioning
RAN topologies
Work plan for Rel-19
Content

## Slide 3
Background and general observations
Background for RAN SI
RAN level SI has studied on the following key topics and all captured in TR 38.848 for further study:
  4 representative use cases:
    Inventory; sensors; positioning; command
  3 categories of devices:
    Device A: Passive device, backscattering transmission w/o energy storage
    Device B: Semi-passive device, backscattering transmission with energy storage
    Device C: Active device, equipped with independent signal generation
  4 RAN connectivity topologies:
    Topology 1: BS ↔ Ambient IoT device
    Topology 2: BS ↔ intermediate node ↔ Ambient IoT device
    Topology 3: BS ↔ assisting node ↔ Ambient IoT device ↔ BS
    Topology 4: UE ↔ Ambient IoT device
General observations
A follow up WG SI is expected to start in Rel-19.
If WG will study on all the above 4 use cases, 3 categories of devices and 4 topologies, the evaluation and study would take at least 18 month.
However, it is doubted that whether we need to work on such a huge scope at the first release, or only concentrate on the most basic and commonality subset of the scope.
By focusing on only basic subset of the above scope, although still challenging, it would be possible to finish SI and WI in Rel-19. The benefit is to meet the vertical customers’ requirement in a faster way at 2025Q4.

## Slide 4
Ambient IoT use case
Use case category | Use Cases identified in TR 22.840 by SA1 | Max E2E latency | Communication Range | Positioning Accuracy | Data Rate | Message Size | Device density | Device speed
inventory | 1; 2; 5; 7; 16; 21; 24; 27 | ~1s | 30 m (indoor) | 3 m, 90% | <1000 bits/s | <256 bit | 1.5 million per km2 | < 6 km/h
sensor | 3; 6; 11; 13; 15; 18; 19; 20; 22; 23; 24; 25; 26 | 1~30s | 50 m (indoor), 200 m(outdoor) | NA | <1000 bits/s | <100 bytes | 1000 per km2 | Static
Positioning | 2; 4; 7; 8; 9; 10; 12; 14; 16; 24; 27 | 1~10s | 50 m (indoor), 200 m(outdoor) | 1~3 m, 90% | <1000 bits/s | 256 bits | 1000 per km2 | 5 km/h (indoor) 20 km/h (outdoor)
Activator/command | 17; 28 | NA | NA | NA | NA | NA | NA | NA
Use cases
Whether to include all the 4 use cases into R19 WG SI?
  TR 38.848 captured the following representative use cases: Inventory; sensors; positioning; activator.
Observation: Inventory and sensor use case share similar requirements except message size, while positioning requires specific design on L1/L2 signaling and architecture
Proposal 1: Similar as taking eMBB as 5G design baseline, use case of inventory can be considered as basic use case for ambient IoT design. The design can compatiable with sensor and activator, while positioning use cases are considered as technical enhancement on top of baseline.

## Slide 5
Ambient IoT Device categories
Device categories
RAN SI studied on the following 3 categories of devices:
  Device A: Passive device, backscattering transmission w/o energy storage
  Device B: Semi-passive device, backscattering transmission with energy storage
  Device C: Active device, equipped with independent signal generation
 | Device A/B Passive/Semi-passive device | Device C Active device
Waveform/frame structure/line code | Yes | Yes
Modulation | ASK/FSK/BPSK | ASK/FSK/BPSK/QPSK
Channel coding | No or simple coding | Yes
Duplexing mode | Full duplex at reader, half duplex at device | FDD at both reader and device
Periodic synchronization signaling | No | Yes
Broadcast channel | No | Yes
PHY DL/UL shared channel | Yes | Yes
L2/L3 procedures | Yes | Yes
Potential WG standardization work comparison

## Slide 6
Design options for passive and active device based on potential WG work in previous slide
Option 1: Take passive device as basic functionality, semi-passive and active device as enhancement of passive. The design is reused as much as possible.
Option 2: Parallel and independent design between passive and active device, e.g., to support higher power consumption and capability of active device.
Observations:
Option 1 would be possible to fit in R19 SI+WI, if we only focus on passive device design. While option 2 would require 18 months for study.
If active device is to be studied in Rel-19, it should be limited to reuse the basic design of passive device as much as possible, at least for PHY UL/DL shared channel and L2/3 procedures.
To minimize the study and standardization work, the first release can focus on the basic and common part for passive device and active device.
Proposal 2:
  Passive device can be taken as baseline for Rel-19 device design.
  If active device will be added for the SI and WI in Rel-19, the air interface design of passive device should be reused as much as possible for active device, e.g., PHY UL/DL shared channel, L2/3 procedures…, while still allow specific design for passive device to support extreme low power, and for active device to support coverage enhancement.
Device categories
Ambient IoT Device categories

## Slide 7
Ambient IoT：Frequency band and positioning
Which bands should be considered/prioritized in WG level SI: licensed FDD, licensed TDD, unlicensed?
Observation:
  Unlicensed operation would require more study and normative work.
  Since licensed FDD band are lower frequency than licensed TDD band, FDD would be beneficial from coverage point of view.
Proposal 3:
  High priority for low frequency, e.g., licensed FDD
  Coverage, interference need to be considered
Candidate positioning method for SI evaluation, e.g., RSRP, phase difference, AOA, TOA/TDOA
Proposal 4: Rel-19 SI+WI focus firstly on the basic function of Ambient IoT, while positioning can be taken as enhancement feature for further release.
Frequency
Positioning

## Slide 8
Ambient IoT：RAN topologies
Topology 1
Topology 2
Topology 3a with downlink assistance
Topology 3b with uplink assistance
Topology 4
TR 38.848 captured the following 5 topologies, Whether all the RAN topologies will be included in R19 WG SI?
Proposal 5: Design a unified ambient-link interface applicable for topology 1 & 2, which guarantees the ambient IoT device can access to either gNB or intermediate node. Other topologies are de-prioritized in Rel-19.
Topologies

## Slide 9
Work plan
SA1
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Q1
Q2
Q3
Q4
Rel-18
R18 L1 Start
R18 R1
Func. Freeze
R18 R2/3/4
Func. Freeze
R18 ASN.1
Freeze
Rel-19
Q1
Q2
Q3
R19 R2/3/4
Func. Freeze
R19 R1
Func. Freeze
2023.9 R19 L1 Start
SA1 R19 SI: Study on Ambient power-enabled Internet of Things
Start@SA1#97
R18 A-IoT RAN level SI
R19 A-IoT SA2 SI
A-IoT SA2 WI
RAN
SA2
R19 A-IoT RAN1/2/3/4 SI
RAN WG
Complete before Jun 2023
A-IoT RAN1/2/3/4 WI
2022
2023
2024
Approved@RAN#97
TBD
TBD
2025
Option 1: 18 month SI in Rel-19. To study all the 4 key use cases, 3 categories and topology 1&2.
Option 2: 9 month SI + 9 month WI in Rel-19. Focus only on the common and basic functions for passive device. The benefit is to meet the urgent market requirement at 2025.
  Proposal 6: We propose to have a 9 month SI + 9 month WI in Rel-19, with such scope：
      focus on the basic and common design for inventory use case, passive device and common ambient-link air interface for topology 1&2
      If active device is considered into the scope, it reuses design of passive device as much as possible

## Slide 10
Ambient IoT-Potential Objectives
Identify evaluation methodology and KPIs based on RAN design target [RAN1]
  Simulation parameters used to evaluate physical layer designs, link budget template for coverage evaluation
Study on the physical layer aspects, focusing on the basic and common design for inventory use case, passive device and common ambient-link air interface for topology 1&2, including [RAN1]
  Fundamental physical layer signal structure including waveform, frame structure, line/channel coding, (de)modulation, etc.
  Physical signal and channel design including T/F synchronization/tracking, physical unplink and downlink channel
Study on L2/L3 control plane and user plane for passive device, including
  Identify the minimum CP functions, e.g., access/collision control, paging, security, mobility management[RAN2]
  Identify the minimum UP protocol layer and procedures, e.g., RLC/PDCP-less protocol, random access, packet structure[RAN2]
Study on the RAN architecture, including either gNB or UE act as reader, with/without CN connection [RAN3]
Coexistence with UEs and infrastructure with existing 3GPP technologies, e.g., LTE, NR, NB-IoT [RAN1/RAN4]
Study on the spectrum for Ambient-IoT [RAN4]

## Slide 11
Thank you!