## Slide 1: Views on Release 19 RAN content
Source: Vodafone
Agenda Item 4
RWS-230437
3GPP TSG RAN Rel-19 workshop
June 15-16, 2023

## Slide 2
Topic areas for Release 19
Potential new revenue areas
Performance Improvements for deployed features
Cost reduction techniques
Topics to pause while waiting for them to gain market traction
Thoughts on 6G

## Slide 3
Potential new revenue areas for 3GPP with Release 19 work:
Ambient IoT
  use conclusions of Rel 18 RAN study for Rel 19 SID and Rel 19 WID
Sensing/radar
  RAN and SA work to enable use of NR base stations for e.g. drone detection; vehicle detection; and indoor intruder detection.
Timing as a service in LTE
  As many parts of the world (e.g. Africa) do not have NR coverage, expand the Rel 18 functionality to include LTE.

## Slide 4
Release 19 Improvements
NR uplink coverage and capacity
  Mitigate the impact of regulation of 4 down / 1 up TDD split by e.g. sub band full duplex
Extend L1/L2 mobility improvements to inter-site [i.e. inter-CU] cases
UE battery saving. Specify Wake Up Signal/Receiver for
  NR
  NB-IoT (to enable NB-IoT to out-perform rather than just match LORA-WAN)
Continue to enhance MIMO
AI/ML both for PHY layer and RAN
Further improvements for QoE feedback
RAN functionality for SA3 led work on ‘quantum safe’, 256 bit algorithms
****end **********
Proposal: 3GPP should

## Slide 5
Cost reduction work for Release 19
Network energy saving for cells with high load
  Rel 18 focussed on low/medium loaded cells, but
  most gNB/eNB sites have multiple frequency bands (i.e. cells) per sector; and
  as load on the sector decreases, cells are turned off; so
  the remaining cells are then heavily loaded. -> Energy saving on the cells is important!
Specify some network energy saving techniques studied but not specified in Rel 18
Study use of AI/ML techniques for g/eNB energy saving

## Slide 6
Topics for 3GPP to pause work while waiting for them to gain market traction
Broadcast /Multicast
Sidelink
Relays
IAB
Possibly NTN

## Slide 7
6G
A rush to 6G is likely to divert network investments away from the wider rollout of 5G (to serve more customers and machines) towards small, flagship, 6G coverage areas (that benefit few customers)
Rapid 6G timeline diverts R&D investments from optimising 5G equipment (to benefit end customers by reducing cost; improving efficiency; etc) towards IPR that might not benefit customers (c.f. relative cost of NR capable handset compared to LTE handset)
In contrast to 3G, 4G & 5G there is no new, wider, spectrum band available that needs the specification of a new radio technology.
No R&D reports of step changes in radio performance.
 It seems too early to start 3GPP work towards a new 6G radio technology

## Slide 8: Thank you