## Slide 1
RWS-230440
Views on Enhanced Network Energy Saving
5G-Advanced Evolution: Rel-19
  —
  3GPP RAN Release 19 Workshop, 15th – 16th June 2023, Taipei

## Slide 2: Vision for Enhanced Network Energy Saving
Low power consumption with dynamic adaptation by default
Today
      Network designed for high capacity operation as default  implies high energy consumption
        Energy consumption is inelastic to load
      Basic NES techniques to opportunistically reduce energy consumption
Future
      Mobile Networks consume low power consumption by default and can quickly ramp up and down capacity as needed (on millisecond or second range)
        Lead to longer periods of time in energy saving state
Energy Saving
High Consumption (default)
80% of time
Load
High load
Energy Consumption
20% of time
Energy Saving (default)
High Consumption
80% of time
Energy
consumption
20% of time
Slow
adaptation
Fast
adaptation
Time (days)
Sat
Sun
Mon
Tue
Wed
Thu
Fri
Time (days)
Sat
Sun
Mon
Tue
Wed
Thu
Fri
No load
Energy Consumption
Load

## Slide 3: Views on Enhanced Network Energy Saving
NES still has a long road ahead
Overview
      Rel-18 NES is an important step, but by far not enough to guarantee 5G NR future in terms of sustainability and reducing energy costs (Capex)
      In Rel-18 only few techniques were selected for standardization due to lack of time  there is still an immense untapped potential in techniques (see TR 38.864)
        Techniques providing largest energy savings (common signals adaptations) are not yet standardized
Motivation
      The long term success of 5G NR depends on keeping costs and environmental impacts under control. The only way to sustainably meet the growing traffic demand is to further reduce the energy consumption of 5G networks
Potential Solution(s)
      Adaptations of common signals:
        Cell Wake-up Signal for triggering SSB on demand
        Dynamically changing SSB/SIB-1/RACH period
      Extension of Cell DTX/DRX to Idle/Inactive
      Further enhancements of Spatial and Power Domain Adaptations

## Slide 4: Role of Common Signals in Network Energy Consumption
Why adaptation of common signals is so important for Network Energy Savings (NES)?
  At zero and low loads transmission of common signals consume significant power. Only with significant time between transmissions/reception the gNB can reach efficient energy states (light or deep sleep)
    Even at zero load the gNB needs to periodically wake-up to:
      Transmit SSB
      Transmit SIB-1
      (Eventually) transmit paging
      Receive RACH
Active (TX/RX)
Micro sleep (no TX/RX)
Light sleep
Deep sleep
Time
Power
Micro sleep
Active
Light sleep
Large enough gaps are needed for best energy savings
Deep sleep

## Slide 5: Adaptive SSB/SIB-1/RACH Period
Long periods by default
Dynamic SSB/SIB-1/RACH period adaptation
      Dynamic signals adaptation can save significant energy, specially if long periods can be used at zero/low loads
      A long period can be used by default and Rel-19+ UEs can support adaptation to more frequent common signals
        Legacy UEs can be served in another frequency (with more frequent SSBs) if needed  Same as for SSB-less or SIB-less solution, but with much simpler implementation, that is backward compatible
Time
Power
Micro sleep
Active
Light sleep
Deep sleep
20 ms period
High power consumption
160 ms period
Very low consumption

## Slide 6: Wake Up Support for Network
Why?
Cell Wake-Up Signal
      Using a Cell Wake-Up Signal (C-WUS) to trigger SSB (and other common signals) on-demand is one of the most promising NES techniques to significantly save energy (see TR 38.864)
      Possible designs
        Designated time/frequency/code for C-WUS within existing frame for receiving C-WUS
        Using a low power receiver at gNBs  main advantage is that the low power receiver can be always on, avoiding any access delay
Time
Power
Micro sleep
Active
Light sleep
Deep sleep
Legacy SSB - 20 ms period
High power consumption
SSB on-demand
Extremely low consumption
C-WUS

## Slide 7: What else is Needed to Reduce Common Signals?
Not only energy saving techniques, but also mitigation of negative impacts
TR 38.864 also concluded:
        “It is recommended that the normative phase includes not only energy saving techniques (the necessary enhancements would need to be further identified during the normative phase) but also the mitigation of their impacts when network applies network energy savings technique(s).”
  Main impacts discussed and identified during the study item:
      Initial Cell Selection duration grows proportional to SSB interval  can be mitigated with improved ICS
      Random access delay grows proportional to SSB interval  can be mitigated with low power wake-up receiver at gNB
      UE power consumption pre-paging increased with larger SSB interval  can be mitigated with denser pre-paging RS
      Measurement performance  to be studied by RAN 4
Proposal: In Rel-19 standardize techniques to mitigate the impacts of energy saving on initial cell selection/discovery, UE power consumption (paging), measurement performance

## Slide 8: Idle/Inactive Cell DTX/DRX
Overview
      In order to keep a limited scope, Rel-18 Cell DTX/DRX had the following note: “The impact to IDLE/INACTIVE UEs due to the above enhancement should be avoided.”
        This restriction also means a limited energy saving
      Rel-19 can extend Cell DTX/DRX to Idle/Inactive
        Cell DTX/DRX in Idle/Inactive should work in tandem with common signals adaptation
          Allow SSB/SIB/RACH and traffic channels to be concentrated in time, with same periodicity
        Preferably the same mechanism should be used to activate/de-activate
      Rel-19 should include improvements to Cell Search / Initial Access considering Idle/Inactive Cell DTX/DRX

## Slide 9: Enhancements on Spatial and Power Domain Adaptations
Release 18 WI on spatial and power domain adaptations for NES
      Ongoing approach in the WI for spatial domain adaptations
        At least support a baseline, where enabling UEs to measure CSI corresponding to multiple spatial domains patterns (subsets of available spatial elements at gNB) and to report them to the gNB
        Enhancements to the baseline, e.g. reduction of CSI reporting overhead and UE complexity, are not precluded
          It may happen that some beneficial enhancements are not specified due to lack of time
What would be left for Release 19?
      Important enhancements to the baseline approach for spatial and power domain adaptations that may not be finalized by the Release 18 WI (due to lack of time) can be revisited in Release 19
        Efficient ways to reduce overhead of reporting multiple CSI(s), e.g. enabling UEs to select which CSI(s) are reported

## Slide 10: Rel-19 Access Control for NES
Barring / Selection / Re-Selection and Priorities
Release 18 Access Control for NES
      Release 18 networks will bar legacy UEs (Rel-15/16/17)
Why Access Control needs to be revisited in Release 19?
      Release 19 will need again to define Barring and access priorities to bar legacy UEs including Rel-18 UEs
      Features which are needed (common signals adaptation, Idle/Inactive Cell DTX/DRX) will affect the legacy UE ability to camp, obtain system information and perform initial access
        Example: A legacy UE will not be able to transmit C-WUS in a cell which only transmits SSB on demand after receiving C-WUS
      Note: this need will rise again on every release with NES features.
      3GPP should avoid ad-hoc solutions every release: new barring on every release with NES features will lead to unacceptable complexity over time
      A forward-compatible solution should be defined which:
        Minimizes overhead
        Minimizes cell search and initial access delay  a UE can quickly evaluate barring (as originally designed in Rel-15)
        Enables the definition of priorities which allow operators to steer the traffic for UEs with different capabilities to appropriate cells