## Slide 1: Views on Integrated Communication and Sensing for Rel-19
AT&T
June 2023
RWS-230472

## Slide 2: Background and Motivation
  Integrated communication and sensing is a timely topic for 5G-Advanced
  Sensing can provide very valuable assistance information for communication, to enable new use cases and scenarios
  Integrated communication and sensing enables an efficient sharing of spectrum and reuse of the existing wireless network infrastructure for sensing applications
  3GPP SA1 has an ongoing study on use cases and performance requirements for integrated sensing and communication
  Evaluate the ability of the current NR architecture and framework to enable integrated communication and sensing in 5G-Advanced
Communication

## Slide 3: Use Cases
  3GPP SA1 considered a variety of use cases ranging from environment monitoring to intruder detection, traffic safety, health monitoring and immersive sensing
  Different use cases have different performance metrics requirements in terms of range, speed, sensing resolution, etc.
  RAN1 needs to select and prioritize 3-4 representative use cases based on
      Feasibility (performance requirements and NR air interface requirements)
      Potential deployment (good commercial viability)
      Diversity (outdoor/indoor, KPIs small/large range, LoS/NLoS, coordinating devices, etc.)

## Slide 4: Sensing Topologies
  Different sensing topologies depend on where the sensing transmission, reception or computation/aggregation is implemented
  Bi or multi-static sensing distributes the sensing measurement process among different network devices
  Monostatic sensing cannot be fully realized without operation in full duplex mode
  RAN1 to prioritize sensing topologies that are feasible for the NR air interface and architecture
      Network to UE(s) bi-static sensing
      UE-gNB(s) bi-static sensing
      Network-based bi/multi-static sensing

## Slide 5: Channel Model Requirements
  Channel model for integrated communication and sensing should be used to measure both the link quality for communication, as well as sensing accuracy and sensing resolution performance
  The current 3GPP SCM lacks the needed parameters to identify and differentiate sensing targets from clutter
  The 3GPP SCM needs to be modified to enable sensing:
      Considering different sensing use cases and sensing topologies
      Considering different target range, target height, relative mobility, carrier frequency, sensing bandwidth, Tx/Rx device heights, etc.
      Characterizing target radar cross section (RCS) over the range of use cases
Target cluster
SCM cluster n
SCM cluster n-1

## Slide 6: RAN1-led SI: Integrated Communication & Sensing (ICAS)
Justification and Motivation
  Sensing provides valuable assistance information for communication to enable new use cases and scenarios
  3GPP SA1 study on use cases and requirements for integrated sensing and communication
  Current 3GPP channel model inadequate for identifying and characterizing sensing targets
Key Objectives
  Identify and select representative sensing use cases and their corresponding KPIs
  Prioritize possible candidate sensing modes/topologies
      Network to UE(s) bi-static sensing
      UE-gNB(s) bi-static sensing
      Network-based bi/multi-static sensing
  Study modifications to the 3GPP SCM to support the necessary parametrization to evaluate ICAS