3GPP1 TSG RAN WG1 		Tdoc TSG RAN WG1  149/99

Meeting # 1

Espoo, Finland

January 21-22, 1999

Source: 	Nokia

Title: 	Proposal for merging ETSI and ARIB Layer 1 documents to one common 3GPP Layer 1 document

Introduction

The intention of this paper is to help the procedure of generating one common 3GPP Layer 1 specification document by combining two source documents: "UTRA Physical Layer Description"  from ETSI UMTS-L1 and "Volume 3, Specifications of Air Interface for 3G Mobile" from ARIB SWG2. A lot of effort has been put in making both of the source documents, and for that reason we should utilise both of their contents in such a way that the end result is as comprehensive as possible.

This paper contains a comparison of ETSI and ARIB Layer 1 documents chapter by chapter, and item by item, clarifying the differences and giving a suggestion what could be done with each section.

Classification of document comparison results

The comparison of "UTRA Physical Layer Description"  from ETSI and "Volume 3, Specifications of Air Interface for 3G Mobile" from ARIB is shown in the next section. The comparison is divided into tables according to ETSI XX-documentation division. For each item a short description of ETSI and ARIB document contents is given. In the last column there is a classification of the comparison result. The interpretation of the classification is following:

a) Same contents

This means that the main technical contents is the same in both ETSI and ARIB documents. However, since the text may be more complete in the other document, both documents should be used as a source in the merging process. Thus it is proposed that the editor rules are such, that the editor-in-charge should take the main text from that document which is more complete, and add the possible missing parts from the other document.

b) Differences & Suggestion

This means that there are some differences between the technical contents of ETSI and ARIB document. The main differences are listed. Additionally, a suggestion is given what could be done to the differences when merging the ETSI and ARIB document into 3GPP document. In case the suggestion is not accepted with the whole group, the alternative proposal is that both ETSI and ARIB contents for that particular item will be put to square brackets in the first version of the 3GPP L1 document, and the decision between them will be made later.

c) ETSI contents only / ARIB contents only

This means that only one of the documents, ETSI or ARIB, contains this particular item. In this case we propose that the contents will be directly taken to the 3GPP document.

3.  ETSI and ARIB Layer 1 document comparison

Table 1. Transport and physical channels (FDD)

| ETSI, XX.03 | ARIB Vol. 3, v.1.0-0.5 | Classification of comparison result |
| --- | --- | --- |
| 1 | Transport channels |

4. Transport channels

Dedicated:     DCH

Common: BCH,FACH,

PCH,RACH

3.2.1.2 Transport channels

Dedicated:  DCH

Common: BCH, FACH,

PCH,RACH

Same contents

ETSI

FAUSCH

Shared channels

| 2 | Physical channel configuration |
| --- | --- |

5. Physical channels

Primary CCPCH  (1)

Secondary CCPCH (2)

PRACH (2)

DPDCH (3)

DPCCH (3)

SCH (1)

3.2.1.4 Physical channel configuration

Perch  (1) *

Common physical channel (2)

Dedicated physical channel (3)

* the numbers (1),(2),(3) show the correspondent channels in ARIB and ETSI

Differences

terms are different

ETSI : SCH code multiplexing

ARIB: SCH  time multiplexing into Perch

Suggestion

Select terms

| Decision is needed about SCH multiplexing |
| --- |
| 3 | Dedicated uplink physical channels |

5.2.1 Dedicated uplink physical channels

DPDCH: data

DPCCH: pilot / tpc / tfci/FIB

-   SF=256…4
-   number of pilot, tfci and tpc

bits are not defined

3.2.2.4.2 Reverse link dedicated physical channels

DPDCH: (pilot/tpc/) data

DPCCH: pilot / tfci / tpc

-   SF=256…1
-   number of pilot, tfci and tpc bits

are defined

Differences

PCCH field

DPCCH field

Pilot pattern

Suggestion

ETSI:

SF range

ARIB:

number of bits for different fields

| order of fields |
| --- |
| 4 | Dedicated downlink physical channels |

5.3.1 Dedicated downlink physical channels

pilot / tpc / tfci / data

-   SF=256…4
-   number of pilot, tfci and tpc

bits are not defined

3.2.2.4.1 Forward Link Dedicated Physical channels

tfci / data1 / tpc / data2 / pilot

-   SF=256512…1
-   number of pilot, tfci and tpc bits

are defined

Differences

Maximum SF

Pilot pattern

Suggestion

ETSI:

SF range

ARIB:

number of bits for different fields

| - order of fields |
| --- |
| 5 | Multicode transmission |

5.2, 5.3 Dedicated  physical channels in uplink, downlink

Uplink: same as in ARIB

Downlink:

- L1 control is put on only the first downlink DPCH

3.2.6.8.2 Multicode transmission

Uplink: same as in ETSI

Downlink:

L1 control is put on only the first downlink DPCH

Power of L1 control part can be different than the data part

Same contents

main structure of multicode usage

ARIB contents only

| possibility to have smaller power level for L1 control part than data part |
| --- |
| 6 | Physical random access channel |

5.2.2.1 PRACH

- preamble/idleperiod/message

1 ms       / x ms       / 10 ms

- message: I:data, Q:pilot+tfci

- power ramping for preamble

- 8 access slots, 16 signatures

-Signature + tfci together define the short code and spreading factor for message

3.2.2.3.2 Reverse link common physical channel

- 10 ms message, without preamble

- I:data, Q: signature

- no power ramping

-4 access slots, 16 signatures

-32 kbit/s or 128 kbit/s

Differences

preamble

power ramping

Suggestion

ETSI' s RACH structure, since use of preamble and power ramping is probably needed

| 7 | Primary CCPCH (ETSI) vs. Perch (ARIB) |
| --- | --- |

5.3.2.1 Primary CCPCH

slot structure in symbols, SF=256:

pilot  / data

4 / 6

3.2.2.2 Perch channel

slot structure in symbols,

SF=256:

Nsch / Ndata /Npilot

1      /    5     /    4

Differences

Time multiplexing of SCH symbol into this channel or not

order of fields

Suggestion

decision is needed first about SCH multiplexing, then about order of fields

8

Secondary CCPCH (ETSI)  vs.

FL common physical channel (ARIB)

5.3.2.2 Secondary CCPCH

slot structure in symbols (SF=256…4):

pilot       /   data

Npilot    /   Ndata

- rate and SF is broadcasted on BCH => cell specific rate

3.2.2.3.1 FL common physical ch.

slot structure in symbols (SF=64):

data    /   pilot

36     /   4

Differences

Number of bits

Order of fields

fixed vs. cell specific bit rate

Suggestion

| take ETSI structure, its probably good to have different bit rates |
| --- |
| 9 | Synchronisation channel |

5.3.2.3 Synchronisation channel

primary and secondary SCH transmitted in parallel to all other channels

otherwise format is the same as in ARIB

3.2.2.2

- primary and secondary SCH are included in the perch channel

- otherwise the format is the same as in ETSI

Same contents

main structure and idea of synch channel

Differences

SCH  multiplexing scheme : time or code multiplexing

Suggestion

| Decision needed about SCH multiplexing |
| --- |
| 10 | Mapping of transport channels onto physical channels |

6. Mapping of transport channels onto physical channels

Phys.ch                     Transp.ch

Primary CCPCH     --- BCH

Secondary

CCPCH                --- PCH, FACH

PRACH                  --- RACH/FAUSCH

DPDCH,DPCCH    --- DCH

SCH                         ---

PDSCH                  DSCH

PSCCCH DSCH control channel

3.2.1.5 Mapping of transport channels to physical channels

Phys.ch            Transp.channels

Perch            --- BCH

Common physical

channel         --- PCH,FACH,RACH

Dedicated physical

Channel ---- DCH

Differences

Mapping of RACH and SCH is different.

Suggestion

use ETSI mapping for RACH

| decision needed about SCH mapping |
| --- |
| 11 | Timing relationship between physical channels |

7. ETSI        3.2.2.1 ARIB

- Tcell -----  Tsect  (different timing for SCH in different sectors)

-  Td    -----  Tcpch (avoid matched tx patterns in common channels)

-  Td   -----  Tframe (averaging fixed line ATM transmission)

-  Td   ------  Tslot (average interference from dedicated channels)

-  Tm  ------  Tdho (timing needed in soft handover)

-  To   ------   250 us (timing difference between DL and UL DPCH)

-         ------  Toffset (method to get several DL scrambling codes)

Differences

- different names, idea is the same

Suggestion

- take ETSI names for simplification

ARIB contents only

- Toffset parameter in order to get multiple DL scrambling codes

Table 2. Multiplexing, channel coding and interleaving (FDD)

| ETSI, XX.04 | ARIB Vol. 3, v.1.0-0.5 | Classification of comparison result |
| --- | --- | --- |
| 1 | Transport channel multiplexing |

7.2 Transport  channel coding/multiplexing

Following order is used:

-      Add CRC per Tr. block

channel coding

1st interleaving

rate matching

service multiplexing

2nd interleaving

mapping to physical channels

3.2.3.1.1. Multiplexing of different QoS services

3.2.3.7 Rate matching

Following order is used:

-      Transport channel mux

channel coding

service specific rate matching

interleaving, (MIL, 10-80 ms)

radio frame segmentation

service multiplexing

physical channel rate matching

- physical channel FIFO mapping

Main Differences

combined vs. 2 state rate matching

order of 1st interleaving and rate matching

interleaver structures

(TTA) Rate Matcing for Turbo Codes: RMT

- many differences in the details

Suggestion

take ETSI structure, since this has been discussed a long time there and discussion is still going on

| 2 | Channel coding |
| --- | --- |

7.2.1 channel coding

convolutional coding

- BER=10e-3 services

-  rate 1/3, ½, constraint length 9

turbo coding (2 concurrent schemes, TBD):

*    BER=10e-6 services, and data rates >32 kbit/s

8 state parallel concatenated convolutional code

conventional termination

interleaver TBD between (MIL, GF, ALN, ALC)

not defined that several/segmented frames can be combined for turbo coding

*     4-state serial conactenated convolutional code

3.2.3.2.2 Error  correcting coding

convolutional coding

- ½ rate: BCH, PCH,FACH,RACH

- 1/3 rate: <32 kbit/s DCH

turbo coding

1/3 rate: >= 32 kbit/s DCH

4- state parallel concatenated convolutional code

CBP for termination

MIL interleaver

several/segmented frames can be combined for turbo coding

Differences

Suggestion

ETSI: based on turbo code adhoc group results

Turbo code only for BER=10e-6 services and >=32 kbit/s. Conv. coding for others.

8 state parallel turbo

conventional termina-tion method for turbo

ARIB:

conv. coding rates

*  ½ rate for BCH, PCH, FACH, RACH

*   1/3 rate for DCH

turbo coding block can be combined for seve-ral /segmented frames

TBD:

| - turbo interleaver |
| --- |
| 3 | Channel interleaver |

7.2.3,  7.2.7 1st and 2nd interleaver

- structures are TBD

3.2.3.3.1 Channel interleaving

1st interleaver: FSMIL interleaver

2nd interleaver: FIFO mapping

Differences

Suggestion

| - leave it open now since structures are still open in ETSI and discussion is still going on. |
| --- |
| 4 | Coding for Layer 1 control |

7.4.1 TFI coding

- biorthogonal (32,6) coding

Extended TFI

3.2.2.4.1.3 TFCI

- biorthogonal (32,6) coding

Extended TFI

Same contents

| 5 | Error detection | - details not defined |
| --- | --- | --- |

3.2.3.4 Error detection

usage of CRC : retransmission, outer loop power control, selective combinining in uplink soft handover

| 16 bit CRC for all logical ch. | ARIB contents only |
| --- | --- |
| 6 | Coding for slotted mode |

7.5 Coding for slotted mode

- either by puncturing or by higher lower spreading factors

2nd scrambling code possible in DL

3.2.6.6.3 inter-frequency handover

either by puncturing or by higher lower spreading factor

Same contentsDifferences:

- Possibility of a 2nd scrambling code

Table 3. Spreading and modulation (FDD)

| ETSI, XX.05 | ARIB Vol. 3, v.1.0-0.5 | Classification of comparison result |
| --- | --- | --- |
| 1 | Uplink modulation and spreading |

6. Uplink spreading and modulation

BPSK data modulation

different channelisation code for I and Q branch

complex scrambling

3.2.4.2.1.26.Uplink spreading and modulation

BPSK data modulation

different channelisation code for I and Q branch

Gain factor for Q branch

complex scrambling

Same contents

main contents

Differences

In uplink, the gain factor of Q branch is missing from ETSI.

ETSI and ARIB aligned, but gain for DPDCH and DPCCH missing in ETSI

Suggestion

| include the gain factor for Q branch in uplink |
| --- |
| 2 | Downlink modulation and spreading |

7. Downlink spreading and modulation

- QPSK data modulation

- complex scrambling

3.2.4. 2.1.1 FL Spreading Modulation scheme

- QPSK data modulation

- complex scrambling

Same contents

Difference

| 3 | Uplink code generation |
| --- | --- |

6.2 Uplink Code generation and allocation

-Channelisation codes: OVSF

- Scrambling codes: HPSK

short scrambling codes: Very large Kasami length 256

long scrambling codes: same as in ARIB

*   10 ms period

*    quadrature component is 1024 chip shifted

- Synchronisation codes:

=> same as ARIB

- Random access codes: HPSK

=> different from ARIB

3.2.4.2.2 Code generation

- channelisation codes:OVSF codes

- Scrambling codes: HPSK method

short scrambling codes:TBD S2 codes of length 256

long scrambling codes: same as in ETSI

*   36864* 10 ms period

*    quadrature component is

1024 chip shifted version

Synchronisation codes:

=> same as ETSI

Differences

Which code set is used for short scrambling codes

period of UL scrambling code

RACH scheme is different => so will be its spreading

Suggestion

Take from ETSI:

short scrambling code set

10 ms UL code period

RACH codes

| Other parts are same |
| --- |
| 4 | Downlink code generation |

7.2 Downlink code generation and allocation

-Channelisation codes: OVSF

- Scrambling codes:

512 codes in 32 code groups

Gold sequences: same as in ARIB

*   10 ms period

* quadrature component is not yet defined

3.2.4.2.2.Code generation

-Channelisation codes:OVSF codes

- Scrambling codes:

33 code groups

Gold sequences: same as in ETSI

*   10 ms period

* quadrature component is 875 us shifted version of the in-phase component

Same contents

Except that quadrature component for the scrambling code is not yet defined in ETSI

| 5 | Code allocation |
| --- | --- |

3.2.4.2.3 Code allocation

uplink channelisation code: from top half of the code treeaccording to TTA algorithm.

downlink channelisation code: decided by network

- search code :same as ARIB

3.2.4.2.3 Code allocation

reverse link: minimising  peak to average ratio

forward link: TBD

search code: same as in ETSI

Same contents

main contents are same

| 6 | Modulation |
| --- | --- |

chip rates : 4.096, 8.192, 16,384 Mcps

pulse shaping : roll-off 0.22

chip rates : 1.024, 4.096, 8.192, 16,384 Mcps

pulse shaping : roll-off 0.22

Differences

- lowest chip rate differs

Suggestion

- take ETSI chip rates

Table 4. Physical Layer Procedures (FDD)

| ETSI, XX.07 | ARIB Vol. 3, v.1.0-0.5 | Classification of comparison result |
| --- | --- | --- |
| 1 | Power control |

4. Power control

Closed loop power control

SIR based for UL and DL, cycle=0.625 ms

step size 0.25-1.5 dB

In soft handover the MS increases changes its Tx power only if all commands indicate an increase valueas a result of combination of the commands altogether with the reliability estimates

Outer loop adjusts the SIR target

Open loop power control

used only for RACH bursts

based on downlink pathloss and uplink interference

3.2.6.7. Transmitter power control

Closed loop power control

SIR based for UL and DL,

Cycle=0.625 ms

Step size UL: 1 dB, DL: 1 dB

In soft handover MS decreases its Tx power if there is at least one decrease command that satisfied required reliability. Reliability is based on SIR.

Downlink power offset possibility

Outer loop adjusts the SIR target

Open loop power control

used only for RACH bursts

based on downlink pathloss and uplink interference

Differences

step sizes

power offsets

power control in soft handover

level of details is quite different

Suggestion

Main description from both ETSI and ARIB

ETSI:

step sizes

TBD later:

DL power offsets

| Power control in soft handover |
| --- |
| 2 | Cell search |

5. Cell search

- Initial cell search

=> same as in ARIB

- Idle mode cell search

- Active mode cell search

3.2.6.1 Cell detection control

- Initial cell search

=> same as in ETSI

- Idle operation/handover

=> periodical search process

|  | Same contents |
| --- | --- |
| 3 | Synchronisation procedures |

6. Random access procedure

synchronisation to a cell

read BCH and select parameters for RACH burst

etc.

3.2.6.2. Synchronisation procedures

- common ph. ch. synchronisation

-dedicated channel synchronisation

=> defines power control and use of idle patterns during synchronisation phase

- soft handover synchronisation

- softer handover synchronisation

- superframe synchronisation

Differences

ETSI contains only RACH part of the synchronisation

Suggestion

RACH part from

ETSI

| Other synchroni-sation description from ARIB |
| --- |
| 4 | Idle mode tasks |

7. Idle mode tasks

- Paging control

3.2.6.3 Idling operation

| - Paging control | Same contents |
| --- | --- |
| 5 | Rate detection | - |

3.2.6.4 Rate detection

- Blind rate detection by CRC

- TFCI : mapping of TFCI bits to service rate combinations

|  | ARIB contents only |
| --- | --- |
| 6 | Quality supervision | - |

3.2.6.5 Quality supervision

| SIR definition for MS | ARIB contents only |
| --- | --- |
| 7 | DTX | - |

3.2.6.9 Discontinuous transmission

- DTX within a radio frame

| - DTX of radio frames | ARIB contents only |
| --- | --- |
| 8 | Reverse link synchronous transmission | - |

3.2.6.11 Reverse link synchronous transmission

| - alternative technology for low mobility terminals | ARIB contents only |
| --- | --- |
| 9 | Asymmetric transmission control | - |

3.2.6.11.2 Asymmetric tx control

- independent SFs in UL and DL

| - Possibility to have UL: RACH and DL: DCH | ARIB contents only |
| --- | --- |
| 10 | DownlinkTx diversity |

Still open in ETSISTTD

TxAA + STD

Optional in network, for further study for MS

3.2.6.11.4 Forward link TDTD

optional in BS, mandatory in MS

contains predetermined mode and feedback mode

STD for closed loop

TSTD for open loop

(combination of both called TDTD)

Differences

Discussion still going on in ETSI

Suggestion

Put the options in square brackets

Table 5, Physical Layer procedures, continued (FDD)

| ETSI, XX.15 | ARIB Vol. 3, v.1.0-0.5 | Classification of comparison result |
| --- | --- | --- |
| 1 | Handover types |

6. Handover types

soft handover

UTRA to UTRA hard handover

UTRA to GSM hard handover

3.2.6.6

soft handover

hard handover

Differences

Suggestion

| Take ETSI types, since they cover also intersystem handovers |
| --- |
| 2 | Cell sets for handover |

8.2  Contents of Cell sets for handover

1) Handover monitoring set in FDD

2) Handover candidate set

| 3) Active set | - | ETSI contents only |
| --- | --- | --- |
| 3 | Set maintenance |

8.3 Set maintenance

MS sends regular (or event driven) measurement reports to network.

Network decides the update of the sets and reports decisions to MS.

3.2.6.6 Handover

| - same idea as in ETSI | Same contents |
| --- | --- |
| 4 | Handover preparation from UTRA to UTRA/ Soft handover |

9.1 Handover preparation from UTRA to UTRA

Measurement report includes at least :

cell ID

relative signal strength

relative timing information

3.2.6.6.1 Diversity handover

MS measures:

relative timing difference

Differences

ETSI concentrates more on measurement list, ARIB more on synchronisation procedure

Suggestion

ETSI : measurement list

| ARIB: synchronisation procedure |
| --- |
|  | UTRA to UTRA/ Intercell hard handover | - |

3.2.6.6.2 Hard handover

Conditions to measure received signal strength of other cells:

if signal strength of own cell is below certain threshold

| during DTX period | ARIB contents only |
| --- | --- |
|  | UTRA to GSM | 9.2 Handover preparation from UTRA to GSM | - | ETSI contents only |
| 5 | Transmission in handover and handover execution procedure |

10.1 Soft handover

New cell should get following information through the network

max. data rate and other service parameters

MS ID and UL scrambling code

Relative timing information

MS should get following information through own cell

from which frame the new cell initiates the transmission

channelisation codes

relative timing information

3.2.6.6.1 Diversity handover

Synchronisation establishment explained in detail upon soft/softer handover

Differences

- ETSI gives a list what  information will be changed. ARIB explains the synchronisation procedure step by step.

Suggestion

ETSI : measurement list

ARIB: synchronisation procedure

Documents from ETSI

All the TDD documents are proposed to be taken straightly from ETSI, since they have been mainly developed there:

XX.09, UTRA TDD, Transport and physical channels description

XX.10, UTRA TDD, Multiplexing, channel coding and interleaving description

XX.11, UTRA TDD, spreading and modulation description and relevant parts from

XX.12, UTRA TDD, Radio transmission and reception description

XX.13, UTRA TDD, Physical Layer procedures description

Conclusion

This paper was made for a tool for generating the 3GPP Layer 1 documentation by merging ETSI and ARIB Layer 1 documents. For that purpose it contains a comparison of ARIB and ETSI Layer 1 document contents.

In section 2  we have also given our proposal how the editor rules should be defined for generating the first version of 3GPP document. The editor rules should be defined in such a way that the 3GPP document will be as comprehensive as possible right from the beginning.

This means that if the main technical contents is the same in both documents, the editor-in-charge should take the main text from that document which is more complete, and add the possible missing parts from the other document. In that way the end result will be as complete as possible.

# Footnotes

ARIB Vol. 3 ver 1.0-0.5 12/98 and ETSI XX-documents after 9th L1 EG meeting 12/98 were used as source documents.