3GPP TSG RAN WG1 Meeting #102-e		 	R1-200XXXX

e-Meeting, August 17th – 28th, 2020

Agenda item:		8.3.2

Source:		Moderator (Ericsson)

Title:	 	Summary#1 on enhancements for unlicensed band URLLC/IIoT for R17

Document for:	        Discussion and Decision

# Introduction

This document is a revision of R1-2007069 and is intended to facilitate view exchange and discussions for the following assigned email discussin by Mr. Chairman:

[102-e-NR-IIOT_URLLC_enh-03] Email discussiona/approval – Sorour (Ericsson)

- By 8/21 – high priority

- By 8/27 – medium

Companies are encouraged to share their views on the discussion points highlighted below.

# Support of UE-initiated COT for FBE

This section summarizes companies view with respect to the following objective in the WID:

Uplink enhancements for URLLC in unlicensed controlled environments [RAN1, RAN2]: Specify support for UE-initiated COT for FBE with minimum specification effort

It is commonly understood that the support of UE-initated COT in principle is similar to already specified gNB-initated COT.

In order to have a clear understanding of the required specifcaion efforts and keep it at minimum as stated in the corresponding WID objective, it is important to identify the commonalities and differences between UE-initated COT and gNB initated COT with respect to configurations/signalings/UE and gNB behaviours. This would help to have a better understanding on the extra specification efforts needed to enable UE-initated COT in addition to gNB initated COT.

To achieve this goal, it is important to have an overview on companies’ understanding with respect to regulations and NR operations towards the following fundamental queations.

Based on this overview, we can identify the differences in fundamental assumptions. Since the references are regulations and NR operations, it would hopefully be possible to resolve the differencea to reach to a proper common understanding that can serve as the baseline assumption allowed by regulations and NR specifciations.

With the baseline assumption in place, the follow-up discussions to explore different dimentions on the design choices in order to make sound decisions would hopefully be constructive and efficent.

Based on companies views in the submitted contributions, it seems that discussion around the following two questions can be helpful to serve the purpose discussed above.

The first question is as follows:

- Q-A: Can one COT-inititator block another COT-initiator in NR based system?

- Understanding 1: Yes. Some companies percieve that enabling UE-initated COT cause contention between different UEs or between UE and gNB in a sense that a UE intending initiating a COT would be in a position to block the gNB or other UEs in the system to access the channel.

- Understanding 2: No. Some other companies consider that UE-initating COT only improves channel access for the UE and gNB via COT sharing without competing with gNB or other UEs. If UE is intended to initate a COT, it can not decide by itself to transmit in occasisons other than those being scheduled or configured by gNB. The sensing, if needed, is performed immediately before the configured/scheduled transimisison opportunity by gNB. All transmissions (both DL and UL) are remained to be controlled by gNB.

These two different understandings would lead into two different design directions. A design based on underlying Understanding 1 would have solutions to minimize the blocking impact, while those solutions not only would be unnecceesary but also restrictive for a design based on Understanding 2.

Therefore, it is important to reach to a common understanding on this fundamental question based on what regulations and NR operation permits.

The second question is as follows:

- Q-B: What is the understanding on the interaction between idle periods corresponding to different COT-initiators from the regulatory perspective?

- Understanding 1: The initiator of a COT with a corresponding FFP is not allowed to transmit in any of the FFP’s idle interval. A responder that shares a COT within an FFP with a COT-initiator is not allowed to transmit in the idle period of the FFP where its COT being shared.

- Understanding 2: The initiator of a COT with a corresponding FFP is not allowed to transmit in any of the FFP’s idle interval. A responder that shares a COT within an FFP with a COT-initiator is not allowed to transmit in any of the FFP’s idle period of the Cot-initiator.

Figure 1 and Figure 2 illustrate examples to show the difference between these two understanding. Based on companies’ views expressed in contributions, views are devided between these two approaches. Hence, it is important to identify first which understanding is inline with regulations and can be the proper starting point. If the common understanding merges on Understanding 1, it can be discussed further whether decision should be to allow operation as in Understanding 1 or impose additional restrciiton to operate as in Understrading 2.  To make this decision, it is important to consider both signalling aspects and system performance to make a sound decision.

Figure 1: Illustrative example for Understanding 1 and 2 for Q1 without any transmissions

Figure 2: Illustrative example for Understanding 1 and 2 for Q1 with transmissions

### Discussion point A:

| Q-A: Can one COT-inititator block another COT-initiator in NR based system? Options for answers to Q-A Yes, as Understanding 1 No, as Understanding 2 Others (Please describe) |
| --- |
| Company | Options for answers to Q-A | Comments |
| Sony | Yes (Understanding 1) | UL transmission without gNB scheduling would be beneficial to aquire COT in the case that gNB fails aquiring COT. Blocking can be managed by gNB’s configuration of UE’s FFP. |
| Apple |  | The question and the descriptions of the two understandings are not completely clear to us. If blocking means that UE transmission based on a UE-initiated COT may prevent the gNB from accessing the channel, then our answer is yes. (We support understanding 1 in Figure 2.) |
| Intel | Yes (Understanding 1) | In our understanding, two initiating devices can indeed potentially block each other. This could occur among devices from different operators, but this could also occur among devices of the same operator. In this last scenario, when the absence of an incumbent technology cannot be guaranteed, we would assume that a gNB would avoid to potentially configure UL transmissions with non-overlapping resorces, since the LBT success for the gNB and its associated UEs cannot be guaranteed, and in this case if an LBT would occur, this would certainly lead to wastage of resources. Therefore, in some cases it may be beneficial to devices from the same operator to compete each other with the aim to maximize the spectrum utilization, which on the other hand would tend to block each other. In the context of semi-static channel access, this could be managed and mitigated by proper enabling the UE from acting as an initiating COT. In this case, our view is that we should always prioritize the gNB as initiating device and allow the UE to operate as initiating device is some selected circumstances, also under the consideration that the UE is penalized from acquiring and sharing the COT when this is shared with the gNB for other than control information, given that this would need to use a lower ED threshould. |
| DOCOMO | No, as Understanding 2 | Whether UE can initiate COT or not in a Tx occasion should be controlled (i.e., indicated/configured) by gNB for better coexistence |
| Lenovo, Motorola Mobility | Others | Our understanding is understanindg 1, with the restriction that a UE should not transmit in gNB’s idle period. maybe related to the discussion of if one COT-innitiator can block another COT-initiator: it seems two UEs with different FFP start time/FFP duration, should be aware of eachother’s COT, to not transmit in eachother’s idle periods, and hence not block each other. For example, UE1 had data to transmit, but blocked by the end of UE2’s transmission within idle period of UE1. So, in that case, performing LBT by UE1 would result in no transmission by UE1 evenif two UEs have the same idle-U occasions; it is possible that one UE blocks another UE or it is possible the UEs collide; |
| vivo | Others | From our understanding that the FFP configurations for UE initiated COT is ‘known’ by the gNB, and whether there are collisions (contention) between gNB and UE or among UEs depend on gNB’s configuration and are under gNB’s control. From UE perspective, based on its configuration, whether to Tx or Rx is clear; From gNB perspective, gNB can decide whether to Tx or Rx based on the service/UEs priority. For example, in a system, one FFP starting position of gNB and UE#1 are aligned, it is possible that UE#1 will send the configured grant UL trasnmissions, while gNB would like to send PDSCH to UE#2 since UE#2 has higher priority than UE#1. The consequence maybe gNB misses the UE#1’s UL transmission or it is also possible gNB or UE#2 has the capability also receives the transmission by implementing some interference cancellation schemes. |
| Spreadtrum | Yes(Understanding 1) | During the idle period of the FFP, only the initiator cannot transmit. gNB behavious in Understanding 1 is the same as in Rel-16. Furthermore, if a UE can be the initiator, gNB should guarantee the un-collision of gNB’s FFP and UE’s FFP. However, in understanding 2, even during the initiator’s own FFP, additional idle periods are introduced. It breaks the rules of semi-static channel access and complex the gNB and UE’s implementations. |
| Qualcomm | Yes | If not properly configured/scheduled, there can be mutual blocking issue. But gNB configuration/scheduling should handle. As long as the design allows the gNB to handle the issue, we are fine. This is similar issue as in Rel.16 NR-U FBE that we assume gNBs are synchronized on FFP and will not block each other, and even the DL/UL burst starting points in the FFP are synchronized, so they will not block each other as well. We don’t think we need any specific design to minimize the blocking impact. |
| ETRI | Yes (Understanding 1) | Share the view with Apple that meaning of ‘block’ here needs to be clarified. We think UE is not allowed to initiate a COT within a detected gNB-initiated COT, and vice versa. With this understanding, to avoid blocking and provide more opportunity for COT initiation, Rel-17 FBE should allow for gNB and UE to release the COT earlier than the original ending time (right before idle period). |
| Sharp | No, as Understanding 2 | We think this is a fundamental question on how to design FBE protocol in NR based system, especially when UE-initiated COT is involved. Considering the assumed controlled environment and reliability/latency requirements, we think sufficient gNB controlling is required to avoid potential collisions. |
| CATT | Yes (Understanding 1) | In general, we fine with understanding 1. We think it is necessary for gNB to configure UE initiated COT and this can avoid potential collisions between UEs or gNB and UEs. |
| Nokia, NSB | Yes (understanding 1) | there are a few different cases to consider: gNB FFP may block UEs from transmitting an FFP of one UE may block and FFP of another UE depending of the exact configuration of the FFPs However, UE FFP should not preferably block gNB FFP. The may be varous ways of achieving this, including existing mechanisms (semi-static UL-DL config). |
| Samsung | No, Understanding 2 | If transmitters are not coordinated, yes, the iner-blocking between COTs iniated by different transmitter would happen. But in NR system, at least within a seving cell, all UE behaviour is under gNB control, so of course gNB can control whether to enable/disable UE to intiate COT to avoid any potential collsion between gNB/UE or UE/UE. Having said that, we may need to study whether existing mechanism is sufficient, e.g. reusing SFI to cancle CG-PUSCH to disable UE’s COT, or new mechanism is needed, e.g. UE-specific siganling to enable/disable UE’s COT. |
| ZTE |  | We share the similar view with other companies that the meaning of ‘block’ here needs to be clarified. If the understanding 1 is the FFP of the UE can block gNB-initiated COT and understanding 2 is FFP of UE should not block the gNB-initiated COT, we support understanding 2. UE-initiated COT controlled by gNB can easily coordinate the channel access competition between gNB and UE. If the FFP of UE can block gNB-initiated COT, the gNB cannot initiate a COT and transmit the DL transmission (PDSCH or PDCCH) for other UE and share the COT with other UE. In this condition, many UEs may not be able to meet the latency requirement. If the FFP of gNB can block UE-initiated COT, the UE cannot initiate a COT but the UE can share the COT of the gNB. Therefore, the FPP of UE should not block gNB-initiated COT and the FFP of gNB can block UE-initiated COT. |
| HW/HiSi | Yes, as Understanding 1 Given that the question is seeking “an overview on companies’ understanding with respect to regulations and NR operations” rather than the envisioned design principle for this new NR based system | We agree from Understanding 2 on that -If UE is intended to initate a COT, it can not decide by itself to transmit in occasisons other than those being scheduled or configured by gNB. -And that sensing, if needed, is performed immediately before the configured/scheduled transimisison opportunity by gNB. However, we would like to clarify that, in principle, blocking would still happen between UEs initiating COs or between gNB and UE(s) if the configuration/scheduling by gNB is as such. Recall also that in NR-U, being an NR based system, CG UEs with Full BW allocation are configured by the gNB to use random starting offsets for the purpose of attaining channel access precedence and thus blocking other UEs. |
| LG | Yes (Understanding 1) | The blocking should be under gNB controllability. For example, as explained in our paper, the gNB could intentionally configure unaligned FFP starting between gNB and UE so that DL FFP by gNB-initiated COT starts earlier than UL FFP by UE-initiated COT. Given that, according to gNB’s situation and decision, the gNB could make DL FFP by blocking UL FFP, or the UE could get the chance to make UL FFP in case when the gNB doesn’t have a plan for DL FFP. |
| OPPO | Others | One initiator-COT blocks the other initiator-COT: if here means UE vs. gNB, we think the UE should only transmit in the scheduled/configured UL resources, thus, such blocking issue is fully controlled by gNB. If here means UE vs. the other UE, the blocking might be possible. |
| InterDigital | Yes (Understanding 1) | With proper configuration, the gNB can avoid blocking between gNB and UE initiated COT. There may be inter-UE blocking (given that they may not be perfectly synchronized). |

### Discussion point B:

| Q-B: What is the understanding on the interaction between idle periods corresponding to different COT-initiators from the regulatory perspective? Options for answers to Q-B Yes, as Understanding 1 No, as Understanding 2 Others (Please describe) |
| --- |
| Company | Options for answers to Q-B | Comments |
| Sony | Yes (Understanding 1) | Interaction between idle periods of different COT-initiators is not explicitly described in ETSI BRAN. |
| Apple | Understanding 1 | We are more aligned with understanding 1, but wonder if this is allowed: can a UE transmit in the idle period of its own FFP when it is using the COT shared by the gNB? We assume the answer is yes assuming the COT shared by the gNB should be considered separately. |
| Intel | Other | Our understanding is that from a regulation perspective, a device can act as an initiating, a responding or both at the same time, and in general a device is only precluded from transmitting in its own idle period within its own FFP when this is operating as an initiating device. 4.2.7.3.1.2 Device Types (Adaptivity) A device that initiates a sequence of one or more transmissions is denoted as the Initiating Device. Otherwise, the device is denoted as a Responding Device. Frame Based Equipment may be an Initiating Device, a Responding Device, or both. |
| DOCOMO | Yes, as Understanding 1 | Idle periods are determined per device basis |
| Lenovo, Motorola Mobility | Understanding 1 with the restriction that a UE should not transmit in gNB’s idle period. |  |
| Vivo | Yes, as Understanding 1 | We believe understanding 1 is more accurate for the interaction between idle periods corresponding to different COT-initiators from the regulatory perspective. The transmission restriction in idle period is only valid when the transmission acturally occurs in the associated FFP, i.e. the device either initiating a COT from the FFP starting position or sharing a COT of the FFP. |
| Spreadtrum | Yes, understanding 1 | An intitiator should only avoid transmission in its own idle period, which is defined per the intitiator’s FFP. |
| Qualcomm | Yes from regulator perspective, but NR-U design does not need to be limited by regulation | Our interpretation of the two understandings is, for understanding 1, the initiating device’s idle period is honoured, no matter gNB or UE acts as the initiating device. On the other hand, understanding 2 will honor the idle period of “potential” initiating device, no matter the potential initiating device is acquiring the COT or not. The regulation apparently does not consider the case both nodes can be initiating and responding and keep switching roles, or even acting as initiating device and responding device at the same time. Our understanding is the understanding 1 is align with what the regulation requires. However, this does not mean the NR-U behaviour has to directly follow regulation. With understanding 1, there is a chance that the gNB and UE can cooperate to no leave the idle period (gNB transmits in UE idle period, and UE transmits in gNB idle period). This may be unfair to other RATs. This might be the motivation understanding 2 is considered. However, for understanding 2, the idle overhead is doubled, and can be even larger if there are multiple UEs acting as initiating device with different FFP offset. As a result, there can be another option that, gNB FFP idle is always honored, no matter it is gNB COT or UE COT (so we leave a “sticky” idle period for other RATs if they exist), but UE idle period is only honored if gNB knows it is sharing UE COT. |
| ETRI | Yes (Understanding 1) | No description on this in ETSI harmonized specification, which means we can take Understanding 1 that is useful to reduce the latency. |
| Sharp | Yes, as Understanding 1 | Following Understanding 2, if multiple UEs are configured with mis-aligned FFPs, the available time for channel access would be quite limited since UL/DL transmissions are not allowed in neither the idle periods, which does not sound reasonable. |
| CATT | Yes as understanding 1 | We have the same view with VIVO |
| Nokia, NSB | Other | We can identify 4 different cases: Any UE (neither COT responder nor COT initiator) should not transmit during the idle period of a gNB. The gNB as a COT initiator is allowed to transmit during the idle period of a UE. The gNB as a COT responder is not allowed to transmit during the idle period of the UE that initiated the COT. The gNB as a COT responder is not allowed to transmit during the idle period of its FFP |
| Samsung | Yes, as Understanding 1 | We think the regulation is specified from a signle device point of view. |
| ZTE | Other | Similar to Q-A, we think the FFP of UE should not block gNB-initiated COT and the FFP of gNB can block UE-initiated COT. Meanwhile, we support that the UE can continuously share the COT of the gNB and send UL transmissions continuously, regardless of the idle period of the FFP of the UE. For example, when the UE shares the COT of gNB, the UE can send UL transmission at the position where the COT of the gNB overlaps with the idle period of the UE. The impact of this scheme for specification is minimal. |
| HW/HiSi | Understanding 1 (with the clarifications under Comments) | Since the context of Q-B is that each one of the different COT-initiators can be a responder to the other, it is important to make the following clarifications based on Understanding1: -idle-u : No UL (at all from initiator UE) and No DL (in response to inititor UE) -idle-g : No DL (at all from initiator gNB) and No UL (in response to inititor gNB) |
| LG | Yes (Understanding 1) | The answer is purely from the regulatory perspective. On the other hand, considering the coexistence between gNBs/operators, some restriction in terms of not allowing transmission in certain period may be necessary to study. |
| OPPO | Others | For understanding 1, we have the following question, if the gNB initiates a COT in its own FFP until the end of the UE’s idle period and just reserves a small gap for the UE to initiates a UE COT in UE-FFP. Would this be allowed? As shown in example below. If this is allowed, the other gNB or UEs will be blocked for a long time period, which might not be fair for co-existence. For understanding 2, we think it is contradicting to the FFP concept, because it seems that within one FFP there are more than one idle period. In our understanding, we think the UE idle and gNB idle periods should have an aligned starting location. |
| InterDigital | Yes, as understanding 1 | During a COT initiated by a device, the idle periods of other devices can be ignored. This will not lead to hogging the resources, since when the FFP of the COT ends, there will be an Idle period and if configured properly, no other devices will be able to transmit during that Idle period since no other devices will be able to initiate a COT prior to the Idle period, given that the original COT was active. |

## Issue#1-1: UE-initiated COT FFP parameters

In Rel-16, the FFP configuration for gNB initated COT consists of a periodicity where the corresponding offset with respect to a radio frame is implicitly specified. To support UE-initated COT in Rel-17, UE requires knowledge of the corresponding FFP. Companies expressed views whether UE-initated FFP parameters should be obtained from gNB-initated FFP or independently.

An overview of companies’ view is listed below in two alternatives.

- Summary of proposals: Periodicity and offset of FFP parameters for UE-initated COT

- Alt1: Periodicity and offset of FFP parameters for UE-initated COT can be different from the corresponding FFP parameters for gNB-initiated COT.

  - Apple, Beijing Xiaomi, [Charter (FFS on offset)], Ericsson, Intel, InterDigital, LG, MediaTek, Nokia&NSB, Panasonic, QC, Samsung, Sony, Spreadtrum, vivo, WILUS, ETRI

- Alt 2: Periodicity of FFP parameters for UE-initated is assumed the same as corresponding periodicity in FFP parameters for gNB initiated COT. Offset of FFP parameters for UE-initated COT can be different from the corresponding offset in FFP parameters for gNB initiated COT.

  - CATT, Huawei, HiSilicon, OPPO

The corresponding proposals are listed in Section 5.1 for refererence.

### Discussion point Issue#1-1:

| Q1-1: What is your view on Periodicity and offset of FFP parameters for UE-initated COT? Comments on relation to your view on Q-A/Q-B is welcome. Options for answers to Q1-1 Alt 1 Alt 2 Others |
| --- |
| Company | Options for answers to Q1-1 | Comments |
| Sony | Alt 1 | Gives flexibility for gNB to manage UE FFP and also can be used to minimise/avoid the blocking described previously in Discussion Point A. |
| Apple | Alt 1 | We do not see why we should have the constraint that UE’s FFP periodicity has to be the same as gNB’s FFP periodicity. |
| Intel | Alt 1 | We believe that defining a set of offsets and different set of FFPs for the UE-initiated COT would be beneficial for multiple aspects: It allows more flexibility to accommodate for different UL traffic, which may not fit the FFP value for when the gNB operates as an initiating device. It allows to better manage blocking among devices. It allows to align the start of the FFP with the actual UL transmission. If the UL transmission is not aligned with the FFP, the UE would need to perform LBT twice: one time to acquire the COT, and then to resume the COT to initiate transmission. This not only would increase LBT overhead, but impact contention and increase collisions. |
| DOCOMO | Alt 1 | Alt 1 is better to give UEs more chance to access the channel under the gNB’s control |
| Lenovo, Motorola Mobility | Alt 1 |  |
| vivo | Alt 1 | The FFP parameters can be defined per device, that is to say, different FFP periodicities and offsets can be configured between the UE and gNB, and among the Ues This provides more transmission opportunites and accomdating for different services supported in the system. |
| Spreadtrum | Alt 1 | It is up to network’s configuration. |
| Qualcomm | Alt 1 | Alt 2 is a special case of Alt 1. We prefer separate configuration of gNB and UE FFP to support more flexible use cases, adapting to need. Also different Ues may be configured with different FFP and offset. |
| ETRI | Alt. 1. | For better flexibility and more use cases. Can further discuss the need of offset for FFP-g. |
| Sharp | Alt 1 | Firstly, Alt 1 offers better flexibility. In addition, we think enabling configurations of different periodicities of FFP is beneficial to improve latency performance. |
| CATT | Alt 1 | gNB can flexible configure UE FFP’s period and offset based on different Ul traffics |
| Nokia, NSB | Alt 1 | there is no need to align the parameters, as long as the conditions discussed in the point B above are satisfied. |
| Samsung | Alt 1 | We fail to see the motivation to restrict UE’s COT periodicity same as gNB’s. |
| ZTE | Alt1 | Alt1 is preferred that gNB can flexibility establish the UE’s FFP. We do not see a strong motivation to always keep the same periodicity of UE-initiated FFP and gNB-initiated FFP. |
| HW/HiSi | We prefer Alt 2 for the reasons under Comments | In line with the objective of the WID to specify the support for UE-initiated COT for FBE with minimum specification effort, it would be also quite simple to specify only the new higher layer parameters and any necessary channel access procedures required for the UE to establish its semi-static CO based on with the gNB’s semi-static CO in the same channel(s). Configuring the UEs to reuse the gNB’s periodicity to initiate respective semi-static COs in the same channels simplifies configuration/scheduling by gNB of resources for these staggered COs initiated by the gNB and different UEs while respecting the restrictions discussed earlier due to idle period interactions and MCOT durations. |
| LG | Alt 1 | As explained in the above Point A, considering the unaligned FFP starting between gNB and UE, at least an offset between DL FFP by gNB-initiated COT and UL FFP by UE-initiated COT is necessary in terms of configuration. |
| OPPO | Alt 2 | Same view as Huawei |
| InterDigital | Alt 1 | Gives more flexibility to the scheduler. |

## Issue#1-2: Configuration of UE-initiated COT FFP parameters

In Rel-16, the FFP periodicity of gNB initiated COT is provided to the UE by SIB1 or dedicated RRC signalling.

To support UE-initated COT in Rel-17, a UE requires knowledge of the corresponding FFP. Companies expressed views on how a UE obtains information for UE-initated FFP parameters. The views can be summarized in three alternatives as listed below:

- Summary of proposals: Configuration of Periodicity and offset of FFP parameters for UE-initated COT

- Alt1: Periodicity and Offset of FFP parameters for UE-initated COT can be provided to the UE by SIB-1 or dedicated RRC signalling.

  - Apple (FFS on offset before dedicated RRC), Beijing Xiaomi, [Charter (FFS on offset)], Ericsson, Nokia&NSB, QC, Samsung, Spreadtrum (dedicated RRC), WILUS, ETRI (at least SIB-1)

- Alt 2: Offset of FFP parameters for UE-initated COT can be provided to the UE by dedicated RRC signalling.

  - Huawei, HiSilicon, OPPO

- Alt 3: FFS whether the UE FFP duration is explicitly configured, or implicitly determined based on other configurations such as RACH configuration, UL CG configuration, etc.

  - Nokia&NSB

The corresponding proposals are listed in Section 5.2 for refererence.

### Discussion point Issue#1-2:

| Q1-2: What is your view on Configuration of Periodicity and offset of FFP parameters for UE-initated COT? Comments on relation to your view on Q-A/Q-B is welcome. Options for answers to Q1-2 Alt 1 Alt 2 Alt 3 Others |
| --- |
| Company | Options for answers to Q1-2 | Comments |
| Sony | Alt 1 | As we answerd alt 1 in Issue#1-1, periodicity can be provided by SIB or dedicated RRC signalling. |
| Apple | Alt 1 |  |
| Intel | Alt 1 | Same principles used for NR-U can be re-used. |
| DOCOMO | Alt 1 |  |
| Lenovo, Motorola Mobility | Alt-1 or others | Whether the UE can initiate a COT using the CG configuration can be configured per CG configuration. |
| vivo | Alt 1 | Both the periodicity and offset can be configured in SIB1 and/or dedicated RRC signalling, which is beneficial for idle mode UE when it performs random access. |
| Spreadtrum | Alt 1 | SIB 1 or dedicated RRC signalling. Firstly of all, periodicity should be explicity configured, not by other configurations such as Alt 3. Periodicity and offset can be same among the UEs, so it can be configured by SIB1. However, for the connected mode UEs, offsets should be different among the UEs, it would be better configured by dedicated RRC. |
| Qualcomm | Alt 1 | Alt 2 is a special case of Alt 1. We prefer separate configuration of gNB and UE FFP to support more flexible use cases, adapting to need. Also different UEs may be configured with different FFP and offset. |
| ETRI | Alt. 1 | Necessary to apply the offset for FFP-u configuration to control UL burst starting time. At least SIB-1 can be used. Need of dedicated RRC signalling can be discussed. |
| Sharp | Alt 1 | A potential implementation is that, before UE is RRC configured, UE obtains basic FFP parameter via SIB1 (e.g., only an offset, or even the offset is predetermined). Then optional FFP parameters offering better flexibility are delivered to UE via dedicated RRC signalling. |
| CATT | Alt 1 |  |
| Nokia, NSB | Alt 1 as the baseline, consider also Alt 3 | The basic config should be in SIB-1 or RRC. The timing may further be adjusted based on e.g. other configurations. |
| Samsung | Alt 1 |  |
| ZTE | Alt1 | It can be signalled by SIB1 before RRC_connected state, and by dedicated RRC signaling in RRC_connected state. |
| HW/HiSi | (Modified Alt 1) Alt1: Periodicity and Offset of FFP parameters for UE-initiated COT can be provided to the UE by SIB-1 or dedicated RRC signalling. We think this question should be about the signaling options. The parameters that are signaled should be discussed separately, e.g. in issue #1-1. Therefore, we propose the modified Alternative. | It is important to note that uplink transmission with CG are notably well suited for latency reduction in the IIoT uses cases featuring periodic and deterministic data with very low latency requirements. Therefore, configuration of FFP parameters after RRC connection is established is of more importance. In addition, at least different offsets for different Ues are needed and this can only be achieved via dedicated signalling of the UE-specific offsets |
| LG | Alt 2 | The motivation to allow UE-initiated COT on top of Rel-16 is for the enhancement of URLLC traffic/use case. We don’t see the necessity of SIB configuration associated with initial access. |
| OPPO | Alt-2 and Alt-3 | We think alt-3 is also a good alternative, in our understanding, UE initiates a COT in a scheduled/configured resource for the UE to transmit UL. In this sense, Alt-3 seems a natural solution. |
| InterDigital | Alt 1 |  |

## Issue#1-3: UL channels for initiating a COT

With respect to uplink channels that can be used to initiate a COT by UE, compaies views can be summarized as follows:

- Summary of proposals: UL channels for initiating a COT

- Alt 1: Transmission of configured UL channels is supported to initiate a COT

  - Beijing Xiaomi, WILUS

- Alt 2: Transmission of any UL channels is supported to initiate a COT

  - Apple (FFS SRs, P-CSI), Ericsson, Huawei, HiSilicon (scheduled and periodic), [Nokia&NSB], QC, [MTK (Except PRACH)], InterDigital

- Alt 3: Transmission of control or data UL channels with high priority is supported to initiate a COT

  - Lenovo, Motorola

The corresponding proposals are listed in Section 5.3 for refererence.

### Discussion point Issue#1-3:

| Q1-2: What is your view on UL channels for initiating a COT? Comments on relation to your view on Q-A/Q-B is welcome. Options for answers to Q1-3 Alt 1 Alt 2 Alt 3 Others |
| --- |
| Company | Options for answers to Q1-3 | Comments |
| Sony | Alt 2 |  |
| Apple | Alt 2 | FFS SR, P-CSI |
| Intel | Alt 2 |  |
| DOCOMO | Alt 2 |  |
| Lenovo, Motorola Mobility | Alt3 | In our view, a low-priority UL transmission of UE1 should not collide with a high-priroty UL transmission of UE2, if both Ues are successful in initiating a COT. In our view, if gNB is aware of any pending UL transmission, it would initiate a COT, and schedules the UE for UL transmission, so, in our understanding, UE-initiated COT is mostly applicable to configured resources, wherein the gNB is not aware whether there is goining to be any UL transmission on those resources. |
| Vivo | Alt 2 | We see no motivaton to restrict the transmissions that can be used to initiate a COT by UE. Any UL channels/signals can be used to initiate a COT by UE. |
| Spreadtrum | Alt 2 | In addition to the configured UL channels, dynamic scheduled PUSCH/PUCCH can also initiate a COT. Because the transmissions may out of gNB’s COT or not able to share a COT of gNB to a certain UE such as the transmission occasions are at the beginning of a COT. |
| Qualcomm | Alt 2 | Can leave the flexibility to gNB configuration/scheduling |
| ETRI | Alt. 2. |  |
| Sharp | Alt 2 in principal | We think at least supporting PRACH is beneficial. Considering potential specification efforts, it might be better to firstly scope down UL channels to be supported in Alt 2. |
| CATT | Alt 2 |  |
| Nokia, NSB | Alt 2 | We see that all UL channels can benefit from UE initiated FFPs. |
| Samsung | Alt 2 | On top of Alt2, we may consider gNB can configure which UL channels can use UE’s COT. |
| ZTE | Alt2 |  |
| HW/HiSI | Alt 2 (with priority to configured UL) | From regulations perspective, we think that a UE can initiate, and also continue transmitting within, its semi-static CO by transmitting dynamically scheduled uplink channels/signals. However, we would like to clarify that initiating the UE’s semi-static CO using configured uplink transmissions, .e.g. CG, is a priority in this WI as it is well suited for latency reduction in the IIoT uses cases featuring periodic and deterministic data with very low latency requirements. Furthermore, the configured UL transmissions are suitable for operation as an FBE due to their periodic nature. |
| LG | Alt 1 | We think the configured UL channels are sufficient as COT initiator by the UE, but we are open to study other means. |
| OPPO | Alt 2 | In our understanding, COT initiation can be performed in scheduled/configured UL resource. |
| InterDigital | Alt 2 |  |

## Issue#1-4: UE-initiated COT sharing with gNB

In Rel-16, a COT initiated by the gNB can be shared by the UEs in the system. Based on the companies input, it seems there is a common uncerstanding that a COT initiated by a UE can be shared with gNB.

- Summary of proposals: UE-to-gNB COT sharing

- UE-to-gNB COT sharing in semi-static channel access mode is supported.

  - Beijing Xiaomi, Charter, Ericsson, Huawei, HiSilicon, InterDigital, Nokia&NBS, QC, Sony, ZTE,

The related proposals are available in Section 5.4 for reference.

### Discussion point Issue#1-4:

| Q1-2: Do you support UE-to-gNB COT sharing? Options for answers to Q1-4 Yes No Others |
| --- |
| Company | Options for answers to Q1-4 | Comments |
| Sony | Yes | Allowing DL unicast transmission with user plane data on the UE-initiated COT would be beneficial for URLLC operation |
| Apple | Yes |  |
| Intel | Yes | UE’s sharing COT should be allowed and would be highly beneficial. |
| DOCOMO | Yes | No reason not to support COT sharing as it is supported for LBE operation |
| Lenovo, Motorola Mobility | Yes |  |
| vivo | Yes | The UE-initiated COT and gNB-initiated COT should be treated identically. Therefore, the UE-to-gNB COT sharing should be supported. Besides, the ED threshold for COT sharing should also be discussed. |
| Spreadtrum | Yes | We support UE-to-gNB COT sharing and propose to reuse the same mechanism of COT sharing in Rel-16. |
| Qualcomm | Yes |  |
| ETRI | Yes |  |
| Sharp | Yes | We share the similar view with Sony. Futhermore, if PRACH is supported in UE-initiated COT, UE-to-gNB COT sharing is obviously beneficial. |
| CATT | Yes |  |
| Nokia, NSB | Yes |  |
| Samsung | Yes |  |
| ZTE | Yes |  |
| HW/HiSi | Yes | Despite the fact that when both gNB-initiated COT and UE-initiated COT are configured, there is less motivation to introduce UL-DL COT sharing within the UE-initiated semi-static CO, we observe some motivation to introduce such a feature given that target scenario is IIoT/URLLC operation in the unlicensed spectrum. For instance, it would be specifically beneficial for the gNB to transmit CG-DFI immediately after the UL burst without LBT (16us gap). The benefit would be mainly from latency perspective as compared to gNB waiting for the start of the next gNB CO which may be prone to some blocking due to sporadic interference. |
| LG | Yes | We share the same view with Spreadtrum in terms of reusing the same mechanism of COT sharing in Rel-16. |
| OPPO | Yes | We think it is natural to support UE-COT sharing with gNB. The benefit is obvious. |
| InterDigital | Yes |  |

## Issue#1-5: UE/gNb behaviour with UE-initiated COT

In order to specify the corresponding UE/gNB behaviours, companies proposed solutions on how the idle periods and FFPs should be addressed, how COT information and/or related LBT parameters should be indicated to the UE (implicitly or explicitly). It is important to note that the corresponding behaviour in general is similar to those of gNB initated COT.

- Summary of proposals: Interaction between FFPs and Idle periods

  - The UE should be enabled to stop its CO such that it ends before the CCA of a following UE’s frame in the same channel, if any.

    - HW

  - Restricting the UE from transmitting within the idle period of its frame applies to its UL transmissions within the coexisting gNB CO in the same channel.

    - HW

  - Irrespective of the gNB’s and UE’s FFP length, a UE is not allowed to transmit at least within the last 25us of the idle period of the gNB’s FFP.

    - Intel

  - A UE may operate as an initiating device within a gNB’s FFP only in case that FFP is not valid. A valid FFP is a FFP for which the initiating device has succeeded to perform the LBT procedure and accesses that the channel is idle within the latest idle period.

    - Intel

  - Further discuss whether UE initiated COT for FBE based on gNB planning and UL transmission during the idle period are supported.

    - CATT, Sharp,

- Summary of proposals: Channel access rules

  - With respect to channel access procedures, UE/gNB behaviors for gNB initiated COT can be used as the baseline for the UE/gNB behaviors in case of UE initiated COT by exchanging the UE and gNB roles in the procedures.

    - E///, Apple, IntDig, Samsung, MTK (Alt-1)

  - For FBE operation, for UE-initiated COT, before the UL transmission, the UE should (MTK):

    - Alt-2: Carry an LBT at both the frame boundaries and immediately before the transmission.

- Summary of proposals: Explicit indication to UE to initate a COT

  - Dynamic indication of whether to allow UE-initiated COT for the next FFP

  - QC, E///, LG (FFS UE-Common DCI), vivo

- Summary of proposals: Implicit indication to UE to initate a COT

  - If a UL transmission starting time is aligned with the beginning of the FFP provided UE-initiated COT, a UE upon a successful CCA of 9 us, can transmit.

    - E///, Apple, vivo

- Summary of proposals: Indication of COT

  - A UE can send an indication that it has initiated a COT in an FFP

    - IntDig, Sharp.

- Summary of proposals: PRACH in FBE mode

  - Clarify required specifications to enable PRACH transmission of idle UE in FBE mode.

    - QC, Sharp

The related proposals are available in Section 5.5 for reference.

### Discussion point Issue#1-5:

| Q1-5: What is your view on the issues below (as in Proposal summary)? Comments on relation to your view on Q-A/Q-B is welcome. Interaction between FFPs and Idle periods Channel access rules Explicit indication to UE to initate a COT Implicit indication to UE to initate a COT Indication of COT PRACH in FBE mode Options for answers to Q1-5 Describe your preference and reasoning |
| --- |
| Company | Options for answers to Q1-5 | Comments |
| Apple |  | For interaction between FFPs and idle periods, we think the general principle is that we should avoid introducing too many specific restrictions. As long as UE’s FFP period and offset are configured by the gNB, all the behaviors are in gNB’s full control because the UL transmission resources are also configured/scheduled by the gNB. |
| Intel |  | From our perspective, while UE’s FFP and offset are still configured by gNB, it is still important to prioritize the gNB’s as initiating device for the reasons mentioned in our comments in QA. Therefore, we believe that the UE operating as initiating device should be allowed only in certain circumstances based upon the failure of the gNB from acquiring a FFP. |
| DOCOMO |  | Channel access rules UE/gNB behaviors for gNB initiated COT can be used as the baseline Explicit indication to UE to initate a COT DL/UL grant can be used for the indication |
| Lenovo, Motorola Mobility |  | UEs should not transmit in idle periods of gNB FFP Both explicit (e.g., based on cell load,etc.) and implicit schemes (high priority CG transmission) can be useful For UE indicating an initiated COT, we can postpone the discussion till after deciding on high-level aspects of COT initiation (e.g., whether a COT can be initiated in the middle of UE-FFP) for PRACH transmission in idle period, this seems to be a non-essential discussion, considering the priority of UL transmissions are determined based on configuration or scheduling (after transitioning to connected mode) |
| vivo | As Understanding 1 of Q-B Alt1 can be baseline, FFS enhancements likeAlt.2 Dynamic indication can be supported Implicit indication can be supported Not necessary Clarification is needed. | Plesase refer to our comments in Q-B. UE/gNB behaviors for gNB initiated COT can be used as the baseline. FFS: enhancement such as Alt 2 Dynamic indication by gNB can be supported to enable the UE-initiated COT, it gives more flexibility and more efficient for gNB to control the channel usage. Implicit indication or enabling the UE-initiated COT by UE should be supported. UE can choose to initiate the COT if the configured or scheduled resources are aligned with the FFP starting position. The indication of the COT by UE is not necessary, gNB can obtain such information by UL signal/channel detection, the similar way as in gNB-initiated COT. To enable PRACH transmission of idle UE in FBE mode should be clarified. |
| Spreadtrum |  | Interaction between FFPs and Idle periods We do not prefer too many restrictions of interaction between FFPs and Idle periods of gNB and UE. gNB awares all the conditions of UE, so it can guarantee no collision beween idle and FFP. Channel access rules We support gNB initiated COT can be used as the baseline for the UE behaviors in case of UE initiated COT Explicit indication to UE to initate a COT We support this indication to UE, which can give more adaptive COTs initiated by UE and avoid some unneeded channel access. We are open for the other three questions. |
| Qualcomm | Yes for 3. Explicit indication to UE to initiate a COT 5. PRACH in FBE mode | PRACH is allowed to initiate COT for UL transmission in FBE mode |
| ETRI |  | Channel access rules Support 1st bullet. Explicit indication to UE to initate a COT Support. Also can consider RRC signalling to configure the set of FFPs where COT initiation is allowed. |
| Sharp |  | PRACH in FBE mode: if PRACH is not supported in UE-initiated COT, because gNB is not aware of initial access requirement of idle UE, the idle UE has to wait for (probably long time) gNB-initiated COT for other purposes. |
| CATT | Yes for Interaction between FFPs and Idle periods Explicit indication to UE to initate a COT Implicit indication to UE to initate a COT | For Explicit indication to UE to initate a COT,from our point of view, RRC signalling can be used for sem- static indicating to UE to initate a COT. Implicit indication to UE to initate a COT need be supported |
| Nokia, NSB |  | Interaction between FFPs and Idle periods this we discussed in earlier replies Channel access rules reuse gNB procedures as much as possible, details FFS Indication of COT DCI should have an indication of the LBT type, including whether gNB or UE initiates the COT. PRACH in FBE mode should be supported |
| Samsung |  | Interaction between FFPs and Idle periods: It depends on the outcome of QA and QB Channel access rules: Reuse the pricinple in Rel-16 FBE indication to UE to initate a COT: UE needs to know whether to initiate COT. We can first check how to inform UE to indicate a COT or not by existing mechanism, and whether these existing mechanism is sufficient, if not, we can discuss new solutions. Indication of COT by UE: Unecessary. gNB detects UL signals and then gNB knows whether UE initated COT. Channel access rules PRACH: If UE-initiated COT is configured by gNB, e.g. by RMSI, then, PRACH is supported to initate COT. |
| ZTE |  | In order to minimize specification effort, UE/gNB behaviors for gNB initiated COT can be used as the baseline for the UE/gNB behaviors in case of UE initiated COT by exchanging the UE and gNB roles in the procedures. For instance, the behaviors of UE sharing the gNB’s COT should not be restricted from being transmitted during the idle period of UE when the COT of gNB overlaps with the idle period of the UE. |
| HW/HiSi |  | Interaction between FFPs and Idle periods When a UE is configured to initiate its semi-static CO using an offset to the beginning of the gNB frame, the UE should be also enabled to limit its CO such that it ends before the CCA of the following UE’s frame. Note that such a limitation on the UE-initiated semi-static CO is typically more stringent than the inherent limitation MCOT = 0.95 FFPChannel access rules UE/gNB behaviors for gNB initiated |
| LG |  | Interaction between FFPs and Idle periods The interaction is to be with consideration of the coexistence between gNBs/operators. Channel access rules Alt 1 is straightforward and reasonable. Explicit indication to UE to initiate a COT Dynamic indication of whether to allow UE-initiated COT for the next FFP can be considered, where detailed signalling for the indication is to study further. |
| OPPO |  | Interaction between FFPs and Idle periods In our view is given in Q-B. Channel access rules R16 FBE is a baseline. Explicit indication to UE to initiate a COT We are open for discussing the concrete solution. Implicit indication to UE to initate a COT Fine to discuss together with explicit indication. Indication of COT We don’t see the necessity of this, as the gNB can control the UE-initiating behaviour. PRACH in FBE mode We support. |
| InterDigital |  | Channel access rules: UE/gNB behaviors for gNB initiated COT can be used as the baseline for the UE/gNB behaviors in case of UE initiated COT Indication of COT UE to send an indication that it has initiated a COT. |

## Issue#1-6: Other FBE related enhancements

Companies have provided inputs for various enhancements of UE-initated COT operations where the list of corresponding proposals are provided in Section 5.6 for reference.

It is recommended to consider these proposals for discussions, once the basic functionality of UE-initated COT is supported.

# Harmonizing Rel-16 enhancements for UL configured-grant

This section summarizes companies view with respect to the following objective in the WID:

Uplink enhancements for URLLC in unlicensed controlled environments [RAN1, RAN2]: Harmonizing UL configured-grant enhancements in NR-U and URLLC introduced in Rel-16 to be applicable for unlicensed spectrum

Before presenting an overview of the corresponding proposals, one of the companies (Intel) proposed the following due to potentila lack of clarity of the corresponding objective:

- Before discussing any topic in details, RAN1 should first align and clarify the technical scope the objective related to harmonizing the Rel-16 enhancements for CG design among URLLC and NR-U.

- The objective related to harmonizing the Rel-16 enhancements for CG design among URLLC and NR-U should focus exclusively on:

  - Enhancements made during Rel.16 for URLLC specifically on the CG design which are not directly applicable and may require some fine enhancements in order to allow proper operation in the unlicensed spectrum. In this matter, no new additional feature or functionality should be introduced.

  - Enhancements introduced in Rel.16 for NR-U that are not be applicable or feasible to URLLC given that this is targeted to operate in a controlled environment and also given its tight latency and reliability requirements.

With respect to this objective in the WID, companies considered the following high level options for URLLC operations in controlled environement in unlicensed bands:

- Summary of proposals: Harmonizing Rel-16 CG for URLLC unlicensed

- Option 1: Operation based on only URLLC CG features

  - Ericsson, vivo

- Option 2: Operation based on either URLLC CG features or NR-U CG fearures (NW configurability between two independent operational modes)

  - CATT, Ericsson, Huawei, HiSilicon, Intel, DCM, Nokia&NSB, OPPO, Samsung, Sony, Spreadtrum. vivo

- Option 3: Operation based on combined URLLC and NR-U CG features

  - Apple, InterDigital, LG, OPPO, Panasonic, Sharp, TCI, ZTE

### Discussion point Issue#2-1:

| Q2-1: Which option is your preference for the purpose of harmonizing Rel-16 CG for URLLC unlicensed (as in Proposal summary above)? Options for answers to Q2-1 Option 1 Option 2 Option 3 Other Describe your preference and reasoning |
| --- |
| Company | Options for answers to Q2-1 | Comments |
| Sony | Option 2 and 3 | Option 2 for some features, option 3 for other features |
| Apple | Option 3 | We think NR-U CG-UCI design provides us good opportunities to enhance the support for URLLC applications with multiple flows. |
| Intel | Option 2 and 3 | We believe that while it is important to leave up to the NW whether to operate URLLC CG features or NR-U CG features (this could be a starting point), for some features it is beneficial to combine or enhance them from Rel.16. |
| DOCOMO | Option 2 | Option 2 is enough and too much optimization is not necessary |
| Lenovo, Motorola Mobility | Option 1 | We are fine also with option 2 as a second choice |
| vivo | Option 1 or option 2 | To reduce the spec impact, option 1 or option 2 is preferred. The feature by feature combination will involve more effort. |
| Spreadtrum | Option 2 | We do not find any benefit to combine the NR-U and URLLC features for CG-PUSCH. |
| Qualcomm | Option2 and 3 | Should be a case by case study. Need to visit the features in Table 1 below one-by-one and make decision for each of them or each group of them |
| ETRI | Option 2 (and option 3) | In FBE, many of NR-U CG features are very helpful for URLLC. So we prefer to separate operations based on URLLC CG features and NR-U CG features. But if it is found after study that some features are necessary to be combined, then their harmonization can be considered. |
| Sharp | Option 3 or Option 2 | Considering potential specification efforts, we are also open to Option 2. At the beginning phase, further clarification on the objective is necessary. |
| CATT | Option 1 or option 2 | We have the same view with vivo. |
| Nokia, NSB | Option 2 | Both should be supported, but there is no need to align all the feature between Rel-16 GC and NR-U CG. Since NR-U CG is already functional, the main focus is on ensuring the Rel-16 CG can operate on unlicensed spectrum, at least in a controlled environment. |
| Samsung | Option 2 and 3 | Share the same view with Sony, Intel and Qualcomm to review features in table-1. To reduce work load, we may divide features in groups, e.g. HARQ relevant, resource configuration, repetition, and make decision for each group. |
| ZTE | Option 3 | For URLLC operations in unlicensed bands, we need not only consider the latency/reliability target, but also the possible LBT failure. Note that, even in controlled environment, the inter-UE interference among eMBB and URLLC UEs within NR system could cause LBT failure. Therefore, we believe combined features can provide the best performance and make it possible for URLLC operations in unlicensed bands. Meanwhile, we also think the option 2 and 3 should be clarified first. It seems some companies chose option 2 were actually thinking about option 3 :) |
| HW/HiSi |  | The two features of CG-DFI and CG-UCI were introduced to support the decoupling in NR-U CG between the time domain resources and HARQ ID as well as the ability to perform autonomous retransmission on CG resources which has been conditioned upon the expiry of the cg-RetransmissionTimer-r16 which currently mandated for NR-U CG. As such, for harmonizing UL CG enhancements in NR-U and URLLC, it is intuitive to use the cg-RetransmissionTimer-r16 to differentiate which CG Rel-16 features (URLLC or NRU) are applicable in the unlicensed band. If the higher-layer parameter cg-RetransmissionTimer-r16 is provided in ConfiguredGrantConfig, NR-U CG enhancements shall be adopted, Otherwise, URLLC CG enhancements shall be used instead. |
| LG | Option 3 | Some harmonization between URLLC CG features (e.g. PUSCH repetition type B, HPN determination without CG-UCI) and NR-U CG resource allocation would be beneficial to well support URLLC in U-band. But, we are also open to the way of Option 1/2. |
| OPPO | Option 2 and option 3 | Considering new scenario, e.g. unlicensed for URLLC, Features in both NR-U CG and URLLC CG should be supported. So option 2 and option 3 can be considered. |
| InterDigital | Option 3 and Option 2 | Option 1 may add to the latency of a CG transmission when a UE fails to acquire the channel. Furthermore, it doesn't allow NR-U autonomous retransmissions which can be beneficial for URLLC. Option 3 is futureproof since it can combine the benefits of both approaches. |

In order to persue any of these options, it is important to ensure that both Rel-16 NR-U CG features and Rel-16 URLLC features are supported in unlicensed band independelty. An overview of the CG features developed/enhanced in Rel-16 can help to identify issues for such a task. For this purpose, Table 1 provides a list of the UL CG features for Rel-16 NR-U and Rel-16 URLLC that can be easily compared with (R1-2005376) . It can be observed that NR-U CG design aims to improve robustness to combat LBT failures while URLLC CG design aims to reduce latency and ensuring high reliability. Most importantly, due to at least always-configured RRC parameters (e.g. cgRetransmissionTimer), URLLC CG fearures can not be independently configured in unlicesneed band,

Therefore, it is recommended to focus frst on the following:

- Ensure URLLC CG Rel-16 features are supported in unlicensed independently of NR-U CG.

After this step, one can discuss which of the three altenatives above is preferred and how can be achieved.

### Discussion point Issue#2-2:

| Q2-2: Do you agree that the 1st step should be to ensure URLLC CG Rel-16 features are supported in unlicensed independently of NR-U CG? Options for answers to Q2-1 Yes No Other Describe your preference and reasoning |
| --- |
| Company | Options for answers to Q2-2 | Comments |
| Sony | Yes | At least some of them otherwise there is no harmonising of both CGs. |
| Apple | No | My understanding of the proposal is to take either NR-U CG or URLLC CG as a whole, not combining them in any way. We do not see this as an absolutely necessary step. On the contrary, it is something we should discuss and decide. E.g. if we go with Option 3 for Q2-1, we do not have to do this. |
| Intel | No | Our understanding is similar as Apple. Q2-2 needs to be discussed further, and it may depend on the outcome of Q2-1. |
| DOCOMO | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |
| vivo | Yes | URLLC CG Rel-16 features should be supported in the unlicensed band independtly of NR-U CG. It should be considered as a special case for controlled environment in unlicensed band. |
| Spreadtrum | Yes | It can configure the URLLC CG-PUSCH transmissions in unlicensed band. |
| Qualcomm | No | Given 2-1, we do not need to have this step. It is feature by feature discussion. |
| ETRI | Yes | URLLC CG features should be supported as the baseline for unlicensed URLLC in FBE. |
| Sharp | No | We think the first step could be resolving Q2-1. Sharing the similar view as Apple/Intel, the discussion on Q2-2 depends on the output of Q2-1. |
| CATT | Yes | We need clarify whether PUSCH repition type B is included in URLLC CG Rel-16 features. |
| Nokia, NSB | Yes | Since the NR-U CG design is already functional, the focus shall be on Rel-16 CG operation |
| Samsung | It depends on the outcome of Q2-1 |  |
| ZTE | No | As we commented above, for harmonizing Rel-16 CG for URLLC in unlicensed band, it cannot simply based on features only from URLLC or NR-U. For example, if cg-RetransmissionTimer introduced in NR-U is not supported, retransmissions cannot be performed on configured grant configuration. If gNB cannot schedule retransmission by DG-PUSCH because of gNB LBT failure, there would be no chance for retransmission, which impacts the reliability. |
| HW/HiSi | Yes | In addition to multiple active CG configurations, we think that TDRA enhancements introduced in Rel-16 in eURLLC including CG, e.g., PUSCH repetition type B, are suitable for configuring consecutive UL transmissions within the UE-initiated CO without gaps. Orphan symbols ans splitting of nominal repetitions can be handled by proper gNB configurations. Also, the use of FDRA Type 2 introduced for NR-U in Rel-16 is not limited to operation in unlicensed spectrum and it is more suitable to ulfil the OCB and PSD requirements without power backoff compared to FDRA Type 0/1. |
| LG | Yes | We think there seems no reason with another way. |
| OPPO | No | Depending on harmization scheme. For option 3, 1st step may not be required. For option 2, 1st step is necessary. |
| InterDigital | No | We have similar view as Apple. |

Table 1: Configured grant (CG) features supported in Rel.16 NR-U and Rel.16 URLLC (R1-2005376)

| CG features | Rel.16 URLLC | Rel.16 NR-U |
| --- | --- | --- |
| Multiple CG configurations | Supported | Supported |
| HARQ process number/ ID determination | Associated with the configured/indicated first TO, calculated based on the equation defined in TS 38.321 | Decide and reported by the UE in CG-UCI |
| Management of HARQ process number/ ID among multiple CG configurations | Not shared between different CG configurations in the same BWP | Can be shared between different CG configurations in the same BWP |
| RV determination | One of the three RV sequence can be configured and associated with TO {0,0,0,0}; {0,3,0,3}; {0,2,3,1} | Decide and reported by the UE in CG-UCI |
| Flexible initial transmission occasion (TO) | If the CG is configured with Configuredgrantconfig-StartingfromRV0 set to ‘off’, the initial transmission only starts at the first TO of the K repetitions; otherwise, the initial transmission TO depends on the configured RV sequence and K repetitions. | Multiple consecutive potential Tos are configured by cg-nrofPUSCH-InSlot-r16 and cg-nrofSlots-r16, can start initial transmission at any Tos depending on the LBT results. |
| Repetition scheme(s) | PUSCH repetition Type A and PUSCH repetition Type B | Similar as PUSCH repetition Type B without supporting segmentation. (no support of cross-slot resource allocation, and if collide with invalid symbol(s), drop the repetition) |
| CG-Downlink feedback information (DFI) | No support. If Re-scheduling UL grant is not received, UE assumes ACK. | Support, If CG-DFI is not received, UE assumes NACK. |
| CG Re-transmission timer | No support | Support and always configured |
| CG Re-transmission scheme | Only support Re-transmission scheduled by UL grant | Support automatic re-Transmission on the same or different CG configuration decided by UE, and support re-Transmission scheduled by UL grant |

In the following, some of the proposals are presented in more details with respect to solutions to achieve Option 2:

- Summary of proposals: Option 2 for harmonizing Rel-16 CG for URLLC unlicensed

- Configuration of (cg-RetransmissionTimer) should not be mandated when configured grant Type 1 and Type 2 are configured on unlicensed spectrum. (E///)

- DFI flag in DCI 0_1 is not present if the higher layer parameter (cg-RetransmissionTimer) is not configured. (E///)

- The UE is expected to send CG-UCI in every PUSCH only when the higher layer parameter (cg-RetransmissionTimer) is configured (E///)

- For harmonizing UL CG enhancements in Rel-16, if the higher-layer parameter cg-RetransmissionTimer-r16 is provided in ConfiguredGrantConfig, NR-U CG enhancements shall be adopted, otherwise, URLLC CG enhancements shall be used instead. (HW)

- Further study whether and how to decouple the configuration of cg-RetransmissionTimer and other HARQ procedures for CG-PUSCH, e.g. flexible HARQ Process ID and RV selection by UE (Samsung).

### Discussion point Issue#2-3:

| Q2-3: If Option 2 was your preference, what is your solution to achieve that? Do you find any of the proposals above reasonable to achieve that goal? If not, what would be your solution? Options for answers to Q2-3 Describe your preference and reasoning |
| --- |
| Company | Options for answers to Q2-3 | Comments |
| Sony | The above proposals can be a start perhaps with a bit more flexibility in the configurations by considering some of the proposals for Option 3 (below). | There isn’t a discussion point for Option 3 which we believe provides flexibility in using the features in both CGs. Perhaps at the start we can merge Option 2 & 3 as a single option where the some of the features in both CGs can be combined/configured. We should also consider L1 priority for unlicensed URLLC as it is one of the important features introduced for URLLC in Rel-16. |
| Intel | Please see our comments for Q2-1 and Q2-2. |  |
| DOCOMO |  | All of the above proposals can be considered |
| Lenovo, Motorola Mobility | HW’s porposal | HW’s proposal seems simple and reasonable if option 2 is chosen. |
| Vivo | Fowlloing can be the baseline to achieve option 2: Configuration of (cg-RetransmissionTimer) should not be mandated when configured grant Type 1 and Type 2 are configured on unlicensed spectrum. For harmonizing UL CG enhancements in Rel-16, if the higher-layer parameter cg-RetransmissionTimer-r16 is provided in ConfiguredGrantConfig, NR-U CG enhancements shall be adopted, otherwise, URLLC CG enhancements shall be used instead. | As noted, currently the cg-RetransmissionTimer is always configured when operating on unlicensed spectrum, and many NR-U CG features are tied with the cg-RetransmissionTimer. Therefore, we think first step is to remove the mandated parameter for supporting URLLC CG feature in unlicensed band. Then depending on whether cg-RetransmissionTimer is configured or not, the operation based on either NR-U CG fearures or URLLC CG features can be achieved. |
| Spreadtrum |  | We support HW’s proposal. |
| Qualcomm | Option 2 & Option 3 | Option 2 is one way with certain subset of functionalities. It can be option 3 version to support UE-initiated COT sharing. |
| ETRI |  | HW’s proposal seems a reasonable option. |
| CATT |  | From our perspective, 1.Configuration of (cg-RetransmissionTimer) should be optional 2. If the higher-layer parameter cg-RetransmissionTimer-r16is configured, NR-U CG enhancements should be executed, otherwise, R16 URLLC CG should be used. |
| Nokia, NSB | Option 2 | NR-U CG and Rel-16 CG should be as independent as possible. HW proposal is one reasonable way of achieving this. Alternatively, switch between URLLC CG an NR-U CG could be a new field, or some other existing field. Ultimately this may be up to RAN2 to decide as long as the basic split of functionalities is clear. |
| Samsung | It depends on the outcome of Q2-1 |  |
| ZTE |  | Although it is expected that option 2 has the less spec impact, it may not be suitable for URLLC use cases in the unlicensed band. We think some simple combination of NR-U features and URLLC features can improve the latency and reliability with limited spec impact as well, e.g. resource allocation based on URLLC and retransmission based on NR-U. |
| HW/HiSi | If the higher-layer parameter cg-RetransmissionTimer-r16 is provided in ConfiguredGrantConfig, NR-U CG enhancements shall be adopted, Otherwise, URLLC CG enhancements shall be used instead. | Basically, that also implies that a gNB would be able to configure Type 1 / Type 2 CG for operation in unlicensed spectrum without providing the UE with cg-RetransmissionTimer-r16 |
| LG | Share the same view with Samsung’s comment that it depends on the outcome of Q2-1. |  |
| OPPO | HW’s porposal | HW’s proposal seems simple and reasonable if option 2 is supported. |
| InterDigital | We share the same view with Samsung and LG that it depends on the decision on Q2-1. |  |

In the following, some of the proposals are presented in more details with respect to solutions to achieve Option 3 by combining the features from NR-U and URLLC CG:

- Summary of proposals: Option 3 for harmonizing Rel-16 CG for URLLC unlicensed

- For URLLC in controlled environment, a UE selects the HARQ Process ID by implementation from a configured pool of processes for an initial transmission on a CG, as in NR-U. (IntDig)

- A UE can prioritize transmissions over retransmissions on CG resources. The conditions to do so are FFS. (IntDig)

- PHY prioritization of HARQ-ACKs introduced in Rel-16 is supported also with NR-U CG. Interaction of CG-UCI and HARQ-ACK codebooks of different priorities is FFS. (NOK)

- If the same CG operation as licensed band is supported in unlicensed band, it would be useful that at least functions relate to autonomous retransmission on CG and COT sharing are separately enabled/disabled by the configuration. (QC)

- For multiple active configured grant configurations, whether/how to support simultaneous preparations of multiple CG-PUSCHs in different RB sets needs to be discussed (QC)

- Support joint DFI indication for multiple CG configurations (Sharp)

- CG-UCI is always transmitted even when the CG PUSCH is being transmitted over a licensed carrier (TCL)

- For URLLC over unlicensed band, the retransmission mechanism of CG-PUSCH in NR-U can be reused (ZTE)

- Support PUSCH repetition Type B for URLLC operation in unlicensed band (ETRI, LG, NOK, QC, Samsung, Sony, ZTE)

- Support of L1 priority in unlicensed CG (Sony)

Corresponding proposals are provided in Section 5.7 for reference.

# References

R1-2005376	Enhancements for unlicensed band URLLC/IIoT	vivo

R1-2005433	Discussion on unlicensed band URLLC/IIoT	ZTE

R1-2005515	Enhancements for IIoT/URLLC on Unlicensed Band	Ericsson

R1-2005571	Enhancements for unlicensed band URLLC/IIoT	Sony

R1-2005635	On the enhancements for unlicensed band URLLC/IIoT	MediaTek Inc.

R1-2005703	Enhancements for unlicensed band URLLC/IIoT	CATT

R1-2005736	UL transmission for URLLC on unlicensed band	Beijing Xiaomi Software Tech

R1-2005768	Enhancements for unlicensed band URLLC/IIoT	TCL Communication Ltd.

R1-2005871	Uplink enhancements for URLLC operating in unlicensed spectrum	Intel Corporation

R1-2005931	Enhancements for unlicensed band URLLC/IIoT	Lenovo, Motorola Mobility

R1-2006060	Enhancement for unlicensed band URLLC/IIoT	OPPO

R1-2006072	Enhancements for unlicensed band URLLC/IIoT	InterDigital, Inc.

R1-2006141	Enhancements for unlicensed band URLLC/IIoT	Samsung

R1-2006247	On UL Enhancements for IIoT/URLLC in Unlicensed Controlled Environment	Nokia, Nokia Shanghai Bell

R1-2006277	Discussion on enhancements for unlicensed band URLLC/IIoT	Spreadtrum Communications

R1-2006316	Discussion on unlicensed band URLLC/IIOT	LG Electronics

R1-2006344	Enhancements for unlicensed band URLLC/IIoT	Panasonic Corporation

R1-2006356	Discussion on enhancements for URLLC in unlicensed bands	ETRI

R1-2006516	URLLC uplink enhancements for unlicensed spectrum	Apple

R1-2006574	Potential enhancements for unlicensed band URLLC/IIoT	Sharp

R1-2006651	Considerations for unlicensed IIoT	Charter Communications

R1-2006730	Discussion on enhancements for unlicensed band URLLC	NTT DOCOMO, INC.

R1-2006801	Uplink enhancements for URLLC in unlicensed controlled environments	Qualcomm Incorporated

R1-2006888	Discussion on enhancement for unlicensed URLLC/IIoT	WILUS Inc.

R1-2006929	Uplink enhancements for URLLC in unlicensed controlled environments	Huawei, HiSilicon

# Appendix

## Issue#1-1 related proposals

### R1-2005736	Beijing Xiaomi Software Tech	UL transmission for URLLC on unlicensed band

Proposal 2: FFP parameters for UE initiated COT should be flexibly configured by gNB, and both UE dedicated configured or cell common configured should be considered.

### R1-2006651	Charter Communications	Considerations for unlicensed IIoT

Proposal 1: UE-initiated CO is configured with one LBT attempt for channel access per periodic CO, similar to the gNB-initiated case. It is to be studied further if a time offset for the UE LBT needs to be defined relative to the start of the periodic CO in order to avoid collisions with DL LBT.

### R1-2006356	ETRI	Discussion on enhancements for URLLC in unlicensed bands

Proposal 1: A time offset is included in the configuration information of the FFP for UE-initiated COT.

Proposal 2: Discuss necessity of simultaneous configuration of DL FFP and UL FFP in a serving cell.

### R1-2005515	Ericsson	Enhancements for IIoT URLLC on Unlicensed Band

Proposal 1 FFPs for UE initiated COT and gNB initiated COT can be the same or different or mis-aligned.

### R1-2006929	Huawei, HiSilicon	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 1: For a gNB to configure a UE to initiate semi-static CO in an unlicensed channel(s), the gNB configures the UE with the higher layer parameters of the gNB’s semi-static CO in the same channel(s) as in Rel-16 and the new higher layer parameters required for the UE to initiate its semi-static CO based on the gNB’s semi-static CO.

Channel access procedures necessary for the UE to initiate and transmit within its semi-static CO should be specified.

Proposal 2: For UE-initiated semi-static CO in a given unlicensed channel, the UE should be configured with an offset to the beginning of the coexisting gNB frame in the same channel.

### R1-2005871	Intel Corporation	Uplink enhancements for URLLC operating in unlicensed spectrum

Proposal 1: The gNB’s and UE’s FFP can be misaligned through an offset time, which indicates the laps of time between the gNB’s FFP and the UE’s FFP.

### R1-2006316	LG Electronics	Discussion on unlicensed band URLLC IIOT

Proposal #2: Consider configuration of unaligned FFP timing between the FFP stating with gNB-initiated COT and the FFP starting with UE-initiated COT.

### R1-2006247	Nokia, Nokia Shanghai Bell	On UL Enhancements for IIoT URLLC in Unlicensed Controlled Environment

Proposal 6: At least the duration of the UE FFP can be different from the duration of the gNB FFP. FFS whether the UE FFP duration is explicitly configured, or implicitly determined based on other configurations such as RACH configuration, UL CG configuration, etc.

### R1-2005571	Sony	Enhancements for unlicensed band URLLC IIoT

Proposal 1: Support configurations of different Fixed Frame Period between UE-initiated COT and gNB-initiated COT.

### R1-2005376	vivo	Enhancements for unlicensed band URLLC IIoT

Proposal 2: It is beneficial to support asynchronized FFPs since it provides more transmission chances for gNB and UE

Proposal 3: Different FFP length can be considered for gNB and UE.

## Issue#1-2 related proposals

### R1-2006516	Apple	URLLC uplink enhancements for unlicensed spectrum

Proposal 1-1: A default value for the period of UE’s FFP is included in SIB-1. The period of UE’s FFP can be configured to a UE via UE-specific RRC signaling.

Proposal 1-2: The offset of UE’s FFP can be configured to a UE via UE-specific RRC signaling. FFS whether/how to define/signal a default offset.

### R1-2005736	Beijing Xiaomi Software Tech	UL transmission for URLLC on unlicensed band

Proposal 1: FFP parameters/UL channels should be configured/indicated by gNB for a UE initiated COT for FBE.

Proposal 2: FFP parameters for UE initiated COT should be flexibly configured by gNB, and both UE dedicated configured or cell common configured should be considered.

### R1-2005515	Ericsson	Enhancements for IIoT URLLC on Unlicensed Band

Proposal 2 FFP for UE initiated COT can be provided to the UE by SIB or dedicated RRC configuration.

### R1-2006247	Nokia, Nokia Shanghai Bell	On UL Enhancements for IIoT URLLC in Unlicensed Controlled Environment

Proposal 7: Support flexible determination of the start the UE FFP by the UE based on gNB configuration.

Proposal 9: A UE should be able to determine exclusively from information in the scheduling DCI, whether a scheduled PUSCH transmission should be transmitted according to shared gNB COT or UE-initiated COT.

### R1-2006801	Qualcomm Incorporated	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 1: Study the following two alternatives for UE FFP configuration

Alt 1. UE is explicitly configured with a FFP period and offset, where the period can be the same or different from gNB FFP period, and the offset is with respect to gNB FFP offset

Alt 2. COT initiating is introduced as a property of some RRC configured UL transmissions, including CG-PUSCH

FFS: Which other RRC configured UL transmission can be configured to start a COT

### R1-2006141	Samsung	Enhancements for unlicensed band URLLC IIoT

Proposal 1: gNB can configure FFP parameters for UE-initiated COT by RMSI or UE-specific RRC signaling.

### R1-2006277	Spreadtrum Communications	Discussion on enhancements for unlicensed band URLLC IIoT

Proposal 1: Regarding the period of UE-initiated COT (Tx_UE), it can be separately configured by higher layer singling

Proposal 2: The starting positions are given by the FFP.

Proposal 3: Configure the un-overlapped COTs that are initiated by gNB and UE.

### R1-2006888	WILUS Inc.	Discussion on enhancement for unlicensed URLLC IIoT

Proposal 1: For Rel-17, regarding the signaling for FBE operation when a UE operates an initiating device, it should be supported that a gNB provides UE(s) with high layer signaling by SIB1 or dedicated configuration as like that of signaling a gNB-initiated COT in Rel-16 NR-U.

index.

## Issue#1-3 related proposals

### R1-2006516	Apple	URLLC uplink enhancements for unlicensed spectrum

Proposal 1-4: At least PRACH, CG/DG-PUSCH, SR and HARQ-ACK should be allowed to trigger UE-initiated COT. FFS other channels/signals.

### R1-2005736	Beijing Xiaomi Software Tech	UL transmission for URLLC on unlicensed band

Proposal 3: Configuring periodical UL channels, such as CG-PUSCH, at the beginning of FFP, will facilitate UE to initiate a COT successfully.

### R1-2006072	InterDigital, Inc.	Enhancements for unlicensed band URLLC IIoT

Proposal 1: UEs can initiate COTs in FBE to use configured UL resources (CG, PRACH, PUCCH).

### R1-2005931	Lenovo, Motorola Mobility	Enhancements for unlicensed band URLLC IIoT

Proposal 1: For supporting URLLC in unlicensed band, only UEs with high priority data/control can be allowed to initiate a COT for FBE.

### R1-2005635	MediaTek Inc.	On the enhancements for unlicensed band URLLC IIoT

Proposal 1: For FBE operation, UE-initiated COT is used for connected mode only. RACH transmission to use a gNB initiated COT in FBE.

### R1-2006247	Nokia, Nokia Shanghai Bell	On UL Enhancements for IIoT URLLC in Unlicensed Controlled Environment

Proposal 8: No restrictions to UE FFP configuration based on gNB FFP configuration are introduced other than what is already specified in TS 37.213 regarding UL transmissions within the idle period of the gNB FFP.

### R1-2006801	Qualcomm Incorporated	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 1: Study the following two alternatives for UE FFP configuration

Alt 1. UE is explicitly configured with a FFP period and offset, where the period can be the same or different from gNB FFP period, and the offset is with respect to gNB FFP offset

Alt 2. COT initiating is introduced as a property of some RRC configured UL transmissions, including CG-PUSCH

FFS: Which other RRC configured UL transmission can be configured to start a COT

### R1-2006888	WILUS Inc.	Discussion on enhancement for unlicensed URLLC IIoT

Proposal 2: It should be further discussed whether or not it can be allowed to support UE-initiated COT using scheduled channels and signals under the channel access mode for FBE operation.

Proposal 3: It should be further discussed on collision issue of UL transmission within a channel occupancy of initiated COTs by multiple UEs.

## Issue#1-4 related proposals

### R1-2005736	Beijing Xiaomi Software Tech	UL transmission for URLLC on unlicensed band

Proposal 5: gNB initiated COT sharing can be exploited to enable transmission of UL channels outside UE initiated COTs.

### R1-2006651	Charter Communications	Considerations for unlicensed IIoT

Proposal 2: A UE-initiated CO in semi-static channel access can be shared with the gNB.

### R1-2005515	Ericsson	Enhancements for IIoT URLLC on Unlicensed Band

Proposal 3 With respect to channel access procedures, UE/gNB behaviors for gNB initiated COT can be used as the baseline for the UE/gNB behaviors in case of UE initiated COT by exchanging the UE and gNB roles in the procedures.

### R1-2006801	Qualcomm Incorporated	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal4: UE can share its initiated COT to gNB.

### R1-2005571	Sony	Enhancements for unlicensed band URLLC IIoT

Proposal 2: UE-to-gNB COT sharing in FBE should be supported.

### R1-2005433	ZTE	Discussion on unlicensed band URLLC IIoT

Proposal 1: gNB and UE can perform some transmission during the current channel occupancy time by sharing COT when the channel sensed to be busy.

Proposal 2: For gNB sharing the UE-initiated COT, the case when the gap between the DL and DL transmission bursts is more than 16us should be considered.

## Issue#1-5 related proposals

### R1-2006516	Apple	URLLC uplink enhancements for unlicensed spectrum

Proposal 1-3: A UE is allowed to perform LBT for UE-initiated COT if:

Parameters for UE’s FFP are configured.

The UE has not detected any DL signal before UL transmission in the overlapping DL FFP.

The UE has a transmission starting at the UE’s FFP boundary.

FFS other conditions

### R1-2005703	CATT	Enhancements for unlicensed band URLLC IIoT

Proposal 1: Further discuss whether UE initiated COT for FBE based on gNB planning and UL transmission during the idle period are supported.

### R1-2005515	Ericsson	Enhancements for IIoT URLLC on Unlicensed Band

Proposal 3 With respect to channel access procedures, UE/gNB behaviors for gNB initiated COT can be used as the baseline for the UE/gNB behaviors in case of UE initiated COT by exchanging the UE and gNB roles in the procedures.

Proposal 4 If a UL transmission starting time is aligned with the beginning of the FFP provided UE-initiated COT, a UE upon a successful CCA of 9 us, can transmit.

Proposal 5 Support both Implicit and explicit indications of the channel access

### R1-2006316	LG Electronics	Discussion on unlicensed band URLLC IIOT

Proposal #3: Consider dynamic indication of whether to allow UE-initiated COT for the next FFP, based on the transmission of an UE-common DCI

### R1-2006929	Huawei, HiSilicon	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 3: For UE-initiated semi-static CO in a given unlicensed channel, the UE should be enabled to stop its CO such that it ends before the CCA of a following UE’s frame in the same channel, if any.

Proposal 4: For UE-initiated semi-static CO in a given unlicensed channel, restricting the UE from transmitting within the idle period of its frame applies to its UL transmissions within the coexisting gNB CO in the same channel.

### R1-2005871	Intel Corporation	Uplink enhancements for URLLC operating in unlicensed spectrum

Proposal 2: Irrespective of the gNB’s and UE’s FFP length, a UE is not allowed to transmit at least within the last 25us of the idle period of the gNB’s FFP.

Proposal 3: A UE may operate as an initiating device within a gNB’s FFP only in case that FFP is not valid. A valid FFP is a FFP for which the initiating device has succeeded to perform the LBT procedure and accesses that the channel is idle within the latest idle period.

### R1-2006072	InterDigital, Inc.	Enhancements for unlicensed band URLLC IIoT

Proposal 2: A UE can initiate a COT in an FFP for a transmission occurring later in the FFP.

Proposal 3: A UE can send an indication that it has initiated a COT in an FFP.

### R1-2005635	MediaTek Inc.	On the enhancements for unlicensed band URLLC IIoT

Proposal 3: For FBE operation, for UE-initiated COT, before the UL transmission, the UE should:

Alt-1: Carry an LBT at the frame boundaries of a dedicated FFP

Alt-2: Carry an LBT at both the frame boundaries and immediately before the transmission.

### R1-2006801	Qualcomm Incorporated	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 2: Study how to transmit PRACH in idle period in FBE when UE works as initiated-COT device.

Proposal 3: gNB can send a dynamic indicator in a DCI for UE to initiate COT by LBT, while gNB maintains the FFP structure for UE by properly picking the granted UL transmission time

### R1-2006141	Samsung	Enhancements for unlicensed band URLLC IIoT

Proposal 2: A UE can transmit UL signals within its COT after UE finishes LBT before the start of COT, and shares its COT to gNB. gNB may transmit DL transmission within a UE-initiated COT after detection of UL signal from the UE.

### R1-2006574	Sharp	Potential enhancements for unlicensed band URLLC IIoT

Proposal 1: Clarify required specifications to enable PRACH transmission of idle UE in FBE mode.

Proposal 2: Clarify whether to indicate COT duration in FBE mode.

Proposal 3: Clarify how to determine the idle period for UE-initiated COT in FBE mode.

## Issue#1-6 related proposals

### R1-2006516	Apple	URLLC uplink enhancements for unlicensed spectrum

Proposal 1-5: Consider supporting the configuration of a priority level restriction for PUSCH, SR, HARQ-ACK for triggering UE-initiated COT.

### R1-2005736	Beijing Xiaomi Software Tech	UL transmission for URLLC on unlicensed band

Proposal 4: To guarantee continuous channel occupation, padding signals may be needed to fill the gaps between multiple UL channels in a UE initiated COT

### R1-2005703	CATT	Enhancements for unlicensed band URLLC IIoT

Proposal 1: Further discuss whether UE initiated COT for FBE based on gNB planning and UL transmission during the idle period are supported.

### R1-2006356	ETRI	Discussion on enhancements for URLLC in unlicensed bands

Proposal 2: Discuss necessity of simultaneous configuration of DL FFP and UL FFP in a serving cell.

### R1-2006316	LG Electronics	Discussion on unlicensed band URLLC IIOT

Proposal #1: Consider gNB-controlled UE-initiated COT mechanisms for FBE based U-band environments, in order to avoid potential collision/blocking between UE’s UL transmission and gNB’s essential DL transmission

### R1-2005931	Lenovo, Motorola Mobility	Enhancements for unlicensed band URLLC IIoT

Proposal 2: For the case of UE-initiated COT with configured grant PUSCH transmission, the number of repetitions applied to a transport block at the beginning of the acquired FFP is less than the number of repetitions associated with PUSCH transmissions of the configured grant (in transmission occasions other than those of the beginning of the acquired FFP).

Proposal 3: For the case of UE-initiated COT with configured grant PUSCH transmission, the transmit power at the beginning of the acquired FFP can be higher than the transmit power associated with PUSCH transmissions of the configured grant (in transmission occasions other than those of the beginning of the acquired FFP).

Proposal 4: For the case of UE-initiated COT with configured grant PUSCH transmission, solutions should be considered to avoid LBT before a high priority UL transmission at the beginning of the acquired FFP.

### R1-2005635	MediaTek Inc.	On the enhancements for unlicensed band URLLC IIoT

Proposal 2: For FBE operation, for UE-initiated COT, the UE is explicitly signalled or implicitly determines a second fixed frame period which could be the same or different from the fixed frame period used by the gNB.

### R1-2006730	NTT DOCOMO, INC.	Discussion on enhancements for unlicensed band URLLC

Proposal 1: Study the solution to initiate COT when no node initiates COT at the beginning of FFP

### R1-2006060	OPPO	Enhancement for unlicensed band URLLC IIoT

Proposal 1: UE-initiated COT for FBE should be supported with minimum specification effort.

### R1-2006344	Panasonic Corporation	Enhancements for unlicensed band URLLC IIoT

Proposal 1: Multiple starting time offset for configured grant can be reused to support UE-initiated COT.

Proposal 2: If DG-PUSCH is used for UE-initiated COT together with CG-PUSCH, CP extension for multiple starting time offset as in CG-PUSCH is also supported for DG-PUSCH.

### R1-2006801	Qualcomm Incorporated	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 5: Study ED thresholds selection when UE share its COT to gNB.

Proposal 6: Study the scheme that UE can share its COT to the other UEs through gNB.

### R1-2006574	Sharp	Potential enhancements for unlicensed band URLLC IIoT

Proposal 4: Identify required enhancements to implement higher level autonomous UL transmission.

### R1-2005768	TCL Communication Ltd.	Enhancements for unlicensed band URLLC IIoT

Proposal 2: It is proposed to further investigate the scenario when DL symbols occur in the middle of an UL scheduled resource.

### R1-2005376	vivo	Enhancements for unlicensed band URLLC IIoT

Proposal 1: It is beneficial to enable UE as an initiating device for FBE operation.

### R1-2005433	ZTE	Discussion on unlicensed band URLLC IIoT

Proposal 2: For gNB sharing the UE-initiated COT, the case when the gap between the DL and DL transmission bursts is more than 16us should be considered.

## Issue#2 related proposals

### R1-2006516	Apple	URLLC uplink enhancements for unlicensed spectrum

Proposal 2-1: Consider enhanced CG-UCI on unlicensed spectrum to allow the UE to autonomously adapt certain transmission parameters such as MCS.

### R1-2005703	CATT	Enhancements for unlicensed band URLLC IIoT

Proposal 2:  Consider CG PUSCH mechanism in NR-U or URLLC CG mechanism in licensed band as baseline with potential enhancements to be applicable for unlicensed spectrum.

### R1-2005515	Ericsson	Enhancements for IIoT URLLC on Unlicensed Band

Proposal 6 Configuration of (cg-RetransmissionTimer) should not be mandated when configured grant Type 1 and Type 2 are configured on unlicensed spectrum.

Proposal 7 DFI flag in DCI 0_1 is not present if the higher layer parameter (cg-RetransmissionTimer) is not configured

Proposal 8 The UE is expected to send CG-UCI in every PUSCH only when the higher layer parameter (cg-RetransmissionTimer) is configured

### R1-2006356	ETRI	Discussion on enhancements for URLLC in unlicensed bands

Proposal 3: Enhance the PUSCH repetition type B for URLLC-U operation.

Proposal 4: In FBE, for PUSCH mapping type B, the idle symbols are regarded as invalid symbols.

### R1-2006929	Huawei, HiSilicon	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 5: For harmonizing UL CG enhancements in Rel-16, if the higher-layer parameter cg-RetransmissionTimer-r16 is provided in ConfiguredGrantConfig, NR-U CG enhancements shall be adopted, otherwise, URLLC CG enhancements shall be used instead.

### R1-2005871	Intel Corporation	Uplink enhancements for URLLC operating in unlicensed spectrum

Proposal 4: Before discussing any topic in details, RAN1 should first align and clarify the technical scope the objective related to harmonizing the Rel-16 enhancements for CG design among URLLC and NR-U.

Proposal 5: The objective related to harmonizing the Rel-16 enhancements for CG design among URLLC and NR-U should focus exclusively on:

Enhancements made during Rel.16 for URLLC specifically on the CG design which are not directly applicable and may require some fine enhancements in order to allow proper operation in the unlicensed spectrum. In this matter, no new additional feature or functionality should be introduced.

Enhancements introduced in Rel.16 for NR-U that are not be applicable or feasible to URLLC given that this is targeted to operate in a controlled environment and also given its tight latency and reliability requirements.

### R1-2006072	InterDigital, Inc.	Enhancements for unlicensed band URLLC IIoT

Proposal 4: For URLLC in controlled environment, a UE selects the HARQ Process ID by implementation from a configured pool of processes for an initial transmission on a CG, as in NR-U.

Proposal 5: A UE can prioritize transmissions over retransmissions on CG resources. The conditions to do so are FFS.

### R1-2006316	LG Electronics	Discussion on unlicensed band URLLC IIOT

Proposal #4: Consider new equation for determining HARQ process ID (e.g., based on NR-U CG resource allocation) in order to support multiple TB transmission per period.

Proposal #5: Consider to adopt PUSCH repetition type B for NR-U CG resource allocation to support flexible resource allocation.

Proposal #6: Consider to handle the orphan symbol created after segmentation under some condition in unlicensed band to avoid unnecessary LBT/CAP procedure.

### R1-2006730	NTT DOCOMO, INC.	Discussion on enhancements for unlicensed band URLLC

Proposal 2: Support CG-PUSCH with/without CG-DFI or CG-UCI by configuration in unlicensed band

### R1-2006247	Nokia, Nokia Shanghai Bell	On UL Enhancements for IIoT URLLC in Unlicensed Controlled Environment

Proposal 1: Two operation modes can be considered independently; NR IIoT Rel-16 based CG with NR based HARQ procedure and without CG-UCI, and NR-U based CG including CG-UCI and possibility of UE COT sharing.

Proposal 2: PUSCH repetitions type-B should be supported for unlicensed band operation when using NR IIoT Rel-16 based CG, without NR-U specific enhancements. FFS: required spec changes, if any.

Proposal 3: The use of PUSCH repetition type-B together with NR-U based multi-slot allocations should not be considered.

Proposal 4: Frequency hopping can be considered for UL resource allocation type 2 in case of wideband (>20 MHz) operation.

Proposal 5: PHY prioritization of HARQ-ACKs introduced in Rel-16 is supported also with NR-U CG. Interaction of CG-UCI and HARQ-ACK codebooks of different priorities is FFS.

### R1-2006060	OPPO	Enhancement for unlicensed band URLLC IIoT

Proposal 2: It is necessary to harmonize NR-U configured grant and NR configured grant.

Proposal 3:  Both option 1 and option 2 can be studied to harmonize NR-U configured grant and NR configured grant.

- Option 1: NR-U CG mode and NR CG mode can be configured for each configured grant

- Option 2: Enhanced configured grant combining features in NR-U and NR configured grant

### R1-2006344	Panasonic Corporation	Enhancements for unlicensed band URLLC IIoT

Proposal 3: If the same CG operation as licensed band is supported in unlicensed band, it would be useful that at least functions relate to autonomous retransmission on CG and COT sharing are separately enabled/disabled by the configuration.

Proposal 4: For multiple active configured grant configurations, whether/how to support simultaneous preparations of multiple CG-PUSCHs in different RB sets needs to be discussed.

### R1-2006801	Qualcomm Incorporated	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 7: NR-U CG-PUSCH shall support type A PUSCH repetition introduced in Rel.16 URLLC by reinterpreting the # of repetitions in consecutive slots as the # of repetitions in consecutive transmission occasions.

Proposal 8: NR-U CG-PUSCH shall support type B PUSCH repetition introduced in Rel.16 URLLC with the proposal in this contribution.

### R1-2006141	Samsung	Enhancements for unlicensed band URLLC IIoT

Proposal 3: Support configurable cg-RetransmissionTimer to avoid unnecessary autonomous retransmission for CG-PUSCH. Further study whether and how to decouple the configuration of cg-RetransmissionTimer and other HARQ procedures for CG-PUSCH, e.g. flexible HARQ Process ID and RV selection by UE.

Proposal 4: Further study how to support Type-B PUSCH repetition over unlicensed band.

### R1-2006574	Sharp	Potential enhancements for unlicensed band URLLC IIoT

Proposal 5: Support joint DFI indication for multiple CG configurations.

Proposal 6: Support DFI indication in DCI format 0_2.

Proposal 7: Support configuration of multiple UL transmission opportunities in frequency domain.

### R1-2005571	Sony	Enhancements for unlicensed band URLLC IIoT

Proposal 3: Configurability of the NR-U CG feature (e.g. CG-DFI and CG-UCI) should be considered in an unlicensed controlled environment.

Proposal 4: URLLC CG features (e.g. L1 priority and Type B PUSCH repetition) should be supported in unlicensed operation.

### R1-2006277	Spreadtrum Communications	Discussion on enhancements for unlicensed band URLLC IIoT

Proposal 4: Reuse the existing parameter or introduce a new parameter to configure NR-U UL CG enhancements or URLLC UL CG enhancements that can be used by a UE

### R1-2005768	TCL Communication Ltd.	Enhancements for unlicensed band URLLC IIoT

Proposal 1: CG-UCI is always transmitted even when the CG PUSCH is being transmitted over a licensed carrier.

Proposal 3: For CG transmission, if dynamic SFI is configured but the UE cannot decode dynamic SFI, semi-static flexible symbols in the scheduled resource are used for PUSCH.

Proposal 4: The TDRA table is extended with the indication of number of repetitions. Each TB is indicated by a SLIV and number of repetitions. A SLIV only corresponds to one TB and not to PUSCH repetition of a TB.

Proposal 5: The number of entries in the new TDRA table increases based on the number of the scheduled TBs, the maximum allowed number of repetitions for each TB, the number of bits in TDRA field of DCI.

### R1-2006888	WILUS Inc.	Discussion on enhancement for unlicensed URLLC IIoT

Proposal 4: It should be further discussed whether or not to possibly transmit configured-grant PUSCH with repetition at candidate SS/PBCH block positions with same SS/PBCH block index after the detection of the SS/PBCH block

### R1-2005433	ZTE	Discussion on unlicensed band URLLC IIoT

Proposal 3: For CG PUSCH, the repetition pattern for URLLC over unlicensed band is determined as follows.

The starting symbol of the first repetition, the duration of a repetition and the ending symbol of last repetition is determined by NR-U rules.

Back-to-back repetitions with segmentation across the slot boundary or invalid symbols is supported as in Rel-16 URLLC.

Proposal 4: For CG PUSCH, it is configurable to enable or disable the feature of starting the initial transmission at the last repetition when K≥8.

Proposal 5: For URLLC over unlicensed band, CG-UCI is transmitted per actual repetition.

Proposal 6: For URLLC over unlicensed band, the interaction with DL/UL directions for Type 1 CG PUSCH and Type 2 CG PUSCH without the first PUSCH (including all the repetitions) is determined as follows.

If dynamic SFI is not received and not provided EnableConfiguredUL-r16, the actual repetition is not transmitted if it conflicts with a semi-static flexible symbol.

If dynamic SFI is not received but provided EnableConfiguredUL-r16, the actual repetition can be transmitted.

Proposal 7:  For URLLC over unlicensed band, the retransmission mechanism of CG-PUSCH in NR-U can be reused.

### R1-2005376	vivo	Enhancements for unlicensed band URLLC IIoT

Proposal 4: Option 1 or option 2 is preferred to support UL CG for URLLC in unlicensed band.

- Option 1: only support URLLC CG mechanism in unlicensed band.

- Option 2: NW can decide to use either URLLC CG mechanism or NR-U CG mechanism in unlicensed band.

- Option 3: feature-by-feature discussion or combination of some features from NR-U and URLLC CG mechanism.