3GPP TSG RAN WG1 Meeting #104-e		 				R1-2102175

E-meeting, January 25th – February 5th, 2021

Agenda item:		8.3.2

Source:		Moderator (Ericsson)

Title:	 	Summary#6 - URLLC/IIoT operation on Unlicensed Band

Document for:	        Discussion and Decision

# Introduction

This document is revised version of R1-2102173 and is intended to facilitate exchange of views and discussions for the following assigned email discussion by Mr. Chairman:

[104-e-NR-R17-IIoT_URLLC-03] Email discussion on enhancements for unlicensed band URLLC/IIoT – Sorour (Ericsson)

- 1st check point: Jan 28

- 2nd check point: Feb 2

- 3rd check point: Feb 4

The list below, provides a high level categorization of the topics that are addressed in the contributions submitted to this meeting. Detailed discussions with respect to each topic can be found section 2.

Discussion topics:

- FFP parameters configuration -periodicity and offset

- Additional transmission conditions in idle periods

- RRC enabling COT initiation functionality

- COT-initiator determination

- COT-initiation control/cancelation/overriding

- Scheduling and UE-to-gNB COT restrictions

- Indication of UE-initiated COT to gNB

- UE-to-UE COT sharing via gNB

- UE-initiated COT in Inactive/Idle mode

- Other FBE topics (ED sensing threshold, Processing time, CP extension, Capability, DL within UL, etc.)

- NR-U and URLLC CG harmonization

- Enhancements on PUSCH repetition

Summary of exchanged views and status of the discussion during the meeting is provided in the next section.

During the meeting, the following topics were prioritized for discussion with more focus on the first three topics:

- FFP parameter configuration (section 2.1.5)

- Additional constraints on idle periods (section 2.2.1)

- COT-initiator determination (section 2.4 )

- NR-U and URLLC CG harmonization – Main issues (section 2.11.1)

- Applicability of LBE constraints to FBE (start w discussions in section 2.6.1)

- Discussions on set of proposals with majority support

  - UE initiated COT restrictions (section 2.6.4)

  - Indication of UE-initiated COT to gNB (section 2.7)

  - UE-to-UE COT sharing via gNB (section 2.8)

During the online session on 27th January, the following agreements were made:

Agreement:

- PUSCH repetition Type B is supported for unlicensed band operation when using NR IIoT Rel-16 based CG

  - FFS whether/how to enhance

Agreement:

- In semi-static channel access mode, UE FFP periodicity is chosen from the following set of values in ms: {1, 2, 2.5, 4, 5,10}.

  - FFS on other values

During the online session on February 2nd, the following agreements were made:

Agreement:

- In semi-static channel access mode:

- An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT

- FFP period for UE-initiated COT can be configured independently from FFP period of gNB-initiated COT, if the UE indicates the corresponding capability

- FFP offset for UE-initiated COT is the starting point of first UE FFP relative to the radio frame X boundary.

  - The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT

    - FFS on X (e.g. X=0, or X= even index number)

Agreement:

In semi-static channel access mode when a UE can operate as initiating device,

- Select one of the following alternatives to determine whether a scheduled UL transmission is based on UE-initiated COT or sharing a gNB-initiated COT:

- Alt-a: Determination based on the content in the scheduling DCI

  - FFS on whether the corresponding field(s) can be absent in DCI

    - If absent, determination based on the rules applied for configured UL transmissions is applied

  - FFS whether/how to handle the case when the gNB schedules an UL transmission in the next gNB’s FFP period

  - Alt-b: Determination based on the rules applied for a configured UL transmission

During the online session on February 4th , the following agreements were made:

Agreement:

In semi-static channel access mode when a UE can operate as UE-initiated COT,

- Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT:

  - Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT

  - Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT.

Agreement:

- In semi-static channel access mode, sharing a UE initiated COT through the gNB to other intra-cell UEs for UL transmissions, is not supported.

# Discussions

## Discussion topic: FFP parameters configuration - periodicity and offset

The proposals 1-1 to 1-4 below, aim to capture the views with respect to the discussion topic, on high level.

### Dependency between UE FFP and gNB FFP periodicity configuration

Proposal 1-1:

- In semi-static channel access mode, down-select one of the following alternatives:

- Alt-1: FFP Periodicity for UE-initiated COT is configured as the same, or integer multiple of, inter factor of the FFP periodicity configured for gNB-initiated COT

  - HW, QC, Intel, ETRI

- Alt-2: FFP Periodicity for UE-initiated COT is configured independently from FFP periodicity of gNB-initiated COT

  - E///, Samsung, vivo, DCM, Xiaomi,

| Question: What is your view on Proposal 1-1? |
| --- |
| Company | Comment |
| Sony | We prefer Alt-2. With Alt-2, the gNB can always configure UE’s FFP Period as multiple integer factor to that of the gNB. |
| vivo | Alt-2 is preferred. We see no implementation issue with independent FFP periodicity of gNB and UE. On the contrary, it can bring flexibility and fit better to the URLLC traffic. |
| Futurewei | Alt-2 |
| Intel | We prefer Alt-1, for the following reasons: If no constrain is imposed to the gNB on how to configure the u-FFP and g-FFP periodicity, the gNB has a very large set of permutations among which it can choose from. Some of which, would negatively impact both the gNB’s and UE’s behavior since the idle periods of the two devices would not occur with a periodic cadence, and the starting position of the u-FFP and g-FFP relative to each may also vary. In this case, the two devices would need to calculate and keep track for each FFP where the idle period of the other device would lie. As an example, if the g-FFP is equal to 5ms, and the u-FFP is chosen to be 1ms, and the first u-FFP is shifted in time by 2ms relative to the first g-FFP, then if we apply a shift of 2ms to the start of every g-FFP, there will be the start of the u-FFP. However, if the u-FFP is equal to 2ms, this is no longer valid, as shown in figure below. In order to avoid the issue mentioned above, in our option the gNB should chose the u-FFP (or g-FFP) such that this is always an integer factor or a multiple of the current g-FFP (u-FFP) value. While the u-FFP and g-FFP cannot be varied frequently, it is still possible to change them over time as long as a minimum observation time of 200 ms has passed without making any changes. As mentioned above, if no limitations are imposed on how the gNB can change the u-FFP relative to a g-FFP, then there are a very large number of possible choices. This would impose to the UE that at any given time it should prepare transmissions under several assumptions, which overcomplicates the UE’s implementation and would impact its computations complexity. |
| CATT | Alt-2 |
| LG | Alt-2 |
| Panasonic | We prefer Alt.2. Considering Proposal 1-2 in Section 2.1.2, we think Alt.2 can realize FFP periodicity for UE-initiated COT as the same or integer multiple of the FFP periodicity configured for gNB-initiated COT. |
| ZTE | We prefer Alt-2 |
| Nokia, NSB | Alt-2. We are concerned that Alt-1 may introduce unnecessary constraints at gNB. It is true that the relative timing of the UE FFP as compared to the gNB FFP will vary as a function of the SFNm, but is this really a concern for UE complexity? |
| Sharp | We prefer Alt-2 which provides desirable configuration flexibility. We are not clear/convinced why/how UE implementation complexity is reduced by Alt-1. |
| ETRI | We prefer Alt-1. Benefit of supporting additional flexibility is not clear. |
| Qualcomm | Alt-1. We think the UE complexity can be reduced a lot by adding this limitation. We prefer the UE FFP starting points are at a limited set of relative locations with respect to gNB FFP starts. If we allow Alt 2, in most cases, the UE FFP start will keep changing with respect to gNB FFP start. Sometimes it will be at the beginning, and sometime, it will be at the end, and sometime it will fall into the idle period. We will need to have different rules for different instance of UE FFP, which complicates both gNB and UE planning. In addition, We do not see the obvious benefit for Alt-2 even if it has high complexity. If we apply some limitations to gNB FFP duration as we did for Rel.16, we don’t see why not applying the same limitation to UE side. |
| NEC | We support Alt-1. |
| OPPO | Alt-1 is preferred, some restriction is needed to keep the UE complexity low. |
| InterDigital | We support Alt-2. The gNB can choose if it wants the UE’s FFP to be an integer multiple or factor of the gNB’s FFP. |
| DOCOMO | Alt-2 |
| Lenovo/Motorola Mobility | Alt-2: in case of reconfiguration of gNB-FFP parameters, the UE-FFP periodicity might need to be updated if tied to gNB FFP periodicity. considering the FFP parameter update rate is not sooner than once every 200ms for both gNB-FFP and UE-FFP; relating UE-FFP parameters to gNB-FFP parameters could effectively slow down update rate of UE-FFP parameters. |
| Samsung | Alt-2. DL and UL traffic is typically independent, it makes sense to support independent FFP for gNB and UE, otherwise, the gain of UE-initiated COT degrades materially. |
| Spreadtrum | Alt-2. UE-FFP parameters depends on its own traffic types especially configured grant UL transmission, it varies with DL traffic. Furthermore, if needed, gNB can configured UE-FFP into integer multiple of, or inter factor of the FFP periodicity of gNB-FFP. |
| Apple | Even though we see some additional flexibility provided by Alt-2, we also acknowledge the additional complexity at the UE to support Alt-2. Therefore, we have slight preference for Alt-1. |
| WILUS | We prefer Alt-2 to provide more flexibility for FFP parameters configuration and we don’t see any clear benefit to restrict the configuration as like Alt-1. |
| Xiaomi | Alt 2. As we have analyzed in our contribution, FDM manner operation can be realized on different LBT bandwidth, thus no need to restrict the gNB/UE FFP configuration. |
| HW/HiSi | We prefer Alt-1. Our first preference within Alt-1 is the same FFP periodicity. In that case the specification and implementation impact is minimized, where the former is the objective in this WID. Having the inter multiple/factor relationship would at least simplify the UE implementation and provides a great amount of flexibility if this is desired. Going with Alt-2 complicates the UE implementation but only allows for very few additional configurations. As shown in the table below, most configurations are already supported. Furthermore, with Alt-2, and for a combination of FFPu and FFPg that does not possess the inter-factor/integer multiple relationship, the configured offset,which is supposed to control the time shift between the start of the UE frame and the start of the gNB frame, becomes meaningless for subsequent frames since the time shift will be realized neither every UE frame nor every gNB frame. With Alt-1 however, the configured offset results in the same time shift following the maximum periodicity of gNB FFP and UE FFP. Table 1 - Example for supported combinations of FFPu and FFPg when one is a multiple of the other FFPg 1 2 2.5 4 5 10 FFPu examples 1 Yes Yes Yes Yes Yes 2 Yes Yes Yes Yes 2.5 Yes Yes Yes 4 Yes Yes Yes 5 Yes Yes Yes Yes 10 Yes Yes Yes Yes Yes In response to Sony, It is important to note that, as long as there is no rule specified to ensure that the integer multiple/inter-factor relationship is maintained in any combination of FFPg and FFPu configured to the UE, the UE cannot expect that such relationship is maintained. As such, the UE implementation would have to be designed to handle the general case of any combination of FFPg and FFPu, including those combinations that do not achieve the desired relationship. |
| Moderator | As proposed by companies, it is better to discuss together the topics in section 2.1. The @All: The discussion for this topic is merged with other topics in this section and is summarized in -> Section 2.1.5 |

### Range values of UE FFP periodicity

Proposal 1-2:

- In semi-static channel access mode, down-select one of the following alternatives:

- Alt-1: UE FFP periodicity is chosen from the following set of values in ms: {1, 2, 2.5, 4, 5, [8],10}.

  - Intel, DCM, Spreadtrum, Sharp (+8ms)

- Alt-2: UE FFP periodicity can be any integer number of slots with the duration at least 1ms and at most 10ms.

  - Samsung, E///, Spreatrum,

- Alt-3: UE FFP periodicity can be a subset of the period of tdd-UL-DL configuration or the gNB FFP configuration.

  - ZTE

| Question: What is your view on Proposal 1-2? |
| --- |
| Company | Comment |
| Sony | Alt-1. |
| vivo | Alt-2 is preferred. The minimum and maximum value of the UE FFP periodicity can be defined. However, the exact value of the FFP periodicity should not be limited. Since it should adapt better to the URLLC traffic patterns, there is no need to impose the restrictions for gNB FFP on the UE FFP. |
| Futurewei | Alt 1. {1, 2, 2.5, 4, 5, 10}. |
| Intel | We prefer Alt-1, but with no additional values compared to those selected during Rel.16. The reason is that other values would not allow to maintain the starting position between the first g-FFP and the first u-FFP the same over time within a 20 ms period (which is the period length used in Rel.16 to make sure the g-FFP is aligned with an even radio frame), and this would complicate the way how the offset would be defined over time. |
| CATT | Alt.1 the similar view with Futurewei {1, 2, 2.5, 4, 5, 10} which is the same as period of gNB-initiated COT |
| LG | Alt 1. {1, 2, 2.5, 4, 5, 10}. |
| Panasonic | Alt.1. We are open to include 8. |
| ZTE | Either alt-1 or alt-3 is ok. For Alt-2, we are not sure why do we need so many values which may complicate the pattern, e.g. 7ms and 9ms. |
| Nokia, NSB | Alt-2. It would make sense to have FFP periodicity aligned with the periodicity of UL CG. |
| Sharp | Our preference is Alt-1 as the baseline. Furthermore, if the main purpose of UE-initiated COT is for CG PUSCH transmission, the range of FFP-u periodicity should refer to the range of CG PUSCH periodicity configuration. Thus, adding 8ms in the ranges values of UE FFP periodicity may provide better support to CG PUSCH. |
| ETRI | We prefer Alt 1 with {1, 2, 2.5, 4, 5, 10}. |
| Qualcomm | Alt-1. {1, 2, 2.5, 4, 5, 10}. |
| OPPO | It seems Alt-1 is a subset of Alt-2. The benefit of having range wider than Alt-1 is not clear to us. Thus, we prefer Alt-1. |
| InterDigital | Alt-1. We have no objection to including {8}. |
| DOCOMO | Alt-1 with {1, 2, 2.5, 4, 5, 10} ms |
| Lenovo/Motorola Mobility | Alt-2 can cover more CG & RACH periodicities than Alt-1. If needed, 2.5ms can also be added to have all gNB-FFP periodicities for UE-FFP periodicities. If the same FFP pattern (starts of FFPs) is to be retained within every 20 ms, then Alt-1 excluding 8 ms. |
| Samsung | Alt-2. The main motivation for UE initiated COT is to support URLLC traffic more efficiently, thus, it is natural to support existing CG UL transmission periodicity by UE FFP periodicity |
| Spreadtrum | Alt-2 Our first choice is alt-2, because UE-FFP parameters depends on its own traffic types especially configured grant UL transmission, it varies with DL traffic. However, we can also first adopt alt 1 as baseline and then some new values can be added. |
| Apple | I removed Apple from Alt-2 because our proposal of per-CG configuration does not imply the support of any periodicity. These two are independent. Alt-1 {1, 2, 2.5, 4, 5, 10} |
| WILUS | Alt-2 is preferred considering CG UL transmission in UE initiated COT |
| Xiaomi | Alt 2. In EN 301893, the restriction of FFP is within the range of 1 ms to 10 ms. We don,t see the need to add additional restriction beyond this. |
| HW/HiSi | As commented above on proposal 1-1, a rule for the UE FFP periodicity should be defined, since according to our view the UE FFP periodicity should depend on the configured gNB periodicity. Therefore, we think proposal 1-1 should be agreed firstly. However, to allow some progress in the discussion, we could for now (until proposal 1-1 is agreed) have the following modification of Alt-1: “UE FFP periodicity is chosen from the following set of values in ms: {1, 2, 2.5, 4, 5, [8],10}, where the conditions on the chosen value given the configured gNB FFP periodicity are FFS” |
| Moderator | As proposed by companies, it is better to discuss together the topics in section 2.1. The @All: The discussion for this topic is merged with other topics in this section and is summarized in -> Section 2.1.5 |

### Dependency between UE FFP and gNB FFP offset configuration

Proposal 1-3:

- In semi-static channel access mode, down-select one of the following alternatives:

- Alt-1: For configuration of UE FFP offset, the UE is configured with an UE FFP offset to the beginning of the latest gNB frame in the same channel.

  - HW

- Alt-2: Support independent configuration for UE FFP start position and gNB FFP start position.

  - Samsung, E///, Lenovo/MOT

| Question: What is your view on Proposal 1-3? |
| --- |
| Company | Comment |
| Sony | Alt-2. This offers full flexibility in configurating UE’s FFP. |
| Vivo | 2.1.3 and 2.1.4 should be discussed together, from the offset configuration perspective, they seem belong to the same topic. |
| Futurewei | Alt-2 |
| Intel | Agree with Vivo, that topic 2.1.3 and 2.1.4 should be discussed together. |
| CATT | Alt-2, offset can be flexibly configured for UE’s FFP |
| LG | Alt-1 |
| Panasonic | Alt.2 |
| ZTE | If the least common multiple between gNB’s FFP and UE’s FFP is kept as 20ms. A common start position can be applied, i.e. the boundary of even indexed radio frame. |
| Nokia, NSB | Alt-2. Whether the offset is relative to even indexed SFN or e.g. SFN 0 depends on proposal 1-1. |
| Sharp | We think that Proposal 1-3 is related to Proposal 1-1 and it is better to discuss them together. Since our preference for Proposal 1-1 is Alt-2, our preference for Proposal 1-3 is Alt-2 consequently. We think it is better to discuss Proposals 1-3 and 1-4 together. Regarding Alt-1, we would like to know what “gNB frame” is referring to (e.g., radio frame or gNB FFP). |
| ETRI | Prefer Alt-2. Alt-1 may give confusion or unnecessarily be complex when UE FFP period is different from gNB FFP period. |
| Qualcomm | Alt-2. We do not see any benefit to bond the starting positions of gNB and UE. |
| OPPO | Alt-1 |
| InterDigital | Alt-2. We agree with Sharp that support for Alt-2 in Proposal 1-1 leads to support for Alt-2 for Proposal 1-3. |
| DOCOMO | Alt-2 |
| Lenovo/Motorola Mobility | Alt-2: in case of reconfiguration of gNB-FFP parameters, the UE-FFP offset might need to be updated if tied to gNB FFP parameters. considering the FFP parameter update rate is not sooner than once every 200ms for both gNB-FFP and UE-FFP; relating UE-FFP parameters to gNB-FFP parameters could effectively slow down update rate of UE-FFP parameters. |
| Samsung | Alt-2. |
| Spreadtrum | Alt-2. UE-FFP start point depends on its own traffic periodicity and arriving time, especially configured grant UL transmission, it varies with DL traffic. |
| Apple | Alt-2 |
| WILUS | Alt-2 |
| HW/HiSi | Alt-1. We do not think that Alt-2 and Alt-1 are mutually exclusive. Alt-2 means that the start positions are indicated independently, and as agreed earlier, these start positions can be different. As concluded in the previous meeting, potential collisions or blocking are controlled/mitigated by gNB. It is intuitive that the gNB would use the UE FFP offset to control potential collisions between the UE FFP and gNB FFP starting positions. Therefore, regardless of the reference point assumed for signaling the offset, what matters is when the first UE frame starts after configuration with respect to the latest gNB frame. |
| Moderator | As proposed by companies, it is better to discuss together the topics in section 2.1. The @All: The discussion for this topic is merged with other topics in this section and is summarized in -> Section 2.1.5 |

### Range values of UE FFP offset:

Proposal 1-4:

- In semi-static channel access mode, down-select one of the following alternatives:

- Alt-1: UE FFP start position is determined by UE-specific offset with reference to SFN 0. The offset value range is 0 ≤ offset ＜periodicity

  - E///, Samsung, Sharp, ETRI, DCM

- Alt-2: Offset in FFP of UE-initiated COT is the starting point of first UE-initiated COT relative to the boundary of even indexed radio frame.

  - Spreadtrum, ZTE, Intel

| Question: What is your view on Proposal 1-4? |
| --- |
| Company | Comment |
| Sony | Alt-1. Unclear what Alt-2’s benefit is over Alt-1. |
| vivo | Currently, we slightly prefer Alt-1. |
| Futurewei | Alt-1 |
| Intel | We prefer Alt-2. Please notice that Alt-1 can be seen a special case of Alt-2: since the g-FFP would always align with SFN 0 (from Rel.16, the g-FFP aligns with every even radio frame), if the u-FFP offset if counted from SFN 0, this would be equivalent to state that the offset of the u-FFP is counted from the first g-FFP. Now the natural question to ask if Alt-1 is used is what would happen over time if the g-FFP and u-FFP vary? In this case, in our opinion, it would be quite complicated to derive how a g-FFP and u-FFP overlap in time, and how the idle period of one device lies into the other device FFP, while this would be much simpler with Alt-2 since a device can always use the closest even radio frame as a reference. |
| CATT | Alt.1 range is 0 ≤ offset ＜periodicity and reference point need be further studied. |
| LG | Alt-1 |
| Panasonic | Alt.1. |
| ZTE | If the least common multiple between gNB’s FFP and UE’s FFP is kept as 20ms. A common start position can be applied, i.e. the boundary of even indexed radio frame. |
| Nokia, NSB | Which of these alternatives should be down-selected depends on proposal 1-1 (see also comment to proposal 1-3) |
| Sharp | Our preference is Alt-1. Different FFP patterns would be resulted by Alt-1 and Alt-2. We are wondering whether the FFP pattern resulted in Alt-2 is allowed by regulation on periodicity. |
| ETRI | Prefer Alt-1 for value range, and prefer Alt-2 for the reference point. |
| Qualcomm | Alt.2. This depends on proposal 1-2 as well. |
| OPPO | Alt-1 |
| InterDigital | Alt-1. |
| DOCOMO | Alt-1 |
| Lenovo/Motorola Mobility | Alt-1. For proposal 1-2, if Alt-1 is adopted, then Alt-2 can also be used. |
| Samsung | Alt-1. Whether Alt-2 works depending on the candidate value of UE FFP periodicity discussed in 2.1.2. Alt-2 does not work, if FFP periodicity is not inter factor of 20ms. Alt-1 works anyway, the same mechanism as CG UL transmission offset determination. |
| Spreadtrum | Alt-2. From our understanding, offset of UE FFP can be deemed as the first channel access occasion in one 20ms. Considering slot format configuration, DL and UL slots and symbols are also inter factor with even frames. Thus, even frames is more suitable for UE and gNB FFP periodicity and offsets. Actually, gNB-initiated COT is based on the starting point of even frames. Furthermore, the offset of UE FFP can be larger than 10ms, however, alt 1 cannot support this case. Above all, Alt 2 has more flexibility and reasonable configuration compared with alt 1. |
| Apple | This depends on Proposal 1-2. Alt. 2 if we only support periodicity of {1, 2, 2.5, 4, 5, 10}. |
| WILUS | Alt-1 is preferred, and we are not clear for the benefit of Alt-2. |
| HW/HiSI | For alt-1, why is the UE specific offset with reference to SFN 0? Shouldn’t the reference be determined by proposal 1-3? Proposal 1-4 does not need to consider the reference. We would support the following Proposal at first : Alt1’: UE FFP start position is determined by UE-specific offset with reference to SFN 0. The offset value range is 0 ≤ offset ＜periodicity |
| Moderator | As proposed by companies, it is better to discuss together the topics in section 2.1. The @All: The discussion for this topic is merged with other topics in this section and is summarized in -> Section 2.1.5 |

### Summary of FFP parameter configurations

Based on the comments provided, it is better to discuss together the topics in previous sections since the proposals are inter-related. The key point is that one group suggests considering configuration of UE FFP is dependent on configuration of gNB FFP in order to reduce UE complexity. The other group are not convinced yet on the impact on UE complexity and suggest independent configuration to fully benefit operation with UE-initiated COT.

After GTW meeting on January 27th, moderator initiated a discussion to understand the UE. complexity issue. The ambitious is that by proper understanding, we can make an informed decision.

The discussion on RAN1 reflector is reflected below.

Moderator (Sorour):

To facilitate discussion, I have provided some illustrations. Below, I will refer to examples in this xls.

ftp://ftp.3gpp.org/tsg_ran/WG1_RL1/TSGR1_104-e/Inbox/drafts/8.3.2/Phase1/gNB%20and%20UE%20FFP%20configuration%20v2.xlsx

- It seems to me that Alt-1 intention is that when UE is configured by a gNB FFP (Tx), UE determines a channel access grid. Any FFP configuration aligned with this grid, would provide the predictability that somehow UE needs to perform some procedures. It seems to me this is not related to do sensing. As you see in the example for CG below. More related to idle periods.

- In  the example in the xls, I tried to show that with that understanding, how some UE-FFP configuration would fall on the grid and some not (makes as OK or Not OK).

- When it comes to configuration of UL transmission, it is OK that the periodicity of e.g. CG is different from UE-FFP. But to benefit UE-initiated COT, some of the transmission occasions should be aligned with  the channel access grid (marked “A”) in the figure. The remaining in between no need to be aligned (“marked B”).

Is this a correct understanding?

If yes, then I understand the reasons and the restrictions. And can formulate better the proposal to cover the whole picture. And we can understand and analyze better the extent of restrictions.

Intel (Salvatore):

From our view, Alt-1 allows to minimize UE complexity and simplify its implementation for multiple reasons (please correct me if I am wrong or I may have missed anything):

- The first reason is aligned with the description you provided in the prior email, except that the grid should be based on the g-FFP’s boundaries. Our assumption is indeed that each device would need to define a channel access grid, and this is done to determine where the idle period of the other device would fall over time within its own FFP. By restricting that the u-FFP and g-FFP must be the same, or either integer multiple or factor of each other, we ensure that the idle periods would fall over time in the same positions and that a device that intend to transmit would need to account for a more limited number of conditions while most of the configurations are still valid. While for the gNB, this may not be an issue, for the UE this may impact its complexity, and implementation.

Let me clarify further this point, by using your illustrations:

For case #1 when g-FFP is 10ms, for u-FFP=1 regardless of the offset value that is chosen, the idle period of the g-FFP would fall always in the same place within a u-FFP. In this scenario, the g-FFP’s idle period would fall within the tail of every 10 u-FFP1 (i.e, #7 and #17). However, for u-FFP=4, this may fall differently every 10ms and this would also depend on the offset used: for offset of 8ms, the idle period of g-FFP would fall within the middle or the end of u-FFFP #1 and #3, respectively; for offset of 7ms, the idle period of g-FFP would fall toward the end of u-FFP #1 and in the initial part of u-FFP #4.

This example highlights that based on the FFP periods and offset, there may be a very large number of conditions that the UE would need to take into account before preparing a transmission, but by applying Alt-1 this would be reduced drastically. Notice that similar conclusions can be also drawn for case #2, and case #3.

- Depending on how the offset or shift among u-FFP and g-FFP is defined, this may become meaningless over time:

  - If the offset or shift among u-FFP and g-FFP is defined every radio frame, by using your illustration and by focusing again on case #1, only for u-FFP1 the offset among u-FFP and g-FFP would remain the same. For u-FFP2 and u-FFP3, if we apply an offset of 8ms or 7ms, respectively, from the starting boundary of the 2nd g-FFP, this would no longer fall to the starting position of a u-FFP.

  - If the offset or shift among u-FFP and g-FFP is defined every even radio frame (our preference), similar conclusions can be drawn.

- Impact on complexity may also affect the UE in the moment when the u-FFP and/or the g-FFP would be changed. Let me elaborate more on this: A UE may usually prepare a transmission in advance, and the transmission itself may depend on the length of u-FFP and in some cases where the g-FFP’s idle period lies within the u-FFP. While this may not occur frequently and earlier than 200 ms (based on regulatory requirements), either the g-FFP or u-FFP may be varied over time. When this occurs, if we limit the possible the value of u-FFP or g-FFP that could be chosen when the other remain the same, this may also reduce the number of hypothesis that a UE may need to consider when preparing the following transmission.

Qualcomm(Changlong):

I fully agreed with Salvatore’s points. Basically, if we allow independent FFP period configuration for gNB and UE, in most cases, the UE FFP starting points will keep changing with respect to gNB FFP starting points. Sometimes it will be at the beginning, and sometime, it will be at the end, and sometime it will fall into the idle period. We will need to have different rules for different instance of UE FFP, which complicates both gNB and UE planning. Besides, we do not see the obvious benefit for Alt-2 even if it has high complexity. If we apply some limitations to gNB FFP duration as we did for Rel.16, we don’t see why not applying the same limitation to UE side.

In addition, for point 2 in Salvatore’s reply, it is also related to Proposal 1-4. The subitem b corresponds to Alt-2 in proposal 1-4. In fact, the benefit of point 1 will keep for both Alt-1 and Alt-2 in proposal 1-4. i. e., regardless of whether the offset is referred to SFN0 or even indexed radio frame, the benefit is kept since the least common multiple between gNB’s FFP and UE’s FFP is always 20ms ( based on the latest agreement “In semi-static channel access mode, UE FFP periodicity is chosen from the following set of values in ms: {1, 2, 2.5, 4, 5,10}”). Of course, it is simple for reference to even indexed radio frame.

Thanks again for your time and assistance.

Sharp (Huifa)

We are also trying hard to understand the restrictions and underlying reasons of Alt 1. Our current understandings are as the follows. Please correct me if there is wrong understanding.

The current assumptions of channel access grid:

- Channel access grids are based on g-FFP’s boundary.

- UE prepares UL transmission based on channel access grids.

Accordingly, I have questions on these assumptions and my understandings are as follows:

- Is it the only way to make grids based on g-FFP’s boundary? What if the channel access grid is of deterministic granularity, e.g., 1ms or 0.5ms?

- In this case, after configurations of gNB FFP and UE FFP, UE can calculate the combination patterns of gNB/UE FFP instances for the coming duration (e.g., 20ms, 40ms, …, even 200ms). UE can check the condition per grid, e.g., whether gNB idle period and/or UE idle period fall into the grid. The complexity of this calculation is not high to my understanding.

- Then, UE can prepare UL transmission according to the conditions of grids within the coming duration. Complexity of this procedure is not high either, even if the pattern changes with time.

- With this, UE has the related knowledge of FFP for UL transmission preparation in advance. When the FFP configurations are changed, UE may just repeat the above procedures.

LG(Sukchel):

Basically, I seem to have similar observation with Huifa on this issue in terms of: 1) why channel access grid needs to be based on gNB FFP, 2) why UE is required to prepare UL data by fitting such restrictive channel grid, 3) why UE complexity is reduced with Alt 1 especially.

First of all, we think it is undesirable to fit channel access grid to gNB FFP and then fit UL data preparation to the grid, without considering UL traffic pattern UE actually need to transmit timely.

In addition, from our perspective, as long as different FFP periodicities are allowed between UE and gNB, Alt 1 and Alt 2 would have almost same complexity.

For example, even assuming that UE FFP period = 2.5 ms and gNB FFP period = 4ms in case of Alt 2, a same channel access pattern for the UE would be repeated per every 20ms. (i.e., the pattern would not be changed across 20ms).

| Comment: Moderator recommendation is to continue discussion to establish mutual understanding and then, make an informed decision this meeting. |
| --- |
| Company | Comment |
| Moderator | @All: Could proponent of Alt 1 and Alt 2 check if the corresponding proposals regarding the offset are correct? Please provide text for description of offset value. Updated Proposal 1: In semi-static channel access mode, down-select one of the following alternatives: Alt-1: FFP periodicity for UE-initiated COT is configured as the same, or integer multiple of, inter factor of the FFP periodicity configured for gNB-initiated COT FFP Offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the boundary of the even indexed radio frame. The offset value (Please help to provide proper description) Alt-2: FFP periodicity and offset for UE-initiated COT is configured independently from FFP periodicity and offset of gNB-initiated COT. FFP offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the radio frame boundary. The offset value range is 0 ≤ offset ＜periodicity (Please help to provide proper description) |
| CATT | We prefer Alt-2 because gNB has flexibility of scheduling and compared with alt.1, we don’t think alt.2 introduces more complexity |
| Samsung | We still prefer Alt-2. We suggest some modification of Alt-2 for FFP offset aspect as below. Alt-2: FFP periodicity and offset for UE-initiated COT is configured independently from FFP periodicity and offset of gNB-initiated COT. FFP offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜periodicity FFS X=0, or X= even index number, depending on whether additional periodicity value other than {1, 2, 2.5, 4, 5,10} is supported. In my understanding, for any periodic configuration, e.g. periodic PUCCH/CG PUSCH/periodic SRS or UE FFP configuration, the same mechanism to determine the location for each transmission/FFP can be used. For one example, for SR PUCCH, a SR PUCCH is in a slot with number ns in a frame with number nf if (nf*Nslot,frame + ns – offset) mod periodicity =0. Same equation can be directly reused for UE FFP determination. And it can be seen that, if the periodicity is {1, 2, 2.5, 4, 5,10}, the equation is equivalent to using even indexed radio frame as reference boundary. We’d like to share our understanding of complexity issue, please correct me if I’m wrong. In our understanding, if there is no complexity issue for a UE to determine existing periodic PUCCH/PUSCH/SRS location, there would be no real challenge for a UE to determine UE FFP location. They are all periodic transmission/configuration, so we still don’t fully understand why it is difficult to support a UE to independently derive its UE FFP location. If the complexity concern is variable location of gNB idle period within a UE FFP which may impact UE’s UL transmission planning, we’re not sure how much additional complexity is. For CG UL transmission planning, several factors are to be considered, e.g. whether it is conflicted with semi-static DL symbol or flexible symbol by SFI or any DCI, and gNB idle period is just one of these several factors. As we know, the location of DL symbol within each UE FFP can be different, and we think companies all agree that the interaction between DL symbol and UE FFP is not unacceptable for UE complexity, then, why gNB idle period would be dramatic complexity? |
| Sharp | Regarding proposal formulation, we are fine with Alt-2 part in principle. For the second bullet of Alt-2, how about the following updates for easier understanding: FFP offset for UE-initiated COT is the starting point of first FFP for UE-initiated COT relative to the starting point of radio frame with SFN=0. |
| Qualcomm | We prefer Alt-1. gNB and UE definitely need additional efforts to handle the idle period which is floating during different FFPs. Basically, if we allow independent FFP period configuration for gNB and UE, in most cases, the UE FFP starting points will keep changing with respect to gNB FFP starting points. Sometimes it will be at the beginning, and sometime, it will be at the end, and sometime it will fall into the idle period. We will need to have different rules for different instance of UE FFP, which complicates both gNB and UE planning. Besides, we do not see the obvious benefit for Alt-2 even if it has high complexity. If we apply some limitations to gNB FFP duration as we did for Rel.16, we don’t see why not applying the same limitation to UE side |
| Futurewei | We still prefer Alt 2, which offer more flexibility. We think that Alt-1 reduces the number of opportunities for a UE to initiate a COT. While apparently this simplify the planning in fact may lead to increased collisions, which will tend to happen over and over periodically. Spreading (randomizing) in time reduces the possible collisions and allow more UE to initiate COT ( to access channels). |
| vivo | We also prefer Alt.2. About the complexity issue, we share all the views with Samsung. |
| DOCOMO | We prefer Alt-2. Regarding offset value range in Alt-2, maybe it’s better to clarify “The offset value range is 0 ≤ offset ＜periodicity for UE-initiated COT” |
| Sony | Firstly, I would like to clarify that it is the FFP “period” we are talking about not the “periodicity”. I think we corrected that last meeting but the word “periodicity” keeps coming back. These two have very different meaning as periodicity > period. Secondly, we prefer Alt 2. The argument presented for Alt 1 assumes that the UE cannot transmit during and after gNB’s Idle Period and so the UE needs to be aware of gNB’s Idle Period when it has initiated a COT. We have not agreed to this yet. And for the case where the UE has no intention to initiate a COT, it doesn’t matter what the relative position of UE’s starting FFP and gNB’s Idle Period, the UE just needs to monitor the period after gNB’s Idle Period to detect whether the gNB initiated a COT. |
| ETRI | We prefer Alt-1. We share the view with Qualcomm. There are diverging views on UE implementation complexity, but to us it is no doubt that some combinations in Alt-2 would at least complicate the overall operation in FBE. Especially different offsets between gNB FFP start and UE FFP start would result in different DL/UL processing timelines, which may greatly increase the scheduler complexity. In addition, the different offsets and irregular idle mode overlap patterns may cause additional spec issue. As an example, we are discussing dynamic indication of UE’s COT indication. The indication mechanism may be complicated or its signaling overhead may be larger if the position of the next UE COT (and even the number of next UE COTs in a unit duration) varies in time. Besides, we think allowing different periodicities between gNB FFP and UE FFP itself gives sufficiently large flexibility. We do not clearly understand the benefit of additional flexibility of Alt-2. If there’s no clear use case for it, it would be safer to take Alt-1. |
| LG | We prefer Alt 2 with slight update as below. Alt-2 (updated): FFP periodicity and offset for UE-initiated COT is configured independently from FFP periodicity and offset of gNB-initiated COT. FFP offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the radio frame boundary of the even indexed radio frame. The offset value range is 0 ≤ offset ＜periodicity |
| ZTE | We still prefer Alt.2 for flexibility. And we believe alt.1 can be achieved by proper configuration. We share the same view as LGE that the second bullet should be revised as we have 4ms period which cannot be divided exactly by 10ms. |
| Intel | We prefer Alt1. When comparing Alt1 with Alt-2, in addition to Qualcomm’s arguments, it is also important to note that: The channel grid is again only an abstraction, and the u-FFP and g-FFP can be indeed unaligned. Alt-1 does not pose any constrains on the offset or misalignment of the FFPs, but just on the choice of u-FFP relative to g-FFP. Alt-1 is not very restrictive. Based on the u-FFP agreed during this meeting, and based on the table provided by HW, only 6/25 configurations are precluded with a clear advantage in terms of complexity saved. The DL and UL traffic can be still separately handled. If the offset is at the symbol level, and Alt-1 is used, the position of the idle period of the gNB related to the UE’s FFP would be still following a specific and predefined position, which will be easily computable since it is shifted always by a given number of symbols. If Alt-2 is used, the position of the idle period would change over time, and the UE would need to prepare even for additional cases. Regardless of the offset value (whether this is at the symbol or ms or slot level), the offset among u-FFP and g-FFP would remain current over time, and the idle period of the gNB would have the same cadence. Similarly, as Alt-2, the text of Alt-1 could be further improved and generalized as follows: Alt-1: FFP periodicity for UE-initiated COT is configured as the same, or integer multiple of, inter factor of the FFP periodicity configured for gNB-initiated COT FFP Offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the boundary of the even indexed radio frame. The offset value (Please help to provide proper description) The offset value range is 0 ≤ offset ＜periodicity |
| Nokia, NSB | Our preference is Alt 2, which offers full fdlexibility for the network. |
| InterDigital | We prefer Alt-2. We believe that the flexibility is especially important to ensure that multiple UEs can have as many non-overlapping times when CG aligns with their FFPs to limit collisions. |
| Huawei, HiSi | First, we would like to note that we had provided our comments on the RAN1 reflector on the example cases and understanding kindly suggested by the Moderator. However, that email was not captured above. So, we are reproducing it in part as follows: HW/HiSi (Mohamed): Regarding the example cases provided in the XLS, I think combining the offset values with the issue of FFPg and FFPu may not help understand the issue. In fact, as Salvatore and Changlong have explained, the value of the offset (i.e., amount of time shift) does not matter in that context. This is due to the fact that when neither FFPu evenly divides FFPg nor FFPg evenly divides FFPu, the set of different time occasions at which the UE has to apply certain rules/special handing is always neither contained in every FFPg nor in every FFPu, regardless of the offset value in use. So, for instance in v2 Case-1 below, u-FFP3 should be also OK regardless of offset =7 or 8 (unless we agree on a further constraint that FFPu does not cross the SFN boundary) Also for v2 Case-2, yes u-FFP1 is not OK, whereas both u-FFP2 and u-FFP3 are OK, regardless of the offsets (again unless we agree on a further constraint that FFPu does not cross the SFN boundary). I agree with Sorour’s observation about CG periodicity though, but this can be achieved for almost any “OK” FFPu configuration given the flexibility in CG periodicities So in the above examples, if FFPg divides FFPu, the operations related to UE COT and gNB COT would be repeated at the same time occasions and applying the same respective rules every FFPu (being the maximum of these two FFPs). This is not the case if no such relation exists; the UE would have a different set of time occasions associated with different rules to apply across multiple UE FFPs When companies, including Huawei, mention the offset in their arguments, they refer to the additional draw back that even a desired time shift between gNB frame start and UE frame start would be neither achieved every gNB frame start nor every UE frame start. Second, we prefer Alt-1 Please see the underlined in our reply above. We also share all the views expressed by Intel regarding the dependency between the gNB FFP and UE FFP. In response to Sony and other companies with aligned views, Alt-1 does not presume that UE transmission in gNB idle period is always not allowed. It should be noted that even for the agreed rules below the UE has to be aware of the gNB idle period in each FFPu and prepare transmissions according to the associated rule; and more condit are FFS. Not only that, the UE would need to monitor for DL transmission for potential gNB COT initiation after each gNB idle period which would be in a different time occasion every FFPu according to Alt-2. Agreements: In semi-static channel access mode: When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, down-select one of the following: … When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE: If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. FFS on other conditions for determining the corresponding UE or gNB initiated COT Note: A configured UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT. Although we stressed the offset value, range, and reference point are not related to the key difference between Alt-1 and Alt-2, we think the following version of Alt-1 could be simpler at this stage: Alt-1: FFP periodicity for UE-initiated COT is configured as the same, or integer multiple of, inter factor of the FFP periodicity configured for gNB-initiated COT FFP Offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the boundary of the even indexed a reference radio frame. The offset value (Please help to provide proper description) The offset value range is 0 ≤ offset ＜periodicity |
| Apple | We prefer Alt-1. For Alt-1, the definition of the offset seems to be clear already. What is missing is the range. We can also use 0 ≤ offset ＜periodicity. |
| Lenovo/Motorola Mobility | We prefer Alt-2. As commented before, we have the following concerns regarding Alt1: in case of reconfiguration of gNB-FFP parameters, the UE-FFP periodicity might need to be updated if tied to gNB FFP periodicity. considering the FFP parameter update rate is not sooner than once every 200ms for both gNB-FFP and UE-FFP; relating UE-FFP parameters to gNB-FFP parameters could effectively slow down update rate of UE-FFP parameters. |
| Moderator | @All: Thank you all very much for making efforts and providing comprehensive explanations to address the concerns. Two alternatives are discussed. From proponent’s perspective, the main motivation for each alternative can be summarized as following: Alt 1: When FFPu evenly divides FFPg no FFPg evenly divides FFPu, the set of different time occasions at which the UE has to apply certain rules/special handing is always contained in every FFPg or in every FFPu, regardless of the offset value in use. This reduces the complexity to handle idle periods. Alt 2: Periodicity of UE FFP should be based on UL traffic to benefit from UE-initiated COT that is intended to improve UL Companies’ view: Alt-1: Intel, ETRI, QC, NEC, OPPO, Apple, HW/HiSi Alt-2: Sony, vivo, FW, CATT, LG, Nokia/NSB, Sharp, IDC, DCM, Lenovo/MOT, Samsung, WILUS, Xiaomi, Spreadtrum, ZTE @All: during the extensive discussions, pros and cons off each alternative is discussed. It is time to make a decision and select one of the alternatives that is proposed below: Updated Proposal 1: In semi-static channel access mode: Down-select one of the following alternatives: Alt-1: FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT Alt-2: FFP period and offset for UE-initiated COT are configured independently from FFP period and offset of gNB-initiated COT. FFP offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) |
| Moderator | @All: During GTW on Jan 28th, proposal 1 was discussed. Although no consensus to adopt an option, the Chairman recommended to find a common ground that addresses the concerns of both camps. One immediate thought was to extend the range values for gNB initiated COT such that Alt-1 will be more inclusive with respect to cases that can support. Investigating this approach, moderator realized that multiple integer period of gNB initiated COT seems to be confined within 20ms. Assuming that this assumption is correct (not confirmed or dismissed yet), this approach cannot further be pursued. Another approach is to support Alt-1for UE-initiated COT by default and Alt-2, in case Ue indicate its capability. The reason is that Alt-2 includes Alt-1. Main arguments for proponents of Alt-1 is complexity. Therefore, in addition to proposal 1 where either Alt-1 or Alt-2 should be selected, Proposal 1-a is formulated from complexity point of view. @Request to All: Please review Proposal 1-a that it is properly formulated. If you have suggestion for another proposal that to resolve the dead-lock, please share your suggestion. Due to lack of time, please focus on new proposals that have a chance to reach consensus. Please indicate whether Alt-1 and/or Alt-2 in Proposal 1A and/or Proposal 1B, is acceptable to you. Proposal 1A: In semi-static channel access mode: Down-select one of the following alternatives: Alt-1: An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT Alt-2: FFP period for UE-initiated COT is configured independently from FFP period of gNB-initiated COT. FFP offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) New Proposal 1B: In semi-static channel access mode: An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT FFP period for UE-initiated COT can be configured independently from FFP period of gNB-initiated COT, if the UE indicates the corresponding capability FFP offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) |
| Sharp | Our first preference is Alt-2 in Proposal 1A and we can live with Proposal 1B. |
| CATT | Alt.1 should be based on UE capability. So we suggest Modified Proposal 1B as follows: New Proposal 1B: In semi-static channel access mode: FFP period for UE-initiated COT can be configured independently from FFP period of gNB-initiated COT An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT FFP period for UE-initiated COT can be configured independently from FFP period of gNB-initiated COT, An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT , if the UE indicates the corresponding capability FFP offset for UE-initiated COT is the starting point of first UE-initiated COT relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) We prefer Alt.2 in Proposal 1A and if Proposal 1B with our suggestion is accepted, we are also fine with it. |
| LG | Although we appreciate FL’s effort to find a middle ground by Proposal 1B with UE capability, it would not be desirable since gNB has to initially select/configure its FFP period (via SIB) without knowing presence of the UEs capable of Alt-2. Going back to the following table showing possible UE/gNB FFP period combinations in Alt-1, I’d like to share my observation and concern as below. Among total 36 combinations, only 24 combinations will be supported by Alt-1 by precluding 12 combinations (33%), thus it is too restrictive. Some short UE FFP periods such as 1 or 2 msec which will be important to support low latency URLLC transmission, will not be supported together with some gNB FFP periods such as 2.5 or 5 msec by Alt-1. For some combinations such as {gNB FFP, UE FFP} = {2.5, 1} or {5, 2}, the LCM (Least common multiple) of UE/gNB FFP period is at most 10 msec, and it means that a same operation pattern in terms of LBT sensing and/or idle period will be repeated in every 10 msec and thus will not be involved with larger complexity compared to other cases with same LCM value such as {gNB FFP, UE FFP} = {10, 2}. FFP-g period (msec) 1 2 2.5 4 5 10 FFP-u period (msec) 1 2 2.5 4 5 10 With the above observations, we think a potential middle ground or compromise between Alt-1 and Alt-2 could be to support some of 12 combinations which will essentially be required for URLLC and/or with not significant complexity. |
| vivo | Thanks a lot for moderator’s effort! Although Alt-2 in proposal 1A is our preference, we can accept CATT’s version of the New Proposal 1B for progress. |
| Qualcomm | We prefer Alt-1 in Proposal 1A. Proposal B is acceptable as well. Do not agree with CATT. Alt-1 is subset of Alt-2. Therefore, supporting Alt-2 or not should be UE capability. |
| Samsung | We really appreciate FL’s great efforts. Although we’re still not convinced by the complexity caused by independent gNB/UE FFP, we’re open to find a middle ground. We share the same understanding with LG, if the LCM (Least common multiple) of UE/gNB FFP period is not much larger than 10ms, e.g. LCM is at most 20ms, the complexity would be not much different from Alt-1. Samsung originally supports UE FFP periodicity of any integer number of slots to reduce latency for CG UL transmission. To reduce the combination and keep LCM of UE/gNB FFP period within 20ms, we can compromise to only supports UE FFP period {1, 2, 2.5, 4, 5,10} as suggested by ZTE. In short, we support original proposal 1A Alt-2 with the restriction that candidate UE FFP period is {1, 2, 2.5, 4, 5,10}. |
| DOCOMO | Same as Sharp, our first preference is Alt-2 in Proposal 1A and we can live with Proposal 1B. |
| Panasonic | Our first preference is Alt.2 in Proposal 1A, but we can live with Proposal 1B. |
| OPPO | Proposal 1B is an icebreaking proposal so it is better for making progress. I understand companies may have different views thus willing to stick to Proposal 1A, but seems we are running in circle. Only similar comments are to be repeated again. |
| ETRI | Our first preference is Alt-1 in Proposal 1A, and we are also fine with FL’s Proposal 1B. Regarding CATT’s proposal, we agree with Qualcomm that Alt. 2 should be based on UE capability because Alt-1 is a subset of Alt-2. |
| Sony | We prefer Alt-2 in Proposal 1A. We are fine with Proposal 1B. |
| TCL | We are supportive of proposal 1A, with preference to Atl-2. |
| Intel | Many thanks to the FL for the incredible effort in finding a compromise. We are Ok with Alt.1 in proposal 1A, and we would be also OK with proposal 1B. |
| Apple | Our first preference is Alt-1 in Proposal 1A, but we are fine with Proposal B. Maybe we could also agree that the set of values supported for UE FFP period is the same as the gNB’s FFP period, that is, {1, 2, 2.5, 4, 5,10}. This would allow more UEs to support the advanced capability suggested by Alt-2. |
| InterDigital | We prefer Alt-2 in Proposal 1A, but we are fine with proposal 1B. |
| Huawei, HiSilicon | We support Alt-1 of Proposal 1A. We are also fine with Proposal 1B but we agree with QC’s and ETRI’s views regarding CATT’s suggested modification as the UE should be signaling what it is capable of, not what it is incapable of. Following modification is suggested for the offset definition in either proposals for more accuracy since the UE may or may not initiate a COT in the first UE FFP: Proposal 1A: In semi-static channel access mode: Down-select one of the following alternatives: Alt-1: An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT Alt-2: FFP period for UE-initiated COT is configured independently from FFP period of gNB-initiated COT. FFP offset for UE-initiated COT is the starting point of first UE-initiated COTUE FFP relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) New Proposal 1B: In semi-static channel access mode: An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT FFP period for UE-initiated COT can be configured independently from FFP period of gNB-initiated COT, if the UE indicates the corresponding capability FFP offset for UE-initiated COT is the starting point of first UE-initiated COTUE FFP relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) To answer Moderator’s earlier question on what other gNB FFP values could be added, we think that 1.25ms could be also achieved, e.g., with SCS 30kHz or higher @ LG and Samsung, as long as the condition in either Alt-1 of Proposal 1A or Proposal 1B is applied, we think that more UE FFP period values can be available between 1ms and 10ms in addition to the agreed set that just mirrored the gNB FFP period values, e.g., 3 ms, 6 ms, and 8 ms which would give more flexibility especially with the shortest gNB FFP periods. In our understanding, there is no need anyway for the UE FFP period to evenly divide the 20ms duration due to the time shifted start by applying the offset. It should be noted though that we support these additional values with the applying the condition, the LCM{FFPg,FFPu} could be upto 40 ms. |
| ZTE | As commented in the email discussion and also mentioned by Samsung, we think another possible solution is that we fix the value range of UE's FFP that is same as gNB's (no more values compared to what is agreed), and adopt Alt.2 as in such case certain flexibility can be maintained and it will not impose significant complexity compared to Alt.1. Proposal 1-B would be acceptable to move forward but maybe some restriction should be added to the max value of UE FFP (e.g. 10 ms) as the intention of the main bullet is to reduce complexity, we do not expect to expand the value range of UE FFP too much. @Huawei, if alt-1 is applied and the UE’s FFP values is between 1ms and 10ms, the LCM should still be up to 20ms, right? |
| Moderator | @CATT: In addition to comments above that Alt-1 is a sub-set of Alt-2, from the complexity point of view, if the UE does not indicate capability, then should support the least complex version. As it is claimed Alt-2 is more complex than Alt-1, that justified the formulation of the proposal to associate the capable UEs to Alt-2. @LG/Samsung: On the comment “LG: it would not be desirable since gNB has to initially select/configure its FFP period (via SIB) without knowing presence of the UEs capable of Alt-2.”, I guess your comment is applicable to any feature with capability. I guess the main criticism towards Alt-1 was that it limits the performance in the sense, for a UL transmission, e.g. CG, let’s say a configuration of periodicity of 3 slots would match the best the UL traffic, but in this case, gNB perhaps has to start with another periodicity based on its gNB FFP and closest to 3 slots, e.g. 2 slots. For example, if gNB FFP is 10ms, the gNB would choose 2ms for UL (overprovision). Then after UE indicates its capability, can switch to 3ms. That also goes inline with issues with the proposal by Samsung. If we limit the set, then there is not much gain with removing the dependency because one can always overprovision or not, depending on prioritizing latency or resource overbooking. So, in that sense, adding missing combinations for the current set as LG proposes, or reusing the same set for UL but independently, does not change the eventual performance as compare to Alt-1. My understanding was that proponent of Alt-2 are interested in flexibility not achievable by Alt-1. @Apple: The reason that is not included now that is that some companies argued that Alt-1 provides restrictions on the periodicities that can be configured. Samsung had the same proposal but to agree on Alt.2 if this set is agreed for UE initiated COT. I think it is better to wait with this discussion for the next step if 1B is agreed. Since there are two proposal on having this set, one as Apple suggests and one as Samsung, considering initial concerns raised towards Alt-1. @ZTE: It is already agreed that UE FFP should be limited between 1ms and 10ms. Agreements: In semi-static channel access mode, FFP Period for UE-initiated COT is separately provided from FFP period for gNB-initiated COT. o Note: Any value for the period, shall be at least 1ms and at most 10ms. o Note: Aim for low complexity operation to handle gNB and UE COT interactions Current Status: Proposal 1B is acceptable: Sharp, QC, DCM, Panasonic, OPPO, ETRI, Sony, Intel, Apple, IDC, HW/HiSi, ZTE Proposal 1B is NOT acceptable yet 😊 CATT, TCL, Samsung, LG @CATT, TCL, Samsung, LG: Based on the discussion so far, would Proposal 1B be acceptable to you? |
| Intel | We support proposal 1B, or in alternative Alt 1 in proposal 1A. |
| CATT | For the sake of the progress, we are fine with Proposal 1B |
| Sharp | We are fine with the new Proposal 1B. |
| Apple | We are fine with the new Proposal 1B. |
| Xiaomi | Fine with the new Proposal 1B. |
| LG | First of all, our first preference is still Alt-2 in Proposal 1A. Besides, supporting Alt-1 + some of other combinations useful for URLLC is also acceptable. We are not supportive with Proposal 1B due to gNB restriction to set initial gNB FFP without knowing UEs’ capabilities. |
| Spreadtrum | Fine with the new Proposal 1B. |
| Samsung | Although we're not convinced yet, for the sake of progress, we can live with proposal 1B, if the same position/logic is applied to proposal 4-1A as suggested by FL. |
| ZTE | Thanks for the FL's clarifications. We could be fine with proposal 1B, although our 1st preference is alt-2 in proposal 1A and without adding more values to the set of UE FFP. |
| DCM | We are fine with Proposal 1B, while our 1st preference is still Alt-2 in Proposal 1A |
| Panasonic | We are OK with Proposal 1B (1st preference is Alt-2 in Proposal 1A). |
| vivo | We are fine with proposal 1B for progress. |
| Lenovo/Motorola Mobility | Support Alt-2 proposal 1A. For proposal 1B, we think the sub-bullet on independent FFP configuration should have the same indent as the bullet above it; otherwise seems conflicting with the bullet above it |
| Qualcomm | We are OK with proposal 1B and our first preference is Alt-1 in Proposal 1A. |
| Apple | Fine with proposal 1B |
| CATT | For the sake of the progress, we are also fine with proposal 1B. |
| Ericsson | Fine with proposal 1B |
| Xiaomi | Fine with the new Proposal 1B. |
| Nokia, NSB | We are ok with Proposal 1B |
| LG | @FL: Thank you for providing the explanation. Firstly, I think my above comment “it would not be desirable since gNB has to initially select/configure its FFP period (via SIB) without knowing presence of the UEs capable of Alt-2.” might be applicable to only some particular features with capability rather than any features. Main reason of our concern is that unlike UE FFP, gNB FFP is single and common for all the UEs while UE FFP is just specific to one UE. Let me provide some situation. For example, in the beginning, the gNB may hesitate to configure 2.5 msec as gNB FFP period since with the period, UE FFP period of 1 or 2 msec useful for URLLC is not supported together for the UE without the capability of Alt-2. After some time, some UEs could report the capability of Alt-2, but even in this case, the gNB couldn’t reconfigure its period to 2.5 msec since other UEs already configured with UE FFP parameters may not have the capability of Alt-2. Considering such situation, we think Alt-1 would be involved with restriction to gNB and/or UE undesirable for URLLC support. |
| IDC | We can accept Proposal 1B. |
| Moderator | @LG: Thanks for the discussion. It could be as well the case you raise. But consider this scenario that there are different UEs with URLLC traffic and for some of the periodicity of 1 ms would be find and some 2 ms. Please note that not all cases for IIoT/URLLC the bounded latency is 1ms. The main point is nothing can be perfectly aligned. That’s why I mentioned the NW can over/under provision until it knows better about UEs. Another question is that the UE indicates its capability after initial access. The URLLC services would be more applicable during dedicated RRC (Note this is different from UE initiated Cot to improve initial access on unlicensed for FBE). Current Status: Proposal 1B is acceptable: Sharp, QC, DCM, Panasonic, OPPO, ETRI, Sony, Intel, Apple, IDC, HW/HiSi, ZTE, CATT, Xiaomi, Spreadtrum, Panasonic, vivo, Qualcomm, Nokia/NSB [Samsung] (if the same position/logic is applied to proposal 4-1A as suggested by FL) Proposal 1B is NOT acceptable yet (prefer still Proposal 1A-Alt 2) TCL, LG, [Samsung] Proposal 1A: In semi-static channel access mode: Down-select one of the following alternatives: Alt-1: An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT Alt-2: FFP period for UE-initiated COT is configured independently from FFP period of gNB-initiated COT. FFP offset for UE-initiated COT is the starting point of first UE-initiated COTUE FFP relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) New Proposal 1B: In semi-static channel access mode: An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT FFP period for UE-initiated COT can be configured independently from FFP period of gNB-initiated COT, if the UE indicates the corresponding capability FFP offset for UE-initiated COT is the starting point of first UE-initiated COTUE FFP relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) |
| Moderator | The following was agreed in GTW, Jan. 27th: Agreement: In semi-static channel access mode, UE FFP periodicity is chosen from the following set of values in ms: {1, 2, 2.5, 4, 5,10}. FFS on other values The following was agreed (Proposal 1B) in GTW, Feb 2nd: Agreement: In semi-static channel access mode: An FFP period for UE-initiated COT is configured as the same, integer multiple of, or inter-factor of the FFP period configured for gNB-initiated COT FFP period for UE-initiated COT can be configured independently from FFP period of gNB-initiated COT, if the UE indicates the corresponding capability FFP offset for UE-initiated COT is the starting point of first UE FFP relative to the radio frame X boundary. The offset value range is 0 ≤ offset ＜FFP period of UE-initiated COT FFS on X (e.g. X=0, or X= even index number) |

## Discussion topic: Additional constraints on transmission during idle periods

The proposals 2-1 below, aim to capture the views with respect to the discussion topic, on high level.

Other proposals address additional details.

Please if needed, prioritize the discussion of Main design issues.

### Main design issues

Proposal 2-1:

- In semi-static channel access mode, decide among the following alternatives:

  - Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB

    - Panasonic, Samsung, Apple (if strong concern), Lenovo/MOT, Sharp, OPPO?, ZTE

  - Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB.

    - E///, ETRI, Xiaomi

  - Alt-3: As an initiating device, “by default” the UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB.

    - Introduce support for gNB-controlled UE-initiated UL transmissions during gNB idle periods, when e.g. the gNB has no intention to acquire the COT in the subsequent FFP.

    - Nokia

  - FFS other alternatives

| Question: What is your view on Proposal 2-1? |
| --- |
| Company | Comment |
| Sony | It isn’t clear what’s the benefit in Alt-1 & Alt-3. Also it isn’t clear, what is the UE behaviour after gNB’s Idle Period for case where the UE’s COT ends after gNB’s Idle Period? If the UE initiated the COT can the UE still transmits after gNB’s Idle Period? Can the gNB initiates a COT during the CCA phase of the gNB’s Idle Period? Given the lack of info on Alt-1 or Alt-3, we would prefer Alt-2. |
| vivo | We support Alt-2. Alt-2 is more reasonable since a device should only prioritize the idle period which belongs to the FFP it uses, e.g., the idle period of the its own FFP if it operates as an initiating device; or the idle period of the FFP associated to another device if it shares the COT initiated by another device. In other cases, there is no further restrictions for the transmission. Therefore, when UE initiates a COT, it can transmit during the idle period of any FFP associated to the serving gNB. |
| Futurewei | Alt -2. |
| Intel | We support Alt-3. We believe that as a default behaviour a UE should never transmit within a gNB’s idle period, since this would block the gNB’s from acquiring the next FFP. Highest priority should be always given to the gNB to operate as an initiating device. |
| CATT | Alt-2. |
| LG | Alt-1 is preferable compared to Alt-2. |
| Panasonic | We prefer Alt.1 or Alt.3. In our view, at least the restriction that UE should not transmit in the serving gNB’s idle period would be needed from the perspective of coexistence with other RAT. |
| ZTE | Alt-1 is preferred |
| Nokia, NSB | Alt-3 (or Alt-1). Note that Alt-3 is an enhancement on top of Alt-1. In our opinion, Alt-2 (which basically assumes no additional restrictions as compared to what already agreed) has the main disadvantage that an NR-U system (gNB + UE) could be continuously transmitting on an unlicensed channel, potentially causing regulatory issues. |
| Sharp | Our preference is Alt-1 and we are fine with Alt-3 as further optimization. Alt-1 could solve potential problems when the UE COT is initiated and the CG PUSCH transmission overlaps with the idle period of gNB FFP, including 1) the gNB cannot obtain a COT during next gNB FFP, 2) 5% idle period without transmission cannot be always guaranteed (e.g., the channel might be continuously occupied with small gaps by gNB and UE of one FBE network in turn). Furthermore, Alt-1 could be beneficial for coordination among different FBE networks, e.g., only exchanging gNB FFP configuration information might be sufficient. Detail of how to implement Alt-1 can be further studied. |
| ETRI | We support Alt-2. Protection of some of gNB’s idle periods can be achieved based on proper scheduling or other method (e.g., shortening a UE COT, disabling a UE COT initiation) on top of Alt-2. |
| Qualcomm | Alt-1 to meet regulatory requirement. |
| NEC | We support Alt-1. |
| OPPO | Alt-1 is preferred. But we are open for Alt-3. |
| InterDigital | Alt-1 to ensure fair coexistence. |
| DOCOMO | We prefer Alt-2, which is aligned with current agreements. gNB can control not to transmit UL during the idle period of gNB’s FFP if necessary |
| Lenovo/Motorola Mobility | Alt-1; in our view this restriction could give a chance to gNB to initiate a COT in case it has (at least) DL data (which could be urgent data e.g., with high priority HARQ-ACK) for several UEs. @ Sony: In our understanding, the restriction enforces muting during gNB-idle period, and the UE may use the remaining UE-FFP part afterwards. If the gNB succeeds, the gNB can initiate the COT. |
| Samsung | Alt-1 for fair coexistence. |
| Spreadtrum | Alt-2 UL transmissions are under control of gNB. Proper configuration and scheduling can achieve similar effects as alt 1 and alt 3. |
| Apple | We are fine with both Alt-1 and Alt-2. The optimization in Alt-3 seems unnecessary. |
| WILUS | We prefer Alt-1 and we are open for Alt 3 to enhance Alt-1. |
| Xiaomi | Alt 2. In EN 301893, a device is not allowed to transmit only in the idle period of its own FFP configuration. From our opinion,we think no need to restrict the UE not to transmit in gNB’s idle period. |
| HW/HiSi | In our view, Alt-2 captures the proper idle period interaction rule. The UE should not be allowed to transmit in the gNB idle period if the gNB has initiated CO in the associated FFP and the UE’s transmission is sharing gNB COT as a response. Therefore, further prioritization of gNB COT can be achieved through the determination rules of COT initiator for configured and scheduled UL transmissions. |
| Moderator | Summary of views: Need for more clarification on Alt-1 or Alt-3 Sony Alt-1: LG, Panasonic, ZTE, Nokia/NSB, Sharp (1st), QC, NEC, OPPO (1st), IDC, Lenovo/MOT, Apple, WILUS(1st) Alt-2: vivo, FW, CATT, ETRI, DCM, Spreadtrum, Apple, E///(1st), Sony, HW Alt-3: Intel, Panasonic, Nokia/NSB, Sharp(2nd), OPPO(2nd), WILUS(2nd) @Moderator: In the discussion companies discussed coexistence issues, regulations, and NW controlled operation. Moderator tries in the following to summarize and provide some views to motivate the updated proposal. Is there an issue with regulation? The current agreement meets the regulatory requirements as Xiaomi explained. It was also discussed when the corresponding agreement was made. Is there an issue for coexistence? If there are coexisting NW, at moderate, high loads, without coordination between NW, none of the NW would perform properly as one tends to jam the other, and vice versa. Hence, the key for coexistence is coordination. But that I mean that even with Alt-1, as long as NW don’t coordinate idle periods, it does not matter whether if it is muted or not. Now, it seems that muting the idle periods, simplifies the coordination for a NW. For example, the NW would need to coordinate the FFP periods. Deployments scenario: For FBE operation, a common use case is isolated NW in factories and private premises. That is no coexisting NW. Which means there is no need for additional restrictions by Alt 1 or Alt 3. However, in case of coordinated coexisting NWs, Alt 1 and AL 3 would simplify coordination. Hence, including design options that simplifies operations in some scenarios seems to be reasonable that can be used when needed. If that sense, a different approach than Alt 3 is that to assume as default “restriction” is not needed. If needed, it can be enabled by NW. The advantage is that by default, not to have overhead in the system, specially when the most common use case would be single NW. However, in design, to have an option to put more restrictions if that helps coordination and hence coexistence, especially in deployment scenario with co-existing NWs. Based on this logic, I would like to encourage companies to consider Alt 4 below (similar to Alt 3, but “default” is the current agreement. Updated Proposal 2-1: In semi-static channel access mode, decide among the following alternatives: Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB. Alt-3: As an initiating device, “by default” the UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB (i.e. Alt-1). Support enabling/disabling Alt-2 [by RRC]. Alt-4: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB (i.e. Alt-2) Support enabling/disabling Alt-1 [by RRC]. |
| CATT | We prefer Alt.2 and for the sake of the progress, alt.4 is fine with us. |
| Samsung | We prefer Alt.1 and for the sake of the progress, we’re fine with alt.4, if the RRC configuration is a simple on/off signaling for all FFP rather than bitmap for specific UE FFP occasions as discussed in section 2.3. |
| Sharp | We could accept Alt-4 suggested by moderator. |
| Qualcomm | We prefer Alt-1. | We prefer Alt-1. |
| Futurewei | We prefer Alt 1. For the Alt-4 we have a similar discussion about gNB canceling future UE FFP . Therefore, gNB should have the means to protect its idle period of the next FFP. Not sure what would be the intention to cancel UE transmission just in selected idle periods (via RRC) |  |
| vivo | We prefer Alt.2. We share the views with moderator’s on for URLLC in unlicensed band with controlled environment which contains only devices operating on the unlicensed band installed by the facility owner. There is no need for additional restrictions by Alt 1 or Alt 3. Even if coordination among NW is needed, gNB can avoid this by not configuring/scheduling the UL transmission in the one or two OSs right before the gNB FFP. |
| DOCOMO | Same as CATT, our first preference is Alt.2 but we can live with Alt. 4 for the progress |
| Sony | Our previous preference was Alt.2 (I have added it in the Moderator’s comment above). For coexistence management, this is under a controlled environment and the gNBs in the network can be configured or deployed to minimize interference. Muting to allow gNB to initiate a COT would still present some problems. How does the UE know whether the gNB had initiated a COT after gNB’s Idle Period if the UE’s COT overlaps the gNB’s Idle Period? I have drawn below the problem, where the gNB initiates a COT during its Idle Period and the UE continues to transmit after being muted during gNB’s Idle Period (time t3-t5), this would cause a collision (time t5-t6). |
| ETRI | We prefer Alt-2. We still do not see the need to give such restriction for “all” the gNB idle periods by Alt-1. How to protect “some necessary” gNB idle periods can be separately discussed. |
| LG | We prefer Alt-1. |
| ZTE | We still prefer Alt. 1. Because gNB’s COT can be shared by multiple UEs, while UE’s COT cannot, if UE is allowed to transmit during the idle period of gNB’s FFP, then gNB can hardly initiate a COT and the chance of other UEs to share gNB’s COT is reduces, which is not pursued for the purpose of URLLC. So we still believe to prioritize gNB’s COT is beneficial and controllable. |
| Intel | We prefer Alt-3, given that it should be always precluded to the UE to block a gNB’s from acquiring the following FFP – as previously mentioned the gNB should always have the highest priority in acquiring the COT. By adding a level of configurability, it is possible to give the opportunity to the gNB to actually allow the UE from transmitting in its idle period, when the gNB has no intention to operate as an initiating device (e.g., it does not have nothing to transmit), and avoiding in any cases that a UE and gNB may block each other. |
| Nokia, NSB | Our preference is somewhere in between Alt-1 and Alt.2. If UE transmissions were allowed in all idle periods of the gNB, the channel would be occupied essentially all the time by a given cell, which seems unfair from channel access point of view. However, if a gNB does not initiate an FFP at some point, it should be allowed for the UE to transmit during the related idle period. This could be seen as Alt 3, but RRC alone is not sufficient for enabling such behavior. |
| InterDigital | We prefer Alt-1. For the sake of progress we are fine with Alt-3 or Alt-4. |
| Huawei, HiSi | We prefer Alt-2 The UE transmission in gNB idle period is limited to the case when UE operates as an initiating device, and we are already discussing rules on when to allow the UE to initiate COT. Thus, further prioritization of gNB COT can be achieved as such If the behavior of Alt-1 is in action or enabled by another alternative, what would be the need to have rule based on “If the transmission is confined within a gNB FFP before the idle period of that gNB FFP”? In our understanding, UL transmission would be always confined within gNB in such a case. |
| Apple | We are flexible on this issue, given that none of the alternatives violates the regulations. It seems that the new Alt-3 is different from the old Alt-3. If I understand correctly, the old Alt-3 supports enabling/disabling dynamically, but the new Alt-3 support it by RRC. We do not see much difference in Alt-3 and Alt-4, because the only difference is the default behavior. |
| Moderator | @All: I have removed Alt-4 since there was not much support and companies OK with Alt-4, prefer Alt-2 in principle. Companies’ view: Alt-1: LG, Panasonic, ZTE, Nokia/NSB, Sharp, QC, NEC, OPPO, IDC, Lenovo/MOT, Apple, WILUS, FW, Samsung Alt-2: vivo, CATT, ETRI, DCM, Spreadtrum, Apple, E///, Sony, HW/HiSi Alt-3: Intel, Panasonic, Nokia/NSB, Sharp(2nd), OPPO(2nd), WILUS(2nd), E///(2nd) Updated Proposal 2-1: In semi-static channel access mode, decide among the following alternatives: Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB (previous agreement). Alt-3: As an initiating device, “by default” the UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB. The UE transmission during the idle period of any FFP associated with the serving gNB can be enabled by RRC |
| Moderator | @All: Additional comments after further reviewing the comments after GTW 28th Jan @Sony: The UL transmissions are controlled by gNB such that Ul and DL in the same cell do not collide. If gNB intentionally schedules/configures UL transmission that would collide with its own, still would be under gNB control and collision could be controlled/mitigated. Please recall discussion in previous meeting and following conclusion: Conclusion: For operation on unlicensed channels and irrespective of the adopted LBT mechanism (LBE or FBE), all transmissions in DL and UL are controlled by gNB similarly to licensed channels, and potential collisions or blocking are controlled/mitigated by gNB. @FW: If understood correctly, you prefer to provide protection in a dynamic way. Please see comment below to Apple for adding dynamic option as FFS. @ETRI: To your comment, “How to protect “some necessary” gNB idle periods can be separately discussed”, that is the intention of Alt-3 to provide some protection when needed. I think the discussion is taking place and it would be good to progress as well. @ZTE: To your comment “if UE is allowed to transmit during the idle period of gNB’s FFP, then gNB can hardly initiate a COT and the chance of other UEs to share gNB’s COT is reduces, which is not pursued for the purpose of URLLC.”, although this scenario is valid, there are other scenarios that is more UL heavy and utilizing transmission in gNb idle periods could reduce delay. The question is should the design have some always-in built-in restrictions without any flexibility to adjust based on operation scenario? @Apple: Alt-3 is originated based on Nokia’s comment. Which based on description it seems dynamic control was intended. However, considering deployments scenarios and arguments in favor of Alt-1 or Alt-2, it is better to at least include RRC control and discuss whether dynamic control could be considered additionally. To add FFS for dynamic enabling/disabling in Alt-3 @HW/HiSi: To your comment “If the behavior of Alt-1 is in action or enabled by another alternative, what would be the need to have rule based on “If the transmission is confined within a gNB FFP before the idle period of that gNB FFP”? In our understanding, UL transmission would be always confined within gNB in such a case.”, Yes, of course that would be the case and consequence. General: We cannot make any progress considering all the inter-action between different topics. The group has to conclude whether we should impose a high-level restriction in protocol or not. And if so, should it be permanent or depending on the mode of operation. @Request to All: Could you please consider if Alt-3 can be supported? The reason is that Alt-3 provides a flexible design that can be adjusted based on use-case without complication and simplifies coordination if needed. Both camps for Alt-1 and Alt-2 have justifications for use cases in mind. Considering different scenarios, a design based on Alt-3 provides enough needed flexibility for proper operation. If Alt-3 supported, Alt-1 is default which can be switched to Alt-2 by RRC. Updated Proposal 2-1: In semi-static channel access mode, decide among the following alternatives: Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB Note: In case Alt.2 is supported, it should be captured as conclusion due to previous agreement. Alt-3: A UE as an initiating device, “by default”, is not allowed to transmit during the idle period of any FFP associated with the serving gNB. The UE transmission during the idle period of any FFP associated with the serving gNB can be enabled by RRC. FFS on dynamic enabling/disabling |
| Sharp | Our first preference is Alt-1 and we can accept Alt-3. |
| LG | We prefer Alt-1 and can also accept Alt-2 since anyhow, gNB could control to avoid potential interference from a UE to idle period of gNB FFP by well configuring configured UL resource for the UE. We don’t see the reason to introduce UE-specific configuration between Alt-1 and Alt-2 rather than defining common UE behavior on this aspect involved with coexistence. |
| vivo | Our preference is Alt.2. We did not see the need for additional signaling used to always or dynamically to protect gNB’s idle period. For Alt-3 of the Updated Proposal 2-1, we disagree the default behavior is Alt-1. Alt-2 should be the default behavior, since Alt-2 is complied with the regulation, the “mirror” of the gNB-initiated COT. Alt-1 is additional restrictions added on top of Alt-2. |
| Qualcomm | Our first preference is Alt-1 and we can accept Alt-3. |
| Samsung | Our first preference is Alt-1. We can accept Alt-3 by RRC configuration (a simple on/off signaling for all FFP), not dynamic indication, because the presence/ coordination of other gNB/node should be semi-static. |
| DOCOMO | Our first preference is Alt-2. As Alt-2 is already agreed UE behavior, we think Alt-4 is better middle ground than Alt-3. However, we can live with Alt-3 if majority companies support it. |
| Panasonic | Our first preference is Alt.1, but we are OK with Alt.3. |
| OPPO | Although we prefer Alt-1, but we support Alt-3 to make the gNB controlled behavior and move the WI forward. |
| ETRI | We share the same view with vivo. We prefer Alt-2, and think that Alt-1 can be considered on top of Alt-2. However, for the sake of progress, we can accept Alt-3 if majority companies support it. |
| Sony | Thanks the moderator’s response to Sony’s comment. Since gNB can control the interference, then there really isn’t any reason for Alt-1. Hence, we prefer Alt-2. |
| Intel | Our preference remains for Alt-3. In principle it should be always precluded to the UE to block a gNB’s from acquiring the following FFP, and therefore the gNB should always have the highest priority in acquiring the COT. However, by adding a level of configurability, it is possible to give the opportunity to the gNB to actually allow the UE from transmitting in its idle period, when the gNB has no intention to operate as an initiating device (e.g., it does not have nothing to transmit) so that to enhance the spectral efficiency in these cases. |
| Apple | We are fine with Alt-3 as the compromise, but we do not see the need for dynamic control. So we prefer to remove the FFS and conclude. |
| InterDigital | We agree with Alt-3. |
| Huawei, HiSilicon | We share the same views as Sony and vivo and support Alt-2. Alt-2 should be the default behavior, Alt-1 is a further restriction. gNB can achieve the purpose of Alt-1 or Alt-3 by proper scheduling of UL resources for dynamically scheduled UL, and for configured UL, either by proper configuration or by dynamically cancelling all UL before the intended gNB idle period(s). |
| ZTE | Although we prefer Alt.1. To make progress, we can accept Alt-3 without the FFS. |
| Moderator | @All: Below is copy of moderator comments on reflector: I personally think nothing is needed (Alt-2) and NW can control. Alt-1 unnecessarily puts 3gpp technology by design in disadvantage even when there no other NW (carrying constant overhead as compared to WiFI 6). So, based on the same reasoning as above, I recommend but not to have such a built-in unnecessary restriction that it is not even required by regulations. Then on Alt-3, I added FFS to reflect Nokia’s original proposal but do agree that in this context, FFS is not needed. Any such discussions can be further pursued in section 2.5. I would prefer Alt-4 but honestly, it does not matter any way. The UE doesn’t start UE initiated Cot until it is provided with configurations. Having enable/disable functionality at the same time, does not change anything, whether default is based on Alt-3 or Alt-4. The only impact would be on idle/inactive (if agreed) and that provides some protections during idle period when UEs send RACH which gives an advantage to Alt 3 as compared to Alt-4. Alt-3 is not extreme as Alt-1 and it has the potential of making coordination simpler if needed (comparing to Alt-2). @LG, vivo, Sony: Based on the explanation above, could Alt-3 be acceptable to you? @vivo, Apple: Agree that dynamic signaling should not be included. That is a separate discussion. @All: Moderator suggests to remove FFS form Alt3. Current Status: Alt-3 is acceptable: Sharp, QC, DCM, Panasonic, OPPO, ETRI, Intel, Apple, IDC, ZTE Alt-3 is NOT acceptable yet: LG (Alt1/Alt2), vivo(Alt2), Sony (Alt2), HW/HiSi (Alt2) @LG, vivo, Sony, HW/HiSi: Based on the discussion so far, would Proposal updated Alt-3 be acceptable to you? Updated Proposal 2-1: In semi-static channel access mode, decide among the following alternatives: Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB Note: In case Alt.2 is supported, it should be captured as conclusion due to previous agreement. Alt-3: A UE as an initiating device, “by default”, is not allowed to transmit during the idle period of any FFP associated with the serving gNB. The UE transmission during the idle period of any FFP associated with the serving gNB can be enabled by RRC. FFS on dynamic enabling/disabling |
| Intel | We are ok with the Alt-3 as updated by the moderator. |
| Sharp | We are fine with the updated Proposal 2-1 (First preference is Alt-1 and second preference is Alt-3). |
| Apple | We are ok with the updated Alt-3. |
| CATT | We are fine with Alt-2. |
| Xiaomi | We are fine with the updated Proposal 2-1, and support Alt-2 |
| LG | First of all, our first preference is still Alt-1. Besides, Alt-2 is also acceptable considering possible gNB control by well configuring UL resource to avoid idle period of gNB FFP. We are not supportive with Alt-3 since common UE behavior is required for this coexistence issue rather than per-UE configuration. |
| Spreadtrum | Proposal 2-1 (Alt-3 without FFS) |
| Samsung | We are OK with Alt.3 as updated by the moderator (i.e., without FFS). |
| DCM | We are fine with Alt-3, while our 1st preference is still Alt-2 |
| ETRI | We are OK with Alt-3. (1st preference is Alt-2) |
| ZTE | Alt-3 without FFS is acceptable to us, while our 1st preference is still alt-1 |
| Panasonic | We are OK with Alt.3 as updated by the moderator (i.e., without FFS). |
| vivo | We support Alt.2. |
| Lenovo/MOT | Support Alt-1 We are wondering how RRC signaling in Alt-3 can protect gNB-idle period to serve dynamic URLLC- DL data? |
| Qualcomm | we can accept Alt-3 and our first preference is Alt-1 |
| Apple | Fine with Alt-3 without FFS |
| CATT | We are fine with Alt.2 |
| Xiaomi | We are fine with the updated Proposal 2-1, and support Alt-2 |
| Nokia, NSB | We do not agree on the update for Alt-3 and prefer the previous wording for it. The point with the previous wording was that dynamic signaling is necessary to be able to adapt to gNB choice of using the FFP or not. |
| Sony | We do not agree with Alt-3 as it was established that the gNB is in control of the interference so there really isn’t any point of restricting the UE from transmitting in gNB’s idle period. We still prefer Alt-2. In fact, Alt-3 should be the other way round, i.e. by default the UE is allowed to transmit in gNB’s idle period if UE initiated a COT and can be configured otherwise. But still we prefer Alt-2. |
| IDC | We are fine with alternative 3. |
| Moderator | @Lenovo/MOT: Not sure if I understood your question and relation to URLLC DL data. In principle, if behavior as Alt-1 is preferred, the gNB will not enable transmission in idle. That means you can have Alt-1 by using Alt-3, where the NW does not configure or enable corresponding RRC parameter. @LG: On the comment: “We are not supportive with Alt-3 since common UE behavior is required for this coexistence issue rather than per-UE configuration.”, it is difficult to understand how this is consistent with other discussions. For example, if not mistaken, Alt-c in proposal 4-1A is originally proposed by LG which by configuration requires different behavior from UE (if UE assume UE-initiated COT can transmit in idle period, if it assumes gNB initiated COT, can transmit in gNB idle period). In short, whether any transmission is allowed in idle period by RRC, is nothing but cancelation by TDD configurations, etc. It is just coupled for FFP configuration. Additionally, if behavior as Alt-1 is preferred, the gNB will not enable transmission in idle. That means you can have Alt-1 by using Alt-3, where the NW does not configure or enable corresponding RRC parameter. @Nokia: Please refer to the previous discussions that why inclusion of dynamic signaling was opposed by companies and can in fact be achieved by solutions discussed under 2.5. Current Status: Alt-3 without FFS is acceptable (as a compromise btw Alt1 and Alt 2): Sharp, QC, DCM, Panasonic, OPPO, ETRI, Intel, Apple, IDC, ZTE, Spreadtrum, Samsung, ETRI, Panasonic, Qualcomm, Ericsson Alt-3 is NOT acceptable yet: LG, Lenovo/Mot (Alt1) vivo, Sony, CATT, Xiaomi, HW/HiSi -> (Alt2) Nokia/NSB (Alt 3 with dynamic signaling) Updated Proposal 2-1: In semi-static channel access mode, decide among the following alternatives: Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB Note: In case Alt.2 is supported, it should be captured as conclusion due to previous agreement. Alt-3: A UE as an initiating device, “by default”, is not allowed to transmit during the idle period of any FFP associated with the serving gNB. The UE transmission during the idle period of any FFP associated with the serving gNB can be enabled by RRC. |
| Moderator | In order to check whether there was a convergence by check point 2, Moderator asked the following questions: Question 1: Can you be supportive of Alt-3 in Proposal 2-1? Some companies provided input to the question above, that is listed below. |
| LG | NO. We still don’t see the essentiality to introduce RRC configuration on this issue. |
| Vivo | No. We all agreed the conclusion made in the last meeting that potential collisions or blocking are controlled by gNB. Protect gNB’s idle period can be achieved by proper configuration/scheduling. We do not think additional restriction is needed. |
| CATT | No, Alt.2 is already supported and we can’t see any motivation to add additional restriction and RRC configuration. |
| Apple | We are OK with Alt-3. |
| Intel | YES - our understanding is that if the UE is operating as a responding device within a gNB’s COT, then the UE is not allowed by regulation to transmit within a gNB’s idle period. However, if the UE operates as initiating device, then the UE does not have any restrictions, besides not transmitting in its own idle period. Now in this last case, if the gNB has something scheduled to transmit, and would like to operate as initiating device, then the UE could potentially block the gNB from acquiring its next FFP, since the UL transmission would collide with the gNB’s idle period. In order to prevent this from happening, Alt-3 seems to us the more logical way to move forward: - If the gNB has the intention to always acquire a FFP, the UE should be prevented from transmitting in the idle period of that FFP; - Otherwise, if the gNB has no intention to acquire some FFP, then the gNB can enable a UE from transmitting in the idle period of those FFPs. With that said, Alt-3 is preferred. |
| Xiaomi | No From our understanding, UL transmission is either configure by gNBor dynamic scheduled by Gnb. By a proper UL/DL configuration/SFI indication and scheduling, the blocking case can be avoided |
| Nokia/NSB | With the understanding that dynamic enabling /disabling of use of gNB’s idle period selectively will be discussed under 2.5, we are ok with Alt3 as a compromise. |
| Moderator | @All: Based on the feedback on Question 1 above, it is clear that there is no convergence. @All: I hope the group is clear that if none of the alternatives in proposal 2-1 is agreed, that means that by default Alt-2 (current status) stands. Please remember the FFS in agreement corresponds to Proposal 2-1. I will prepare a proposed conclusion in case of no agreement for Proposal 2-1, for completeness. I am still hopeful we can converge, but I need to prepare such that there is a clarity on the status. Agreements: For semi-static channel access mode, When gNB operates as an initiating device The gNB is not allowed to transmit during the idle period of any FFP associated with the gNB in which the gNB initates a COT When a UE operates as an initiating device The UE is not allowed to transmit during the idle period of any FFP associated with the UE in which the UE initates a COT When a UE shares a COT initiated by the gNB during an FFP associated with the gNB The UE is not allowed to transmit during the idle period of that FFP in which the UE shares the COT initiated by the gNB When the gNB shares a COT initiated by a UE during an FFP associated with the UE The gNB is not allowed to transmit during the idle period of that the FFP in which the gNB shares the COT initiated by the UE FFS whether/how to support additional restrictions to the idle period ================================== @All: Feel free to continue discussion, especially if it helps progress. Current Status: Alt-3 without FFS is acceptable (as a compromise btw Alt1 and Alt 2): Sharp, QC, DCM, Panasonic, OPPO, ETRI, Intel, Apple, IDC, ZTE, Spreadtrum, Samsung, ETRI, Panasonic, Qualcomm, Ericsson Nokia/NSB [With the understanding that dynamic enabling /disabling of use of gNB’s idle period selectively will be discussed under 2.5] Alt-3 is NOT acceptable yet: LG, Lenovo/Mot (Alt1) vivo, Sony, CATT, Xiaomi, HW/HiSi -> (Alt2) Nokia/NSB (Alt 3 with dynamic signaling) Updated Proposal 2-1: In semi-static channel access mode, decide among the following alternatives: Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB Note: In case Alt.2 is supported, it should be captured as conclusion due to previous agreement. Alt-3: A UE as an initiating device, “by default”, is not allowed to transmit during the idle period of any FFP associated with the serving gNB. The UE transmission during the idle period of any FFP associated with the serving gNB can be enabled by RRC. Note: In case of no agreement on selection of one of the alternatives above, it should be captured as conclusion that Alt-2 is supported due to previous agreement. |
| Sony | Support the updated proposal |
| Huawei, HiSilicon | We are Ok with the updated proposal. @ Intel, we do not think that the common understanding of Alt-3 is as described in your comment above. In other words, the RRC configuration in Alt-3 is not intended to selectively enable/disable the UE transmission during the gNB idle period of certain gNB FFPs. This is in fact why we asked this question on the reflector and we did not see an objection to the answer received from the moderator as below: “The RRC configuration is not meant to enable/disable the UE transmission during the idle period of selected gNB FFP , right? That is the language, “idle period of any FFP associated with the serving gNB” is the same as in Alt-1 for example Sorour: Yes, that is my understanding.” We understand that Alt-3 is switching between Alt-2 and Alt-1 by RRC configuration. However, while applying Alt-2 as the default and agreed behaviour, gNB can selectively protect a given gNB idle period by either proper UL scheduling, configuration, or UL cancellation in that idle period for all intra-cell UEs. |
| Intel | We could be OK with Alt-3 or Alt-1, but we really believe that Alt-2 would be a very bad design choice, since we should always constrain blocking from happening, and this should be imposed by the design itself. @HW thanks for the comment, and sorry if my prior comment was misleading. Our understanding is the same as the group: switching between Alt-1 and Alt-2 for all FFPs done by RRC configuration. |
| Apple | OK with the updated proposal. |
| ZTE | We are OK to list the alternatives for now. Our preference is Alt-1 and can be ok with Alt.3 as we mentioned that it is beneficial for the URLLC use cases. We disagree that Alt-2 would be supported in case of no agreement on the proposal. Naturally Rel-16 behavior of FBE should be the baseline where both gNB and UE cannot transmit in the idle period of gNB’s FFP. |
| CATT | We prefer Alt.2 based on previous agreement and we can’t see any motivation to add additional restriction for UE to execute UL transmission on the idle period of gNB FFP. |
| vivo | We are fine with the proposal. |
| Panasonic | We are OK to list the alternatives. We share same view with Intel and ZTE that Alt.1 or Alt.3 is preferred. |
| Samsung | Fine with the updated proposal. We prefer Alt.1, and also OK with Alt.3. |
| Sharp | The intention of Note is not fully clear to us. Suppose that agreement on selection cannot be achieved for now, shall the group continue the discussion, e.g., in next meeting? Or it means that Alt 2 would be the de facto down-selection result? Our views on additional motivation of Alt3/Alt1 are also copied in the follows for easy tracking. (Sorry for the redundancy if you already checked it) One of our concerns is from network coordination perspective. With Alt3/Alt1, network coordination can be simplified, which was also summarized by moderator. We can consider it as kind of periodicity on system level. Although FBE is targeting at controlled environments such as confined factory scenario, we cannot preclude coexistence deployment that consists of multiple gNBs from different vendors, all operating with 5G NR. Such deployment may be reasonable considering cost at the factory owner’s side. Without the mechanism by Alt3/Alt1, to perform network coordination, information of gNB FFP and UE FFP configurations and furthermore related dynamic indications on idle periods/COT initiation needs to be exchanged and severe scheduling restriction would be imposed to each gNB. Things become even worse for multiple UEs configured with different UE FFP periods/offset. The network coordination would become very difficult. Thus, long-term based (permanently as in Alt1 or semi-statically as in Alt3) mechanism of system periodicity is required. |
| LG | We are fine with the proposal. |
| Nokia, NSB | We support the proposal |
| Qualcomm | Support the updated proposal. We prefer Alt.1, and also OK with Alt.3. |
| InterDigital | We are fine with the updated proposal. |
| ETRI | We support the proposal. |
| Futurewei | We support Alt -3 . For this proposal, as we mentioned before, our preference is to have just selected UE FFP disabled that would collide with the gNB LBT, i.e. only those UE FFP that could block gNB COT start. But we could live with the present Alt-3 as well. |
| Moderator | @All: It would operate as Mohamed described in case of misunderstanding (please see HW/HiSi last comment). @Sharp: The intention of the Note is when we decide to conclude this discussion, in case there is no consensus to select any Alt (Alt1 or Alt 2 or alt3), it means there is no consensus to include additional restrictions. That means Alt 2 would be the status. Then we should capture that as a conclusion. On when: I mentioned in my email that my observation is that the views are firm. Not sure extending to next meeting would change anything. Up to you of course if you want to leave it open until next meeting. Feedback on your preference before I communicate with Wanshi would be helpful. Current Status: Alt-3 is acceptable (as a compromise, companies 1st preference is Alt1 or Alt 2): Sharp, QC, DCM, Panasonic, OPPO, ETRI, Intel, Apple, IDC, ZTE, Spreadtrum, Samsung, ETRI, Panasonic, Qualcomm, Ericsson, Nokia/NSB, Futurewei Alt-3 is NOT acceptable: LG, Lenovo/Mot (Alt1) vivo, Sony, CATT, Xiaomi, HW/HiSi -> (Alt2) Updated Proposal 2-1: In semi-static channel access mode, decide among the following alternatives: Alt-1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB Alt-2: As an initiating device, the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB Note: In case Alt.2 is supported, it should be captured as conclusion due to previous agreement. Alt-3: A UE as an initiating device, “by default”, is not allowed to transmit during the idle period of any FFP associated with the serving gNB. The UE transmission during the idle period of any FFP associated with the serving gNB can be enabled by RRC. Note: In case of no agreement on selection of one of the alternatives above, it should be captured as conclusion that Alt-2 is supported due to previous agreement. |
| Moderator | Updated proposal 2-1 was not agreed during GTW, Feb 4th. |

### Other design issues

- Proposal 1: Support allowing only UEs with high priority data/control to initiate a COT for FBE.

  - Lenovo/MOT

- Proposal 2: Once a device, initiates or responds a COT, remains initiator or responding until the end of corresponding FFP.

  - FW

- Proposal 3: UE initiating a COT within a Gnb-initiated COT could be allowed only if transmission overlaps with the Gnb FFP idle period.

  - MTK

| Question: What is your view on Proposals 1 to 3? |
| --- |
| Company | Comment |
| Sony | Proposals seemed to impose additional restrictions. It would be good to understand the rationale behind such restrictions. |
| Vivo | Currently, we do not see the necessity for above restrictions. |
| Futurewei | Proposal 2. |
| Intel | Same as other companies, we do not see the technical reason for the proposal above. |
| CATT | We need check the motivation of above proposals. |
| LG | We share the same view with Sony and vivo. It seems premature at this stage to have such restrictions. |
| Nokia, NSB | Proposal 1 could make sense for RRC CONNECTED mode but should be discussed in RAN2. We disagree with Proposals 2 and 3. Proposal 2: A UE could initiate a COT by transmitting at the start of a UE FFP. The UE could stop transmitting before the Gnb idle period to give an opportunity to the Gnb to acquire the channel. After the Gnb has acquired the COT, the UE may operate as responding device, even if the transmission is contained within the UE FFP. Proposal 3: from regulatory perspective, there is no guarantee that LBT at Gnb fails even if the UE is transmitting during the Gnb idle period. From performance perspective, allowing UE-initiated transmissions during Gnb idle prevent may prevent the Gnb to transmit critical signals such as SSB. |
| Sharp | Reasons/motivations of Proposal 1 and Proposal 3 need clarifications. Regarding Proposal 2, we would like to see clarification on whether the following cases are forbidden by the constraints in Proposal 2: case 1: within a Gnb FFP, Gnb initiates a Gnb COT (initiator), then UE initiates a UE COT (initiator), then Gnb shares the UE COT (responder) case 2: within a Gnb FFP, Gnb initiates a Gnb COT (initiator), UE shares the Gnb COT (responder), UE initiates a UE COT (initiator) |
| ETRI | Currently we do not think the proposals are needed. |
| Qualcomm | Do not see the need for these restrictions so far. |
| OPPO | These aspects may be related to section 2.3, section 2.4. We can first discuss 2.3 and 2.4 then come back to additional restrictions. |
| InterDigital | We don’t support all the three proposals |
| DOCOMO | We don’t see the necessity for Proposals 1 and 3 at this stage, but support Proposal 2. We don’t see the necessity of COT overridden, i.e., once a device initiates COT, it remains until the end of the corresponding FFP. |
| Lenovo/Motorola Mobility | Proposal 1: The intention is to provide more opportunity for a UE having high-priority data/control to be able to initiate a COT (not blocked by low-priority data/control transmissions of other Ues). As suggested by OPPO, the proposal can be discussed along with proposals in sections 2.3 and 2.4. Proposal 2: we disagree. If Gnb obtains the channel after successful CCA in Gnb-idle period, it can initiate Gnb-COT. Proposal 3: it’s fine as long as the UE does not transmit during the Gnb-idle period. Maybe we can reword the proposal to: UE initiating a COT within a Gnb-initiated COT could be allowed only if transmission “duration” overlaps with the Gnb FFP idle period with no transmission during the Gnb-idle period. |
| Samsung | We don’t see the necessity for proposal 1~3. |
| WILUS | Currently, we do not see the need for those proposal 1~3 and need to clarify further the motivation for those proposals 1~3. |
| HW/HiSi | Proposal 1: Not support Proposal 2: Ok in principle, but it should be clarified what additional restriction is proposed to the conclusion made last meeting: Conclusion: If a device X at a given time is initiating a COT, the applicable FFP for the device X is the FFP associated with X. If a device X at a given time is sharing a COT initiated by a device Y, the applicable FFP for the device X is the FFP associated with Y. Note 1: One of the devices X and Y is a UE and the other is its serving gNB. Note 2: Whether or not there is additional restriction on idle period is still FFS. Proposal 3: Need to understand better. For instance, both gNB and UE may not know at the beginning of the UE FFP whether a CG UL transmission would occur and overlaps with gNB idle period |
| Apple | The proposals seem to be related to the issues in Section 2.3 and 2.4. They can be revisited later on if needed. |

## Discussion topic: RRC enabling COT initiation functionality

The proposals 3-1 and 3-2 below, aim to capture the views with respect to the discussion topic on high level.

Other proposals address additional details.

Please if needed, prioritize the discussion of Main design issues.

### Main design issues

Proposal 3-1:

- In semi-static channel access mode, UE COT-initiating functionality can be enabled/disabled by RRC.

  - FFS details.

  - MTK, E///, Apple, LG, InterDigital, FW

Proposal 3-2:

- In semi-static channel access mode, down-select one of the following alternatives:

  - Alt-1: As part of a CG UL configuration, enable/disable UE COT-initiating functionality for the CG UL transmissions aligned with the configured UE FFP boundaries. Details FFS.

    - Apple, IDG

  - Alt-2: As part of UE FFP configuration, enable/disable UE COT-initiating functionality for the UL transmissions aligned with a set of UE FFP boundaries. Details FFS.

    - E///, LG?, FW?, MTK?

  - FFS on other alternatives.

| Question1: What is your view on Proposal 3-1? Question2: If you are supportive of Proposal 3-1, what is your view on Proposal 3-2 which describes alternatives to realize Proposal 3-1? |
| --- |
| Company | Comment |
| Sony | Proposal 3-1 is already agreed since we already agreed that UE’s FFP period and offset are configurable in RRC. Is this proposal suggesting we have another additional parameter that enable/disable UE’s COT initation? Proposal 3-2: We prefer not to down-select any alternatives. We need some clarification on the alternatives: Alt-1 is limiting as it suggest that UE can only initiate a COT for CG-PUSCH. Does this means UE can never initiate a COT if it is being scheduled by Gnb to start its DG-PUSCH or PUCCH at the beginning of UE’s FFP. Alt-2: Is this suggesting that some configured UE FFP cannot be used for UE initiation? How does this work with the dynamic indicator in the issue discussed in Section 2.4.2? |
| vivo | For Proposal 3-1, is it for all UL channels/signals, separate RRC parameters can be used to enable/disable the UE COT-initiating functionality when UE’s FFP period and offset are configured? We are not sure about the benefit or motivation to disable the UE COT-initiating functionality for some channels once the UE’s FFP period and offset are configured. Regarding proposal 3-2, for Alt.2, what does it mean the UL transmissions aligned with a set of UE FFP boundaries, the intention is to introduce some bitmap like signalling to indicate which UL transmission that aligned with a UE’s FFP boundary can initiate COT, which UL transmission that aligned with another UE’s FFP boundary cannot initiate COT? What is the benefit of this additional signalling compared to the implicit rule that the UE can initiate COT if the UL transmission resources are aligned with the UE FFP boundary; Otherwise, UE cannot initiate COT. |
| Futurewei | Alt 3-1, For 3-2: Note that the FFP configuration should respect the minimum time interval FFP configuration change, and the fact that a single configuration may be used for initiating COT for this minimum time interval. In our understanding the starting points for initiating COTs have very precise determination through the offset and periodicity. Therefore, we agree with Sony that we need further explanations before down-select. |
| Intel | We do not see the technical need for neither of the options above. Our understanding is that the operation of UE’s has initiating device is currently conditional to the network to provide the u-FFP parameters. When the UE can operate as an initiating device, then the COT sharing procedure can be used, and the baseline of the procedure is that of Rel.16. |
| CATT | For proposal 3-1，configuration of UE’s FFP period and offset are already agreed. Proposal 3-2 is related to section 2.4.1 and section 2.4.2. In addition, we need clarify what means “UE COT-initiating functionality”. We need clarify whether this is related to UE capability or not. |
| LG | On Proposal 3-1, we have similar observation with Sony that whether UE COT-initiating functionality is enabled/disabled for a UE would be based on whether UE FFP period and offset are provided to the UE or not. On Proposal 3-2, we prefer Alt-2 (vivo’s understanding in above seems correct) to handle/control potential UE congestion at a same UE FFP boundary by distributing the Ues over multiple UE FFP boundaries, especially in case when PRB-interlace with coarser resource granularity is used since it may be hard to ensure that all of potential URLLC Ues are well configured with the FDMed CG PUSCH resources to be aligned with a same UE FFP boundary. |
| Panasonic | We support Proposal 3-1, but share the similar observation with Sony, CATT, and LG. |
| ZTE | We are fine with proposal 3-1. For 3-2, our preference is alt-1 since this is useful for configured grant. For the grant-based, the enable/disable can be left to implementation, e.g. whether or not to schedule the transmission aligned with the FFB boundaries. |
| Nokia, NSB | Proposal 3-1 is not clear. As it is already agreed that UE FFP parameters can be configured via RRC, this means UE COT-initiating functionality can already be enabled/disabled by RRC. If the proposal is to introduce an additional RRC mechanism to enable/disable UE COT-initiating functionality in specific occasions/UE FFPs (i.e. Alt-2 e.g. to protect Gnb transmissions), then we believe it would be better to specify additional constraints on transmissions during Gnb idle periods, as discussed for proposals in Section 2.2, mainly because this approach is more robust from a regulatory perspective. Proposal 3-2: in our opinion Alt-1 is more related to proposal 1 in section 2.2.2 (support allowing only Ues with high priority data/control to initiate a COT for FBE). |
| Sharp | We are not clear on the intention of Proposal 3-1. To our understanding, UE COT-initiating functionality is implicitly enabled/disabled by UE FFP configuration as the follows: Presence of UE FFP configuration ( enabled Absence of UE FFP configuration ( disabled Thus, if this is the common understanding, UE FFP configuration seems to be sufficient for “enable/disable UE COT-initiating functionality” itself. Regarding Proposal 3-2, we have the similar question on the intension of “a set of UE FFP” as vivo. |
| ETRI | Basically UE’s COT initiation can be determined based on conditions. For example, UE may perform the COT initiation when a UE FFP includes a UL from the beginning, and would skip the COT initiation otherwise. On top of that, Proposal 3-1 can be applied to provide additional flexibility/controllability. In that sense, we support Proposal 3-1. For Proposal 3-2, we prefer Alt-2. |
| Qualcomm | We support proposal 3-1. In our opinion, after the UE FFP parameters are configured, RRC can further configures whether a specific UL transmission can initiate a COT or not. If yes, the UE FFP parameters will be applied. For Proposal 3-2, we prefer Alt-2. |
| OPPO | Our understanding is that once the UE FFP configuration is provided to the UE, by default the UE is allowed to initiate the COT at the FFP boundary. Then additional signaling may be added by the Gnb to forbid the UE to perform COT initiation. |
| InterDigital | We support proposal 3-1. For the case where there is an ongoing Gnb-initiated COT, the UE can be configured with either using the Gnb-initiated COT or a UE-initiated COT for the transmission of a CG. The configuration can indicate under what circumstances a UE-initiated COT may be used (for example based on the priority of the data). For proposal 3-2, Alt-1 could enable this behavior. |
| DOCOMO | We don’t see the necessity of either Proposal 3-1 or 3-2 and share the same view with intel |
| Lenovo/Motorola Mobility | Proposal 3-1: clarification of the RRC signaling is needed (agree with Sony) Proposal 3-2: fine with Alt-1. Would be good to clarify the use-case for Alt-2. |
| Samsung | Proposal 3-1 needs more clarifications. Does it mean a dedicated RRC signaling to enable/disable UE’s COT in addition to UE FFP parameter configuration? If yes, what is the motivation? Proposal 3-2, explanation for Alt-2 is needed. And benefit/motivation for each alternative would be helpful for discussion. Lastly, what’s the relation between 2.3 and 2.5/2.6? It seems all these are about how to enable/disable UE’s COT. |
| Apple | For proposal 3-1, we think it is fine to use the FFP configuration to enable the UE-initiated COT. For proposal 3-2, we see some value of Alt 1, as explained in our contribution: “If multiple UEs are configured with overlapping resources for UL transmissions (i.e., CG PUSCH) to increase the probability of UEs using the resources, the collision issue has been handled by random offset for UEs’ LBT so that one UE’s transmission can prevent other UEs from starting their transmission. However, for UE-initiated COT with FBE, the FFP boundary is pre-defined and cannot move. Therefore, it could make sense to allow only one UE (or very few UEs) to initiate their own COT for a particular resource. In this sense, it can be useful to introduce configuration for each CG configuration to enable or disable UE-initiated COT.” |
| WILUS | We tend to share the view from Nokia and Sharp. Depending on whether UE FFP parameters are configured by RRC or not, the UE COT-initiating functionality can already be enabled/disabled by the RRC. |
| HW/HiSi | For Proposal 3-1, our understanding is that if the gNB does not intend to allow the UE to initiate CO in a semi-static manner, it should not provide the UE with the UE FFP semi-static configuration as the default behavior would be to only share the gNB CO as per Rel-16 spec For Proposal 3-2, we share the same views as Sony -Alt-1 UE initiated COT is not limited to CG, it also applies to any configured/scheduled UL -Alt-2 As we understand it is discussed in Section 2.4 |
| Moderator | Proposal 1-3 was not well formulated. The intention was as described by Nokia: The proposal is to introduce an additional RRC mechanism to enable/disable UE COT-initiating functionality in specific occasions of UE FFPs. Alt-2: vivo’s understanding of Alt-2 is correct in principle: For the UL transmissions aligned with a set of UE FFP boundaries, the intention is to introduce some bitmap like signalling to indicate which UL transmission that aligned with a UE’s FFP boundary can initiate COT, which UL transmission that aligned with another the UE’s FFP boundary cannot initiate COT. Please note that Alt-2 is the same as Alt-c in Proposal 2.4.The reason that it is included here is that it appeared that it is part of configuration where the intention of topic is 2.4, is that for the transmissions that are aligned with the boundary, where the UE can assume that can initiate a COT or can share a COT (two possibilities), how the UE determines which hypothesis is valid? Therefore, we need a solution as Alt-a or Alt-b. From moderator point of view, considering Alt-c as part of configuration, is a more proper way of problem formulation. There are two methods for doing that, as Alt-1 and Alt-2. For Alt-2, please see LG’s motivations and for Alt-1, Apple. The reason to have proposal 1-3, was to see if there is a support for such functionality in general. In case there is, which option is preferred, Alt-1, Alt-2 or both. But maybe, now the intention is clear and the proposal is not needed. So, it is better to remove it and keep only Proposal 3-2. Based on the comments, please find below the revised proposal that is hopefully clearer: @All: Based on discussion above, Proposal 3-1 is not needed, and Proposal 3-2 is updated as the following. @All: Alt-2 in this proposal is in principle same as Alt-c. @All: Could you please provide your view on following proposal? Updated Proposal 3-1: In semi-static channel access mode, support enabling/disabling UE COT-initiating functionality in specific occasions of corresponding UE FFPs by RRC. Updated Proposal 3-2: In semi-static channel access mode, down-select one of the following alternatives: Alt-1: As part of a CG UL configuration, enable/disable UE COT-initiating functionality for the CG UL transmissions aligned with the configured UE FFP boundaries. Details FFS. Alt-2: As part of UE FFP configuration, enable/disable UE COT-initiating functionality for the UL transmissions aligned with a set of UE FFP boundaries. Details FFS. FFS on other alternatives. |
| CATT | We prefer Alt-2 and enable/disable UE COT-initiating functionality is only related to FFP configuration regardless of UL configuration on CG or DG. |
| Samsung | We still fail to see the necessity of proposal 3-2. If a UE FFP is disabled by the RRC configuration, does it mean (a) a UE has to drop the CG PUSCH aligned with the FFP boundary, or a (b) UE can still transmit the CG PUSCH but this CG PUSCH does not initiate a COT (e.g. if gNB has initiated gNB’s FFP and the CG PUSCH is within gNB’s FFP, UE can transmit CG PUSCH using gNB's FFP)? If go with (a), we already have existing mechanisms to cancel CG PUSCH, we don’t see the necessity of new mechanism. If go with (b), it does not solve inter-UE blocking issue as mentioned by some companies. |
| Sharp | It seems that Alt-2 is more general, which can be used for both CG and DG UL transmission. We can understand the motivations for Alt-1 but not clear why to limit the enabling/disabling functionality to CG case. |
| Qualcomm | We prefer Alt-2. |
| Futurewei | We prefer Alt-2 looks more flexible. |
| vivo | We don’t support additional signaling to enable/disable the UE-initiated COT. |
| DOCOMO | We don’t support the proposal. We think current specification is enough to enable/disable COT initiation as commented in Section 2.5.1. |
| Sony | Since this is related to Section 2.4.1, then Alt-1 is more relevant. Alt-2 would contradict or complicate the options in Section 2.4.2 since for the Scheduled UL transmission we have dynamic indicators. Hence it would be good that we sort out Section 2.4 before returning to this section. Therefore our preference is not to make any decision on this issue |
| ETRI | We prefer Alt-2. |
| LG | We prefer Alt-2. |
| Intel | We share exact same concerns as Samsung, and we fail to understand the technical reason of this proposal. If the goal is to converge on Alt-c of Section 2.4, we think that the whole discussion should occur jointly. By agreeing on either Alt-1 or Alt-2, we only agree on whether the UE should operate in a configurable manner as an initiating device, but there will be no understanding on the assumption on whether the UE can effectively operate as such as an initiating device in case the gNB has already acquired a FFP, and the UE’s FFP falls within it. Also Alt-2 is targeted to all the UEs, while Alt-1 is targeted only to CG-UE. |
| Nokia, NSB | In our view it is best to revisit this issue later after we’ve agreed on 2.4. The alternatives are kind of imbalanced, since Alt-1 relates to configured grants and Alt 2 relates to all UL transmissions. For the system to work, there is not strict need to support either of these options. |
| InterDigital | We don’t think that Alt-c translates to Alt-2. Alt-c means that for the case where a transmission could use either gNB-initiated COT or UE-initiated COT, the UE receives a configuration to determine its behavior. For example, the configuration could allow the UE to use a gNB-initiated COT if it exists or use a UE-initiated COT if there is no gNB-initiated COT, or select a COT based on, for example, transmission priority. On the other hand, Alt-2 could disable a UE from transmitting altogether (e.g. when there is no gNB-initiated COT). We are ok with Alt 2. |
| Huawei, HiSi | We share the same views as Samsung, Intel and Nokia which we had expressed in the previous round as well |
| Apple | If the intention is to list the proposals without down-selection now, we are fine with it. We can continue to discuss the issue. |
| Moderator | Some companies either are not supportive of any of the alternatives, or suggested to discuss this topic if needed after concluding the discussion in section 2.4. @All: The discussion is postponed until the discussion in section 2.4 is concluded and will be resumed if needed. |
| Moderator | @All: Please see the discussion in Section 2.4.1 with respect to Alternative Proposal 4-1B. |

### Other design issues

- Proposal 1: A UE-initiated COT cannot cross the boundary of even indexed radio frame

  - Spreadtrum

- Proposal 2: Consider to align the assumption of FFP type for multiple RB sets in a carrier/BWP under the unaligned FFP structure between UE and gNB.

  - LG

- Proposal 3: Consider to define the FFP including or starting with essential DL/UL transmission occasions (such as SSB or CORESET#0) as default FFP-g.

  - LG

| Question: What is your view on Proposals 1 to 3? |
| --- |
| Company | Comment |
| Futurewei | We are not sure that understand these options, and how they provide benefits. |
| LG | Firstly, considering the case where multiple RB sets (requiring individual LBT) are within a carrier or BWP under the unaligned FFP starting structure between gNB and UE, it is required for UE to assume a same FFP type (i.e., gNB FFP or UE FFP) for the multiple RB sets to avoid potential UL-to-DL interference, even if the result of LBT for the multiple RB sets is different. For this reason, we think the Proposal 2 is necessary as the UE assumption. Secondly, considering the case where SSB or CORESET#0 are at the beginning or within FFP duration, the FFP needs to be assumed by UE as a default gNB FFP based on gNB-initiated COT, then with the assumption, the UE is not allowed to initiate COT for the FFP and would not try to initiate COT for the FFP to avoid potential UL-to-DL interference due to COT initiation by UE. For this reason, we also think the Proposal 3 is necessary. |
| Nokia, NSB | Proposal 1: this depends on the discussion in proposal 1-1, but in general no need to introduce such restriction. Proposal 2: unclear proposal (please clarify). Proposal 3: in our opinion this could be up the gNB configuration |
| Sharp | We feel that these proposals could be discussed later if the motivations/necessity are clarified. |
| ETRI | If we understand correctly, Proposal 2 is to clarify the FFP-related behavior for wideband operation. We think some issues regarding wideband operation, e.g., per carrier/BWP or per RB set application, need to be handled in the WI. Proposal 2 can be a starting point. |
| Qualcomm | We do not see the benefit for proposal 1 and proposal 3. Proposal 2 is not necessary since only single FFP parameter can be used per UE. Therefore, the FFP type should be identical for multiple RB sets. |
| Lenovo/Motorola Mobility | Would be good to clarify the use-case and benefits of these proposals. |
| Huawei, HiSi | We prefer to discuss these other details later on |
| Apple | We also prefer not to discuss these now. We should focus on the main design aspects first. |

## Discussion topic: COT-initiator determination

In this section, the views for configured and scheduled UL transmissions with respect to the discussion topic are captured.

Discussions are needed to decide how to determine a COT initiator for a UL transmission.

### Configured UL transmissions aligned with UE FFP boundary:

Agreements (RAN1#103-e):

In semi-static channel access mode:

- When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, down-select one of the following:

  - Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT

  - Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT.

  - Alt-c: The UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration.

- When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE:

  - If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT

  - Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT.

- FFS on other conditions for determining the corresponding UE or gNB initiated COT

- Note: A configured UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT.

Summary of companies view for above agreement:

- Alt-a:

  - HW(+clarification), ZTE, Nokia (some updates for partial dropping overlapping w idle), MTK (with some updates on processing), DCM, Spreadtrum, WILUS, OPPO (w updates), Sharp, Charter, Apple (+Altc)

- Configure btw Alt-a and Al-b Alt-c:

  - Intel

- Alt-b:

  - Samsung, ETRI, vivo

- Alt-b + Alt-c:

  - E///, CATT, LG, QC, Sony, FW, Samsung?, ETRI?, vivo?

| Question: Alt b + Alt-c or Alt a + Alt-c above, is intended to describe the case that by RRC configuration, a UE can not initiate a COT for UL transmissions aligned with a set (configured) of UE FFP boundaries. Then, the rule (i.e. Alt-a or Alt-b) is applied on the UL transmissions aligned with Ue FFP boundaries that UE can initiated COT. Can you please correct/adjust/update, if needed? Can you please provide your view? |
| --- |
| Company | Comment |
| Sony | We prefer Alt-c. It isn’t clear why we suddenly have a mixture of Alt-b + Alt-c. |
| vivo | We only prefer Alt –b, so we delete our company name from Altb + Alt-c. We prefer to define a simple and unified rule for all UL transmissions when the configured/scheduled UL resources are aligned with the UE FFP boundary. The resource allocation is under gNB’s control, if gNB does not want UE to initiate the COT, just schedules/configures the UL resource to not align with the UE’s FFP boundary. The main motivation to support UE-initiated COT is that for configured UL transmission, let UE decide the transmission opportunity based on the configuration and its buffer status to reduce the latency and improve resource usage efficiency. Therefore, when UE initiated COT is supported, that additional indication from gNB as in Alt-c to indicate the UE-initiated COT is NOT allowed for configured UL transmission obviously deviates from the intention of supporting UE initiated COT. For Alt-a, UE always needs to detect the existence of the gNB-initiated COT firstly and then decides whether to transmit in an UE-initiated COT or not, it causes unnecessary power consumptions at the UE side. In addition, gNB-initiated COT may not accommodate the CG transmission profile better than the UE-initiated COT for CG transmission. |
| Futurewei | We prefer Alt-c. We agree with Sony that combination of Alt-b+Alt-c is new while Alt-c disappeared. |
| Intel | First of all, we would like to understand what “ Alt-b + Alt-c”, means. Our understanding is that in last meeting we made an agreement to downselect among Alt-a/Alt-b and Alt-c. Secondly, we would like to clarify our position, since it was misinterpreted (correct in red): As we discussed last meeting our preference is to Alt-a: we would like to remark that based on Rel.16, the UE would need to perform in any cases presence detection to assess whether a g-FFP is valid or not. Therefore, this option would not be any different than supporting the Rel.16 behavior. However, while we understand the power consumption concerns of the proponent companies of Alt-b, which may arise in some scenario, we would be OK to compromise through Alt-c, which in our understanding means that whether Alt-a or Alt-b is used would be left up to gNB’s configuration. |
| CATT | We prefer Al-c. If a UE can’t initiate a COT for UL transmissions aligned with a set (configured) of UE FFP boundaries by RRC configuration, UE need use gNB-initiated COT for UL transmission (modified Alt.a) |
| LG | We also prefer Alt-c. We also share the same view with Sony since it would be sufficient to configure whether UE-initiated COT is allowed per each of the configured UL occasions aligned with UE FFP boundary. Moreover, the following UE behaviour/assumption was agreed in the last meeting for a configured UL transmission not aligned with a UE FFP boundary. When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE: If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. However, the above behaviour/assumption would cause potential problem in UE/gNB interaction aspect and FBE regulation perspective. For example, considering the case in the above figure, in case when the UE has initiated COT by transmitting C-UL #1 and also it has detected gNB-initiated COT in FFP-g #2 (before C-UL #3), it is reasonable that the UE assumes the C-UL #3 (not aligned with a UE FFP boundary) corresponds to gNB-initiated COT. Therefore, the above agreement needs to be slightly updated accordingly as below (e.g. change of the sentence starting with “If” and the sentence starting with “Otherwise”). If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT. |
| Panasonic | We prefer Alt-a. Alt.a seems to have unified behavior between “when a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE” and “when a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE”. |
| ZTE | Alt-a is preferred. Alt-a + Alt-c can be also considered if proposal 3-1 is agreeable. |
| Nokia, NSB | We stick to Alt-a (with some updates to handle the case where the UE transmission partially overlaps with the gNB idle period) as Alt-b (e.g. the UE assumes that the configured UL transmission corresponds to UE-initiated COT even if the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that the gNB has initiated that gNB FFP) may cause some regulatory issues (NR-U systems continuously transmitting on an unlicensed channel), as we also put in our reply to proposal 2-1. |
| Sharp | Our preference is Alt-a. Regarding switching rules by RRC configuration, we think that should be independently discussed. We need to firstly determine the baseline rule. However, there seems no such configuration flexibility if Alt-b is adopted. |
| ETRI | In our view, Alt-b is sufficient. We fail to see a use case of Alt-a or Alt-c for configured UL starting from a UE FFP boundary. The following proposal can be considered together with Alt-b. Proposal: UE expects that a configured UL starting from a UE FFP boundary is always confined within the UE-initiated COT |
| Qualcomm | Al-c. Alt-a is very complicate while Alt-b removes the flexibility of gNB. |
| OPPO | Alt-a is our preference. With Alt-b, the UE assumes to initiate COT by default and leaving gNB to avoid the UE COT initiation by scheduling is definitely a scheduling restriction. |
| InterDigital | Alt-c. Alt-a suffers from ambiguity if the UE misdetects the gNB-initiated COT. Alt-b inhibits COT sharing among multiple UEs (if UE-to-UE COT sharing is not possible). Alt-c can configure either of the behaviors in Alt-a or Alt-b. Furthermore, it can provide some flexibility in case an FFP is initiated by the gNB but does not have the requirements for the UE’s transmission (e.g. if the CAPC of the gNB-initiated COT doesn’t match that required for the UE’s transmission). |
| DOCOMO | We prefer Alt-a. We don’t see the necessity of COT overridden when gNB has already initiated COT |
| Lenovo/Motorola Mobility | Alt-a; It would be good to clarify what would be the UE assumption (w.r.t. DL and UL transmissions after the configured uplink transmission is performed) in Alt-b in the following case: the configured grant transmission is within a gNB-initiated FFP |
| Samsung | We prefer Alt-b. We’re open to Alt b+ Alt c depending how to understand “UE-initiated COT is based on gNB configuration” in Alt c. We don’t support Atl-a, because there would be miss-understanding between UE and gNB if UE does not correctly detect whether gNB has initated the COT. |
| Spreadtrum | We support Alt-a. UE detects gNB-intiated COT in plenty of scenarios, both in Rel-15 and Rel-16 we had already agreed. So it does not make sense to preclude alt a based on mis-detection. Furthermore, Alt-a gives unified solution of aligned with UL-initiated COT or at the middle of the COT for RRC configured UL transmission. |
| Apple | We think there is not much difference between Alt-a and Alt-b in terms of the effectiveness in acquiring the channel. So we are open to consider both. Maybe the meaning of Alt-c is not exactly clear to us. Does it mean that for each configured UL transmission, there is an RRC parameter that controls whether it can initiate the COT? And if configured, the UE always initiates its own COT if it aligns with FFP boundary? If this understanding is correct, it seems to be the same/similar to Alt 1 in Proposal 3-2. |
| WILUS | We support Alt-a since it seems to have the unified behavior regardless of a configured UL transmission is aligned with a UE FFP boundary or not as mentioned by Panasonic. |
| Xiaomi | We are open to this issue, but have a question related to the R1# 103 agreement. That is, if the LBT band occupied by gNB COT is different from the LBT band allocated to the CG-PUSCH. How can UE share the gNB COT? Or, are we always assuming the DL/UL transmission must be on the same LBT band(s)? |
| HW/HiSi | Alt-a is our preference Alt-a prioritizes gNB COT over UE COT and inherently provides more protection to the gNB idle period. In contrast to gNB COT which in principle can be shared by all intra-cell UEs, a UE initiated COT can be shared only to the serving gNB and the initiating UE may proceed with UL transmissions in the gNB idle period if resources were configured as such apriori. We think that a clarification is needed for any restrictions imposed on top of the rule stated in following agreement achieved earlier in RAN1#102-e: Agreements: A UE initiates a COT in an FFP associated with the UE, if the UE transmits a UL transmission burst starting at the beginning of the FFP and ending at any symbol before the FFP’s idle period after a successful CCA of 9us immediately before the UL transmission burst. In the previous meeting, we agreed as cited above to “down-select one of the following:”. We think that the newly introduced Alt-b+Alt-c goes against that agreement. Anyway, we are not supportive of Alt-c. Such gNB configuration would not be flexible to cope with the dynamics DL/UL transmissions on frame by frame basis. For instance, if the gNB had disallowed the UE to initiate its CO for a given FFP, but the gNB did not/failed to initiate its preceding CO, the UE has no chance to transmit a latency sensitive CG UL transmission and any subsequent UL transmissions till the end of that gNB FFP. Whereas, in both Alt-a and Alt-b the UL transmission(s) would still be transmitted. |
| Moderator | Please see the explanation by Moderator in section 2.3.1 that why Alt-2 in section 2.3.1 is basically the same as Alt-c. Alt-c can be considered as part of configuration. Therefore, it is more suited for the topic under discussion in section 2.3. This section, aims for a solution that resolves ambiguity. It means that after RRC configuration, there are UL transmissions that one can use two assumptions (hence ambiguity). We are trying to find out what is a good solution to decide which assumption is applicable. Therefore, the intention by Alt-a+Alt-c or Alt-b+Alt-c was that, after RRC, when Alt-c is applied, for the remaining UL transmissions at FFP boundaries Alt-a is applied , or Alt-b. (one can say fallback to Alt-c). If one does not support Alt-c at all, then we would have only Alt-a or Alt-b. If one supports only Alt-c, it is in fact Alt-b + Alt-c where some flexibility is provided. Please see for example Qualcomm comment above. I hope by this explanation, it is clear why the problems are structured in this way and such formulation does not violate any agreement because no functionality is excluded. @All: Considering the above description, if there is a change in preference, please indicate, in additional to any potential comment. |
| CATT | We prefer Alt.c and for the sake of the progress, we can also consider Alt-a+Alt-c or Alt-b+Alt-c. |
| Samsung | Since we have not identified the necessity for proposal 3-2, currently, we still support Alt b with preference. |
| Qualcomm | Alt-c |
| Futurewei | Alt-c |
| vivo | Alt-b. We share the views with Samsung. |
| DOCOMO | We still prefer Alt-a |
| Sony | We do not think this corresponding to Alt-2 of Section 2.3.1 because this issue is specifically about Configured UL Transmission. This is more aligned with Alt-1 of Section 2.3.1. Secondly, we do not think there is a need to mix Alt-b + Alt-c. Alt-b forces UE to initiate a COT even if the gNB had already initiated the COT and the CG-PUSCH is still within gNB’s COT. The fallback should be Alt-a + Alt-c. So we are fine with Alt-a + Alt-c. |
| ETRI | We prefer Alt-b, although we support Alt-2 in Proposal 3-2. The correlation between Alt-2 and Alt-a/b/c is not clear to us. For the sake of progress, we are also fine with Alt-c. |
| LG | We prefer Alt-c. |
| ZTE | We still prefer Alt.a, as the same reason explained in 2.2.1, prioritize gNB’s COT is beneficial and controllable for URLLC use cases. Alt.a + alt.c can be considered but the details of alt.c should be clarified first. |
| Intel | Our first preference is still Alt-a. However, for the sake of progress we are OK to be flexible and agree on Alt-c. However, we share same concerns as Sony, and we do not believe that Alt-2 in section 2.3.1 is same as Alt-c here. We think instead Alt-1 in section 2.3.1 is more in line with Alt-c. Anyway, as we suggested above, we believe that the two proposals should be jointly discussed and not separately. |
| Nokia, NSB | We still support Alt-a, with the clarifications described in our previous reply. |
| InterDigital | Alt-c |
| Huawei, HiSi | We still support Alt-a Alt-c. Such gNB configuration in Alt-c would not be flexible to cope with the dynamics DL/UL transmissions on frame by frame basis. For instance, if the gNB had disallowed the UE to initiate its CO for a given FFP, but the gNB did not/failed to initiate its preceding CO, the UE has no chance to transmit a latency sensitive CG UL transmission and any subsequent UL transmissions till the end of that gNB FFP. Whereas, in both Alt-a and Alt-b the UL transmission(s) would still be transmitted. |
| Apple | Maybe one possibility is to remove Alt-c from this list and discuss it under configuration. Then Alt-a or Alt-b would apply when the transmission is allowed to use UE-initiated COT. |
| Moderator | @Apple: For a set of boundary in FFP configuration. If configured UL is aligned with those boundary, the transmission is not base UE-initiated COT, but rather COT sharing. @Xiaomi: Good point. Perhaps we should have a discussion on LBT BW in FBE framework to clarify the operation (separately). Companies’ view: Alt-a: Panasonic, ZTE, Nokia/NSB, sharp, OPPO, DCM, Lenovo/MOT, Spreadtrum, WILUS, HW/HiSi, Sony, Intel Alt-b: vivo, ETRI, Samsung, E/// Alt-c: Sony, FW, CATT, LG, QC, IDC, E/// Agreements (RAN1#103-e): In semi-static channel access mode: When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, down-select one of the following: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. Alt-c: The UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration. When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE: If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. FFS on other conditions for determining the corresponding UE or gNB initiated COT Note: A configured UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT. |
| Moderator | @All: There have been questions on Alt-c which I clarified in the updated proposal below (Proposal 4-1A). We had discussion that how Alt-c can be considered independently as Alt-a and Al-b as part of configuration, where the rules in Alt-a and Alt-b would are applicable for a subset of UE FFP boundaries by configuration in section 2.3.1. I thought it would be better understood if the relation is formulated clearly. Hence, I formulated Alternative Proposal 4-1B to clarify the relation. Hopefully, by comparing these two version of proposal, one can see that Alt-c just provides a level of flexibility to the NW by configuration. Please note that the proponent of Alt-c, assume Alt-b in Proposal 4-1B. However, you can see that the configuration in Alt-c, can be also applied to Alt-a. @All: It is important for me that we have a clarity on the problems and solutions that we discussed. If you see value in the approach in proposal 1-4B, If you are supportive of Alt-a in Proposal 1-4A, you would support Alt-a, in Proposal 1-4B too. If you are supportive of Alt-b or Alt-c in Proposal 1-4A, you would support Alt-b, in Proposal 1-4B 😊 @All: It is interesting to know that for our system design, which approach is preferred by you? Proposal 1-4A or Proposal 1-4B? And if your view on Alt-a7Alt-b/Alt-c has changed. Proposal 4-1A: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. Alt-c: A subset of the UE FFP boundaries are determined by configuration such that if the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, it is based on UE the initiated COT. In the absence of configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT. FFS on configuration of the subset Alternative Proposal 4-1B: In semi-static channel access mode when a UE can operate as UE-initiated COT, When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP: If the UE is provided by configuration with a subset of the UE FFP boundaries, If the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, select one of the following alternatives: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT it is based on UE the initiated COT. Otherwise, the selected Alt-a or Alt-b above, is applicable. FFS on configuration of the subset |
| Sharp | Since with the flexibility by Proposal 4-1B, gNB can assign gNB-initiated COT when needed, we think the drawback of Alt-b is less critical. Thus, we support Proposal 4-1B with Alt-b. |
| CATT | Regarding Alt-c of Proposal 4-1A, we suggest description of Alt-c should be based on whether there is gNB configuration or not. So we proposes modified Proposal 4-1A as follows: ================================================================= Proposal 4-1A: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. Alt-c: A subset of the UE FFP boundaries are determined by configuration such that if the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is allowed based on sharing a COT initiated by gNB based on UE-initiated COT by gNB configuration. Otherwise, it is based on UE the initiated COT. In the absence of configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT. FFS on configuration mechanism of the subset =========================================================== Regarding Proposal 4-1B, description of proposal 4-1B should be based on whether NB is configured or not, so we proposes modified Proposal 4-1B as follows: Alternative Proposal 4-1B: In semi-static channel access mode when a UE can operate as UE-initiated COT, When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP: In the absence of configured subset, if If the UE is provided by configuration with a subset of the UE FFP boundaries, If the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, select one of the following alternatives: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT it is based on UE the initiated COT. Otherwise, A subset of the UE FFP boundaries are determined by configuration such that if the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is allowed based on UE-initiated COT by gNB configuration the selected Alt-a or Alt-b above, is applicable. FFS on configuration mechanism of the subset We prefer modified Proposal 4-1B and Alt.c of Proposal 4-1A with our suggestion. |
| LG | In general, we think that either Proposal 4-1A or Proposal 4-1B could probably be possible way to go, but before going with the details of those proposals, it seems to need clarification on one thing for the original Alt-b. In case of Alt-b, it states that UE assumes the configured UL TX aligned with UE FFP boundary corresponds to UE-initiated COT, BTW, one question is what would be the UE behaviour in case where the UE detects DL by gNB-initiated COT before the configured UL but the gap between the DL and the UL is not sufficient? (e.g. even in such case, the UE could create UE-initiated COT without LBT…?) |
| vivo | We support Alt-b of Proposal 4-1A. Configuring the UL transmission aligned with UE’s FFP boundary but design other solutions to disallow the UE to initiate the COT is redundant operation or error configuration. In addition, it contradicts the motivation for supporting UE-initiate COT when the UL transmission is configured aligned with UE’s FFP boundary. For LG’s question, for the case that the UL transmission is aligned with UE’s FFP boundary, 9us gap can be ensured by UE-self if there is no gNB scheduling for this UE or by gNB if gNB schedules the UE. |
| Qualcomm | We prefer modified Proposal 4-1B and modified Alt.c of Proposal 4-1A in CATT. Basically, we think whether the CG can initiate a COT or not is enabled by gNB via configuration. |
| Samsung | We support Alt-b of Proposal 4-1A. As commented in 1st round, there’re already several mechanisms to cancel a CG UL transmission at the start of UE FFP boundary, e.g. cell or UE-specific DL indication by UL/DL configuration or SFI, DL/flexible indication by SFI, UE-specific dynamic scheduling overriding CG transmission, gNB transmits DL without gap before CG UL transmission (to block 9us LBT at UE side). By using these mechanisms, gNB already has sufficient flexibility to enable/disable a UE FFP, why we still need additional bit-map configuration for a sub-set of UE FFP? |
| DOCOMO | We still don’t see strong motivation to introduce additional configuration and hence, our first preference is Alt-a in Proposal 4-1A. But we can live with Alt-a in Proposal 4-1B for the sake of progress. |
| OPPO | We don’t really understand proposal 4-1B ( So our preference is proposal 4-1A. |
| ETRI | We prefer Alt-b of Proposal 4-1A. We think that if UE already initiated a UE COT, then a configured UL aligned with the UE COT can always be assumed to correspond to the UE COT if the configured UL is confined with the UE COT. If UE did not initiate the UE COT, then of course the configured UL should correspond to a valid gNB COT if any. That is our understanding on Alt-b. |
| Sony | Reading Samsung’s & ETRI’s comment, it isn’t clear what Alt-b of Proposal 4-1A is. It seemed to suggest that the UE ALWAYS initiates a COT regardless if it is still within gNB’s intiated COT. If we are considering mechanism to cancel a UE’s initiated COT then we are fine with Alt-a of Proposal 4-1A. |
| TCL | Our preference is for proposal 4-1 A. |
| Intel | As for proposal 4-1A, our first preference is Alt-a. However, we could leave with Alt-c, if in absence of any configured subset, we would assume that the UE’s assumption would be based on presence detection, which based on Rel.16 is the mechanism that a UE should already follow in order to assess on whether it can transmit or not within a g-FFP. Therefore, the text should be modified as follows: Alt-c: A subset of the UE FFP boundaries are determined by configuration such that if the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, it is based on UE the initiated COT. In the absence of configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT is based on sharing a COT initiated by gNB. FFS on configuration of the subset Same comment applies to proposal 4-1B. We would be fine with this proposal, as long as the UE would perform presence detection to assess whether it should operate as initiating or responding device when no configuration set is provided. As explained above this mechanism would not be any different than that already supported in Rel.16. In this case, the proposal should be modified as follows: In semi-static channel access mode when a UE can operate as UE-initiated COT, When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP: If the UE is provided by configuration with a subset of the UE FFP boundaries, In the configured subset is provided: If the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, select one of the following alternatives: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT it is based on UE the initiated COT. In the absence of configured subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, the selected Alt-a or Alt-b above, is applicable. FFS on configuration of the subset |
| Apple | We are now quite confused about what Alt-c is. Our original understanding was that there is a single configuration parameter that basically allows the UE to use UE-initiated COT (enabling/disabling), but it seems that that is not the correct understanding. Does Alt-c mean that for the configured UL transmissions aligned with UE FFP boundary, some of them would correspond to UE-initiated COT, and some of them would share gNB’s COT, and which ones are determined by gNB configuration? If this is the case, we do not see the motivation for such kind of configurations. |
| InterDigital | Our preference is for proposal 4-1 Alt-c. We believe that both Alt-a in proposal 4-1 and proposal 4-2 can suffer from misdetection of gNB-initiated COT. |
| Huawei, HiSilicon | We appreciate the moderator’s efforts to accommodate companies’ views. However, we share the same views as vivo and Samsung on the need for such additional pre-determined configuration that needs to be further overridden by the dynamics of DL and UL transmissions. Furthermore, in the previous meeting, we agreed as cited above to “down-select one of the following: … Alt-a…Alt-b…Alt-c”. It should be noted that inserting Alt-a or Alt-b under Alt-c is not a down selection of one alternative and goes against that agreement. We do realize the benefit of Alt-a in Proposal 4-1A as it inherently provides more protection to the gNB idle period. Therefore, we support Proposal 4-1A with Alt-a |
| ZTE | We share the similar views as other companies that a bitmap is not needed. Similar to Apple’s comment our original understanding of alt-c is a single parameter enabling/disabling UE-initiated COT which is more acceptable. So proposal 4-1A is preferred, and we support Alt-a which is a simpler solution since the overlapping between gNB COT and UE COT can be avoided. |
| Moderator | @HW/Hi: We can stick to Proposal 1A. As moderator, I am not insisting on 1B. I explained my reasons why I tried to present 1B, because we added Alt-c in the last minute and to show that when one understands the proposal, it is about the configuration and not, resolving ambiguity as it is the task here. Anyway, we focus on 1A but hopefully, the problems and solutions we are discussing are better understood. @CATT: It is not clear why UL cannot be transmitted in Alt-c if it is not configured as UE initiated COT. Moderator will try to ask group for clarification @LG: In case of Alt-B, since UE initiates a COT, there should be a gap of at least 100us before UL transmission. @OPPO: Sorry OPPO 😊 Maybe no need to bother anymore. Let’s focus on 1A. The intention was to highlight 1c is part of configuration. Anyway. I use your already indicated preference. Please check if you disagree. @Apple: The proposal was about UE decision on a UL is aligned with a given FFP boundary. Alt-c suggests by configuration UE knows whether for that given boundary, it is gNB o UE initiated COT. @Intel: It is not clear to me if the UE has to determine whether it shares gNB COT, how the assumption would be base don configuration. Moderator will try to ask group for clarification @All: Samsung raises a fair question that considering other tools in toolbox, whether flexibility by configuration (Alt-c approach) is really needed. Please provide your view. @All: Below is copy of moderator comments on reflector: On COT determination for configured UL (Proposal 4-1A (Alt-a, Alt-b, Alt-c), Proposal 4-1B(Alt-a/Alt-b)) Alt-a undoubtedly is the most complicated one because it needs tracking. Alt-b is the simplest one Alt-c is simpler than Alt-a but more complex than Alt-b Alt-c is also simple but makes UE to make exception by RRC for some FFP boundaries. Considering the discussion for FFP configuration and complexity aspects, at least it is not clear when proponents of Proposal 1A-Alt1, would support Proposal 4-1A/Alt-a. The complexity of the latter is indeed more that argued complexity for Proposal 1A-Alt2. =============================================== Current Status: 4-1A (Alt-a): DCM(1st), OPPO?, Sharp?, Sony, Intel(1st), ZTE 4-1A (Alt-b): Vivo, QC(?), Samsung 4-1A (Alt-c): QC, CATT: with CATT mod LG?, Intel(2nd with mod), IDC(1st) 4-1B (Alt-a): DCM(2nd) 4-1B (Alt-b): Sharp @All: General: Let’s focus on Proposal 1A. Please if there is any adjustment in your position, indicate (by email would be fine). Question to companies, who were arguing on complexity of Proposal 1-Alt-2, in case they are supportive of Alt-a in this proposal: Can you please explain how the complexity aspects are justified in this case and not for proposal 1-Alt-2 and more importantly, could they consider adjusting to Alt-b in this proposal 😊? Question to all/supportive of Alt-c: Based on comment from CATT and Intel, the determination of COT for Alt-c based on configuration is not clear to me, anymore. Should be considered at all? Please read below. To me it seems we shouldn’t consider Alt-c anymore and we should focus on Alt-a and Alt-b. That’s why I put Alt-c in [..]. Please read below and comment. CATT suggests Alt-c means that by configuration, whether UE is allowed to transmit UL (and if does, it would be based on UE initiated COT), or not. If not, then it means that UL resources are canceled by configuration. In that case, please look at Samsung comment above. It is not clear to me if this version of Alt-c is really relevant to this discussion. It is more related to cancellation by configuration which is a topic of section 2.5. Intel suggests (and also my understanding for Alt-c), that either UL would be by configuration based on UE initiated COT or gNB initiated COT where in the latter, it would share gNB COT. Now, the question is whether in Alt-c in this case, UE has to determine whether gNB has initiated a COT? Then it would fall back to Alt-a and it is not simple anymore. If the UE only assumes it should be based o gNB initiated Cot (my original understanding), then Intel has a good point that what if gNB has not initiated a COT? So, it doesn’t work really. Updated Proposal 4-1A (Moderator comment: Based on comment above, should Alt-c be part of this proposal?) : In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. [Alt-c: A subset of the UE FFP boundaries are determined by configuration such that if the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, it is based on UE the initiated COT. In the absence of configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT. FFS on configuration of the subset] |
| Intel | Once again Alt-a is our first preference, and I would not categorize it as more complex. In Rel.16, to be able to transmit within a g-FFP a UE has to assess whether that g-FFP is valid (i.e. ,the gNB has successfully assessed that the channel is idle and acquire the FFP by performing a transmission) or not, and based on prior agreements this should be also supported for the case when the configured resources are not aligned with a u-FFP. With that said, in our understanding Alt-a is already something that the UE has to support, and therefore the extension to the case when the configured grant resources are aligned with a u-FFP could be considered rather a trivial extension. As for Alt-c, we are not fine with the current text, and at this point we would rather prefer not to support it any further unless in case of absence of configured subset, the UE would support Alt-a, which has being mentioned many times is the baseline behavior from Rel.16, and also for the Rel.17 when the configured resources do not align with the u-FFP. As mentioned above, we would be OK to compromise for the sake of progress if majority companies prefer Alt-c, as long as either we leave as FFS the behavior in absence of configured subset, or we support Alt-a in this case. |
| CATT | We suggest removing the bracket for Alt-c For alt-c, in our understanding, if the configured UL transmission is aligned with an FFP boundary, basic rule is UE can initialize COT for this configured UL transmission. But sometimes, this will potential affect gNB-initiated COT due to LBT failure when the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB as shown in below figure. It leads to that gNB can’t schedule other UE/ transmit broadcast signalling. So we need gNB configuration/ control for UE-initiated in order to reduce the interference on gNB-initiated COT from UE-initiated COT and the conflict among UE-initiated COT among UEs. Actually gNB can configure semi-static transmission pattern and when UE determine whether UE can initiate COT or ot, UE need check gNB configuration. If UE is allowed to initialize COT, UE can initialize COT. If not, UE need use gNB-initiated COT. We aren’t sure whether NW can completely resolve this issue by SFI/dynamic scheduling and this will introduce unnecessary gNB scheduling overhead and complexity. So we think Alt.c is necessary and we proposes below modified Alt.c Alt-c: A subset of the UE FFP boundaries are determined by configuration such that if the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is allowed based on UE-initiated COT by gNB configuraiton based on sharing a COT initiated by gNB. Otherwise, it is based on UE the initiated COT. In the absence of configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT. FFS on configuration mechanism of the subset For Proposal4-1A, our further comment is that eventhough Alt-c in Proposal 2-1 is accepted, if gNB semi-statically configures that UE is allowed to transmit during the idle period of gNB-initiated COT by RRC, interference issue from UE-initiated COT to gNB-initiated COT still happens. In addition, based on previous agreement, Alt-2 in Proposal 2-1 is already supported and we can’t see any motivation to add additional restriction. |
| Sharp | Our consideration is that both Alt-a and Alt-b of Proposal 4-1A have relative drawbacks. Our original preference was Alt-a of Proposal 4-1A. We adjusted our preference to Proposal 4-1B that could address the drawbacks. However, 4-1B was not recognized by most companies and the proposal is conditioned on RRC configuration of UE FFP subset. Thus, as we commented before, it might be better to focus on Alt-a and Alt-b of Proposal 4-1A. Our first preference is Alt-a of Proposal 4-1A and we are fine with Alt-b. |
| Apple | Based on CATT’s motivation, Alt-c seems to be addressing the same issue as Proposal 2-1. If we go with Alt-3 in Proposal 2-1, we already have a solution to control UE-initiated COT/transmission in gNB FFP’s idle period. Therefore, we do not think we need a duplicate solution here. On Alt-a vs Alt-b, we tend to agree with Intel that the UE would need to monitor the configured/broadcast DL signal anyway, so Alt-a should not cause more power consumption/complexity at the UE. But on the other hand, Alt-b does not cause any problem either, as far as we can see. Maybe proponents of Alt-a can clarify what kind of issues Alt-b may cause. From our perspective, it seems Alt-a and Alt-b work equally well. |
| Xiaomi | Support both Alt-a and Alt-b. For Alt-c, CATT raised a situation when CG-PUSCH conflicts with DL transmission, but from our opinion, it can be solved by a proper UL/DL configuration. If CG-PUSCH conflicts with DL symbols, it will be dropped. So Alt-c seems unnecessary. |
| LG | First of all, our first preference is still Alt-c in order to provide gNB controllability and adaptation. But, before making any decision, the original Alt-b seems to need some clarification (as already commented in another email and also to the draft) since some of configured UL in Alt-c would apply the behavior of Alt-b. In order to finalize whole picture on the configured UL case, we need some clarification on the previous agreement below. (In fact, I had already commented these two points to the draft, but I didn’t get answer to provide clear understanding). Agreements: In semi-static channel access mode: When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, down-select one of the following: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. Alt-c: The UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration. When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE: If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. FFS on other conditions for determining the corresponding UE or gNB initiated COT Note: A configured UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT. Firstly, regarding the above yellow part of Alt-b, I commented the following point to the draft. So, I’d like to get the corresponding answer. [Sukchel] Based on vivo’s reply and FL’s reply received via the draft, the configured UL in above Alt-b would require at least 9us or 100us for UE-initiated COT. Then, my question is what would be the UE behavior/assumption in case where the gap between the gNB COT’s DL (detected before the configured UL) and the configured UL is shorter than 9us or 100us? Could the UE create UE-initiated COT even in such case? Or would the UE transmit the configured UL based on gNB COT? Or should the UE treat the configured UL as invalid resource? In case of Alt-b, it states that UE assumes the configured UL TX aligned with UE FFP boundary corresponds to UE-initiated COT, BTW, one question is what would be the UE behaviour in case where the UE detects DL by gNB-initiated COT before the configured UL but the gap between the DL and the UL is not sufficient? (e.g. even in such case, the UE could create UE-initiated COT without LBT…?) Secondly, regarding the above blue part, I also commented the following point to the draft. Thus, also I’d like to hear the opinion in this. Moreover, the following UE behaviour/assumption was agreed in the last meeting for a configured UL transmission not aligned with a UE FFP boundary. When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE: If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. However, the above behaviour/assumption would cause potential problem in UE/gNB interaction aspect and FBE regulation perspective. For example, considering the case in the above figure, in case when the UE has initiated COT by transmitting C-UL #1 and also it has detected gNB-initiated COT in FFP-g #2 (before C-UL #3), it is reasonable that the UE assumes the C-UL #3 (not aligned with a UE FFP boundary) corresponds to gNB-initiated COT. Therefore, the above agreement needs to be slightly updated accordingly as below (e.g. change of the sentence starting with “If” and the sentence starting with “Otherwise”). If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT. |
| Spreadtrum | Proposal 4-1A, especially Alt-a. we can live with Alt-b for second choice. Alt-a is not complex from our understanding. A UE anyway should monitoring whether there is DL transmission or not. It will not increase the complexity. Alt-c is an improved Alt-b. it related with UE-initiated COT configuration. If this subset is configured, all UL transmission should keep to this subset limits. So from our understanding, the point for Alt-c is this subset of UE-initiated COT mechanism can be supported or not. |
| Samsung | We support Alt-b with the same motivation to reduce complexity as proposal 1B. For Alt-c, as we previously commented, we think there're many existing ways to cancel CG UL transmission, we don't think we need additional subset configuration. So, currently, we'd like to delete Alt-c. |
| DCM | We prefer Alt-a and share the view with Intel |
| ETRI | In our understanding, intention of Alt-b is NOT to force UE to always initiate a COT for a UE FFP which contains a configured UL in the beginning, but is to follow COT duration and idle period of the UE FFP for the configured UL transmission if the UE COT is initiated by the UE. UE’s COT initiation/cancellation behavior and its indication can be separately handled under discussion topic 2.5. With that understanding, we still prefer Alt-b. We do not see a strong need of Alt-a/c. |
| ZTE | We prefer Alt-a and share the similar view with Intel and DCM in terms of the complexity. Alt-b, although from the rule itself looks simpler, but the consequence is more complex as we need to further discuss how to handle the overlapping between gNB initiated COT and UE initiated COT. |
| Panasonic | We prefer Alt-a and agree to Intel’s comment. |
| vivo | We support Alt-b. Alt-a increase UE power consumption and contradicts with the motivation to support UE initiated COT. |
| Lenovo/Mot | Prefer Alt-a Alt-c wording is not clear (seems the step in Alt-a is needed there as also mentioned by the FL); having a subset of boundaries seems an optimization |
| Qualcomm | Alt-c |
| Apple | Alt-a and Alt-b seem almost the same to us. Do not see the need for Alt-c. More detailed comments in the doc. |
| HW/HiSilicon | In response to your question about our preference for proposal 4-1A, we do agree that Alt-a is more complex than Alt-b as it requires tracking gNB COT initiation and confinement of the UL transmission within gNB FFP. In fact, if you recall, I made that exact comment in the last GTW to clarify that if the UE needs to go through this, then it makes sense that we keep the set of corresponding time occasions limited, the same, and repeating every UE FFP or gNB FFP to reduce the complexity. It should be noted though that based on the agreement achieved in the previous meeting, the UE will have to conduct that complex tracking anyway for any configured UL transmission other than the one aligned with the boundary of the UE FFP Agreements (RAN1#103-e): In semi-static channel access mode: When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, down-select one of the following: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. Alt-c: The UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration. When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE: If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT. FFS on other conditions for determining the corresponding UE or gNB initiated COT Note: A configured UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT. -As such, we noted down Alt-a of Proposal 4-1A as our preference due to the fact that it is consistent with already agreed procedures for configured UL starting after UE FFP boundary, it prioritizes gNB COT while coping with the dynamics of whether UE determines that gNB has initiated COT or not and the duration of the configured UL. And finally, it has been receiving majority support in our understanding. -Having said so, if the majority opinion is leaning towards Proposal 4-1A Alt-b, we can be flexible in that regard. |
| IDC | We are for Alt-c. Arguments related to cancelling UL CG are not relevant to this proposal. The purpose of this proposal is to determine how an UL CG is transmitted, not whether it should be transmitted. If there is no gNB-initiated COT it is clear the UL CG can only be transmitted using UE-initiated COT. This shows that Alt-B is the simplest solution given that it works regardless of if there is an ongoing gNB-initiated COT. Though such a solution affects COT sharing and takes away a gNB's scheduling flexibility. If there is a gNB-initiated COT, then Alt-A could suffer from misdetection (i.e. in some cases UE will use a UE-initiated COT assuming there were no gNB-initiated COT, causing confusion). On the other hand, Alt-C can be used to enable the appropriate behavior based on gNB's scheduling needs. |
| Xiaomi | Support both Alt-a and Alt-b. For Alt-c, CATT raised a situation when CG-PUSCH conflicts with DL transmission, but from our opinion, it can be solved by a proper UL/DL configuration. If CG-PUSCH conflicts with DL symbols, it will be dropped. So Alt-c seems unnecessary. |
| Nokia, NSB | We are still supportive of Alt-a |
| LG | We don’t see why Alt-c in Proposal 4-1A would cause large complexity not to be supported. If a UE is configured with a subset of UE FFPs based on the Alt-c, the UE just applies Rel-16 behavior for the configured UL (aligned with UE FFP boundary) within the subset. For the configured UL out of the subset, the UE just assume UE-initiated COT. Note that for a UE FFP not having the configured UL at the boundary, the UE anyhow need to perform Rel-16 behavior for the UE FFP based on detecting of gNB-initiated COT by default. |
| Moderator | @CATT: Thanks for clarifying Alt-c. Now we understand better. It is very much appreciated. However, as commented by Apple, Alt-c is similar as Alt-3 in proposal 2-1. Also comment by Samsung, there are other means to achieve the same goal, even in a more dynamic manner. @ETRI: Your understanding of Alt-b, should be the common understanding. The discussion is about: If a UE transmit, what would be the UE assumption on initiator of the COT? @LG: Sorry for missing your questions. On first one (yellow), I think you should not look at the operation like this. When we establish these rules, let’s say Alt-b, that gives guideline to gNB how allocated resources. Therefore, gNB in case of Alt-b, should ensure a gap of at least 100us such that the UE can transmit. Otherwise, the UE can not initiate a COT. This is not special about Alt-b. It is common for all alternatives. On second one (blue), I don’t understand why the previous agreement could cause issue with regulation. The discussion was that for C-UL#3, we had two choices, COT-initiator based on C-UL#1, or gNB for FFP-g#2. Both of them are valid. But we needed to decide on one. The decision was to prioritize UE initiated first. If that is not the case (which is the case in this example), check whether gNB initiated a COT. With your suggested changes, which is also fine, you prioritize gNB initiated Cot first, then UE. One can debate which is better or which is worse. Personally, I don’t think there a much difference where the current agreement, makes it simpler for UE, in case it initiated a COT before (similar discussion on Alt-a and Alt-b). So, it is not clear to me what the issue is. Basically, we have two choices for design and had to pick one. I hope that clarifies. @LG/IDC: Moderator asked to be more clear on description of Alt-c and asked specific questions. Could you please clarify your description of Alt-c? Is it similar to CATT? @Proponenet of Alt-a: Apple raised the case that Alt-a and Alt-b are similar and asked the proponents of Alt-a if they can clarify what kind of issues Alt-b may cause. On motivation for less complexity and UE support for such an operation, Rel-16 and previous agreement for UL configured grant is referred. Although true, but the question is that in Alt-a, UE first prioritizes to check if gNB initiated a COT, and if not, checks if UE initiated a COT. That is the reverse for configured UL transmission that are not aligned with the boundary (please see discussion with LG on comment blue). @CATT, QC, LG, IDC: Please review the comments above. There are some issues with Alt-c which does not it in this discussion. Could you be OK to remove Alt-c? It seems the same functionality raised by CATT can be as well achieved by different means? Current Status: 4-1A (Alt-a/Alt-b): Apple, Xiaomi 4-1A (Alt-a): Intel, DCM, ZTE, Panasonic, Lenovo/MOT, HW/HiSi, Nokia/NSB, Sharp(1st), Spreatrum(1st) 4-1A (Alt-b): Vivo, Samsung, ETRI Sharp(2nd), Spreadtrum(2nd) 4-1A (Alt-c): QC, CATT, LG, IDC @All: Moderator proposals, based on majority of UE and questions/comments toward Alt-c is to remove Alt-c. Would that be fine specially with CATT, QC, LG? Hopefully, if that is the case, we can focus on Alt-a and Al-b. Please continue discussion and provide answer to above questions. Updated Proposal 4-1A (Moderator suggests to remove Alt-c from this discussion) : In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. [Alt-c: A subset of the UE FFP boundaries are determined by configuration such that if the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission is based on sharing a COT initiated by gNB. Otherwise, it is based on UE the initiated COT. In the absence of configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT. FFS on configuration of the subset] |
| Sony | After reading the comment, it is even more confusing. It isn’t even clear what’s the difference between Alt-a and Alt-b. The way Alt-b is phrased, it seemed to suggest that the UE always assume it is the COT initiator regardless if gNB had already initiated a COT. This suggest that the UE can “steal” the gNB’s COT whenever it wants. Hence: If this is the intended behaviour, then Alt-a is the only sensible choice. If this is not the intended behaviour and that the UE would only initiate a COT if it has determined that it is under the gNB’s COT, then how is this any different to Alt-a? Based on the above, our preference is Alt-a. |
| LG | @FL: Thank you for the comments on the yellow and blue parts. On the yellow part, if I follow your previous explanation, should the gNB always guarantee the gap before the configured UL in case of Alt-b, even though the UE may not always transmit (sometimes may skip) the configured UL? It means, wouldn’t be possible to support the configured UL transmission by UE based on shared-gNB COT without LBT or override DL transmission? We think such restriction would be quite inefficient and inflexible. On the blue part, in the following figure, considering the case where UE initiated COT by C-UL #1 but gNB didn’t detect the UE COT due to channel condition/interference and the gNB initiated COT for FFP-g #2, with current agreement for the C-UL not aligned with UE FFP boundary, there would be misalignment between UE and gNB that the UE would transmit C-UL #3 based on UE COT but the gNB would expect the UE transmits C-UL #3 based on shared-gNB COT. This is the reason why we have reconsidered the agreement. |
| Moderator | In order to check whether there was a convergence by check point 2, Moderator asked the following question, based on the status of the summary before GTW: Question 2: Can you be supportive of removing Alt-c from Proposal 4-1A, i.e. agree to Proposal 4-1A with only Alt-a and Alt-b ? Some companies provided input to the question above, that is listed below. |
| LG | NO. I don’t understand why this is enforced even though the reason of removal is not understood. Again, this is clarification from my side: For the configured UL in the subset, UE behavior is the same as Rel-16. For the configured UL not in the subset, UE assume UE-initiated COT. Note that Rel-16 UE behavior, anyhow, is necessary as default at least for the configured UL in the UE FFP not having the configured UL aligned with boundary. LG confirmed the following understanding is correct when asked by Moderator: for the configured UL in the sub-set, following Rel-16, if UE does not detect gNB initiated COT, the UE does not transmit. for the configured UL in the sub-set, UE transmit assuming UE-initiated COT. |
| Intel | Yes – Our preference is Alt-a, and we believe that Alt-c would be rather a over-optimized solution for a corner case. For proposal 4-1A, we are OK to remove Alt-c. We though this could be a compromised solution, but it is becoming very controversial and complex. As already mentioned, we prefer Alt-a, which would need to be broadly used by the UE when operating in FBE mode (both initiating or responding device), and its extension to the case when the CG resources are aligned with a u-FFP could be considered rather a trivial extension to a corner case. |
| vivo | Support. RRC configured way may delay UE’s configured UL Tx at some FFP boundary if gNB has nothing to transmit or gNB does not get the channel; |
| CATT | No, 1. In our understanding, if the configured UL transmission is aligned with an FFP boundary, basic rule is UE can initialize COT for this configured UL transmission. But sometimes, this will potential affect gNB-initiated COT due to LBT failure when the UE is allowed to transmit during the idle period of any FFP associated with the serving gNB as shown in below figure. It leads to that gNB can’t schedule other UE/ transmit broadcast signalling. So we need gNB configuration/ control for UE-initiated in order to reduce the interference on gNB-initiated COT from UE-initiated COT and the conflict among UE-initiated COT among UEs. 2. We aren’t sure whether NW can completely resolve this issue by SFI/dynamic scheduling and this will introduce unnecessary gNB scheduling overhead and complexity. Even though Alt-3 in Proposal 2-1 is accepted, if gNB semi-statically configures that UE is allowed to transmit during the idle period of gNB-initiated COT by RRC, interference issue from UE-initiated COT to gNB-initiated COT still happens. |
| Apple | Yes. We do not exactly understand the motivation/use cases for Alt-c. I don’t seem to see a clear explanation from LG. For the use case that CATT explains, isn’t this exactly Alt-3 in Proposal 2-1 addresses? That is, if gNB configures that UE does not transmit in gNB FFP’s idle period, the issue is avoided. |
| Xiaomi | Yes |
| Nokia/NSB | Yes |
| Moderator | @All: Based on the feedback on Question 1 above, it is clear that there is no convergence to remove Alt-c. Instead, based on carination of LG/CATT, Alt-c is updated as the following. @LG, CATT: Please review if the update captures your proposal properly. @CATT: I used your update as well. But ti my it does not match the description. It seemed to me, that you have another condition in mind to cancel UL transmission in case it overlaps with gNB FFP idle period (looking forward not backward). Please make necessary changes if needed. ========================================= @All: Feel free to continue discussion, especially if it helps progress and clarifications. Current Status: 4-1A (Alt-a/Alt-b): Apple, Xiaomi 4-1A (Alt-a): Intel, DCM, ZTE, Panasonic, Lenovo/MOT, HW/HiSi, Nokia/NSB, Sharp(1st), Spreatrum(1st) 4-1A (Alt-b): Vivo, Samsung, ETRI Sharp(2nd), Spreadtrum(2nd) 4-1A (Alt-c): QC, CATT, LG, IDC Updated Proposal 4-1A: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. Alt-c: A subset of the UE FFP boundaries are determined by configuration such that following applies: If the configured UL transmission is aligned with an FFP boundary in the subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT If the configured UL transmission is aligned with an FFP boundary that is not in the subset, the UE assumes that the configured UL transmission is allowed based on gNB-initiated COT, that is if the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, the UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, the UE does not transmit the configured UL transmission. In the absence of configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT. FFS on configuration mechanism of the subset |
| Sony | Just to note we support Alt-a. We also support the updated Proposal 4-1A (i.e. with all 3 alternatives still on the table) |
| Huawei, HiSilicon | Our preference is still Alt-a First, We do not think that Updated Proposal 4-1A properly captures the intended behaviour as explained by the proponent above and quoted herein: “For the configured UL in the subset, UE behavior is the same as Rel-16. For the configured UL not in the subset, UE assume UE-initiated COT.” Second, in response to LG’s comments on the reflector on the agreed behaviour for configured UL after the UE FFP boundary being contradictory to Alt-a and prioritizes UE COT, we would like to clarify that order of conditions has to be checking UE initiated COT first , then gNB initiated COT. This due to the very fact that this configured UL transmission is after the UE FFP boundary, which means that the UE has to continue transmitting based on the same FFP if the UE has initiated the COT, or else transmit as responding device in the gNB COT if initiated. Third, LG has raised the case when UE does not determine that gNB initiated a COT in Alt-a. And also, in Alt-3 as described by LG, for the configured UL in the sub-set following Rel-16, if the UE does not detect gNB initiated COT, the UE does not transmit. It should be noted that not only would that first UL transmission aligned with the UE FFP boundary be disallowed, but also any subsequent UL transmission within that UE FFP or within the undetermined gNB FFP would be disallowed. This is because from the UE’s perspective, neither the gNB has initiated its COT nor the UE was allowed to initiate its COT. As we mentioned earlier, we do not think such pre-determined RRC configuration can cope with the dynamics of DL and UL transmissions. |
| Intel | First of all, if the intention is to down-select among the alternatives we are supportive of Alt-a. For the cons of each individual alternatives: Alt-b would prevent a UE from operating within a gNB’s FFP in case this would have already acquired the FFP and the CG resources would fall within it. In this case, the UE would be forced to perform an additional LBT, and the gNB would be also forced to leave a sufficient gap in order not to block the UE. We feel that this is really unnecessary and would add overhead and loss in spectral efficiency. Alt-c would be a very complex solution, introduced to rather over-optimize a corner case. If the motivation is to agree to this proposal as whole, we do not understand the meaning of making such agreement given that we have already made a similar agreement before. |
| Apple | We are fine with the updated proposal. But so far we are still not clear about the motivation/use case of Alt-c. If it is about the gNB FFP’s idle period, Alt-c in Proposal 2-1 with a single RRC parameter would be able to handle it already. If it is about something else, we would like to understand more so that it can be taken into account in the future discussion. |
| ZTE | We share the same view as Intel that there is no need to agree all the alternative again. If down-selection is intended we support Alt-a for the same reason mentioned before. |
| CATT | We prefer Alt-c and we would like to modify description of Alt-c based on agreed alt-c in the last meeting as follows: Alt-c: A subset of the UE FFP boundaries are determined by configuration the UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration such that following applies: If the configured UL transmission is aligned with an FFP boundary in the subset and UE is allowed to initialize COT based on gNB configuration, the UE assumes that the configured UL transmission corresponds to UE-initiated COT If the configured UL transmission is aligned with an FFP boundary and UE isn’t allowed to initialize COT based on gNB configuration that is not in the subset, the UE assumes that the configured UL transmission is allowed based on gNB-initiated COT, that is if the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, the UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, the UE does not transmit the configured UL transmission. In the absence of gNB configuration configured subset, the UE assumes that the configured UL transmission corresponds to UE-initiated COT. FFS on gNB configuration mechanism of the subset |
| vivo | We support Alt.b if down-selection. Alt.a adding more UE complexity and causing UE power consumption, it requires UE always to first determine whether gNB occupies the channel or not, but in case the CG configuration is aligned with UE’s FFP boundary, UE does not need to do that. Based on last meeting conclusion, the collision and blocking is under gNB’s control. |
| Panasonic | We are OK with the updated proposal. If down-selection is intended, we support Alt.a. |
| Samsung | We still support Alt-b, if down-selection. For Alt-a, as explained by other companies, there would be miss-understanding on whether gNB has initiated a COT and more power consumption at UE side to check gNB transmission. For the updated Alt-c, it seems more complicated without clear benefit. |
| LG | @FL: Firstly, I’m not sure if you already checked my previous reply on the above yellow and blue parts. Secondly, thank you for the update on Alt-c. But, it seems to be seen a bit complicated due to unnecessarily long explanation, thus I modified as below (seems similar with CATT’s modification). Alt-c: the UE assumption on whether the transmission is allowed to correspond to UE-initiated COT is based on gNB configuration such that following applies: If the transmission is within the UE FFP which is configured to allow UE-initiated COT by gNB, the UE assumes that the transmission corresponds to UE-initiated COT. If the transmission is within the UE FFP which is configured not to allow UE-initiated COT by gNB, the UE assumes that transmission is allowed based on gNB-initiated COT, that is: - If the transmission is confined within a gNB FFP before the idle period of that gNB FFP and the UE has already determined that gNB initiated that gNB FFP, the UE assumes that the transmission corresponds to gNB-initiated COT. - Otherwise, the UE does not preform the transmission. FFS on details of the gNB configuration @Apple: Thank you for asking the motivation of Alt-c. The Alt-c is motivated with at least two aspects: 1) for distribution of UEs initiating COT over multiple UE FFPs to avoid UE congestion on a same UE FFP, 2) for ensuring FFP period dedicated to gNB to avoid potential interference with UEs initiating COT. With Alt-c, gNB could control flexibly/adaptively various NW situations by proper configure each UE FFP either to allow or not to allow UE-initiated COT. @Intel: @Samsung Regarding your concern on the complexity of Alt-c, I would share the same observation with vivo and my thinking is quite different from yours. With Alt-c, whether UE FFP corresponds to UE-initiated COT or gNB-initiated COT is semi-statically determined based on RRC configuration. On the other hand, in case of Alt-a, whether UE FFP corresponds to UE-initiated COT or gNB-initiated COT would be dynamically determined, so for UE, it is required to detect DL signal for each UE FFP. Therefore, with this observation, I think the complexity involved with each of three alternatives would be Alt-a > Alt-c => Al-b. @HW: Regarding your concern on applying Rel-16 behaviour so that UE couldn’t transmit without gNB COT, with Alt-c, it would be up to gNB configuration. If gNB think a UE FFP would be essentially used for UL transmission from the UE, then the gNB can configure the UE FFP to allow UE-initiated COT. @ALL: I’d like to share my observations so far on each alternative below: Alt-a: it would require increased UE complexity. Alt-b: it would restrict gNB operation flexibility. Alt-c: hard to consensus on RRC configuration. According to these observations and considering current difficult situation, I would suggest a middle-ground proposal as below as a compromise. Alt-d: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, and the gap between the DL signal based on the gNB FFP detected by the UE and the transmission is less than the gap required for LBT to initiate COT, the UE assumes that the transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the transmission corresponds to UE-initiated COT. |
| Nokia, NSB | We still support Alt-a |
| Qualcomm | We support Alt-b, if down-selection. Previously, we prefer Alt-c. But the current Alt-c is not the same as we think. To move forward, we can make the change. |
| InterDigital | For the sake of progress, we are OK with removing Alt-c. We now support Alt-a. |
| ETRI | We support Alt-b. Alt-b may provide better flexibility than Alt-a if we introduce UE’s COT initiation control signalling (as an outcome of issue 2.5 later). Based on Alt-b, the configured UL can correspond to either UE COT (if gNB allows the UE COT initiation) or gNB COT (if gNB indicates cancelling the UE COT initiation). However, if we take Alt-a, the configured UL should only correspond to gNB COT if confined. Regarding Alt-c (the last version from LG), in our understanding, it is equivalent to (Alt-b + agreeing UE’s COT initiation control signalling). We think UE’s COT initiation control can be separately discussed in discussion point 2.5. |
| Moderator | ========================================= @All: Please see the updated view above. Summary of views, listed above. No consensus yet. Based on companies input and better understanding the proposals, to keep the problems and solutions relevant: With respect to compromised Alt-d suggested by LG, one way is to add instead FFS1 as sub-bullet of Alt-a. FFS1: Whether the following condition should be additionally met when the UE determines the gNB is initiated COT in that gNB FFP: The UE detects a DL signal in that gNB FFP where the gap between the DL signal and the configured UL transmission is less than 100us. With respect to Alt-c, one way is to add instead FFS2 as sub-bullet of Alt-b. FFS2: Whether based on gNB configuration the UE is allowed to assume UE-initiated COT for the configured UL transmission. Note in this case, if the UE is not allowed to make the above assumption by configuration, UE follows Rel-16 behaviour. I will not add FFS1 and FFS2 instead of Alt-c unless this approach is supported by all, or there is no objection. Current Status: 4-1A (Alt-a/Alt-b): Apple, Xiaomi 4-1A (Alt-a): Intel, DCM, ZTE, Panasonic, Lenovo/MOT, HW/HiSi, Nokia/NSB, Sharp(1st), Spreatrum(1st), Sony, IDC, Futurewei 4-1A (Alt-b): Vivo, Samsung, ETRI, Ericsson, QC Sharp(2nd), Spreadtrum(2nd) 4-1A (Alt-c): QC, CATT, LG, IDC Updated Proposal 4-1A: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. Alt-c: the UE assumption on whether the transmission is allowed to correspond to UE-initiated COT is based on gNB configuration such that following applies: If the transmission is within the UE FFP which is configured to allow UE-initiated COT by gNB, the UE assumes that the transmission corresponds to UE-initiated COT. If the transmission is within the UE FFP which is configured not to allow UE-initiated COT by gNB, the UE assumes that transmission is allowed based on gNB-initiated COT, that is: - If the transmission is confined within a gNB FFP before the idle period of that gNB FFP and the UE has already determined that gNB initiated that gNB FFP, the UE assumes that the transmission corresponds to gNB-initiated COT. - Otherwise, the UE does not preform the transmission. FFS on details of the gNB configuration |
| Moderator | The following was agreed in GTW, Feb. 4th: Agreement: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a configured UL transmission that is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT. |

### Scheduled UL transmissions

Agreements (RAN1#103-e):

In semi-static channel access mode, a UE should be able to determine whether a scheduled UL transmission should be transmitted according to shared gNB COT or UE-initiated COT.

- UE determines the initiator of a COT based on at least one of the following alternatives:

  - Alt 1: Introduce additional bit field in the scheduling DCI

  - Alt 2: Based on ChannelAccess-CPext field in DCI

  - Alt. 3: Based on a predetermined rule(s)

  - Alt. 4: Based on RRC signalling

  - Alt. 5: Based on MAC CE

  - FFS other alternatives

- FFS on overriding possibility and/or the assumption

- Note: A scheduled UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT.

Summary of companies view for above agreement:

- Based on pre-determined rule (Alt-3):

  - HW, ZTE, Apple, vivo, DCM, NEC, Charter

- Based on content of scheduling DCI. (Alt-1/Alt-2):

  - Intel, ETRI, E///, QC, Samsung, Nokia, Sony, CATT, Spreadtrum, WILUS, OPPO, Sharp, FW (+ Alt4 or Alt5)

  - Alt2: E///, QC, Samsung, Nokia, OPPO, Sharp

  - If DCI field not provided, fallback to Alt-3: E///, ETRI

- Other alternative: Based on DMRS cyclic shift

  - MTK

| Question: Can you please correct/adjust/update, if needed? Can you please provide your view? |
| --- |
| Company | Comment |
| vivo | Out predetermined rule for Alt-3 is: If the scheduled UL transmission is aligned with the UE FFP boundary, UE initiates the COT. |
| Futurewei | We prefer Alt-1/Alt-2, we could leave with Alt 4 as well. |
| Intel | We prefer Alt-2, with the understanding that indication should not be limited to ChannelAccess-CPext, but should be extended to both fall-back and non-fall-back DCIs. Since how to indicate the channel access type and CP extension for FBE is still unresolved and under discussion in Rel.16, we would prefer to resume this discussion and make any conclusion only after RAN1 would make a conclusive agreement for the gNB’s initiated device first. |
| CATT | We prefer Alt-1/Alt.2. |
| LG | Alt-3 is slightly preferred. However, it may need to clarify first on the EDT used to perform LBT for UE-initiated COT before deciding the method for UE’s determination of the scheduled UL transmission (e.g. whether it is done based on shared-gNB COT or UE-initiated COT). |
| Panasonic | We prefer Alt.1 or Alt.2 with fallback to Alt.3. |
| ZTE | We think the predetermined rule that has been agreed is flexible enough, i.e. the UE initiate a COT if the scheduled UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP, otherwise share the gNB’s COT. We fail to see alt.1 or alt.2 can provide more flexibility, and meanwhile there will be some problem for cross-FFP scheduling. If a common design between CG and grant-based transmission is desirable, then the predetermined rule similar as Alt-a for CG can be adopted. |
| Nokia, NSB | Alt. 2 or Alt .1. It is good to also take into account the ongoing Rel-16 discussion on ChannelAccess-CPext field for FBE. In addition, some predetermined rules may be defined for the overriding case e.g. with cross-FFP scheduling. |
| Sharp | Our preference is Alt 2. To our understanding, one of general design targets is to let gNB control. For the scheduled UL transmission case, by using the scheduling DCI format and even more reusing the ChannelAccess-CPext field, the gNB can reliably control both the COT association and UL transmission. |
| ETRI | We prefer Alt-1/Alt-2 with fallback to Alt-3. |
| Qualcomm | Alt-2 or Alt-1. They are more flexible than the other schemes. |
| OPPO | Alt-2 |
| InterDigital | Alt-1 or Alt-2 |
| DOCOMO | We prefer Alt 3 and same rule can be used as configured UL |
| Lenovo/Motorola Mobility | Alt-3; if the scheduled transmission is within an acquired gNB-FFP, it is transmitted according to shared gNB COT, otherwise similar rules as for CG transmission are applicable. |
| Samsung | Alt 2. ChannelAccess-CPext field is already there, in fallback DCI and normal DCI. Because the LBT type is different for initiating UE COT or using gNB’s COT, it is natural to use LBT indication to dynamically disable/enable UE COT for flexibility without any additional cost. |
| Spreadtrum | Alt-1 or Alt-2 |
| Apple | We think it is good to separate two cases depending on whether the PUSCH falls into the same gNB’s FFP as the scheduling DCI. If yes, it is good to use ChannelAccess-CPext field to indicate because it allows the possibility of no LBT. If it is in another FFP, we think it is reasonable to follow the same/similar behavior as configured UL transmission |
| WILUS | Alt-2 or Alt-1 to provide more flexibility. |
| Xiaomi | Alt 3 is slightly preferred. |
| HW/HiSi | Our view is already captured, i.e. Alt3 Since the gNB dynamically controls the timing of the scheduled UL transmission, it can simply choose whether or not to fulfil the main requirement for the UE-initiated COT which is aligning the start of the UL transmission with the beginning of the UE FFP as per the agreement below from RAN1#102-e. Agreements: A UE initiates a COT in an FFP associated with the UE, if the UE transmits a UL transmission burst starting at the beginning of the FFP and ending at any symbol before the FFP’s idle period after a successful CCA of 9us immediately before the UL transmission burst. Given that the timing of the scheduled UL transmission is already involved in the determination of the COT initiator, we do not see the need to introduce a new field in the scheduling DCI and increasing the dynamic overhead as in Alt. 1. In fact, we observe that applying the aforementioned rule in Alt. 3 would be more general and already covering Alt. 2 that is based on the ChannelAccess-CPext field in the scheduling DCI. Therefore, we propose to support Alt. 3 for scheduled UL transmissions. |
| Moderator | Status: Alt-3: vivo, LG, ZTE, DCM, Lenonvo/MOT Alt-1/Alt-2: FW, CATT, Pana&ETRI(fallback to Alt 3), Nokia/NSB, QC, Spreadtrum, WILUS, Sony Alt-2: Intel, OPPO, Samsung, E///(fallback to alt3), Apple( for same COT, other COT Alt 3) @All: It seems the approach by Panasonic, ETRI is the most complete. If DCI based option is not viable e.g. when the corresponding fields are not provided, a default behavior is needed. And that would be nothing but fallback to Alt-3. In other words, if NW does not provide any signaling, pre-determined rule determines the behavior. However, by DCI signaling, the NW can have some flexibility. @All: More discussion is needed. Could companies provided they view on the following option as well: Possible solution: DCI based (Alt-1/Alt-2), and fallback to Alt 3 ? |
| CATT | We prefer Alt-1/Alt-2 and for the sake of the progress, we also consider that Alt-1/Alt-2+Al-3 |
| Samsung | Although it would be the corner case that gNB does not configure a bit field for LBT indication, we’re fine to support Alt-2 + Alt-3 in case of no bit field for LBT in non-fallback DCI as a complete solution. |
| Sharp | We are fine with the proposed solution (DCI based when DCI indication is available; fallback to Alt 3 when DCI indication is not available) |
| Qualcomm | Alt-1/Alt-2. |
| Futurewei | Alt-1/Alt-2 , adding rules for fallback just add complexity, unnecessary in our opinion |
| vivo | Prefer Alt-3. As we explained in 2.3.1, UE-initiated COT should be enabled by default. Then other signaling can be used to disable this functionality if necessary. There is no need to enable this functionality by signaling. |
| DOCOMO | We still prefer Alt-3, but can live with possible solution: DCI based (Alt-1/Alt-2), and fallback to Alt 3, for the sake of progress. |
| Sony | Our preference was Alt-1 or Alt-2, which was somehow not captured in the Moderator’s comment above and so I have added it (see track changes in Moderator’s comment). For Alt-3 it would be good to know what the pre-determined rule is. |
| ETRI | We are fine with the Moderator’s proposal. |
| ZTE | Alt.3 as it is flexible enough. We still fail to see what additional flexibility can be provided by Alt.1/2 compared to the existing agreement. Maybe the proponents of Alt.1/2 can elaborate more? |
| Intel | We prefer Alt-2, with the understanding that indication should not be limited to ChannelAccess-CPext, but should be extended to both fall-back and non-fall-back DCIs. However, we would prefer to resume this discussion and make any conclusion only after RAN1 would make a conclusive agreement for the gNB’s initiated device first. |
| InterDigital | We support Alt-1/Alt-2 with fallback to Alt.3 |
| Apple | One issue here is that Alt 3 is not really defined. Another thing that is not clear to me is if we support Alt-1 or Alt-2, my assumption is that the indication is always present. Then in what cases do we need fallback? Or the intention is that there is one state indicated in the DCI that corresponds to certain predefined behavior (Alt-3)? |
| Moderator | @Apple: Alt-3 is not defined, but will be a semi-static rule. For Alt-17Alt-2, if the corresponding field in DCI s not configured, a fallback is needed. Companies’ view: Alt-1: Alt-2: Intel, OPPO, Samsung, Apple? Alt1/Alt2: CATT, QC, FW, Sony, Intel(2nd), IDC, Nokia/NSB, Spreadtrum, WILUS Alt 3: vivo, DCM, ZTE, LG, Lenovo/MOT Alt1/Alt2 and fallback to Alt3: CATT(2nd), Samsung(2nd), sharp, ETRI, IDC, E///, Panasonic, ETRI |
| Moderator | Clarifications/comments: Question raised on description of pre-determined rules in Alt3 Moderator understanding is that the rules are the ones applied for UL configured transmission discussed in previous section. Question raised with respect to the need for fallback in Alt1/Alt2 and description on fallback Moderator understanding is that Alt1/Alt2 depends on DCI content (field, etc). If the corresponding fields that convey the information, are not configured, then DCI based approach is not applicable. In that case a fallback solution is needed. It seems the obvious choice for fallback is to reuse the predetermined rules for UL configured grant and apply in this case. On the comment by some companies that we don’t see the need for fallback, moderator explanation is none of these fields can be mandated to be present in DCI. They would be optional. Hence, to complete the design determining, the fallback behavior should be considered too. Alt1/Alt2 with or without fallback on Alt3, or Alt 3 are preferred by companies. @All: Please see the updated proposal based on the clarification above and whether it is acceptable. Only Alt1/Alt2 and Alt3 are keep. Alt1/Alt2 are categorized as DCI based where the details are left for further discussion. Alt-3, as well as the fallback for Alt1/Alt2 is described as the rule for UL configured grant. The decision for UL configured grant would be applicable here. Proposal 4-2: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a scheduled UL transmission is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: Determination based on the content in the scheduling DCI FFS on whether the corresponding field(s) can be absent in DCI If absent, determination based on the rules applied for configured UL transmissions is applied (Alt-b) Alt-b: Determination based on the rules applied for a configured UL transmission |
| CATT | We are fine with proposal 4-2 |
| LG | We prefer Alt-b to pursue a common rule both for scheduled UL and configured UL with consideration of UE implementation/complexity. |
| vivo | We are fine with the proposal 4-2 and we support Alt-b. |
| Qualcomm | We prefer Alt-a in Proposal 4-2. |
| Samsung | We are fine with the proposal 4-2 and we support Alt-a. |
| DOCOMO | We are fine with the proposal and prefer Alt-b. |
| Panasonic | We are fine with Proposal 4-2. |
| ETRI | We are fine with Proposal 4-2. We prefer Alt-a and are also okay with Alt-b (2nd preference). |
| Sony | We are fine with Proposal 4-2. We prefer Alt-a of Proposal 4-2. |
| TCL | We are fine with proposal 4-2. |
| Intel | We are fine with proposal 4-2. However, if the intention is to select one alternative by this meeting our preference is for Alt-a. |
| Apple | The main benefit of Alt-a compared to Alt-b in our view is that it allows the gNB to signal “no LBT” to the UE (when the gap is controlled well), while the UE would always need to perform LBT if it initiates its own COT. But for Alt-a, we would like to understand how it would work if the scheduled UL transmission is not in the same COT as the scheduling DCI. In this case, the gNB cannot predict whether it can acquire COT in the next FFP. In our view, it is natural to also follow the same scheme as configured UL transmission in this case. |
| InterDigital | We are fine with Proposal 4-2. We prefer Alt-a of Proposal 4-2. |
| Huawei, HiSilicon | We are fine with Proposal 4-2. For further selection between alternatives, we prefer Alt-b This is due to the fact that start of the scheduled UL is a deciding factor in the rule of Alt-b, and therefore, Alt-b inherently covers the effect of a DCI field(s), if present. |
| ZTE | We are fine with proposal 4-2 and prefer Alt-b, for the same reason as mentioned by Huawei. We do not think alt-a can provide more flexibility. |
| Moderator | @Apple: With Alt-a, the full responsibility is on gNB. The UE does not have to bother about the gap or either determining depending the scheduled transmission is at FFP boundary or not, which node has initiated a COT. On the question of scheduled UL is not in the same COT, the moderator view it is gNB’s responsibility to be compliant with regulations in the sense that if whatever gNB signals, even in advance, gNB has to guarantee that it fulfills the regulation. However, if more discussion is needed, it can be taken separately, in conjunction to next FFP scheduling. Current status: Proposal 4-2 is stable and supported by all companies so far. |
| Sharp | We are also fine the Proposal 4-2. Our preference is Alt-a. |
| Apple | On the case where the gNB schedules UL transmission in the next FFP, we would like to add an FFS point for now, as suggested below. From gNB perspective, it can only indicate the UE to initiate its own COT, because it cannot predict whether it can acquire the channel in the next FFP. It should not be a problem if we adopt Alt-b in Proposal 4-1A because the design is consistent. However, if we adopt Alt-a in Proposal 4-1A, the question is whether we want the UE to always initiate its own COT in this case. We think it is better for UE to have consistent behavior. Therefore, we would like to add the FFS and we can revisit after we make decision for Proposal 4-1A. Proposal 4-2: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a scheduled UL transmission is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: Determination based on the content in the scheduling DCI FFS on whether the corresponding field(s) can be absent in DCI If absent, determination based on the rules applied for configured UL transmissions is applied (Alt-b) FFS how to handle the case when the gNB schedules an UL transmission in the next FFP period Alt-b: Determination based on the rules applied for a configured UL transmission |
| CATT | We are fine with proposal 4-2 and we support Alt-a. |
| Xiaomi | OK with Proposal 4-2. |
| Intel | We support the proposal. |
| LG | First of all, we are also fine with Proposal 4-2 itself. Between two alternatives, our preference is still Alt-b to pursue a common rule both for scheduled UL and configured UL with consideration of UE implementation/complexity. |
| Spreadtrum | Support the proposal |
| Samsung | Support the proposal |
| ETRI | Support the proposal |
| DCM | We are fine with Proposal 4-2 and prefer Alt-b |
| ZTE | We are fine with Proposal 4-2 and prefer Alt-b. |
| Panasonic | Support the proposal |
| vivo | Support the proposal |
| Lenovo/MOT | Ok (after the update to clarify “based on the rules applied for a configured UL transmission” as requested in an earlier email) |
| Qualcomm | We are fine with Proposal 4-2 and prefer Alt-a |
| Xiaomi | OK with Proposal 4-2. |
| Nokia, NSB | We are ok with Proposal 4-2 |
| Sony | We are fine with Proposal 4-2 and we support Alt-a |
| IDC | We agree with proposal 4-2 |
| Moderator | @Lenovo/MOT: The Alt-b is Alt-a is removed now. The reason was to highlight that the fallback would be same behavior as for UL configured grant. The current proposal should be clear now because the pre-determined rules are what we have agreed and will agree upon outcome of Proposal 4-1A. @All: New FFS is added by Apple. In moderator’s view that can be discussed under section 2.6.3. However, it is fine to be added here as a reminder to address this issue while investigating Alt-a. I hope it is still fine with you. Current status: Stable and Supported by all companies Moderator: Given that companies are fine with new FFS proposed by Apple. In case of concern, FL suggests removing FFS since it is covered in the context of topics in section 2.6.3. Proposal 4-2: In semi-static channel access mode when a UE can operate as UE-initiated COT, Select one of the following alternatives to determine whether a scheduled UL transmission is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: Determination based on the content in the scheduling DCI FFS on whether the corresponding field(s) can be absent in DCI If absent, determination based on the rules applied for configured UL transmissions is applied (Alt-b) FFS how to handle the case when the gNB schedules an UL transmission in the next FFP period Alt-b: Determination based on the rules applied for a configured UL transmission |
| Moderator | The following was agreed (Proposal 1B) in GTW, Feb 2nd: Agreement: In semi-static channel access mode when a UE can operate as initiating device, Select one of the following alternatives to determine whether a scheduled UL transmission is based on UE-initiated COT or sharing a gNB-initiated COT: Alt-a: Determination based on the content in the scheduling DCI FFS on whether the corresponding field(s) can be absent in DCI If absent, determination based on the rules applied for configured UL transmissions is applied FFS whether/how to handle the case when the gNB schedules an UL transmission in the next gNB’s FFP period Alt-b: Determination based on the rules applied for a configured UL transmission |

## Discussion topic: COT-initiation control/cancelation/overriding

The proposals 5-1 and 5-2 below, aim to capture the views with respect to the discussion topic, on high level.

Other proposals address additional details.

Please if needed, prioritize the discussion of Main design issues.

### Main design issues

Proposal 5-1: A UE can be dynamically signalled to cancel/override the assumption on the initiator of a COT with respect to one or more FFP boundaries of the corresponding FFP configuration.

- FFS details

- E///, OPPO, LG, HW/HiSi

Proposal 5-2: Support at least one of the following alternatives to dynamically cancel/override the assumption on the initiator of a COT

- Alt-1: group common ecessary using DCI format 2_0 can be used for COT-initiation cancelation/overriding purposes

  - E///, OPPO, LG

- Alt-2: Scheduling DCI can be used for COT-initiation cancelation/overriding purposes

  - E///

- Alt-3: the UE should be provided with a parameter to limit its COT to an indicated duration such that it ends before the idle period/CCA of a subsequent frame for another UE in the same channel.

  - HW/HiSi

- FFS other alternatives

| Question 1: What is your view on Proposals 5-1? Question 2: In case, you are supportive of Proposal 5-1, what is your view on Proposal 5-2? |
| --- |
| Company | Comment |
| Sony | Proposal 5-1: Is the cancelling/overidding FFP the currently UE initiated COT or is this to stop UE from initiating future FFP? If it is for future FFP, how is this different to Proposal 6-3 below? Proposal 5-2: If this is regarding cancelling/overriding a UE initiated COT, then we prefer Alt-2 since this can be used to control individual UE. Alt-1 prevents all Ues from initiating the COT which seemed like a sledgehammer way of doing things. Besides Alt-1 should already be supported in Rel-16. |
| Futurewei | Agree with Proposal 5-1; For Proposal 5-2 we think that they are not mutually exclusive. Both Alt-2 and Alt-3 should be supported. They can serve different purposes. One is to cancel the COT initiation and the other (in our understanding) to limit the COT duration. |
| Intel | We would like to ask the proponent companies of these proposals to please clarify their technical reason. Why would a gNB need to cancel or override a COT initiator? In our understanding this is counter-productive from a system level performance, since an initiating device would be basically asked to give up the COT that it has acquired, and this would clearly lead to additional LBT overhead. We would like to remind that even if a device is an initiating device, it could always allow other devices to transmit by simply sharing its COT. So we are really unclear why we need any additional signaling and spec impact, when the COT sharing procedure could be used instead. |
| CATT | We need check the motivation& reason of COT cancellation mechanism |
| LG | We share the same view with Futurewei that the alternatives under Proposal 5-2 are not mutually exclusive. In this context, we are supportive with Proposal 5-1 and all of Alt-1/2/3 under Proposal 5-2 to provide dynamic/adaptive controllability for gNB. |
| Nokia, NSB | We are not supportive of introducing any new dynamic cancellation mechanism. With respect to the need for canceling/overriding UE-initiated COT transmissions, operation with semi-static channel access (FBE) is not any different from operation with dynamic channel access (LBE) and there is no need to introduce additional cancelation mechanisms as compared to what already supported in R16. |
| Sharp | We are open to discussions on Proposal 5-1 and Proposal 5-2. |
| Qualcomm | Need more discussion to clarify the proposals. We are in general supportive to enable a behavior that UE contends for the UE FFP if gNB failed to or didn’t attempt to start a COT at the gNB FFP boundary. Wonder if this case is covered by the proposals. |
| OPPO | We support proposal 5-1 and 5-2. For the motivation, one example is that the gNB would like to inform the UE to change the COT from UE initiated COT to gNB’s COT. |
| InterDigital | We agree with Proposal 5-1. For Proposal 5-2 we agree with Alt-1/2 |
| DOCOMO | We don’t support either proposal. We think current specification is enough to enable/disable COT initiation. For dynamically scheduled UL, DL/UL grant can be used (not) to schedule the UL at the beginning of next COT explicitly, and hence, no additional signaling is necessary. For configured UL, assuming semi-static flexible symbols are configured for the UL corresponding to the beginning of next FFP and SFI is configured for the UE in shared spectrum, the configuration of EnableConfiguredUL can enable/disable the COT initiation semi-statically. If gNB wants to dynamically change the UE behavior of enabling/disenabling COT initiation by configured UL such as CG-PUSCH, scheduling a DG-PUSCH overlapping with the CG-PUSCH is enough as DG-PUSCH can override CG-PUSCH. |
| Lenovo/Motorola Mobility | In our view, proposal 5-1 is not needed, we can directly discuss proposal 5-2. We prefer Alt-1. |
| Samsung | It is unclear what the benefit of proposal 5 is. We already have mechanism discussed in 2.4 and existing mechanism, e.g. SFI indicating flexible symbol to cancel high-layer configured transmission. Why do we need additional signaling? |
| WILUS | We are not supportive with the Proposal 5-1 to introduce a new dynamic cancellation mechanism. |
| HW/HiSi | We do not see a need for Proposal 5-1. UL cancellation should be applied as in Rel-16. If the gNB cancels UL transmission(s) on the resources at the beginning of a UE FFP, the behavior is already defined by the earlier agreements that only sharing gNB is possible for any subsequent UL within that UE FFP. Our proposal listed as Alt-3 has not been captured under the right discussion point. In fact, our proposal is not related to COT initiation or dynamic cancellation or overriding of its assumption. Our proposal is rather related to controlling UE COT duration for collision avoidance between UEs by gNB configuration as shown in the following figure: Figure 3. gNB controls collisions/blocking between URLLC UEs configured with different FFP parameters without interrupting the operation of URLLC UE1 through providing a COT duration parameter . We further noted that the existing mechanism for UL cancellation cannot be applied since it is cell-specific group common signaling and would result in cancelling the UL resources to be used in the subsequent frame for another UE. |
| Apple | It is not clear to us why such overriding mechanism is needed. Would like to understand better the use cases. |

### Other design issues

Proposal 1: If COT cancellation is supported

- A time duration t is to be introduced to process the cancellation signal and cancel the ongoing transmission

- The UE should be configured semi-statically about the time instants when it should cancel an ongoing UE-initiated COT.

- Cancellation should be defined as a UE capability. The UE signals its support of the cancellation of an ongoing UE-initiated COT.

  - MTK

Proposal 2: gNB may send a PDCCH to cancel a low priority UE’s transmission and release the corresponding UE initiated COT in order to support high priority URLLC transmission of another UE.

- Once a UE initiated COT is released by gNB, the UE may not initiate another COT for the same transmission/service until gNB reschedules its UL transmission.

- NEC

Proposal 3: The COT of the gNB can block the UE initiated COT, but the COT of the UE shall not block the gNB initiated COT.

- ZTE

| Question: What is your view on Proposals 1 to 3? |
| --- |
| Company | Comment |
| Sony | We support the cancellation time of Proposal 1. We support Proposal 2 but this should not be restricted to only low priority UE since L1 priority is used of intra-UE prioritization rather than inter-UE prioritization. Also, the gNB can take over as the COT initiator after canelling UE initiated COT so that gNB can schedule other Ues. |
| Futurewei | Support cancellation. The details should be FFS. For Proposal 1 we support the first bullet. We do not support the second bullet. We are OK with third bullet. For Proposal 2, we think that the text “low priority”, “high priority” should be removed. It should be left to gNB to decide which transmission is canceled. With this text amendment we support Proposal 2. If we accept Proposal 1 and 2, Proposal 3 is not necessary |
| Intel | Please see our comments to topic 2.5.1. |
| CATT | We need check the motivation& reason of COT cancellation. |
| LG | It seems there are some duplications. Proposals 1 and 2 seem to be some details related to the above Issue 2.5.1. Proposal 3 seems to be some principle related to the above Issue 2.2.1. |
| Nokia, NSB | Proposal 1 and 2 are related to dynamic cancelation of UE-initiated COT transmission. See our reply in section 2.5.1. We are ok with Proposal 3 as this is basically proposing to introduce additional constraints on UE-initiated transmissions during gNB idle period (see proposal 2-1). |
| Qualcomm | Support proposal 1. For proposal 2, is it already supported by SFI mechanism, say the CG-PUSCH at the beginning of UE FFP is cancelled by SFI Need more discussion on proposal 3 to clarify the proposal |
| NEC | Support Proposal 2. SFI mechanism changes the transmission from UL to DL for all Ues including URLLC UE, which would delay the transmission of URLLC UE to the next FFP. Since only one UE can obtain the transmission COT at a time, it is also not necessary to send group common DCI. Agree to remove the text “low priority”, “high priority” and that gNB can decide which UE’s transmission should be cancelled and COT released. |
| Lenovo/Motorola Mobility | Defining a timeline and UE-capability for an ongoing COT cancellation seems reasonable to us. |
| Huawei, HiSi | As explained earlier, we are not supportive of Proposal 5-1 |

## Discussion topic: Scheduling and UE-to-gNB COT sharing restrictions

In this section, few restrictions that are proposed, are highlighted.

Discussions are needed to decide whether to apply any of the restrictions below.

### Constraint on DL content

Proposal 6-1: When a UE operates as an initiating device, this is allowed to share its FFP with its associated gNB, and the gNB is allowed both control and data transmissions as long as a DL burst contains at least a transmission per switching point which is dedicated for the UE that initiated that FFP.

- Note: A gNB is not allowed to schedule UL transmissions within a shared u-FFP rather than those for the UE that originally initiated that FFP.

- Intel

| Question: What is your view on Proposals 6-1? |
| --- |
| Company | Comment |
| Sony | We think this restriction is not useful for latency purpose. However, we think there is a work around for this restriction. We have proposed in our T-doc R1-2100857, that the gNB should be able to cancel a UE initiated COT and take over as the COT initiator. In that way the gNB does not need to act as a responding device and can therefore schedule other Ues. |
| Futurewei | We agree with the Note (based on ETSI regulations), For the main proposal, it is not clear why a DL transmission per switching point is necessary. We find it unnecessarily restrictive. We share a similar view with Sony. |
| Intel | Just to clarify, given the comment from Sony, this proposal is not related to cancellation, but related to the UE’s COT sharing procedure. Our intent was to start triggering discussion regarding on how to define the UE’s COT sharing procedure and what may need to be modified and changed compared to the procedure defined in Rel.16 for LBE. Also the note below the proposal is out of context, and in our contribution was a separate observation, and this should be definitely discussed separately. In the broad discussion of the UE’s initiating procedure there are several aspects that we think should be considered: One aspect is related to the ED threshold to use when determining whether the channel is busy or idle. In our perspective, given that URLLC in unlicensed spectrum is intended for control environments where the incumbent technology may be absent, we no longer see any technical argument in supporting procedure meant to ensure fair-coexistence with other technologies. Therefore, we believe that the ED threshold used by the UE should be determined solely from its transmit power, and not derived based on parameter ul-toDL-COT-SharingED-Threshold-r16, which imposes the UE to use the gNB’s TX power for the calculation of the ED threshold when the COT is used by the gNB for other than DL control transmissions. This in our opinion is clearly detrimental from a UE perspective, and is no longer helpful for co-existence purpouses. The second aspect is whether we should discern the UE’s COT sharing procedure between the case when the gNB’s uses the COT for control or data transmission. In Rel.16, we defined two different procedures for this case, and again the motivation was to ensure fair-coexistence with other technologies. So in our perspective, we no longer need to define two mode of operations. In this matter, we provided proposal 2.6.1, which indicates that a UE is allowed to share its FFP with a gNB and we do not need to discern between the case when the gNB uses the UE’s FFP to transmit data or control information. The third aspect is how the UE’s FFP should be used by gNB’s, when this is shared. In this matter, our ecessarying is that based on our interpretation of the ETSI BRAN: The gNB’s in each switching point should always transmit something to the UE’s that initiated the COT, whether this is data or unicast or broadcast control information. The gNB is not allowed to schedule UL transmissions within a shared UE’s FFP to other Ues rather than that that originally initiated that FFP. For this we refer to the following text extrapolated from the ETSI BRAN: Sec. 4.2.7.3.1.4: “(3) An Initiating Device is allowed to grant an authorization to one or more associated Responding Devices to transmit on the current Operating Channel within the current Channel Occupancy Time. A Responding Device that receives such a grant shall follow the procedure described in clause 4.2.7.3.1.5.” Sec. 4.2.7.3.1.5: “Clause 4.2.7.3.1.4, point 3) describes the possibility whereby an Initiating Device grants an authorization to one or more associated Responding Devices to transmit on the current Operating Channel within the current Fixed Frame Period.” With that said, we think it would be very beneficial for the progress of this discussion to consider the aspect highlighted above separately, rather than bundling them together. |
| CATT | We want to clarify whether gNB is allowed to send both control and data transmissions to UE that initiated that FFP or not when gNB shares UE-initiated COT. |
| LG | It seems to have relation with whether the gNB’s transmission by sharing UE’s COT could be seen as gNB-initiated COT by another Ues. Limiting to such case, we are supportive with Proposal 6-1 in terms of avoiding potential UE1-to-gNB-to-UE2 COT sharing. |
| Nokia, NSB | As long as the operation is in line with the regional regulations, this should be allowed. |
| Sharp | Does the proposal mean that when gNB shares a UE COT, DL transmission only for other Ues is not allowed? It is not clear why this constraint is required. We agree with the note. |
| ETRI | We agree with the proposal in principle, but it is not clear whether spec update is needed or not for this proposal. |
| Qualcomm | We can follow LBE UL to DL COT sharing design and restrictions. |
| Lenovo/Motorola Mobility | We are fine in principle. If needed gNB can cancel the first UE-COT, and either initiate its own COT or another UE can initiate a COT and share it with gNB such that the other UE can be served. |
| WILUS | If LBE UE to DL COT sharing design and restriction per switching point is intention for this proposal, we are supportive with this. And if it is in line with the regional regulations, it should be allowed. |
| Huawei, HiSi | For the main body of Proposal 6-1, it should be clarified whether the DL burst may also include uni-cast transmissions with user plane data intended for UEs other than the initiating UE. If so, assuming that such a case is not precluded by regulations, following observations should be taken into consideration before supporting it given the operation is in unlicensed controlled environment in which inter-operator coexistence is not a concern while intra-operator coexistence could be a concern in absence of tight synchronization between the cells operating on the same channel(s): Although the calculation of ED threshold (EDT) based on the transmitter’s maximum transmit power is the same as in the dynamic channel access mode, if the gNB shares the CO initiated by the UE without the UE adjusting the EDT for transmitting unicast user plane data to the same UE, there would not be an impact to intra-operator coexistence. However, if the gNB is allowed to share that UE-initiated CO for transmitting unicast user plane data to other UEs as well, it would be advantageous for the gNB to persistently rely on sharing a UE initiated CO except for critical broadcast signals and channels, and there would be an impact to intra-operator coexistence as such. For the note, we think it should be clarified whether or not it corresponds to the issue of cross-COT/FFP scheduling aslo discussed in following proposal 6-2 B) |
| Moderator | @All: Intel has raised three issues that need discussions to reach common understanding (conclusion). During phase 3, I would suggest focusing on first two aspects raised by Intel and share your view whether you agree with the following conclusion, and if not, why. Please suggest improved wording if needed. Proposed Conclusion 6-1A: The constraints on content and duration of DL transmissions in UE-to-gNB COT sharing in case of dynamic channel access mode as specified are not applicable to semi-static channel mode. Proposed Conclusion 6-2B: In semi-static channel access mode, the ED threshold used by the UE should be determined solely from its transmit power even when it shared its COT with the gNB. This means that the ED threshold used by UE is not derived based on parameter ul-toDL-COT-SharingED-Threshold-r16, which imposes the UE to use the gNB’s TX power for the calculation of the ED threshold when the COT is used by the gNB for other than DL control transmissions. |
| Sony | Conclusion 6-1A: The conclusion seemed to be opposite of what Intel suggested. The constraint being discussed is that the gNB as a sharing device CANNOT schedule another UE that is not the UE that initiated the COT. Is the conclusion now saying that the gNB CAN schedule other UEs? |
| Moderator | @All: Please find further clarifications based on Sony’s comment to explain better the scope of the discussion and the reason for conclusion. In 37.213, clause 4.1.3 describes (parts related to constraint on DL duration and content in case of UE-to-gNB COT sharing in dynamic channel access mode are highlighted): If a gNB shares a channel occupancy initiated by a UE using the channel access procedures described in clause 4.2.1.1 on a channel, the gNB may transmit a transmission that follows a UL transmission on scheduled resources or a PUSCH transmission on configured resources by the UE after a gap as follows: - The transmission shall contain transmission to the UE that initiated the channel occupancy and can include non-unicast and/or unicast transmissions where any unicast transmission that includes user plane data is only transmitted to the UE that initiated the channel occupancy. - If the higher layer parameters ul-toDL-COT-SharingED-Threshold-r16 is not provided, the transmission shall not include any unicast transmissions with user plane data and the transmission duration is not more than the duration of 2, 4 and 8 symbols for subcarrier spacing of 15, 30 and 60 kHz of the corresponding channel, respectively. - If the gap is up to , the gNB can transmit the transmission on the channel after performing Type 2C DL channel access as described in clause 4.1.2.3. - If the gap is or , the gNB can transmit the transmission on the channel after performing Type 2A or Type 2B DL channel access procedures as described in clause 4.1.2.1 and 4.1.2.2, respectively. For the case where a gNB shares a channel occupancy initiated by a UE with configured grant PUSCH transmission, the gNB may transmit a transmission that follows the configured grant PUSCH transmission by the UE as follows: - If the higher layer parameter ul-toDL-COT-SharingED-Threshold-r16 is provided, the UE is configured by cg-COT-SharingList-r16 where cg-COT-SharingList-r16 provides a table configured by higher layer. Each row of the table provides a channel occupancy sharing information given by higher layer parameter CG-COT-Sharing-r16. One row of the table is configured for indicating that the channel occupancy sharing is not available. - If the 'COT sharing information' in CG-UCI detected in slot n indicates a row index that corresponds to a CG-COT-Sharing-r16 that provides channel occupancy sharing information, the gNB can share the UE channel occupancy assuming a channel access priority class p= channelAccessPriority-r16, starting from slot n+O, where O=offset-r16 slots, for a duration of D=duration-r16 slots where duration-r16, offset-r16, and channelAccessPriority-r16 are higher layer parameters provided by CG-COT-Sharing-r16. - If the higher layer parameter ul-toDL-COT-SharingED-Threshold-r16 is not provided, and if 'COT sharing information' in CG-UCI indicates '1', the gNB can share the UE channel occupancy and start the DL transmission X= cg-COT-SharingOffset-r16 symbols from the end of the slot where CG-UCI is detected, where cg-COT-SharingOffset-r16 is provided by higher layer. The transmission shall not include any unicast transmissions with user plane data and the transmission duration is not more than the duration of 2, 4 and 8 symbols for subcarrier spacing of 15, 30 and 60 kHz of the corresponding channel, respectively. These constraints are applicable when dynamic channel access is used and are decided assuming coexisting with other technologies. The constrains are not applicable to the semi-static channel access mode (nor per spec, nor per regulation). For example, there is no constraint that when a responding device (e.g. gNB) shares a COT initiated by an initiating device (e.g. UE) to limits its transmission duration (except until idle period) or what to include in the transmission. Hence, from channel access point of view or regulation, no additional restriction is needed. |
| Huawei, HiSilicon | On Proposed Conclusion 6-1A: We think the current wording could be misleading as some aspects of UL-to-DL COT sharing in LBE is still applicable in our view. For instance, the condition on the content that DL transmission from the responding gNB should at least include a transmission intended for the initiating UE. We propose to consider the following rewording as a starting point: Proposed Conclusion 6-1A: The constraints on content and duration of DL transmissions in UE-to-gNB COT sharing in case of dynamic channel access mode as specified are not applicable to can be relaxed in the case of semi-static channel mode in a unlicensed controlled environment. Note: A DL transmission burst from the responding gNB should at least include a transmission intended for the initiating UE On Proposed Conclusion 6-2B: We think it would be easy to get consensus on that at least transmitting DL containing unicast user plane data to the UE that initiated the CO without adjusting its EDT should be supported. Additional unicast transmissions to other UEs could be FFS Proposed Conclusion 6-2B: In semi-static channel access mode, at least for gNB transmission of a DL burst containing unicast user plane data in response to the initiating UE, the ED threshold used by the UE to initiate the CO should be determined solely from its transmit power even when it shared its COT with the gNB. This means that the ED threshold used by UE is not derived based on parameter ul-toDL-COT-SharingED-Threshold-r16, which imposes the UE to use the gNB’s TX power for the calculation of the ED threshold when the COT is used by the gNB for other than DL control transmissions. FFS: Whether this can be extended to the case in which the DL burst contains additional transmission(s) with unicast user plane data to other UEs |
| Intel | Many thanks to the FL for continuing discussion on this topic. For 6-1A, we are in general supportive with the idea behind the conclusion. Our view is that while the UL-to-DL COT sharing procedure from Rel.16 can be used as a baseline, some of its constrains could be relaxed given that they were posed to solve co-existence issues, which in a system operating in a controlled environment are no longer relevant: among a long list there is the way how the ED threshold is calculated and used, and the fact that control signalling and data transmissions are treated differently in the procedure. However, for the way how the conclusion is written this may lead to further questions and misinterpretation: is the Rel.16 used as a baseline, and what are the constrains (all or some of them)? Our understanding is that with this conclusion we would like to converge on whether some changes are needed or not to be made to the UL-to-DL COT sharing procedure, while the Rel.16 would be used as a baseline. What the constrains are and how to relax them will be discuss separately. Is this the correct understanding? If this is correct, we suggest revising the conclusion 6-1A as follows: Proposed Conclusion 6-1A: The UE-to-gNB COT sharing procedure for the case of dynamic channel access mode is reused as a baseline for semi-static channel mode. However, some of its Tthe constraints on content and duration of DL transmissions in UE-to-gNB COT sharing in case of dynamic channel access mode as specified are not applicable to semi-static channel mode. and should be relaxed. As for 6-2B, we are supportive of this proposal. This is one example of the constraints that have been posed in Rel.16, and which can be relaxed. We think that if the same procedure to determine the ED threshold from Rel.16 is reused, this would be very detrimental from a UE perspective operating as initiating device: a UE would be imposed to use an ED threshold higher than what the ETSI BRAN supports, without any advantages in terms of system performance and co-existence, making acquiring a channel more difficult. This would also simply the design, since we no longer need to treat separately the data and control transmission, and the whole procedure would be more in line with the minimum requirements dictated by ETSI BRAN. As for the third aspect we mentioned: First bullet follows Rel.16, and therefore no changes should be made if we use the Rel.16 procedure are baseline; For the second bullet, our understanding is that our view is covered by proposal 8-1. We do not thing that a FFP initiated by a UE should be shared by a gNB with other intra-cell UEs. This is not supported by Rel.16 and in our understanding, it is not allowed by ETSI BRAN. |
| Apple | We would be fine with Conclusion 6-1A and 6-2B only for well-controlled environment. Is it possible to add a phrase “assuming that FBE is used only in well-controlled environments and the network is not coexisting with other technologies”? This may or may not have spec impact but at least we should have a common understanding on the intended usage for FBE. It is also not clear if 6-1A is allowed by the regulation. But if the group thinks it is allowed, we are fine with it. |
| ZTE | For the proposed conclusion 6-1A, we are fine with either HW’s version or Intel’s. For which constrains that can be relaxed can be further discussed. |
| Futurewei | We support the proposal 6-1A in principle with the following amendment: Proposed Conclusion 6-1A: The UE-to-gNB COT sharing procedure for the case of dynamic channel access mode is reused as a baseline for semi-static channel mode. FFS: whether or not the constraints on content and duration of DL transmissions should be supported, and if supported how they should be relaxed We support the proposal in principle 6-2B, only for UE to initiate a COT. Proposed Conclusion 6-2B: In semi-static channel access mode, the ED threshold used by the UE to initiate a COT, should be determined solely from its transmit power even when it shared its COT with the gNB. Note: This means that the ED threshold used by UE to initiate a COT is not derived based on parameter ul-toDL-COT-SharingED-Threshold-r16, which imposes the UE to use the gNB’s TX power for the calculation of the ED threshold when the COT is used by the gNB for other than DL control transmissions. |
| CATT | In principal, We are fine with intention of proposal 6-1A and proposal 6-1B. From our perspective, 1. the UL-to-DL COT sharing mechanism for LBE from Rel.16 should be made as a baseline. 2. a DL transmission burst from the responding gNB should only belong to the initiating UE. 3. we have concern on the DL burst contains additional transmission(s) with unicast user plane data to other UEs because this can’t be supported in Rel.16 |
| vivo | Thanks a lot Sorour’s explanation! We also think the constraints in the Proposed Conclusion 6-1A is not much clear. By reading the 37.213, clause 4.1.3, it only describes the rules need to be followed between the UE that initiated COT and the gNB responds to the initiating UE. We wondered whether the constraint also include that the whether the responding gNB cannot schedule a different UE than the one initiating the COT. In addition, we would like to suggest to first agree on proposal 8-1, this constraint for FBE mode cannot be relaxed. Then we can discuss to agree on Proposed Conclusion 6-1A and Proposed Conclusion 6-1B. For the Proposed Conclusion 6-2B, we prefer HW’s modification. |
| DOCOMO | We are fine with the Proposed Conclusion 6-1A/6-2B in principle. We think UL-to-DL COT sharing mechanism for LBE in Rel.16 should be the baseline and hence, Proposed Conclusion 6-1A modified by Futurewei is preferred. Also, we prefer Proposed Conclusion 6-2B modified by Huawei for clarification. |
| Nokia, NSB | We support the proposed conclusion P6-1A and P6-2B |
| Qualcomm | We support 6-1B. The proposal 6-1A is not clear for us. |
| LG | On the above proposals, why those are motivated is understood. On the other hand, at this moment, we are a bit not sure (may need to be careful) if any potential coexistence issue could entirely precluded in FBE operation with UE-initiated COT. In this context, firstly, regarding UE-to-gNB COT sharing mechanism, we share the same view with Futurewei and DOCOMO that Rel-16 LBT should be the baseline. Secondly, regarding ED threshold, I’d like to ask following two questions: Wouldn’t be there any potential coexistence issue by using UE TX power based EDT to initiate COT? Wouldn’t ul-toDL-COT-SharingED-Threshold-r16 be used in FBE operation with UE-initiated COT? |
| ETRI | We are fine with both proposals 6-1A and 6-1B. Proposal 6-1A is saying that not the whole UE-to-gNB COT sharing features in LBE but only the features of “the constraints on contents and durations of DL transmissions” are not applicable for Rel-17 FBE. It is well aligned with our understanding on related ETSI BRAN spec. Maybe the wording can be improved to be clearer. |
| Sony | Thanks for Moderator’s clarification. The initial assumption was that Conclusion 6-1A was not allowed by regulations, which we believed was too restrictive. If companies believe the regulations applies only to LBE then we are fine with principle of Conclusion 6-1 and is ok with Huawei’s suggested proposal on the main bullet point with the following editorial, i.e.: Proposed Conclusion 6-1A: The constraints on content and duration of DL transmissions in UE-to-gNB COT sharing in case of dynamic channel access mode as specified are not applicable to can be relaxed in the case of semi-static channel mode in an unlicensed controlled environment. On the note: Note: A DL transmission burst from the responding gNB should at least include a transmission intended for the initiating UE Does this mean that if the gNB wants to schedule another UE (that is not the initiating UE), it must send something back to the initiating UE. That is it has to send some response to the initiating UE in addition to sending data/control to other UEs? |
| Moderator | @All: Based on your feedback, it is clear that we need a discussion to reach to a common understanding for FBE operation. @All: I would like us to spend more time and discuss instead of rushing conclusion. In fact, I noticed from the first meeting that there is different understanding on how to relate Cot sharing constraint in Rel-16 to FBE (in Rel-16) and now Rel-17. Few thoughts from my side: The restrictions on COT sharing mentioned above (duration and content of DL) from spec point of view are solely relevant to LBE. FBE operation in 37.213 is only captured in section 4.0 and 4.3 where in 4.3 refers to ED clause to determine the threshold. So, FBE and LBE are independent. Discussion in Rel-16 were mainly focused on LBE and many constraints on LBE operation were specified, mainly because the baseline was coexisting with Wi-Fi. For FBE, as it states in 4.3, the operation is intended when other technologies are not present. Also, when considering ETSI BRAN, you cant find restriction on the content of transmission as oppose to LBE which includes a lot of conditions for channel access priority class and gap duration within a COT, etc. However, it seems during discussions in Rel-16, this distinction was not well discussed since FBE was addressed almost at the end, while the whole WI/SI mainly focused on LBE. Therefore, it is understandable that we assume let’s use LBE as baseline. While another view is that the constraints on LBE are not relevant for FBE, i.e. the baseline is as 37.213 where there is no constraint. However, as we progress in design, for the system to operate well and avoid complexity and ambiguity, we my end up putting restriction and maybe end up as LBE. But in my humble view, it is a better design approach to assume no restrictions and then, put restrictions when we see the need, as compared to start with restrictions and try to remove them when they are not justified. @All: Let’s use this section for exchanging ideas for the remaining of this week and continue next meeting, hopefully more focused. |
| CATT | We have questions as below 1. What’s benefit on DL transmission on other UEs in UE-to-gNB COT sharing? 2. How can UEs know whether gNB uses other UE-to-gNB COT sharing to transmit DL data or not? |

### Constraint on scheduling

Proposal 6-2: For semi-static channel access mode, at least one of the following is applicable:

- A) UE transmits HARQ-ACK feedback for a PDSCH according to the shared gNB COT as long as the HARQ-ACK is within the same COT containing the PDSCH.

  - Xiaomi

- B) For scheduled UL, the FFP/channel where a UL (each UL repetition in case of repetition) is scheduled can be same or different from the FFP/channel where an associated UL grant is transmitted.

  - ETRI

| Question: What is your view on Proposals 6-2? |
| --- |
| Company | Comment |
| Sony | Proposal A describes the ecessar of a responding device which is already Rel-16 behaviour. Proposal B: Is this suggesting that a scheduled PUSCH repetition can cross gNB’s FFP boundary or UE FFP boundary? It will be good to clarify the scenario. |
| Futurewei | Proposal A: Agree with Sony. Proposal B: Not sure we understand. The initiating FFP gNB needs to transmit a grant in the same operating channel for UE sharing COT as required by ETSI. |
| Intel | We prefer Alt.a. As we pointed out during the prior meeting and above, we believe that cross-FFP scheduling, and HARQ feedback should not be allowed due to the restrictions from the ETSI BRAN. |
| CATT | The same view with Sony for proposal A. For proposal B, if gNB can control UE-initiated COT, UL transmission scheduled across multiple FFPs should be allowed. The detail should be FFS. |
| LG | We share the same view with Sony and Futurewei. |
| Nokia, NSB | Proposal 6-2: A) is ok but probably no agreement is needed as this is true for any UL transmission which is contained in the gNB initiated COT. B) We agree on support of cross-FFP scheduling. Cross-carrier scheduling should be discussed separately. |
| ETRI | We think that Proposal A is gNB scheduling issue. For Proposal B, our intention is to clarify whether cross-FFP or cross-channel scheduling is allowed or not. There was some related discussion in the last meeting. We think that the scheduling flexibility should not be impacted by the FFP structure or the related channel access behavior. For example, it should be allowed in Rel-17 FBE that DCI in 1st FFP schedules PUSCH in 2nd FFP, and DCI in 1st channel (1st RB set) schedules PUSCH in 2nd channel (2nd RB set) in the same carrier. |
| Qualcomm | Not clear what the proposals are for. We believe schedule or trigger UE to transmit in the later gNB FFP is allowed by Rel.16 already, as long as UE will perform another gNB DL detection at the beginning for the later FFP to confirm the gNB has the COT. Proposal A is Rel.16 behavior when UL transmission is in the same FFP as DL trigger. |
| OPPO | For proposal 6-2 A), we don’t remember it was agreed that the PDSCH and the corresponding HARQ-ACK has to be in the same COT. At least in LBE, there is no such restriction. B) we are open to support cross-FFP or cross-COT scheduling. |
| InterDigital | We should not restrict scheduled UL transmissions (including scheduled HARQ-ACK feedback) to be in the same FFP as the scheduling transmission. We agree with Nokia that cross-carrier scheduling should be discussed separately. |
| Lenovo/Motorola Mobility | Proposal A seems fine to us (as a conclusion). Proposal B: Ok. Seems related to section 2.4.2. |
| WILUS | We think Proposal A is already Rel-16 behavior. For proposal B, We agree with Nokia and InterDigital that cross-carrier scheduling should be discussed separately. |

### COT indication for next FFP

Proposal 6-3: No additional specification is necessary for the indication to whether a UE can initiate a COT in a next FFP associated to the UE

- DCM, MTK, Sony

| Question: What is your view on Proposals 6-3? |
| --- |
| Company | Comment |
| Sony | I have clarified the proposal (see track changes for Proposal 6-3 above). At least in our proposal we suggest that there is no need to indicate whether to ban a UE from initiating future FFPs. We agreed with the clarified/modified proposal above. |
| Futurewei | We do not support this proposal. If gNB is allowed to cancel a COT should be allowed to cancel future FFPs as well. For instance, if there are too many Ues trying to initiate COT (i.e. compete with each other) we think that it would be beneficial if gNB cancel future FFPs for these Ues and bring all them together in the gNB initiated COT. |
| Intel | Agree with the above proposal. |
| CATT | We do not agree with this proposal. gNB need indication to whether a UE can initiate a COT in a next FFP associated to the UE in order to reduce interference between UE-initiated COT and gNB-initiated COT or between two UE-initiated COTs. |
| LG | On Proposal 6-3, if it is intended to object to the above Proposals 5-1 and 5-2, then we don’t support this proposal. |
| Nokia, NSB | Agree. |
| ETRI | The proposal seems related to the previous issues. |
| Qualcomm | Need to jointly discuss if cancellation behavior is supported |
| OPPO | Not supportive for proposal 6-3 |
| InterDigital | This is related to Proposal 5-1. The behavior should be that a UE assumes it can initiate a COT in a next FFP unless it has been cancelled or overridden. |
| DOCOMO | We agree with the proposal because of the same reason as Proposal 5-1/5-2 |
| Lenovo/Motorola Mobility | Seems ok. |
| Samsung | We’re fine with the proposal. |
| WILUS | We agree with the proposal. |
| Huawei, HiSi | The relationship to the proposals in Section 2.4 is not clear to us |
| Apple | This should be related to the discussion in Section 2.4 |

### UE initiated COT restrictions

Proposal 6-4:  Restrict UE COT-initiation to high priority traffic.

- MTK

| Question: What is your view on Proposals 6-4? |
| --- |
| Company | Comment |
| Sony | Not agree. This can be achieved with gNB configuration, e.g. by not configuring Low L1 priority CG-PUSCH to start at UE’s FFP boundary. So this restriction is not ecessary. |
| Vivo | It should be discussed in section 2.2.2, same as proposal 1. We do not see the necessity for such restriction. |
| Futurewei | We do not support. It should be left to gNB configuration. |
| Intel | We do fail to understand the technical need of this proposal. It would be good to receive further clarifications. |
| CATT | We have the same view with VIVO. This proposal isn’t necessary. |
| LG | It seems premature at this stage to have such restriction. |
| Nokia, NSB | Not applicable in IDLE/INACTIVE mode. For RRC CONNECTED mode, this should be linked to proposal 1 in section 2.2.2 |
| Sharp | We do not see the necessity of the restriction. |
| ETRI | Currently, we do not see a need of any restriction coming from the transmission priority. |
| Qualcomm | We do not support. It is not necessary to have this restriction. |
| OPPO | Not support |
| InterDigital | We do not agree with this proposal |
| DOCOMO | We do not see the necessity of such restriction |
| Lenovo/Motorola Mobility | Agree. It can be useful to reduce contention. Does this proposal cover DG PUSCH as well? Alternatively, whether the UE is allowed to initiate a COT can be configured per CG-PUSCH configuration. |
| Samsung | We do not see the necessity of the restriction. |
| WILUS | We do not see the necessity of such restriction. |
| HW/HiSi | No. Agree with comment from Sony. |
| Apple | We do not see the need for such restriction as a general rule. But we see the motivation for introducing per-CG parameter to control whether it can initiate a COT. |
| Moderator | Companies’ view: Yes: MTK, Lenovo/MOT No: Sony, vivo, FW, Intel, CATT, sharp, ETRI, QC, OPPO, IDC, DCM, Samsung, WILUS, HW/HiSi Nokia/NSB? @Leonovo/MOT, MTK: can provide motivations for the proposal. @All: Based on majority of view, the following is proposed. Proposal 6-4: UE-initiated COT is supported for high priority transmissions in addition to the low priority. |
| Sony | Support the proposal |
| Huawei, HiSilicon | Although we agree with the moderator’s conclusion, we wonder if there is a need to agree to the proposal if this would be the default case already. |
| Intel | We also support the proposal, and we do not see the technical reason to contain the UE to operate as initiating device only for high priority transmissions. |
| Apple | We support the proposal, with the understanding that whether additional level of control (e.g. per-CG configuration) is introduced will be discussed separately. |
| ZTE | We support the proposal |
| Futurewei | We support in principle the Proposal 6-4. However, we do not see what the value of such proposal is. Are there priorities other than low and high? |
| CATT | We support FL proposal. |
| vivo | Support the proposal |
| Panasonic | We support the proposal. |
| DOCOMO | We support the proposal |
| Sharp | We agree with the proposal as a Conclusion for clarification. |
| Lenovo, Motorola Mobility | In our view, restricting UE COT-initiation to high priority traffic can be one mode of operation, not the only mode, and the intention is to reduce the contention. As we mentioned earlier, an alternative way could be to restrict UE COT-initiation per CG configuration (Proposal 3-2 Alt-1). From that sense, we suggest discussing this scheme as an alternative of/along with Proposal 3-2. |
| LG | We are fine with the proposal. |
| Nokia, NSB | We support the proposal |
| Qualcomm | Support the proposal |
| InterDigital | We are fine with the proposal. |
| ETRI | We are fine with the proposal as a conclusion although we do not see a need to agree on that. |
| Moderator | Companies agree that either the proposal is not needed (agreeing to), or if a special mode of operation is intended for high priority can be discussed under Proposal 3-2 Alt-1), or additional level of control for CG can be discussed separately. Summary of discussion: This discussion is closed with the common understanding that the UE-initiated COT is supported for high priority transmissions in addition to the low priority |

## Discussion topic: Indication of UE-initiated COT to gNB

The proposal below, aims to capture the views with respect to the discussion topic, on high level.

Proposal 7-1:

- In case of semi-static channel occupancy, down-select one of the following alternatives:

  - Alt-1: A UE explicitly indicates whether a UL transmission is based on a COT initiated by UE or gNB.

    - FFS details.

      - IDC, MTK

  - Alt-2: A UE does not explicitly indicate whether a UL transmission is based on a COT initiated by UE or gNB.

    - DCM, Panasonic, vivo

| Question: What is your view on Proposal 7-1? |
| --- |
| Company | Comment |
| Sony | We support Alt-2. |
| Vivo | Support Alt-2. gNB will naturally know the UE-initiated COT by detecting on the configured or schedules resources at the UE FFP boundary. No additional indication is needed. If there is no scheduled or configured UL transmission at the UE FFP boundary, there will definitely be no UE-initiated COT. |
| Futurewei | Alt-2. |
| Intel | We support Alt-2. |
| CATT | We prefer Alt.2. This proposal is related to section 2.4.1 and 2.4.2. Because gNB can control UE-imitated COT, UE needn’t indicate whether a UL transmission is based on a COT initiated by UE or gNB |
| LG | Alt-2. |
| Nokia, NSB | Alt-2. |
| Sharp | Selecting which alternative depends on determination rules/methods of scheduled UL transmission or configured UL transmission. |
| ETRI | We support Alt-2. |
| Qualcomm | Alt-1. The information can be included in CG-UCI, which in Rel.16 already carries COT sharing information. In some cases (if there is any miss detection events), the gNB may not be able to figure out a UE transmission if using UE COT or sharing gNB COT. Similarly, gNB also needs to indicate whether a DL transmission is based on a COT initiated by UE or gNB, possibly in COT-SI, so other Ues can know the COT is sharable or not (We believe we should not support UE to UE COT sharing). Please refer to R1-2101461 for more details. |
| InterDigital | We support Alt-1. This is especially important in case of misdetection of gNB-initiated COT by the UE (in which case the UE initiates a COT and the gNB may assume the UE is using the gNB-initiated COT if it doesn’t receive an indication from the UE). |
| DOCOMO | Alt-2. |
| Lenovo/Motorola Mobility | We prefer Alt-2. Would be good to provide the use-case/justification for Alt-1. |
| Samsung | According to rules in 2.4, gNB knows whether a UE has initiated a COT or not, no need of additional signaling. So, we support Alt-2. But we want to clarify that, if CG-UCI is configured, UE can inform gNB by CG-UCI as in Rel-16. Does Alt-2 exclude this indication? |
| Spreadtrum | Alt-2 |
| WILUS | We support Alt-2. |
| HW/HiSi | Prefer Alt-2 |
| Apple | Is this proposal for CG PUSCH only? |
| Moderator | @Apple: Moderator understanding is that it is only applicable to CG-PUSCH. Companies’ view: Alt-1: QC, IDC Alt-2: Sony, vivo, FW, Intel, CATT, LG, Nokia/NSB, ETRI, DCM, Lenovo/MOT, Samsung, Spreadtrum, WILUS, HW/HiSi Sharp: Depends outcome of proposals 4-1/4-2A. @All: Due to the majority support, FL proposes Alt-2 for consideration. Proposal 7-1: In case of semi-static channel occupancy, a UE does not explicitly indicate whether a UL transmission is based on a COT initiated by the UE or gNB. |
| Sony | Support the proposal. |
| Huawei, HiSilicon | We support the proposal |
| Intel | Support the proposal. |
| Apple | We would prefer to discuss the issue later, because it depends on whether the gNB has a need to know it or not. Due to error cases, the gNB may not know UE’s assumption exactly. If gNB’s behavior depends on whether it is using its own COT or sharing the UE’s COT, Alt-1 would be the way to go; otherwise Alt-2 is fine. E.g., this is related to the issue discussed in Section 2.6.1. |
| ZTE | We support the proposal |
| Futurewei | We support the proposal 7-1. |
| CATT | We prefer this proposal. |
| vivo | Support the proposal |
| Panasonic | We support the proposal. |
| DOCOMO | We support the proposal |
| Sharp | We are fine with the proposal. |
| Lenovo/Motorola Mobility | We prefer to discuss this aspect once further agreements on COT initiation are made. |
| LG | We are fine with the proposal. |
| Nokia, NSB | We support the proposal |
| Qualcomm | We share the same view as Apple. UE can have flexibility to share its COT or not. |
| ETRI | We support the proposal. |
| Moderator | Summary of views: All companies are supportive. However, 3companies (Apple, IDC, QC) indicated to prefer to postpone this discussion until there is more clarity on COT-sharing and determination of COT-initiator. Moderator recommendation: Postpone the discussion and resume it if needed, when details of COT determinations are in place. |

## Discussion topic: UE-to-UE COT sharing via gNB

The proposal below, aims to capture the views with respect to the discussion topic, on high level.

Proposal 8-1:

- In semi-static channel access mode, down-select one of the following alternatives:

  - Sharing a UE initiated COT through the gNB to other intra-cell UEs for UL transmissions, is not supported.

    - HW/HiSi, ZTE, NEC, Intel

  - Sharing a UE initiated COT through the gNB to other intra-cell Ues for UL transmissions, is supported.

    - FFS on details

    - Sony

| Question: What is your view on Proposal 8-1? |
| --- |
| Company | Comment |
| Sony | Just to clarify, we proposed that the gNB can cancel a UE’s COT and take ownership (i.e. become the COT initiator) so that it can schedule another UE. |
| Vivo | Currently, we slightly prefer Sharing a UE initiated COT through the gNB to other intra-cell Ues for UL transmissions, is not supported. |
| Futurewei | We note that both alternatives were quite confusing in their original format. However, with additional explanation from Sony (here above) the intention becomes clear and we support that:” the gNB can cancel a UE’s COT and take ownership (i.e. become the COT initiator) so that it can schedule another UE.” |
| Intel | We also do not support gNB scheduling transmissions to other intra-cell Ues, since as mentioned above this is not allowed by ETSI BRAN. |
| CATT | We prefer “Sharing a UE initiated COT through the gNB to other intra-cell Ues for UL transmissions, is not supported.” |
| LG | We prefer the first sub-bullet: Sharing a UE initiated COT through the gNB to other intra-cell Ues for UL transmissions, is not supported. |
| Nokia, NSB | Sharing a UE initiated COT through the gNB to other intra-cell Ues for UL transmissions, is not supported. This was already discussed for R16 and not agreed due to regulatory concerns. |
| Sharp | We tend to prefer the upper alternative for simplified design. |
| ETRI | We support the first sub-bullet (“not supported”). |
| Qualcomm | Sharing a UE initiated COT through the gNB to other intra-cell Ues for UL transmissions, is not supported. This is aligned with R-16 behaviour. |
| InterDigital | For ease of specification, sharing a UE-initiated COT with other Ues should not be supported in Rel-17. |
| DOCOMO | We don’t support the feature |
| Lenovo/Motorola Mobility | Fine to further discuss the second bullet. In our view, if needed, gNB can cancel the first UE-COT, and either initiate its own COT or another UE can initiate a COT and share it with gNB such that the other UE can be served. |
| Samsung | We have to figure out whether the regulation allows it or not. |
| Spreadtrum | We support the first sub-bullet (“not supported”). |
| WILUS | We agree that sharing a UE initiated COT through the gNB to other intra-cell UEs for UL transmissions is not supported. |
| Huawei, HiSi | We support the first alternative as captured in the proposal |
| Apple | It is not clear if it is allowed by regulation. We prefer the first alternative. |
| Moderator | @Intel: On the comment “We also do not support gNB scheduling transmissions to other intra-cell UEs, since as mentioned above this is not allowed by ETSI BRAN.”, it would be good to discuss more. As we discussed last time “authorization” by regulation does not directly translate to grants in standard technical specifications. Important, and interesting topic for discussion. @Sony, FW, Lenovo/MOT, all: Based on description by companies above, it is not clear the proposed scheme falls in UE-to-UE cot sharing because it seems gNB initiates the COT when it cancels ownership of the UE. It would be good to get clarification. UE-to-UE supported: Sony?, FW?, Lenovo/MOT? UE-to-UE not supported: LG, vivo, Intel, CATT, Nokia/NSB, Sharp, QC, IDC, DCM, WILUS, Apple, Spreadtrum, HW/HiSi @All: Due to the majority support, and the comment to Sony, FW, Lenovo/MOT, FL proposes the following for consideration. Proposal 8-1: In semi-static channel access mode, sharing a UE initiated COT through the gNB to other intra-cell UEs for UL transmissions, is not supported. |
| Sony | We support the proposal. And to clarify our proposal is not UE initiated COT being share to other UEs via the gNB. We proposed that the gNB can cancel the COT that the UE initiated and then the gNB takes over the COT, i.e. acting as COT initiator to schedule other UEs. This proposal seems to contradict the Conclusion proposed in 6-1A. |
| Moderator | @Sony: The Conclusion tries to address that from channel access point of view or regulation is it allowed. However, that does not mean that as a group we can decide to simplify operation. For example, maybe supporting such an operation complicate the design and then we can as well, decide not to support it. |
| Huawei, HiSilicon | We support the proposal |
| Intel | We are Ok with this proposal. @FL: Copying back the related ETSI BRAN text: Sec. 4.2.7.3.1.4: “(3) An Initiating Device is allowed to grant an authorization to one or more associated Responding Devices to transmit on the current Operating Channel within the current Channel Occupancy Time. A Responding Device that receives such a grant shall follow the procedure described in clause 4.2.7.3.1.5.” Sec. 4.2.7.3.1.5: “Clause 4.2.7.3.1.4, point 3) describes the possibility whereby an Initiating Device grants an authorization to one or more associated Responding Devices to transmit on the current Operating Channel within the current Fixed Frame Period.” I agree with you, and also an authorization could be implicitly or explicitly provided. However, if such a procedure is supported, how would we claim during testing compliance procedure that authorization was granted by a UE (initiating device) to another UE (responding device)? This would happen through gNB, which now is the one providing the grant, that is not operating as initiating device, but rather as a responding device. |
| Apple | We support the proposal. |
| ZTE | We support the proposal |
| Futurewei | We support the Proposal 8-1. We agree with Intel that the grant aspect from the UE as initiating device needs to be clarified. For instance: “Proposal: In semi-static access, any transmission from UE used to initiate a COT, as an initiating device, will be considered by gNB as an authorization to share the UE initiated COT for the duration of that COT” |
| CATT | We prefer this proposal. |
| vivo | Support the proposal |
| Panasonic | We support the proposal. |
| DOCOMO | We support the proposal |
| Sharp | We support the proposal. |
| Lenovo/Motorola Mobility | We support FL’s proposal. |
| LG | We are fine with the proposal. |
| Nokia, NSB | We support the FL’sproposal |
| Qualcomm | We support the proposal. |
| ETRI | We support the proposal. |
| Moderator | @Intel/FW: As being involved in ETSI BRAN regulations for FBE/LBE, I have a different understanding on how to interpret “authorization” in regulation with respect to technologies standard and don’t share the same view. But let’s take that discussion separately, hopefully when we meet, if not needed earlier 😊 Current status: All companies support the proposal. @All: Moderator suggests Chairman to endorse the following proposal. Proposal 8-1: In semi-static channel access mode, sharing a UE initiated COT through the gNB to other intra-cell UEs for UL transmissions, is not supported. |
| Moderator | The following was agreed in GTW, Feb. 4th: Agreement: In semi-static channel access mode, sharing a UE initiated COT through the gNB to other intra-cell UEs for UL transmissions, is not supported. |

## Discussion topic: UE-initiated COT in INACTIVE/IDLE mode

The proposals below, aim to capture the views with respect to the discussion topic, on high level.

Proposal 9-1:

- Down-select one of the following options:

  - Option 1: UE-initiated COT for semi-static channel occupancy in IDLE/INACTIVE mode is supported. FFS on details.

    - Intel, E///, QC, Nokia, Samsung, vivo, Sony, IDC, MTK, WILUS, OPPO

  - Option 2: UE-initiated COT for semi-static channel occupancy in IDLE/INACTIVE mode is NOT supported.

    - HW/HiSi, ETRI, DCM, Spreadtrum

  - Option 3: The decision on whether to support RACH transmission to initiate a COT by UE in RRC IDLE/INACTIVE mode is up to RAN2

    - Panasonic

  - Option 4: In case Option 1 is not supported, allow PRACH transmissions in idle period of gNB-FFP. FFS on details.

    - QC

Proposal 9-2:

- If UE-initiated COT for semi-static channel occupancy in IDLE/INACTIVE mode is supported (i.e. Option 1), FFP configuration for a UE to initiate a COT can be indicated by SIB1 or derived by PRACH configuration.

    - FFS on details.

| Question 1: What is your view on Proposal 9-1? Question 2: If you support proposal 9-1. What is your view on proposal 9-2? |
| --- |
| Company | Comment |
| Sony | We support Option 1 of Proposa 9-1 and therefore we support Proposal 9-2, i.e. UE FFP configuration is indicated in SIB1. |
| vivo | Support option 1. Unified behaviour is preferred for RACH transmission for UEs in idle and connected mode. |
| Futurewei | Option 2 for Proposal 9-1. We do not see the necessity/benefits of Option 1. It could lead to additional complications that need to be further clarified. For instance, this feature may lead to a random offset not specified by gNB. Also due to hidden node problem other UEs may transmit in overlapping multiple FFPs. |
| Intel | We are supportive of Option 1. However, we would like to clarify our position: For msgA and msg1 in the 2-step and 4-step RACH procedure, respectively, no explicit or implicit coordination between a UE and a gNB is possible on whether a UE can operate as a responding or initiating device. Therefore, uncoordinated transmissions may occur. For this reason, in this case we prefer to reuse the Rel.16 behaviour an operate a UE transmitting msgA or msg1 only as a responding device. For what concern the transmission of the HARQ-ACK information related to msgB for the 2-step, and msg3 for 4-step RACH, a UE could be instead instructed implicitly or explicitly by the gNB on whether to operate as a responding or initiating device through the use of msgB or msg2, respectively. In this case, our preference is to enable UE’s initiating device for semi-static channel access mode. |
| CATT | We prefer to Option.2 for proposal 9-1 |
| LG | We still prefer Option 2 with consideration of WI scope to support UL enhancement for URLLC UEs which would be known to gNB after RRC connection. |
| Panasonic | We slightly prefer Option 1. To support RACH transmission to initiate a COT by UE in RRC IDLE/INACTIVE mode is useful. If Option 1 is supported, SIB indication should be supported. |
| Nokia, NSB | Option 1. Option 4 is more related to the discussion on whether (or not) UE-initiated transmissions in gNB idle period should be allowed. Proposal 9-2 is ok (FFS). |
| Sharp | We tend to prefer Option 1 for Proposal 9-1 and support Proposal 9-2, which enable PRACH transmission with UE-initiated COT. |
| ETRI | We prefer Option 2. |
| Qualcomm | Support Option 1 for proposal 9-1, and proposal 9-2. |
| InterDigital | Support Option 1 for proposal 9-1 and support proposal 9-2. |
| DOCOMO | Support Option 2 for proposal 9-1 |
| Lenovo/Motorola Mobility | We are ok with proposal 9-1 option 1 and proposal 9-2. |
| Samsung | Support Option 1 for proposal 9-1 and proposal 9-2. |
| Spreadtrum | We prefer to Option.2 for proposal 9-1, considering this is URLLC enhancement. |
| WILUS | We support Option 1 of Proposal 9-1 and support Proposal 9-2, i.e. UE FFP configuration is indicated in SIB1. |
| HW/HiSi | Option 2. URLLC functionality is only discussed in RRC connected. There is no reason to discuss URLLC functionality for IDLE/INACTIVE mode. Which are out of scope in our view. Furthermore, if a UE would be provided with a common FFP for RACH related purposes and then with a different dedicated FFP later, the following issues are observed: Due to the fact that the start of the PRACH transmission may not be aligned with the beginning of the common FFP, the UE may not be able to use that common FFP to initiate a CO using PRACH, even though the ROs would be configured to match the common FFP parameters Since the UE would not be able to use both FFPs simultaneously as per the regulations, once the UE is connected and using the dedicated FFP, it would be difficult to transmit PRACH (e.g., for CFRA) in UE initiated COT if the ROs provided match the common FFP. As agreed in the last meeting, the FFP configuration that is used for initiating CO shall not be changed for at least 200 ms in accordance with FBE regulations from Section 4.2.7.3.1.4 in [2], Therefore, the UE would have to observe at least a 200 ms waiting period to switch from the common FFP to the dedicated FFP or vice versa, which adversely impacts the latency for IIoT/URLLC. Adding up to the previous drawbacks, if the UE would switch between the FFPs, the gNB would not know which FFP currently is applied, which would complicate substantially scheduling, observing idle periods and coordinating UEs. |
| Moderator | @All: No majority view. Continue discussion to decide whether to support this mode or not. |
| ZTE | This might be beneficial for RA-based small data transmission in RRC_inactive state, but that may not fit the scope of URLLC. For the normal RACH procedure, we share the similar concern as Huawei in terms of switching from common FFP to dedicated FFP. |

## Discussion topic: Other FBE issues

Please provide your view for discussions, in case time allows.

### Energy detection sensing threshold

With respect to energy detection threshold for sensing, companies have proposed the following.

- Proposal 1: For semi-static channel access in unlicensed controlled environment, support gNB sharing of the CO initiated by the UE without adjusting the EDT, for transmissions including unicast user plane data to the same UE.

  - HW/HiSi

- Proposal 2: When a UE operating as initiating device acquires its FFP, in any circumstances the ED threshold used to determine whether the channel is busy or idle is calculated solely based on the UE’s transmit power.

  - Intel

- Proposal 3: Study ED thresholds selection when UE share its COT to gNB and  the scheme that UE can share its COT to the other UEs through gNB.

  - QC

- Proposal 4: Clarify first on the energy detection (ED) threshold used to perform LBT for UE-initiated COT before deciding the method for UE’s determination of the scheduled UL transmission (e.g. whether it is done based on shared-gNB COT or UE-initiated COT).

  - LG

| Question: What is your view on Proposals 1 to 4? |
| --- |
| Company | Comment |
| Futurewei | Use the same rules as in gNB FFP initiated COT. This discussion could be left for FFS. |
| CATT | We need consider EDT for UE-initiated COT and the detail should be FFS. |
| Nokia, NSB | These could be studied further, but the same principle as agreed in R16 for LBE could be used as a starting point. |
| Qualcomm | Proposal 3. |
| Huawei, HiSi | The proposals are related to the discussion on DL content in Section 2.6.1 (please see our observations stated therein) We support Proposal 1 based on that understanding |

### Consideration on processing time

With respect to processing time aspects in COT sharing, ETRI has proposed the following.

- Proposal 1: For gNB-to-UE COT sharing, define UE’s processing time required for DL burst detection and UL transmission preparation.

- Proposal 2: For UE-to-gNB COT sharing, consider defining processing time for gNB’s UL burst detection for UE power saving purpose.

| Question: What is your view on Proposals 1 and 2? |
| --- |
| Company | Comment |
| Futurewei | Not supported. We consider that the timing is already defined in the Rel-specs and it does not need additional definition. |
| Nokia, NSB | It is important that gNB knows the UE’s processing time required for DL burst detection, so that it can consider that when scheduling/configuring UL resources. It is less critical that the UE knows the processing time for gNB’s UL burst detection as the available power savings are minimal (due to relatively fast gNB processing time). |
| ETRI | The intention of proposal 1 is to further clarify the condition for UE to transmit UL in a shared gNB COT. For a given UL transmission, UE can only transmit the UL if it successfully detect a DL burst in the same gNB COT. However, currently, since the processing time for DL burst detection is generally undefined (only the PUSCH preparation time is in the spec), there should be an ambiguity that gNB does not know whether UE will 1) actually transmit the UL, or 2) fail to transmit the UL due to lack of processing time. This would impact the UL reliability performance. So we propose to define processing time for UE to perform DL burst detection and UL preparation. Agree with Nokia that Proposal 2 is less important. |
| Qualcomm | More clarification is needed to understand the detailed mechanism for proposal 1 and 2. |
| Lenovo/Motorola Mobility | Wondering what is the issue with Rel-16 operation that motivated proposal 1. |

### CP extension

With respect to CP extension for UE-initiated COT, companies have proposed and observed the following.

Proposal 1: Consider LBT type configuration for the configured UL resource in terms of whether the configured UL is allowed to initiate COT by UE.

- It is FFS whether some handling is needed to apply the CP extension for transmission of the configured UL at the beginning of FFP.

  - LG

Proposal 2: To guarantee continuous channel occupation, padding signals or repetition of transmitted channels may be needed to fill the gaps between multiple UL channels in a UE initiated COT.

  - Xiaomi

Observation 1: Multiple starting time offset for configured grant, which is configured as the amount of CP extension, can be reused to support UE-initiated COT.

Observation 2: It should be clarified that whether the difference of CP extension is called as the change of FFP or not.

Observation 3: If DG PUSCH is used for UE-initiated COT together with CG PUSCH, to support CP extension for multiple starting time offset as in CG PUSCH for DG PUSCH could be considered.

Observation 4: If the difference of CP extension is called as the change of FFP, the start of FFP might be always CG PUSCH if DG PUSCH does not have CP extension. If DG PUSCH supports CP extension, the amount of CP extension for DG PUSCH should be same as that configured to CG PUSCH.

- Panasonic

| Question: What is your view on Proposals 1 and 2 and observations? |
| --- |
| Company | Comment |
| Nokia, NSB | Proposal 1: we think this proposal should be linked to the discussion on Proposal 1 in section 2.2.2 (Support allowing only UEs with high priority data/control to initiate a COT for FBE) and Proposal 3-2 Alt-1 (as part of a CG UL configuration, enable/disable UE COT-initiating functionality for the CG UL transmissions aligned with the configured UE FFP boundaries). Proposal 2: we think this proposal is not needed. LBT failure for a 2nd UL transmission within a UE initiated COT (gap between 1st and 2nd transmission >16us) does not prevent the UE from performing LBT for a 3rd transmission within the UE-initiated COT, and to perform the transmission, in case LBT is successful. Observations 1-4: we think the whole use case of multiple starting time offsets for configured grants with resource allocation smaller than full bandwidth is not clear, as gNB has the possibility to FDM UEs in this case. Note that it is already agreed not to support multiple starting time offsets for configured grants with full bandwidth allocation. |
| ETRI | We have also raised an issue of CP extension for CG PUSCH in our tdoc. We think how to handle the CP extension when it is configured for CG-PUSCH that starts from the beginning of a UE FFP needs to be discussed (figure below). |
| Lenovo, Motorola Mobility | Proposal 1: Seems unnecessary if we allow configurability as we suggest in proposals 3-2 (2.3.1) and 6-4 (2.6.4). Proposal 2: Is CP extension considered as padding or repetition in this context? Not sure we need to consider anything other than CP extension. Another alternative that we also discussed in our contribution can be considered as well: “To guarantee continuous channel occupation, shifting of UL channel earlier in time could be considered to reduce the gap between multiple UL channels in a UE initiated COT.” |

### Capability, DL symbols within UL, etc.

Companies have discussed other aspects for UE-initiated COT with respect to capability, DL transmission with UL, UL to DL gap, etc.

Proposal 1: It is proposed to further investigate the scenario when DL symbols occur in the middle of an UL scheduled resource.

- TCL

Proposal 2: The UE shall support capabilities signaling to inform gNB that it can initiate COTs for semi-static channel access.

- FW

Proposal 3: In the case of UE-to-gNB COT sharing in semi-static channel access mode with a gap > 16us, gNB shall perform an additional CCA. Only when energy was detected with a level below the ED threshold level, gNB can start the transmission.

- Xiaomi

| Question: What is your view on Proposals 1 to 3? |
| --- |
| Company | Comment |
| Futurewei | Support Proposal 2 naturally. We are OK with proposal 3. |
| Nokia, NSB | Proposal 1: handling in this case should be similar to NR-U operation with LBE (R16). Proposal 2: ok but should be handled as part of R17 UE capabilities discussion in RAN2. Proposal 3: it is up to gNB implementation to live up to regulatory requirements in 5 GHz spectrum, i.e. gNB behavior should be according to the proposal but does not need top be captured in specifications. |
| Qualcomm | Proposal 2 is fine, but can be discussed in UE Feature discussion later. Proposal 3 seems to be required by regulation. |
| Huawei, HiSi | Proposal 1: We think this issue can be avoided by proper gNB scheduling Proposal 2: Can be discussed at later stage Proposal 3: We think it was already agreed that channel access procedures and conditions are same asthose for gNB-to-UE COT sharing Agreements: Conditions on the channel access procedures with respect to sensing duration and transmission gap for UE-initiated COT with UE-to-gNB COT sharing is similar as those for gNB initiated COT and gNB-to-UE COT sharing in Rel-16 by exchanging UE and gNB roles. |

## Discussion topic: NR-U and URLLC CG harmonization

Section below aims to capture the views with respect to the discussion topic, on high level.

Other proposals address additional details with respect to RRC parameters for CG harmonization.

Please if needed, prioritize the discussion of Main design issues.

### Main design issues

Agreements (RAN1#103-e):

Down-select one of the following options (target RAN1#104-e):

- Option 1: Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16.

- Option 2-a: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and cg-RetransmissionTimer-r16, respectively.

- Option 2-b: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and new parameter Y, respectively, where X and Y are different from cg-RetransmissionTimer-r16.

- Option 3: CG-UCI based procedures are supported for unlicensed. CG-DFI based procedures are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16

- Note: Procedures based on CG-UCI rely on UE including CG-UCI in CG PUSCH at least as in Rel-16 where the values of the respective fields of CG-UCI are decided by UE.

- Note: Procedures based on CG-DFI rely on automatic re-transmission on CG configuration and reception of CG downlink feedback information (DFI) in DCI for re-transmissions.

Agreements (RAN2#112-e):

From RAN2 perspective

1 	It is assumed that LBT failures only happen infrequently in UCE (unlicensed controlled environment).  A formal definition of UCE and its relationship to semi-static or dynamic access mode is not necessary in RAN2 specifications.

2	cg-RetransmissionTimer can be configured optionally for shared spectrum

3	When cg-RetransmissionTimer is configured, Rel-16 NR-U mechanism is used for HARQ process ID and RV selection.

4	When cg-RetransmissionTimer is not configured, Rel-16 URLLC mechanism may be used for HARQ process ID and RV selection.

5	As a baseline, HARQ processes sharing between multiple CGs are allowed when cg-RetransmissionTimer is configured as in Rel-16 NR-U.

6	HARQ processes sharing between multiple CGs are not allowed when cg-RetransmissionTimer is not configured.

7	FFS if LCH based prioritization can be configured with cg-RetransmissionTimer

8	The assumption for Rel-16 is that the network will not configure autonomousTx and cg-RetransmissionTimer simultaneously per cell.  No optimizations will be pursued to allow the two features be configured together in Rel-16.  No CR is needed for this for now.

9	If a configured grant is deprioritized and/or gNB didn’t get it (e.g. LBT failure and/or tx failure) then we should be able to autonomously re-transmit it.  FFS how to achieve it (using existing mechanisms should be considered as baseline)

Summary of companies view for above agreement:

- Option 1 (Aligned with RAN2 agreement):

  - E///, HW/HiSi, LG, Nokia, ETRI, vivo, CATT, Spreadtrum, OPPO

- Option 2a (Is it aligned with RAN2 agreement for CG-UCI?):

  - Apple, TDC, DCM, Spreadtrum, Panasonic, Sharp, Intel

- Option 2b (Is it aligned with RAN2 agreement for CG-UCI?):

  - Intel, QC, Samsung, Sony, IDC, Panasonic?, Sharp?

- Option 3 (Is it aligned with RAN2 agreement?):

  - ZTE, charter, TCL?, NEC?

| Question 1: Clarification needed whether Option 2a/2b/3 are aligned with RAN2 agreement and if not, whether RAN1 should consider these options. Question 2: What is your view on the alternatives? |
| --- |
| Company | Comment |
| Sony | Our understanding is the RAN2 agreement is a RAN2 perspective and so RAN1 still can take Option 2a, 2b or 3 if it is deemed beneficial. |
| vivo | We support option 1. According to RAN2 agreements, the cg-RetransmissionTimer is the trigger for UE performing the autonomous retransmissions requiring the CG-UCI and CG-DFI. Other options segment the features and result sub-optimal performance with introducing addition specification efforts and clarifications. Although RAN2 agreements says “from RAN2 perspective”, in the end, if RAN1 make different decisions from RAN2, we need to spend additional efforts to make RAN1 and RAN2 spec consistent. |
| Intel | As we mentioned during the GTW, our understanding is that the RAN2 agreement is only an assumption that has been made by RAN2 to move forward, and this is the reason why the agreement starts with “From RAN2 perspective”. RAN2 is actually relying on RAN1 to make the decision, and at this point all options are possible. As for the specific option to support, we prefer either option 2-a or 2b, with slight preference toward 2-b. While it is understood that these two options would lead to a fragmentation of the design, this would allow to cover a larger set of use cases and deployments and allow the network to optimally select the procedure to use, which clearly would allow to boost system performance. |
| CATT | We support Option 1 because option 1 aligns with RAN2 agreement. |
| LG | We are also supportive with Option 1 for the same reason with vivo. Considering UE complexity and specification impacts to implement various combinations of CG-UCI, CG-DFI and CG timer, we need to focus main use case rather than just introducing any workable variants. In case of Option 2-a and Option 3, it might be beneficial in terms of reducing DCI overhead (by enabling CG-UCI and disabling CG-DFI) or UL-SCH loss (by disabling CG-UCI and enabling CG-DFI). In this sense, those options can be considered further only if there is consensus to pursue the above benefits. |
| Panasonic | Our understanding of RAN2 agreement is that depending on higher layer parameter cg-RetransmisisonTimer is configured or not, the functions related to autonomous transmission on CG, i.e., CG retransmission timer, indication of HARQ process ID and RV, are used or not used. We think that these functions including DFI feature could be disabled in URLLC operation in unlicensed band since miss-detection probability at gNB is low and/or the environment where LBT failure probability is low. On the other hand, CG-UCI also include COT sharing information and the function related to COT sharing can be used to reduce LBT delay by using Cat.1 or Cat.2 LBT instead of Cat.4 LBT. If whole CG-UCI field is disabled (CG-UCI is disabled), delay can be increased because of the lack of COT sharing information. In our view, Option 2a/2b/3 are still aligned with RAN2 agreement if functions related to autonomous retransmission on CG and COT sharing (i.e., COT sharing information on CG-UCI) are separately enabled/disabled. |
| ZTE | The RAN2 agreement is only based on RAN2 perspective, and RAN2’s intention is to leave to RAN1 for decision. With support of CG-UCI while disabling CG-DFI for Option3, we agree that CG autonomous retransmission can not be supported. While the re-transmission can still be based on DG re-transmission. As we commented in GTW session, CG-UCI based procedure is more flexible because it allows UE to decide the HARQ-ID and RV instead of using the pre-defined rules as in Rel-16 URLLC, it allows multiple TB transmissions in one period, and it allows UE to report COT sharing information to gNB. These benefits could provide more robustness and flexibility, and therefore we don’t see a need to disable CG-UCI based procedure. |
| Nokia, NSB | We support option 1 due to its simplicity, and because it is fully in line with RAN2’s agreement |
| Sharp | We noticed the expression of “cg-RetransmissionTimer” in the RAN2 112-e agreement and thus it might be better to clarify the follows: For Rel-17 FBE, whether to reuse the parameter cg-RetransmissionTimer-r16 or not (e.g., introduce cg-RetransmissionTimer-r17) Does “cg-RetransmissionTimer” refer to both versions |
| ETRI | We suppot Option 1. Benefit of separating CG-UCI procedures and CG-DFI procedures is still questionable. |
| Qualcomm | We support option 2b. We have the same view as Sony, Intel, Panasonic, ZTE for RAN2 agreement. i. e., the RAN2 agreement is only an assumption that has been made by RAN2 to move forward, and this is the reason why the agreement starts with “From RAN2 perspective”. RAN2 is actually relying on RAN1 to make the decision, and at this point all options are possible. |
| OPPO | We support option1 due to it aligns with RAN2 agreement. |
| InterDigital | We support option 2b (or 2a). The use of CG-UCI should not be tied to the use of CG retransmission. As discussed in Proposal 7-1, CG-UCI could be used to indicated whether a CG transmission assumes a UE-initiated COT. Furthermore, the RAN2 agreement pertains only to HARQ Process ID and RV selection. |
| DOCOMO | We are fine with Option 1 for HPN and RV indication in CG-UCI. As pointed out in GTW session and also by Panasonic, CG-UCI also include COT sharing information. We thinks this should be separately enabled/disabled for flexibility |
| Samsung | Option 2-b. RAN2’s agreement does not conflict with option 2-a/2-b/3, RAN2 also open for CG-UCI/CG-DFI when cg-RetransmissionTimer is not configured, that’s why the wording is ‘may be’ rather than ‘is’ in RAN2’s agreement. And we also share the same understanding with Sony, Intel, Panasonic, ZTE and Qualcomm that RAN2 agreement is only based on RAN2 perspective. For IIOT, we mainly focus on well controlled environment which is typical scenario when cg-RetransmissionTimer is not configured. In this case, CG-UCI and CG-DFI still reduces latency, improve UL/PDCCH transmission efficiency. Therefore, we support separate configuration of cg-RetransmissionTimer and CG-UCI/CG-DFI. The reason for separate configuration for CG-UCI and CG-DFI is, CG-DFI can improve UL/PDCCH transmission efficiency and retransmission latency with/without CG-UCI. |
| Spreadtrum | We support Option 1 because option 1 aligns with RAN2 agreement. |
| Apple | Option 2-a The benefit of enabling CG-DFI without CG retransmission is not clear to us, because the UE would be able to retransmit even if it receives NACK on CG-DFI. So it makes sense that they are enabled/disabled together. On the other hand, enabling CG-UCI by itself is useful because it can better handle LBT failure. (We do acknowledge that if CG retransmission is enabled, CG-UCI needs to be enabled as well.) |
| HW/HiSi | Option 1 In addition to alignment with RAN2 agreement/understanding, when the cg-RetransmissionTimer is configured to allow for autonomous ReTx on CG resources, the UE should be able to perform the retransmission on the earliest resources after the timer expires and thus indicate the UE-selected associated HARQ information in the CG-UCI. If such indication mechanism is not enabled, the UE would at least have to wait for a transmission occasion wherein the time-domain resources match the HARQ ID |
| Moderator | @Sharp: This is up to RAN2. My understanding is that in general, if the associated functionalities remain the same, the same parameter can be reused for next release. Otherwise, r-17 would be introduced. @All: This discussion has become very complicated. Companies have different on impact of RAN2 agreements on RAN1 work. Mainly, two groups: Group 1: Intel, Sony, Panasonic, ZTE, Samsung, Qualcomm, IDC RAN2 agreement is only an assumption that has been made by RAN2 to move forward, and this is the reason why the agreement starts with “From RAN2 perspective”. RAN2 is actually relying on RAN1 to make the decision, and at this point all options are possible. IDC, Panasonic: The RAN2 agreement pertains only to HARQ Process ID and RV selection. Samsung: RAN2’s agreement does not conflict with option 2-a/2-b/3, RAN2 also open for CG-UCI/CG-DFI when cg-RetransmissionTimer is not configured, that’s why the wording is ‘may be’ rather than ‘is’ in RAN2’s agreement. Group 2: Vivo, Hw/HiSi, Nokia/NSB, CATT, LG, ETRI, OPPO, DCM, Spreadtrum Although RAN2 agreements says “from RAN2 perspective”, in the end, if RAN1 make different decisions from RAN2, we need to spend additional efforts to make RAN1 and RAN2 spec consistent. Supportive of Option 1 because it aligns with RAN2 agreement @All: It is not clear to me how to move forward. What is your view about following two actions? Send an LS to RAN2 to ask clearly how “From RAN2 perspective”, should be interpreted from RAN1. Is it as intel describes that RAN2 is actually relying on RAN1 to make the decision, and at this point all options are possible? Is it an agreement to be considered in specifications as vivo explains and RAN1 misalignment with RAN2 would cause additional across-WG work? ….. Impact analysis: RAN1 (specially proponent of Option 2a/2b-3) provide analysis that IF RAN1 assumes to consider RAN2 agreement, whether/how any of the options 2a/2b-3 would be affected. Please share your view and preferably analysis. |
| Sony | Perhaps we can decide based on what RAN1 wants rather than what RAN2 assumed. And if RAN1 decision matches RAN2’s then there is nothing to do. If not we send LS to RAN2 saying “From RAN1 perspective” we prefer Alt-X. |
| Moderator | @All: We can also proceed as Sony suggested. Please note that we aimed to down-select this meeting. It seems views are similar to the last meeting. I copy here the companies’ view. Perhaps chairman can help the progress. Companies’ view: Option 1 (Aligned with RAN2 agreement): E///, HW/HiSi, LG, Nokia, ETRI, vivo, CATT, Spreadtrum, OPPO Option 2a (Is it aligned with RAN2 agreement for CG-UCI?): Apple, TDC, DCM, Spreadtrum, Panasonic, Sharp, Intel Option 2b (Is it aligned with RAN2 agreement for CG-UCI?): Intel, QC, Samsung, Sony, IDC, Panasonic?, Sharp? Option 3 (Is it aligned with RAN2 agreement?): ZTE, charter, TCL?, NEC? |
| Huawei, HiSilicon | We think it is important to understand the technical rational behind the ‘RAN2 perspective’. Therefore, in our view, it is OK to send an LS to RAN2, but it should not be focused only on how “From RAN2 perspective” should be interpreted from RAN1, it should also ask for the technical rational that led to that agreement. In our understanding, when the cg-RetransmissionTimer is configured, the main purpose is to allow for autonomous ReTx on CG resources after the timer expires. However, if the ‘CG-UCI based procedures’ are disabled by Option 2-a/2-b, including the HARQ ID and RV selection, the UE would not be able to perform the retransmission until the TO that matches the HARQ ID as opposed to the earliest TO after the timer expires. This in fact defeats the purpose of enabling autonomous CG retransmissions for the URLLC use cases. This is, in our opinion, the main coupling point between configuring the cg-RetransmissionTimer and enabling the CG-UCI based procedures. While Option 1 allows for operation in the unlicensed spectrum based on URLLC CG , Option 3 mandates the use of CG-UCI based procedures even though the cg-RetransmissionTimer is not configured and not mandated. |
| Intel | We agree with Sony’s statement.We do not think an LS reply is needed, since as per our understanding RAN2 is relying on RAN1 to decide, and they only made assumptions on what RAN1 may prefer, but ultimately it is up to RAN1 to decide. So sending an LS would just postpone the decision in RAN1, rather facilitating it. The agreement is RAN2 is very clear: “From RAN2 perspective”. However, if this may help to down-select one of the options we would be glad to support. As for the preference among options, we would be OK with either Option 2a or 2b. As mentioned the CG-UCI, CG-DFI and cg-retransmissionTimer are meant to solve different issues. By enabling or disabling separately each of them it would be possible to support a wider range of use cases, and allow the network to overcome each issue separately which would lead to a better system performance. |
| Apple | We also feel it may be counter-productive to ask for confirmation from RAN2, and we share the same view as Sony that we can make a decision from RAN1 perspective. To respond to HW/HiSi’s comments, we also agree that if cg-RetransmissionTimer is configured, CG-UCI based procedures need to be enabled as well. However, we think CG-UCI based procedures can be enabled by itself without configuring cg-RetransmissionTimer. |
| CATT | We prefer Option 1 because option 1 is aligned with RAN2 agreement. From our perspective, the main difference between option 1 and other options (Option 2-a/Option 2-b/ Option 3) is whether CG-UCI based procedures and CG-DFI based procedures are allowed to be enabled/disabled independently. For Option 2-a, when CG-DFI based procedure is enabled by cg-RetransmissionTimer but the CG-UCI based procedures is disabled, gNB can’t execute HARQ process combination because gNB doesn’t know the HPID selected by UE. When CG-UCI based procedure is enabled but CG-DFI based procedure as well as cg-RetransmissionTimer is not configured, gNB doesn’t know the HPID and NR-U autonomous reTx does not apply for this case since cg-retransmissionTimer is not configured if gNB decodes neither CG-UCI nor TB. For Option 2-b, if cg-RetransmissionTimer is configured (the NR-U path) and CG-DFI is not configured, when CG-DFI is not configured, its functionality could be replaced by gNB-scheduled retransmissions. For the successful transmission, without the gNB’s feedback (CG-DFI = ACK), the UE will always trigger an autonomous ReTx upon cg-RetransmissionTimer expiry. So in this case, this configuration does not work and the cg-RetransmissionTimer should be linked with the CG-DFI based procedures, at least for acknowledging the successful reception of the CG to prevent from triggering an autonomous ReTx. For Option 3, CG-UCI based procedures are always supported for the URLLC operation in unlicensed band. CG-DFI based procedures are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer. Option 3 is one special case of Option 2-a. When CG-UCI based procedure is enabled but CG-DFI based procedure as well as cg-RetransmissionTimer is not configured, Option3 has the similar issue with option 2-a. |
| vivo | We think sending LS is not necessary. But we share the same views with HW that if LS needs to be sent to RAN2, we should ask for the technical reason why RAN2 made such agreements from RAN2 perspective. As mentioned, if RAN1 made a different decision, additional efforts and inter-action between RAN1 and RAN2 will be involved to resolve the inconsistency in terms of performing autonomous ReTx if there is no CG-UCI and DFI. As seen in 38.321, current the autoRe-Tx can use the CG configuration different from the one used for initial transmission, hence the UE needs to inform NW by CG-UCI about the HARQ ID, NDI. Without CG-UCI, how to perform such re-Tx and this re-Tx is beneficial for recovering the data with low latency. “If cg-RetransmissionTimer is configured, retransmissions with the same HARQ process may be performed on any configured grant configuration if the configured grant configurations have the same TBS.” The main purpose for CG-UCI is used for Re-Tx, no benefit for CG-UCI is only used for initial Tx compared to IIoT way by using the equation to get the HARQ ID, it adding more payload. |
| Panasonic | We agree to Intel’s comment on sending LS to RAN2. For Option 2, we agree to Intel and Apple that CG-UCI based procedures can be enabled by itself without configuring cg-RetransmissionTimer. |
| Samsung | We agree with Sony’s statement that we can focus on what RAN1 wants. Besides, we checked with RAN2 colleagues, actually RAN2 prefer to wait for RAN1’s decision for (1) HARQ Process ID selection when CGRT is not configured (2) dependency of configuring DFI and CGRT. You may check Rapporteur Summary in section 2.5/3.5 in R2-2102073. We prefer option 2b. As commented, it is beneficial to support separate configuration for CG-UCI, CG-DFI and cg-retransmissionTimer, because these features is useful in different scenarios. CG-UCI can reduce latency for initial transmission when CG-DFI and cg-retransmissionTimer are not configured, and CG-UCI also reduces latency for retransmission when CG-DFI is configured, or cg-retransmissionTimer is configured, or both CG-DFI and cg-retransmissionTimer is configured. CG-DFI can reduce PDCCH overhead, improve UL resource efficiency by early termination, and reduce retransmission latency if multi-slots is configured for CG PUSCH, when CG-UCI and cg-retransmissionTimer are not configured. CG-DFI also reduces retransmission latency when CG-UCI is configured. CG-DFI also helps to reduce the impact of CG PUSCH miss-detection when cg-retransmissionTimer is configured. It can be seen, without cg-retransmissionTimer, CG-CUI and CG-DFI is still beneficial for initial and retransmission, because the cg-retransmissionTimer is mainly for retransmission without receiving DFI or UL grant, while autonomous retransmission is still supported by CG-DFI based procedure, and flexible HARQ ID selection is supported by CG-UCI. |
| DOCOMO | As commented above, we are fine with Option 1 for HPN and RV indication in CG-UCI for efficient retransmission of CG-PUSCH using CG-DFI. For initial transmission, URLLC CG has enough flexibility for low latency. However, CG-UCI also includes COT sharing information. We think this should be separately enabled/disabled for flexibility, e.g, operation with URLLC CG including COT sharing information |
| Sharp | Thank you Sorour for the response on the parameter name. Clear on that. We agree with the suggestions from Sony and Moderator. Our preference is Option 2a or 2b. At this phase, will the down-selection become easier if Option 2a and 2b are merged into Option 2? |
| LG | We prefer Option 1. The reason is that the following two sentences are clearly stating that CG retransmission timer and CG-UCI based procedure are coupled, that is, if CG retransmission timer is ON, then CG-UCI based procedure is ON as in Rel-16 NR-U if CG retransmission timer is OFF, then CG-UCI based procedure is OFF as in Rel-16 URLLC 3 When cg-RetransmissionTimer is configured, Rel-16 NR-U mechanism is used for HARQ process ID and RV selection. 4 When cg-RetransmissionTimer is not configured, Rel-16 URLLC mechanism may be used for HARQ process ID and RV selection. Among four options, we think Option 1 is the only option where CG retransmission timer and CG-UCI based procedure are coupled. Nevertheless, if there are still different interpretations among the companies in RAN1, we are fine with sending LS to RAN2 for clarification if companies are also OK, in order to avoid further discussions under different understanding to each other or with RAN2. |
| Nokia, NSB | We support Option 1 as it is fully aligned with RAN2 agreements |
| Qualcomm | We support Option 2b and share the same view as Samsung. |
| ETRI | We prefer Option 1 because Option 1 is considered to be sufficient to satisfy the Rel-16 URLLC requirements in unlicensed controlled environments. Moreover, Option 1 is aligned with RAN2 decision. We agree with Sony that RAN1 can make decision on this issue, and we don’t think the LS to RAN2 is needed at the current stage. |
| Moderator | @Samsung: Thank you for sharing the update from RAN2! That makes the situation easier. @All: Please see the following as Samsung kindly pointed out: Rapporteur Summary in section 2.5/3.5 in R2-2102073 It is clear from the RAN2 summary that we’d better continue our work and decide for an option. It is pity we spent time to understand RAN2 agreement ☹ So, we are back to square one. Below is the updated companies view. You all exchanged your arguments and, there is no change. Please let me know if there is any adjustment to reach a consensus. Summary of companies view on the options for down-selection in the following agreement: Option 1: E///, HW/HiSi, LG, Nokia, ETRI, vivo, CATT, Spreadtrum, OPPO Option 2a: Apple, TDC, DCM, Spreadtrum, Panasonic, Sharp, Intel Option 2b: Intel, QC, Samsung, Sony, IDC, Panasonic, Sharp, Qualcomm Option 3: ZTE, charter, TCL?, NEC? Agreements (RAN1#103-e): Down-select one of the following options (target RAN1#104-e): Option 1: Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16. Option 2-a: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and cg-RetransmissionTimer-r16, respectively. Option 2-b: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and new parameter Y, respectively, where X and Y are different from cg-RetransmissionTimer-r16. Option 3: CG-UCI based procedures are supported for unlicensed. CG-DFI based procedures are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16 Note: Procedures based on CG-UCI rely on UE including CG-UCI in CG PUSCH at least as in Rel-16 where the values of the respective fields of CG-UCI are decided by UE. Note: Procedures based on CG-DFI rely on automatic re-transmission on CG configuration and reception of CG downlink feedback information (DFI) in DCI for re-transmissions. |
| Moderator | During GTW on Feb 5th, the situation of this topic was briefly discussed with Chairman. As it the meeting started, wondering how to interpret RAN2 agreement as the discussion above shows, when we realized later on that RAN2 during this week has summarized that RAN1 can discuss and decide on the option which was the preferred approach by many companies in RAN2. With respect to RAN1, the situation has not changed with companies’ preferences as can be observed above. However, it is clear that a decision should be made in RAN1 soon. As suggested by chairman, few questions are listed below to facilitate the task of comparison between different options for the purpose of decision making and down-selection. As the contributions and discussions in this meeting show, the key questions with respect to complexity, specification impact and feature benefits, were already discussed. However, the justifications and arguments from proponent of an option can more targeted to address the concern of the opponent of an option. For example, some companies expressed that it is not clear the benefit in realistic use cases for any option that option 1 is introduced. The questions are listed based on the inputs provided above and can be updated and improved if needed. Please feel free to provide suggestions to update/improve questions before end of meeting 104-e. @All: Companies are encouraged in the next meeting to continue providing views on at least the following aspects for CG harmonization options (Option 1/2a/2b/c) to facilitate the task of comparison between different options: Assessment of additional value for IIoT/URLLC uses cases in unlicensed band For assessment, using realistic use cases are encouraged. Assessment of complexity and specification impact For assessment, considering enabling/disabling corresponding RRC parameter(s) jointly or independently, when applicable are encouraged. |
| Huawei, HiSi | In the agreement below, the note defines the ‘CG-DFI based procedures’ to “rely on automatic re-transmission on CG configuration and reception of CG downlink feedback information (DFI) in DCI for re-transmissions”. As such, if the CG-DFI based procedures are enabled, both autonomous CG retransmission and CG-DFI are enabled Q1.1 Since autonomous CG retransmissions cannot happen without configuring the cg-RetransmissionTimer, do you think it is possible to enable the ‘CG-DFI based procedures’ without configuring the cg-RetransmissionTimer? Q1.2 Also, is it possible to configure the cg-RetransmissionTimer, but disable both the autonomous CG retransmission and the CG-DFI by disabling the ‘CG-DFI based procedures’ ? Q1.3 Based on the questions above, can the benefits of the CG-DFI be attained without configuring the cg-RetransmissionTimer as hoped from Option 2-b? Assuming that the ‘CG-UCI based procedures’ can be disabled while CG retransmissions are enabled, what would be the benefits of such operation mode given the dependency of the HARQ ID on time-domain resources? Assuming that the ‘CG-UCI based procedures’ can be enabled without configuring the cg-RetransmissionTimer; based on the current spec(quoted below), RV determination cannot be done by the UE, meanwhile the NDI filed is also not useful as CG retransmissions are disabled: Q3.1 What are the benefits attained from using the CG-UCI in such a case? Q3.2 If the key benefit is multiplexing of multiple TBs in one period, could such a benefit be matched, for instance, by configuring shorter CG periodicity without incurring the overhead of CG-UCI in every PUSCH? The higher layer parameter repK-RV defines the redundancy version pattern to be applied to the repetitions. If cg-RetransmissionTimer is provided, the redundancy version for uplink transmission with a configured grant is determined by the UE. If the parameter repK-RV is not provided in the configuredGrantConfig and cg-RetransmissionTimer is not provided, the redundancy version for uplink transmissions with a configured grant shall be set to 0. If the parameter repK-RV is provided in the configuredGrantConfig and cg-RetransmissionTimer is not provided, for the nth transmission occasion among K repetitions, n=1, 2, …, K, it is associated with (mod(n-1,4)+1)th value in the configured RV sequence. |
| vivo | We would like to use following table for making questions to understand better each options. Feature combinations for each option (Note: 0 means the feature is disabled/not configured, 1 means enabled/configured) CG-UCI CG-DFI cg-RetransmissionTimer-r16 IIoT like mechanism: option 1 0 0 0 Opt-2b: combination#1 0 0 1 Opt-2b: combination#2 0 1 0 Opt-2b and Opt-2a: combination#3 0 1 1 Opt-2b, Opt-2a and Opt-3 combination#4 1 0 0 Opt-2b and Opt-3 combination#5 1 0 1 Opt-2b and Opt-3 combination#6 1 1 0 NR-U like mechanism: option 1 1 1 1 For each feature combinations as shown above, How does it work? What is the use case(s)/benefits? Potential specification impacts |
| CATT | For Option 2-a/opion 2-b, we have questions as follows: 1.Why need we revert RAN2’s agreement? 2.What is the benefits on separate configuration on CG-DFI and CG-UCI from RAN1 perspective? 3.What is work mechanism on separate configuration on CG-DFI and CG-UCI? 4.What’s potential specification impacts? |
| ZTE | For Option 1/2a/2b, what are the benefits of disabling CG -UCI based procedure? Because it is more flexible at least in the following aspects: Multiple TBs can be transmitted within a period against possible LBT detection failure. The initial transmission starts at a transmission occasion as long as LBT succeeds for low latency. On the other hand, URLLC based procedure has following restrictions. If a configured grant configuration is configured with startingFromRV0 set to 'off', the initial transmission of a transport block may only start at the first transmission occasion of the K repetitions. Otherwise, the initial transmission of a transport block may start at - the first transmission occasion of the K repetitions if the configured RV sequence is {0,2,3,1}, - any of the transmission occasions of the K repetitions that are associated with RV=0 if the configured RV sequence is {0,3,0,3}, - any of the transmission occasions of the K repetitions if the configured RV sequence is {0,0,0,0}, except the last transmission occasion when K≥8. Note, regarding ‘If cg-RetransmissionTimer is provided, the redundancy version for uplink transmission with a configured grant is determined by the UE’, we think it doesn’t have to be kept for Option 3 in Rel-17. It carries COT sharing information. At least in LBE access mode, UE can share the COT with gNB for DL transmissions. It allows HARQ sharing among CG configurations. |

### Other design issues

Proposal 1:  cg-RetransmissionTimer can be configured for each configured grant independently.

- OPPO

Proposal 2: For harmonizing UL CG enhancements in Rel-16, if the higher-layer parameter cg-RetransmissionTimer-r16 is provided in ConfiguredGrantConfig, NR-U CG enhancements shall be adopted, otherwise, URLLC CG enhancements shall be used instead.

- E///, HW/HiSi

Proposal 3: Support configuration of harq-ProcID-Offset2 for operation in unlicensed spectrum

- E///, HW/HiSi

Proposal 4: For dynamic channel access mode, configuration of cg-RetransmissionTimer should be optional when configured grant Type 1 or Type 2 are configured on unlicensed spectrum.

- E///, ZTE, DCM

- Not support: QC

Proposal 5: Support configuration of phy-PriorityIndex field for CG operation in unlicensed band.

- vivo

Proposal 6: It is necessary to enhance the cg-UCI-Multiplexing field to support CG using NR-U like mechanism for URLLC traffic by taking into account intra-UE prioritization/multiplexing.

- vivo, Nokia, ZTE

| Question: What is your view on Proposals 1 to 6? |
| --- |
| Company | Comment |
| vivo | We would like to suggest prioritizing the discussion on proposal 6, proposal 5, and proposal 1. Proposal 2 and proposal 3 are related to discussions/conclusions in section 2.11.1. Proposal 4 from our understanding do not need to be discussed for controlled environment using FBE mode. We support proposal 6 and proposal 5. For proposal 1, we would like to make the clarification on whether the cg-RetransmissionTimer-r16 is configured per CG configuration or per cell. |
| CATT | We have the same view with VIVO and proposal 2 & proposal 3 are related to discussions/conclusions in section 2.11.1 |
| LG | Proposal 1: open Proposal 2: supportive Proposal 3: open Proposal 4: not support Proposal 5: open Proposal 6: not clear On Proposal 6, it is necessary to clarify what is the intention of it, for example, whether CG-UCI itself needs to be enhanced for CG itself or CG-UCI needs to be considered for the case of intra-UE multiplexing. |
| Nokia, NSB | P1: to our understanding this is already supported P2: We support this P3: We support this (when cg-RetransmissionTimer-r16 is NOT provided) P4: We support this P5: We support this at least when cg-RetransmissionTimer-r16 is NOT provided P6: As a proponent, we would like to clarify that the field may not need to be “enhanced“, but the priority an multiplexing rules associated with UCI transmission may need to be clarified |
| Qualcomm | The discussion here will be conditioned on the outcome of 2.11.1 Proposal 1: open Proposal 2: not support Proposal 3: open Proposal 4: not support Proposal 5: not clear Proposal 6: not clear Proposal 6 and 5 may be out of scope of this section and can be discussed in multiplexing section. |
| OPPO | P1: Supportive due to it keeps the same as Rel-16 P2: Supportive except enhancements on PUSCH repetition. P3: Open P4: Supportive P5: Not supportive. Physical prioritization is out of scope. If physical prioritization is supported for CG only, system could not work well due to dynamic scheduling does not support physical prioritization. |
| InterDigital | P1: We support P2: We do not support P3: We support P4: We support P5: Not clear P6: We support |
| Huawei, HiSi | We support proposals 2 and 3 For Proposal 4, we do not see the need for it given the operation is in controlled environment |

## Discussion topic: Enhancements on PUSCH repetition

The proposals below, aim to capture the views with respect to the discussion topic, on high level.

Proposal 1:

- PUSCH repetition Type B should be supported for unlicensed band operation when using NR IIoT Rel-16 based CG

  - FFS whether/how to enhance

- Nokia, Samsung, HW, QC, Intel, E///, LG, ZTE, Apple, ETRI, vivo, OPPO, WILUS, Lenovo/MOT

Proposal 2:

- Decide whether the use of PUSCH repetition Type B together with NR-U based multi-slot allocations should be supported.

  - Yes: QC, Intel, Samsung

  - No: Nokia, HW/HiSi, Samsung?

Proposal 3:

- Decide whether the use of PUSCH repetition type-A together with NR-U based multi-slot allocations (non-back-to-backType A) should be supported.

  - Yes: Samsung?, QC

  - No: Nokia, ZTE, Intel, Samsung

| Question: What is your view on Proposals 1 to 3? |
| --- |
| Company | Comment |
| Sony | We support Proposal 1. |
| vivo | We support proposal 1 without further optimization; For proposal 2, we do not support to use of PUSCH repetition Type B together with NR-U based multi-slot allocations. For proposal 3, we do not support the use of PUSCH repetition type-A together with NR-U based multi-slot allocations. |
| Intel | We support both proposal 1 and 2, but we do not support proposal 3. As we described in our tdoc, even if Type A is further enhanced for unlicensed operation, LBT overhead may be still unacceptable for URLLC use cases, given that gaps across slots are often unavoidable. |
| CATT | We support proposal 1. |
| LG | We support Proposal 1. In addition, as explained in R1-2100882, an unified RA scheme can be considered to cover PUSCH repetition type A as well. |
| Panasonic | We support Proposal 1. |
| ZTE | We support Proposal 2. Repetition type B allows back-to-back repetitions with segmentation across the slot boundary or invalid symbols, which can provide lower latency. NR-U based multi-slot allocations can increasing probability of LBT success. |
| Nokia, NSB | P1: We support this P2: We do not support this, as it complicates specifications, while the use case is unclear P3: We do not support this since it would complicate channel access design and the use case for this mode of operation on unlicensed spectrum is unclear |
| ETRI | We support Proposal 1. |
| Qualcomm | We support proposal 1/2/3. For proposal 2/3, we believe the URLLC feature can be easily introduced to NR-U type CG-PUSCH. |
| OPPO | We support proposal 1. Yes for proposal 2 In Rel-16 NR-U, Continuous transmission can be achieved by multiple configured grants or appropriate resource allocation for CG. However, it is not always feasible. According to current spec, TB in different configured grant except for auto-retransmission case should be different. However, multiple TBs are not always offloaded from MAC in succession. In some cases, only one TB is offloaded, and then later configured grant is idle and resource allocation interrupts. So to support continuous transmission more flexible, Type B PUSCH repetition scheme in NR configured grant should be considered in unlicensed band. However, multi-slot allocations can improve probability of LBT success. So PUSCH repetition Type B together with NR-U based multi-slot allocations should be supported. |
| DOCOMO | We support Proposal 1 without any enhancement. We don’t support Proposal 2 or 3 with the same reason as Nokia |
| Lenovo, Motorola Mobility | we support both proposal 1 and proposal 2 |
| Samsung | We support proposal 1, i.e. Rel-16 URLLC type-B repetition can be used without combination of NR-U. We also support proposal 2, i.e. the combination of Rel-16 URLLC type-B and NR-U multi-slot allocation. We don’t support proposal 3, because Rel-16 URLLC type-A repetition is already can be implemented by NR-U multi-slot allocation by configuration. |
| Huawei, HiSi | Our views are properly captured for Proposals 1 and 2 Our position is NO for Proposal 3 |

# References

| 1 | R1-2100054 | Further considerations on UE initiated COT for FFP | FUTUREWEI |
| --- | --- | --- | --- |
| 2 | R1-2100103 | Discussion on unlicensed band URLLC/IIoT | ZTE |
| 3 | R1-2100183 | Enhancements for unlicensed band URLLC/IIoT | OPPO |
| 4 | R1-2100229 | Uplink enhancements for URLLC in unlicensed controlled environments | Huawei, BUPT, China Southern Power Grid, HiSilicon |
| 5 | R1-2100270 | Enhancements for IIoT/URLLC on Unlicensed Band | Ericsson |
| 6 | R1-2100378 | Enhancements for unlicensed band URLLC/IIoT | CATT |
| 7 | R1-2100438 | Enhancements for unlicensed band URLLC/IIoT | vivo |
| 8 | R1-2100543 | Enhancements for unlicensed band URLLC/IIoT | TCL Communication Ltd. |
| 9 | R1-2100576 | On the enhancements for unlicensed band URLLC/IIoT | MediaTek Inc. |
| 10 | R1-2100626 | UL enhancements for IIoT/URLLC in unlicensed controlled environment | Nokia, Nokia Shanghai Bell |
| 11 | R1-2100651 | Discussion on enhancements to URLLC/IIoT in unlicensed band | Intel Corporation |
| 12 | R1-2100691 | Enhancements for unlicensed band URLLC/IIoT | NEC |
| 13 | R1-2100791 | Discussion on enhancements for unlicensed band URLLC/IIoT | Spreadtrum Communications |
| 14 | R1-2100857 | Considerations on unlicensed URLLC | Sony |
| 15 | R1-2100882 | Discussion on unlicensed band URLLC/IIOT | LG Electronics |
| 16 | R1-2100995 | Enhancements for unlicensed band IIoT/URLLC | Lenovo, Motorola Mobility |
| 17 | R1-2101015 | Enhancements for unlicensed band URLLC/IIoT | Panasonic Corporation |
| 18 | R1-2101076 | Enhancements for unlicensed band URLLC/IIoT | ETRI |
| 19 | R1-2101115 | Enhancement for unlicensed band URLLC/IIoT | Xiaomi |
| 20 | R1-2101203 | Enhancements for unlicensed band URLLC/IIoT | Samsung |
| 21 | R1-2101291 | Enhancements for unlicensed band URLLC/IIoT | InterDigital, Inc. |
| 22 | R1-2101333 | Unlicensed spectrum operation for URLLC/IIoT | Charter Communications |
| 23 | R1-2101380 | URLLC uplink enhancements for unlicensed spectrum | Apple |
| 24 | R1-2101461 | Uplink enhancements for URLLC in unlicensed controlled environments | Qualcomm Incorporated |
| 25 | R1-2101540 | Enhancements for unlicensed band URLLC/IIoT | Sharp |
| 26 | R1-2101614 | Discussion on enhancements for unlicensed band URLLC | NTT DOCOMO, INC. |
| 27 | R1-2101676 | Discussion on enhancement for unlicensed URLLC/IIoT | WILUS Inc. |

# Appendix

## List of observations and proposals in contributions

- FFP parameters configuration -periodicity and offset

- Additional transmission conditions in idle periods

- RRC enabling COT initiation functionality

- COT-initiator determination

- COT-initiation control/cancelation/overriding

- Scheduling and UE-to-gNB COT restrictions

- Indication of UE-initiated COT to gNB

- UE-to-UE COT sharing via gNB

- UE-initiated COT in Inactive/Idle mode

- Other FBE topics (ED sensing threshold)

- Other FBE topics (Processing time)

- Others FBE topics (CP extension)

- Others FBE topics (Capability, DL within UL, etc.)

- NR-U and URLLC CG harmonization

- Enhancements on PUSCH repetition

### R1-2100229	Huawei, BUPT, China Southern Power Grid, HiSilicon	Uplink enhancements for URLLC in unlicensed controlled environments

Proposal 1: For IIoT/URLLC operation in unlicensed spectrum, providing the UE with FFP parameters by SIB-1 is not supported

Observation 1: For IIoT/URLLC operation in unlicensed spectrum, transmission of initial access signals/channels is not an adequate use case for UE-initiated CO and it should be rather conducted within the gNB-initiated CO.

Observation 2: For IIoT/URLLC operation in unlicensed spectrum, enhancements in RRC_CONNECTED mode are needed whereas enhancements only useable for IDLE/INACTIVE are not needed.

Proposal 2: For IIoT/URLLC operation in unlicensed spectrum, UE-initiated semi-static CO is not supported when the UE is in IDLE/INACTIVE mode.

Proposal 3: For UE-initiated semi-static CO in a given unlicensed channel, the UE should be configured with an offset to the beginning of the latest gNB frame in the same channel.

Observation 3: If the gNB and the UE have different FFP periodicities, Pg and Pu, both the gNB and the UE need to observe the COT and idle period interactions over a period of Po =LCM{Pg , Pu} where LCM is the least common multiple.

UE will have to monitor DL for gNB COT initiation and observe COT interaction/idle period rules at a different set occasions in each UE FFP over the period Po which is generally much longer than FFPu, thus defeating the purpose of providing more flexibility to the UE.

Observation 4: UEs of different periodicities would not be aware of the FBE frame start points of each other, avoiding mutual blocking/collisions among these UEs through gNB configuration becomes quite intricate if not infeasible in some cases.

Observation 5: Configuring the UEs to reuse the gNB’s frame period to initiate respective semi-static COs in the same channels attains the following benefits:

Reduces UE complexity and simplifies observing the COT and idle period interaction rules;

Simplifies avoidance of mutual blocking between UEs configured with different offsets

Observation 6: As long as there is no rule specified to ensure that the integer multiple/inter-factor relationship is maintained in any combination of Pg and Pu configured to the UE, the UE implementation cannot expect that such relationship is maintained, even when gNB exploits it.

Observation 7: Specifying a rule to configure FFPg and FFPu in such way that the longer periodicity is an integer multiple of shorter periodicity, offers a reasonable trade-off between flexibility and UE complexity (Po = MAX{ Pg , Pu } ≤ 10ms), while the flexibility for the configurable combinations of FFPu and FFPg is still very large.

Proposal 4: For UE-initiated semi-static CO in a given unlicensed channel, the periodicity of the UE’s FFP is an integer multiple or inter factor of gNB’s FFP in the same channel.

Observation 8: For gNB to control the collisions/blocking between UEs on the same channel, the existing mechanism for UL cancellation cannot be applied since it is cell-specific group common signaling and would result in cancelling the UL resources to be used in the subsequent frame for another UE.

Proposal 5: For UE-initiated semi-static CO in a given unlicensed channel, the UE should be provided with a parameter to limit its COT to an indicated duration such that it ends before the idle period/CCA of a subsequent frame for another UE in the same channel.

Proposal 6: For determining the COT initiator for configured UL transmissions in semi-static channel access, support Alt-a in the agreement of RAN1#103-e

A clarification should be provided in relation to the above agreement from RAN1#102-e

Proposal 7: For determining the COT initiator for scheduled UL transmissions in semi-static channel access, support Alt. 3 (Based on a predetermined rule(s)) in the agreement of RAN1#103-e.

Proposal 8: For semi-static channel access, sharing the UE initiated CO to other intra-cell UEs, i.e., for UL transmissions, through the gNB is not supported.

Observation 9: In semi-static channel access mode, the calculation of ED threshold is the same as in dynamic channel access mode. Given the operation is intended for unlicensed controlled environment;

If the gNB shares the CO initiated by the UE without adjusting the EDT for transmitting unicast user plane data to the same UE, there would not be an impact to intra-operator coexistence

However, if the gNB is allowed to share the CO initiated by the UE without adjusting the EDT for transmitting unicast user plane data to other UEs as well, it would be advantageous for the gNB to rely on sharing a UE initiated CO except for critical broadcast signals and channels, and there would be an impact to intra-operator coexistence

Proposal 9: For semi-static channel access in unlicensed controlled environment, support gNB sharing of the CO initiated by the UE without adjusting the EDT, for transmissions including unicast user plane data to the same UE.

Observation 10: According to RAN2 agreements, the ‘CG-UCI based procedures’ and the ‘CG-DFI based procedures’ defined in RAN1 discussions shall be both enabled and disabled using the cg-RetransmissionTimer-r16.

Proposal 10: Support Option 1 to align with RAN2 agreements, i.e., both ‘CG-UCI based procedures’ and ‘CG-DFI based procedures’ are enabled/disabled using the cg-RetransmissionTimer-r16.

Proposal 11: Support configuration of harq-ProcID-Offset2 for operation in unlicensed spectrum when the cg-RetransmissionTimer-r16 is not configured.

Observation 11: Either PUSCH repetition type B, or NR-U multi-slot and multi-PUSCH per slot allocation under PUSCH repetition type A, are suitable for configuring consecutive PUSCH transmissions without gaps.

Proposal 12: Combination of Rel-16 PUSCH repetition and NR-U multi-slot allocation is not supported.

Observation 12: For UE-initiated semi-static CO using CG, neither URLLC nor NR-U can benefit from the flexibility in starting the CG transmission since the whole FFP would be skipped if LBT fails at the beginning of an FBE frame.

Observation 13: Rel-16 URLLC and NR-U CG mechanisms related to HARQ procedures are comparable when operating in an unlicensed controlled environment where LBT failures are unlikely to occur.

Observation 14: While not restricted to be used with other NR-U features, FDRA Type 2 is suitable to fulfill the OCB and PSD requirements in the unlicensed channel compared to FDRA Type 0/1.

Observation 15: For supporting IIoT/URLLC transmission with CG in unlicensed controlled environment in Rel-17, there is no need to support a combination of the Rel-16 NR-U and URLLC enhancements.

Proposal 13: For harmonizing UL CG enhancements in Rel-16, if the higher-layer parameter cg-RetransmissionTimer-r16 is provided in ConfiguredGrantConfig, NR-U CG enhancements shall be adopted, otherwise, URLLC CG enhancements shall be used instead.

### R1-2100651	Intel Corporation	Discussion on enhancements to URLLC IIoT in unlicensed band

Proposal 1: When the starting position of both a g-FFP and UE’s FFP is the same, the starting position of the u-FFP within two radio frames starts from an even radio frame.

Proposal 2: The value of the u-FFP value is chosen from the following set of values: {1, 2, 2.5, 4, 5, 10}.

Proposal 3: In order to reduce complexity at the UE, the UE shall assume that over time its FFP shall be always chosen so that this is an integer factor or a multiple of the current g-FFP value.

Proposal 4: A new RRC parameter is introduced to explicitly configure the u-FFP.

Proposal 5: When a UE operating as initiating device acquires its FFP, in any circumstances the ED threshold used to determine whether the channel is busy or idle is calculated solely based on the UE’s transmit power.

Proposal 6: When a UE operates as an initiating device, this is allowed to share its FFP with its associated gNB, and the gNB is allowed both control and data transmissions as long as a DL burst contains at least a transmission per switching point which is dedicated for the UE that initiated that FFP.

Observation 1: A gNB is not allowed to schedule UL transmissions within a shared u-FFP rather than those for the UE that originally initiated that FFP.

Proposal 7: For 2-step RACH procedure and for semi-static channel access mode, a UE is allowed to initiate its own FFP at least when transmitting the HARQ-ACK feedback information for msgB.

Proposal 8: For 4-step RACH procedure and for semi-static channel access mode, a UE is allowed to initiate its own FFP at least for a msg3 transmission.

Proposal 9: u-FFP parameters are provided within SIB1.

Proposal 10: In semi-static channel access mode, a DG UE determines the initiator of the COT based on the content of the scheduling DCI. FFS: on how the information related to the initiator of the COT is carried.

Observation 2: The ETSI BRAN precludes a gNB from performing cross-FFP scheduling.

Proposal 11: If a gNB operates as an initiating device and schedules an UL transmission outside of its FFP, then the DG UE must assume that the scheduled UL transmission would need to be performed as if the UE is the initiating device irrespectively from any explicit indication provided by the gNB.

Proposal 12: When a configured UL transmission is aligned with a u-FFP boundary and ends before the idle period of that u-FFP, whether the UE should always assume that the configured UL transmission correspond to UE-initiated COT or not is up to gNB’s configuration.  If the transmission is confined within a g-FFP before the idle period of that g-FFP, the gNB has not configured the UE to assume that the configured UL transmission correspond to UE-initiated COT, and the UE has already determined that gNB has initiated that g-FFP, then the UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, the UE assumes that the configured UL transmission corresponds to UE-initiated COT.

Proposal 13: The CG-UCI based procedure and CG-DFI based procedure are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and new parameter Y, respectively, where X and Y are different from cg-RetransmissionTimer-r16.

Observation 3: Even if Type A is further enhanced for unlicensed operation, LBT overhead may be still unacceptable for URLLC use cases, given that gaps across slots are often unavoidable.

Proposal 14: Both the NR-U’s repetition scheme and Type B repetition scheme from Rel.16 URLLC design should be further enhanced, potentially to converge into a single repetition scheme.

Proposal 15: When segmentation is applied to a PUSCH transmission occurring across a slot boundary and when CG-UCI is configured to be transmitted, this is included in every actual repetition.

Observation 4: When operating in unlicensed spectrum, the orphan symbol deriving from segmentation is highly detrimental for transmissions within either a UE or a gNB’s initiated COT.  Therefore, RAN1 should discuss how to prevent a UE from performing an additional LBT due to the occurrence of an orphan symbol.

Proposal 16: DCI 0_2 should be enhanced to carry the DFI information based on configuration.

### R1-2100270	Ericsson	Enhancements for IIoT URLLC on Unlicensed Band

Observation 1: Any restriction on UE-initiated COT design should be strongly justified to avoid compromising NR operation in unlicensed bands

Observation 2: The configuration of UE FFP reduces the dependency on DL for UL transmission. The more the UE FFP configuration is matched with UL traffic, the less dependency on DL for UL transmissions is achieved which results in improvement of UL capacity.

Observation 3: Forcing restrictions on UE FFP does not lead to a good coexistence, rather inter-network coordination on UE/gNB FFPs configurations among coexisting networks ensures good coexistence.

Observation 4: Option 1 is aligned with RAN2 agreement.

Observation 5: Many different NR-U CG features are coupled with same higher layer parameter (e.g. cg-RetransmissionTimer).

Proposal 1: For semi-static channel access mode, FFP Periodicity for UE-initiated COT are independently configured from the FFP periodicity for gNB-initiated COT.

Proposal 2: For semi-static channel access mode, the range values for periodicity and offset corresponding to configured grants can be reused as range values for periodicity and offset of UE-FFP. Note that only period values of at least 1ms and at most 10ms are applicable.

Proposal 3: For semi-static channel access mode, no additional restriction on transmission and reception during idle periods is supported.

Proposal 4: In semi-static channel access mode, when a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, the UE assumes that the configured UL transmission corresponds to UE-initiated COT (Alt-b).

Proposal 5: In semi-static channel access mode, when a UE is provided with both gNB FFP and UE FFP, the valid idle period associated to a scheduled UL transmission is determined as follows (Alt2 with fallback to Alt 3):

- For scheduled UL transmission, the associated valid idle period is indicated in the scheduling DCI using ChannelAccess-CPext field in DCI (i.e. Alt 2 in previous agreement), when provided.

  - If ChannelAccess-CPext field in absent in DCI, pre-determined rules similar to configured UL transmissions are applicable (i.e. Alt 3 in previous agreement).

Proposal 6: When a configured DL transmission is aligned with a gNB FFP boundary and ends before the idle period of that FFP associated to the gNB, the UE assumes that the configured DL transmission corresponds to the gNB-initiated COT.

Proposal 7: When a configured DL transmission starts after a gNB FFP boundary and ends before the idle period of the FFP associated to the gNB,

- If the UE determines that the gNB has already initiated the FFP, then UE assumes that the configured DL transmission corresponds to gNB-initiated COT.

- Otherwise, If the transmission is confined within the UE FFP before the idle period of that FFP, and if the UE has already initiated that FFP, then UE assumes that the configured DL transmission corresponds to UE-initiated COT.

Proposal 8: In semi-static channel access mode, when a UE is provided with both gNB FFP and UE FFP, the valid idle period associated to a scheduled DL transmission is determined as follows:

- For scheduled UL transmission, the associated valid idle period is indicated in the scheduling DCI using ChannelAccess-CPext field in DCI, when provided.

  - If ChannelAccess-CPext field in absent in DCI, pre-determined rules similar to configured DL transmissions are applicable.

Proposal 9: A UE can be semi-statically signaled to cancel/override the assumption on the initiator of a COT with respect to one or more FFP boundaries of the corresponding FFP configuration.

Proposal 10: A UE can be dynamically signaled to cancel/override the assumption on the initiator of a COT with respect to one or more FFP boundaries of the corresponding FFP configuration.

- Note: UE specific signaling such as scheduling DCI or group common signaling using DCI format 2_0 can be used for COT-initiation cancelation/overriding purposes.

Proposal 11: For semi-static channel access mode, UE-initiated COT is supported before dedicated RRC and is enabled by SIB-1.

- UE FFP periodicity and offset are implicitly determined based on PRACH configuration corresponding to a PRACH transmission outside the gNB-initiated COT.

Proposal 12: Configuration of cg-RetransmissionTimer is optional when configured grant Type 1 or Type 2 are configured on unlicensed spectrum.

Proposal 13: Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16 (i.e. Option 1).

Proposal 14: Enable configuration of cg-nrofSlots-r16, cg-nrofPUSCH-InSlot-r16 for UL CG without CG-UCI.

- Simplified repetition Type B (without segmentation)

### R1-2101461	Qualcomm Incorporated	Uplink enhancements for URLLC in unlicensed controlled environments

Observation 1: Either supporting UE initiated COT in IDLE/INACTIVE mode or allowing PRACH transmission in idle period can provide more chances for the UE to send PRACH.

Proposal 1: Study the following alternatives for PRACH transmission in idle mode:

Alt.1: Supporting UE initiated COT by PRACH transmission in idle mode;

Alt.2: Allowing PRACH transmission in idle period of an FFP.

Proposal 2: Study the following two alternatives for SSB to PRACH mapping:

Alt.1 Divide PRACH occasions into two groups and SSB is mapped to PRACH occasion per group;

Alt.2: Introduce two PRACH configurations and SSB is mapped to PRACH occasions per PRACH configuration.

Proposal 3: Study the following alternatives for MsgA transmission in idle mode:

Alt.1: Supporting UE initiated COT by MsgA transmission in idle mode;

Alt.2: Allowing MsgA transmission in idle period of an FFP.

Proposal 4: Study the following for RO-to-PO mapping:

Alt.1: Divide PUSCH occasions into two groups and PRACH occasion is mapped to PUSCH occasion per group;

Alt.2: Introduce two sets of PUSCH configurations and each PUSCH configuration is associated with one PRACH configuration.

Proposal 5: FFP Periodicity for UE-initiated COT can be same, or integer multiple of, inter factor of the FFP periodicity for gNB-initiated COT.

Proposal 6: gNB indicates UE to initiate a COT based on ChannelAccess-CPext field in DCI.

Proposal 7: The UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration

Proposal 8: Study ED thresholds selection when UE share its COT to gNB and  the scheme that UE can share its COT to the other UEs through gNB.

Proposal 9: CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and new parameter Y, respectively, where X and Y are different from cg-RetransmissionTimer-r16.

Proposal 10: When cg-RetransmissionTimer is not configured, CG-CUI can be configured including at least HARQ process ID, RV ID and COT sharing information.

Proposal 11: For LBE, configuration of (cg-RetransmissionTimer) should be mandated when configured grant Type 1 or Type 2 are configured on unlicensed spectrum.

Proposal 12: NR-U CG-PUSCH shall support type A PUSCH repetition introduced in Rel.16 URLLC by reinterpreting the # of repetitions in consecutive slots as the # of repetitions in consecutive transmission occasions.

Proposal 13: NR-U CG-PUSCH shall support type B PUSCH repetition introduced in Rel.16 URLLC with the proposal in this contribution.

### R1-2100882	LG Electronics	Discussion on unlicensed band URLLC IIOT

Proposal #1: Support unaligned FFP timing between the FFP stating with gNB-initiated COT and the FFP starting with UE-initiated COT.

Proposal #2: Consider to support dynamic indication of whether to allow UE-initiated COT for the next FFP based on the transmission of UE (group)-common DCI, at least for the control of potential congestion among multiple UEs in a same FFP.

Structure of the common DCI signaling (with indication of COT duration and SFI information) designed in Rel-16 NR-U can be reused.

Proposal #3: Consider LBT type configuration for the configured UL resource in terms of whether the configured UL is allowed to initiate COT by UE.

It is FFS whether some handling is needed to apply the CP extension for transmission of the configured UL at the beginning of FFP.

Proposal #4: Consider to define the FFP including or starting with essential DL/UL transmission occasions (such as SSB or CORESET#0) as default FFP-g.

Proposal #5: Consider to align the assumption of FFP type for multiple RB sets in a carrier/BWP under the unaligned FFP structure between UE and gNB.

Proposal #6: Consider the following aspects for the configuration of the starting offset and the period/duration for UE FFP-u.

Granularity of the starting offset (O_u) for FFP-u

Relationship between FFP-u period (P_u) and FFP-u starting offset

Relationship between FFP-u period and FFP-g period (P_g)

Relationship between FFP-u period and the period (P_c) of configured UL

Relationship between FFP-u period and the duration of FFP-u

Proposal #7: Clarify first on the energy detection (ED) threshold used to perform LBT for UE-initiated COT before deciding the method for UE’s determination of the scheduled UL transmission (e.g. whether it is done based on shared-gNB COT or UE-initiated COT).

Proposal #8: Prefer Alt-c (The UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration) for the configured UL transmission aligned with UE FFP boundary.

Proposal #9: Consider the following UE behaviour/assumption for the configured UL transmission not aligned with UE FFP boundary (by slightly updating the previous agreement).

If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT.

Otherwise, If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT.

Proposal #10: Option 1 is preferable for the CG configuration in terms of enabling/disabling CG-UCI based procedure and CG-DFI based procedure and CG retransmission timer.

Option 2-a and Option 3 can be considered further if there is consensus to pursue the reduction of DCI overhead or UL-SCH loss.

Proposal #11: Consider to adopt PUSCH repetition type B for NR-U CG resource allocation.

Proposal #12: Introduce following three resource allocation parameters replacing existing parameters to support harmonized CG operation.

A RRC parameter for the number of consecutive PUSCH occasions

A RRC parameter for the number of repetition of consecutive PUSCH occasions in slot-level

A RRC parameter for the number of PUSCH occasion used for a TB

Proposal #13: Consider to keep 1 symbol length PUSCH after segmentation under some condition in unlicensed band

Proposal #14: Consider new equation for determining HARQ process ID in order to support multiple TB transmission per periods.

Proposal #15: Consider NDI indication with less overhead other than CG-UCI.

### R1-2100103	ZTE	Discussion on unlicensed band URLLC IIoT

Proposal 1: For UE-initiated COT in FBE,

The FFP can be a subset of the period of tdd-UL-DL configuration or the FFP for gNB-initiated COT.

The offset range can be ms.

The reference location of offset for UE-initiated COT can be the starting of even indexed radio frame.

Proposal 2: The COT of the gNB can block the UE initiated COT, but the COT of the UE shall not block the gNB initiated COT.

Proposal 3: A COT initiated by UE can not be shared with other UE(s) directly or indirectly by gNB.

Proposal 4: After introducing UE-initiated COT, gNB-to-UE COT sharing regulation should be redefined.

Proposal 5: Determine the COT of UL transmission burst based on predetermined rules

The UE should share the COT of gNB when the COT of the gNB is valid.

The UE should initiate a COT when the UL transmission burst is not in a valid COT of gNB and starts at the beginning of the UE’s FFP and ends at any symbol before the UE FFP’s idle period.

Proposal 6: Option 3 is preferred for harmonization of CG-DFI and CG-UCI features for unlicensed:

CG-UCI based procedures are supported for unlicensed. CG-DFI based procedures are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16.

Proposal 7: For mandatory RRC parameters in unlicensed operation,

for dynamic channel access mode (a.k.a. LBE), configuration of (cg-RetransmissionTimer) should not be mandated when configured grant Type 1 or Type 2 are configured on unlicensed spectrum.

harq-ProcID-Offset2 is not supported for unlicensed spectrum.

Proposal 8: The use of PUSCH repetition type-A together with NR-U based multi-slot allocations should not be considered.

Proposal 9: The use of PUSCH repetition type-B together with NR-U based multi-slot allocations should be considered with potential enhancements.

Back-to-back repetitions with segmentation across the slot boundary or invalid symbols is supported as in Rel-16 URLLC.

Configuring additional transmission occasions across a number of slots to ensure K repetitions is supported as in Rel-16 NR-U.

Proposal 10:  For the interaction with DL/UL directions for Type 1 CG PUSCH and Type 2 CG PUSCH without the first PUSCH (including all the repetitions), Rel-16 NR-U feature is used with modifying the repetition to actual repetition.

If dynamic SFI is not received and not provided EnableConfiguredUL-r16, the actual repetition is not transmitted if it conflicts with a semi-static flexible symbol.

If dynamic SFI is not received but provided EnableConfiguredUL-r16, the actual repetition can be transmitted.

Proposal 11:  For URLLC over unlicensed band, CG-UCI is transmitted per actual repetition.

Proposal 12: If Configuredgrantconfig-StartingfromRV0 is set to ‘on’, it is configurable to enable or disable the feature for starting the initial transmission at the last repetition when K≥8. If Configuredgrantconfig-StartingfromRV0 is set to ‘off’, Rel-16 URLLC behavior is used.

Proposal 13: If PHY prioritization introduced in Rel-16 is supported in unlicensed band, how to handle the multiplexing and PHY prioritization of CG-UCI and HARQ-ACK codebooks  should be considered.

### R1-2101203	Samsung	Enhancements for unlicensed band URLLC IIoT

Proposal 1: Support the transmission restriction on gNB’s idle period to ensure fair co-existence with other FBE nodes, i.e. the transmission from neither a gNB not its UE is allowed in gNB’s idle period.

Proposal 2: Support UE-initiated COT for idle UE.

Proposal 3: For UE-initiated COT parameter configuration,

Support independent configuration for UE FFP periodicity and gNB FFP period.

UE FFP periodicity can be any integer number of slots with the duration at least 1ms and at most 10ms.

Support independent configuration for UE FFP start position and gNB FFP start position.

UE FFP start position is determined by UE-specific offset with reference to SFN 0.

The offset value range is 0 ≤ offset ＜periodicity

Proposal 4: For RRC connected mode, support explicit configuration of FFP parameters for UE-initiated COT by UE-dedicated RRC signaling. For RRC idle mode, UE FFP can be indicated by SIB1 or derived by PRACH configuration.

Proposal 5: When a UL transmission is aligned with a UE FFP boundary

In case of scheduled UL transmission, the UE determines whether the UL transmission should be transmitted according to shared gNB COT or UE-initiated COT according to LBT indication by existing bit field ChannelAccess-CPext in the scheduling DCI.

In case of configured UL transmission, the UE assumes that the configured UL transmission corresponds to UE-initiated COT.

Proposal 6: When a UL transmission starts after a UE FFP boundary,

If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT

Otherwise, if the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT.

Otherwise, UE drops the UL transmission.

Proposal 7: To determine gNB-to-UE COT sharing, the following mechanism can be consider:

A UE assumes gNB has initiated a COT if the UE receives explicit indication in DCI 2_0.

A UE assumes gNB has initiated a COT if the UE detects DL transmission at the beginning of gNB FFP.

Proposal 8: Do not support of new signaling transmitted by UE to indicate whether a UE has initiated the COT.

Proposal 9: Support option 2-b for IIOT over unlicensed band:

Option 2-b: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and new parameter Y, respectively, where X and Y are different from cg-RetransmissionTimer-r16.

Proposal 10: For PUSCH repetition over unlicensed band,

Support configurability for Rel-16 NR-U repetition and URLLC type-A/type-B repetition without multi-slot allocation.

Study type-B repetition enhancement with multi-slot allocation.

Proposal 11: For Type-B PUSCH repetition over unlicensed band, support additional gaps to avoid LBT blocking from DL signals/channels or LBT blocking between UEs.

### R1-2101380	Apple	URLLC uplink enhancements for unlicensed spectrum

Proposal 1-1: For a scheduled UL transmission that falls within the same gNB’s COT as the scheduling DCI, the UL transmission shares the gNB’s COT and follows the LBT indication in the DCI via reusing the ChannelAccess-CPext or ChannelAccess-CPext-CAPC field.

FFS details on how to define the ChannelAccess-CPext or ChannelAccess-CPext-CAPC field for this case

Proposal 1-2: Adopt the same behavior when determining whether to share gNB’s COT or use UE-initiated COT for the following two cases:

Case 1: scheduled UL transmission that does not fall within the same gNB’s COT as the scheduling DCI

Case 2: configured UL transmission

Proposal 1-3: For scheduled UL transmission that does not fall within the same gNB’s COT as the scheduling DCI and configured UL transmission,

When the UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE,

If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the UL transmission corresponds to gNB-initiated COT using Cat-2 LBT.

Otherwise, UE assumes that the UL transmission corresponds to UE-initiated COT.

When the UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE:

If the UE has already initiated the UE FFP, then UE assumes that the UL transmission corresponds to UE-initiated COT.

Else if the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the UL transmission corresponds to gNB-initiated COT using Cat-2 LBT.

Otherwise, it is not transmitted.

Otherwise (When the UL transmission overlaps with the UE FFP’s idle period)

If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the UL transmission corresponds to gNB-initiated COT using Cat-2 LBT.

Otherwise, it is not transmitted.

Proposal 1-4: Introduce a RRC parameter to enable UE-initiated COT for a UE, and a RRC parameter to enable UE-initiated COT for each CG configuration, which overrides the per-UE configuration if configured.

Proposal 1-5: If there is strong concern on coexistence, additional constraint can be introduced that the UE is not allowed to transmit in the idle period of gNB’s FFP.

Proposal 2-1: Adopt Option 2-a, i.e., “CG-UCI based procedures” are enabled or disabled for unlicensed using a new RRC parameter, and “CG-DFI based procedures” are enabled or disabled for unlicensed using cg-RetransmissionTimer-r16.

Note: if cg-RetransmissionTimer-r16 is configured, “CG-UCI based procedures” should also be enabled.

Proposal 2-2: For the cases where LBT effect needs to be considered, further consider the support of modified PUSCH repetition Type B with flexible start on unlicensed spectrum.

Proposal 2-3: Consider enhanced CG-UCI on unlicensed spectrum to allow the UE to autonomously adapt certain transmission parameters such as MCS.

### R1-2101076	ETRI	Enhancements for unlicensed band URLLC IIoT

Proposal 1: For the FFP period for UE-initiated COT, {1ms, 2ms, 2.5ms, 4ms, 5ms, 10ms} are supported.

Proposal 2: UE expects that the FFP period of UE-initiated COT is an integer factor or an integer multiple of the FFP period of the gNB-initiated COT.

Proposal 3: The UE FFP offset can be any value within 0 <= offset < UE FFP period with 1-symbol granularity using 1) the smallest SCS configured in the cell as the reference SCS and 2) the boundary of even indexed radio frames as the reference point.

Proposal 4: For FBE, do not support UE-initiated COT for idle/inactive UEs.

Proposal 5: For UE’s COT initiation in FBE, support the followings:

For a UE FFP including a UL from the beginning, UE performs the COT initiation by transmitting the UL if not indicated/configured to cancel the COT initiation. If indicated/configured to cancel, UE skips the COT initiation in the UE FFP.

For a UE FFP not including a UL from the beginning, UE skips the COT initiation.

Proposal 6: For gNB-to-UE COT sharing in FBE, UE determines whether a detected DL burst was transmitted according to a gNB-initiated COT or a UE-initiated COT based on (implicit or explicit) indication from gNB.

Proposal 7: For a configured UL aligned with a UE FFP boundary, if it belongs to both gNB COT and UE’s own COT, the UE assumes that it is transmitted according to the UE-initiated COT.

Proposal 8: UE expects that a configured UL starting from a UE FFP boundary is always confined within the UE-initiated COT.

Proposal 9: For dynamic UL, UE determines a COT associated to the UL according to the following alternatives.

Alt. 1: Based on a predefined rule (e.g., a COT which ends later)

Alt. 2: Based on UL grant (e.g., by reusing the ChannelAccess-CPext field)

Proposal 10: For FBE, the following rules are supported:

A UE can initiate a COT within a gNB-initiated COT, and gNB can initiate a COT within a UE-initiated COT.

As initiating device, the gNB can transmit during any UE FFP idle periods.

As initiating device, a UE can transmit during other UEs FFP idle periods.

A responding device can still transmit in the shared COT even if its transmission collides with the idle period of FFP configured for the responding device.

Proposal 11: Clarify that for scheduled UL, the FFP/channel where a UL (each UL repetition in case of repetition) is scheduled can be same or different from the FFP/channel where an associated UL grant is transmitted.

Observation 1: The UL reliability performance of unlicensed URLLC can be severely degraded if UE’s processing time for DL detection to share a COT is unknown to gNB.

Proposal 12: For gNB-to-UE COT sharing, define UE’s processing time required for DL burst detection and UL transmission preparation.

Proposal 13: For UE-to-gNB COT sharing, consider defining processing time for gNB’s UL burst detection for UE power saving purpose.

Proposal 14: Discuss how to handle the CP extension when configured for CG-PUSCH that starts from the beginning of a UE FFP.

Proposal 15: Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16.

Proposal 16: For FBE, when cg-RetransmissionTimer is not configured, a symbol overlapping with idle period of a FFP associated to PUSCH transmission is regarded as invalid symbol for PUSCH mapping type B.

### R1-2100626	Nokia, Nokia Shanghai Bell	UL enhancements for IIoT URLLC in unlicensed controlled environment

Observation 1: Back-to-back PUSCH repetitions are already supported with NR-U as part of Type A repetitions.

Proposal 1: Non-back-to-back Type A repetitions are not supported in unlicensed band.

Proposal 2: PUSCH repetition Type B should be supported for unlicensed band operation when using NR IIoT Rel-16 based CG, without NR-U specific enhancements. FFS: required spec changes, if any.

Proposal 3: The use of PUSCH repetition Type B together with NR-U based multi-slot allocations should not be considered.

Proposal 4: Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter (Option 1  from RAN1#103-e), i.e. when cg-RetransmissionTimer is not configured, NR-U specific CG features such as CG-UCI, COT sharing indication, UE-selected HARQ process ID and RV, autonomous retransmission, consecutive allocations for different TB and CG-DFI are not supported.

Proposal 5: PHY multiplexing/prioritization introduced in Rel-16 is supported also with NR-U CG. Interaction of CG-UCI and HARQ-ACK codebooks of different priorities is FFS.

On the support for UE-initiated COT for FBE

Proposal 6: As initiating device, the gNB can transmit during any UE FFP idle periods.

Proposal 7: As initiating device, a UE can transmit during other UEs FFP idle periods.

Proposal 8: By default, as the initiating device, a UE cannot transmit during its serving gNB’s idle period.

Proposal 9: Introduce support for gNB-controlled UE-initiated UL transmissions during gNB idle periods, when e.g. the gNB has no intention to acquire the COT in the subsequent FFP.

Proposal 10: A UE determines whether a scheduled UL transmission should be transmitted according to shared gNB COT or UE-initiated COT at least based on the value of ChannelAccess-CPext field in the scheduling DCI (i.e. Alt. 2 from RAN1#103-e). Details are FFS.

Proposal 11: When a configured UL transmission is aligned with a UE FFP boundary and ends before the start of the idle period of that UE associated to the UE:

if the transmission is confined within a gNB FFP before the idle period of that gNB FFP and the UE has already determined that the gNB has initiated that gNB FFP, the UE assumes that the configured UL transmission corresponds to gNB-initiated COT.

if the UE determines that the gNB has NOT initiated that gNB FFP, the UE assumes that the configured UL transmission corresponds to UE-initiated COT.

if the transmission is NOT confined within a gNB FFP before the idle period of that gNB FFP (i.e. the transmission overlaps at least partially with the idle period of that gNB FFP) and the UE has already determined that the gNB has initiated that gNB FFP, down-select one of the following:

The UE only transmits on a subset of the configured UL (time) resources to ensure no transmissions during the idle period of that gNB FFP

Note: this is a slightly clarified version of Alt-a from RAN1#103-e

Proposal 12: Support UE-initiated COT for semi-static channel occupancy in IDLE/INACTIVE mode.

Proposal 13: Assuming support of UE-initiated COT for semi-static channel occupancy in IDLE/INACTIVE mode is agreed, FFP parameters for UE-initiated COT also need to be provided to the UE by SIB-1.

### R1-2100438	vivo	Enhancements for unlicensed band URLLC IIoT

Proposal 1: The FFP period of the UE-initiated COT should be configured without referring to the FFP period of gNB-initiated COT.

Observation 1: Predetermined rules should be used for UE to determine whether a scheduled UL transmission should be transmitted according to shared gNB COT or UE-initiated COT.

Proposal 2: UE assumes that the configured UL transmissions corresponds to UE-initiated COT if it is aligned with the UE FFP boundary.

Proposal 3: PUSCH segmentation should take into account the idle period of a FFP.

Proposal 4: gNB can detect either configured or scheduled transmissions from the beginning of the FFP to determine if the UE has initiated a COT.

Proposal 5: For gNB-to-UE COT sharing, the following options can be further considered:

Option 1: UE detects group-common or broadcast signalling from the beginning of the FFP configured for gNB.

Option 2: gNB indicates the remaining COT information signalling.

Proposal 6: UE-initiated COT should be supported for IDLE mode UE.

Proposal 7: Support option 1 as the framework for harmonization of UL Configured Grant (CG).

Proposal 8: Clarify the configuration of cg-RetransmissionTimer is per CG or per cell when multiple CGs are configured for an unlicensed carrier.

Proposal 9:

Support configuration of phy-PriorityIndex field for CG operation in unlicensed band.

The field of pusch-RepTypeIndicator is NOT configured for operation with shared spectrum channel access for Type 1 CG.

Proposal 10: It is necessary to enhance the cg-UCI-Multiplexing field to support CG using NR-U like mechanism for URLLC traffic by taking into account intra-UE prioritization/multiplexing.

Proposal 11: To ensure the URLLC reliability for CG PUSCH using NR-U mechanism, startingFromRV0 can be used to control whether the RV for initial CG-PUSCH determined by the UE should be 0.

### R1-2100857	Sony	Considerations on unlicensed URLLC

Observation 1: It is beneficial for the gNB to be able to schedule another UE when transmitting under a UE initiated COT.

Observation 2: If a UE that has initiated a COT is not allowed to transmit during gNB’s FFP Idle Period and the gNB can initiate a COT after gNB’s FFP Idle Period, then we have the following issue:

- If the UE transmits after gNB’s FFP Idle Period, it may collide with gNB’s transmission if gNB decides to initiate a COT

- If the UE is not allowed to transmit after gNB’s FFP Idle Period, then the UE’s transmission opportunity may be significantly shortened if gNB decides not to initiate a COT.

Proposal 1: UE determines the initiator of a COT based on a DCI indicator from the gNB, i.e.:

Alt-1: Introduce additional bit field in the scheduling DCI

Alt-2: Based on ChannelAccess-CPext field in DCI

Proposal 2: Allow a UE initiated COT to be passed to the gNB so that the gNB becomes the initiator of the COT.

Proposal 3: For CG-PUSCH that starts at the UE’s FFP boundary, the assumption on whether the UE’s CG-PUSCH transmission is based on a UE initiated COT or gNB initiated COT, the UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration.

FFS on details of configuration

Proposal 4: The gNB does not need to indicate whether a UE can initiate a COT in the next few FFPs.

Proposal 5: If UE is not allowed to transmit during gNB’s FFP Idle Period and the gNB can initiate a COT during that Idle Period, then the UE shall monitor for gNB’s transmission for a period P after gNB’s FFP Idle Period:

- If the UE detects gNB’s transmission then the UE shall not transmit in the remaining portion of its initiated COT

- Otherwise, the UE can transmit in the remaining portion of its initiated COT

Proposal 6: UE initiated COT for semi-static channel access is supported in Idle Mode.

Proposal 7: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and new parameter Y, respectively, where X and Y are different from cg-RetransmissionTimer-r16.

### R1-2101291	InterDigital, Inc.	Enhancements for unlicensed band URLLC IIoT

Proposal 1: IDLE/INACTIVE mode UEs can initiate COTs in FBE at least for PRACH transmission.

Proposal 2: Use Alt-c for CG transmissions occurring at the beginning of a UE FFP. The UE can be configured with COT selection behavior (e.g. if gNB-initiated COT is detected always use gNB-initiated COT, or always use UE-initiated COT, or select between the two based on rules)

Proposal 3: A UE sends an indication of the COT used for a transmission (gNB-initiated or UE-initiated).

Proposal 4: For URLLC in controlled environment, a UE selects the HARQ Process ID by implementation from a configured pool of processes for an initial transmission on a CG, as in NR-U.

Proposal 5: A UE can prioritize transmissions over retransmissions on CG resources. The conditions to do so are FFS.

Proposal 6: CG-UCI based procedures and CG-DFI based procedures are independently enabled or disabled for unlicensed (Option 2). FFS if CG-DFI configuration is tied to cg-RetransmissionTimer-r16 or not (Option 2-a or 2-b).

### R1-2100995	Lenovo, Motorola Mobility	Enhancements for unlicensed band IIoT URLLC

Proposal 1: Start of FFP for UE-initiated COT is not associated with start of gNB-FFP.

Proposal 2: UE-initiated COT for idle/inactive mode UE can be further studied (with lower priority compared to more basic items such as determining if a COT is associated with a UE or gNB).

Proposal 3: UE is not allowed to transmit during idle period of any FFP associated with the gNB.

Proposal 4: Support allowing only UEs with high priority data/control to initiate a COT for FBE.

Proposal 5: If UE-initiated COT for idle/inactive UE is supported, a UE can transmit CG-PUSCH in a gNB-FFP, upon receiving a broadcast signal from gNB at the beginning of the gNB-FFP (subject to existing rules such as sensing prior to transmission).

Proposal 6: For the case of UE-initiated COT with configured grant PUSCH transmission, the number of repetitions applied to a transport block at the beginning of the acquired FFP is less than the number of repetitions associated with PUSCH transmissions of the configured grant (in transmission occasions other than those of the beginning of the acquired FFP).

Proposal 7: For the case of UE-initiated COT with configured grant PUSCH transmission, the transmit power at the beginning of the acquired FFP can be higher than the transmit power associated with PUSCH transmissions of the configured grant (in transmission occasions other than those of the beginning of the acquired FFP).

Proposal 8: For the case of UE-initiated COT with configured grant PUSCH transmission, when a first UL transmission burst is followed by a high priority second UL transmission burst on CG resources and if the gap is more than 16µs between the two transmissions, following solutions can be considered:

Shift the high-priority UL transmission earlier in time to reduce the gap to under 16µs

Apply CP extension for the second transmission to keep the effective gap under 16µs

### R1-2100576	MediaTek Inc.	On the enhancements for unlicensed band URLLC IIoT

Proposal 1: The UE is configured to initiate a COT for PRACH transmission.

- E.g. UEs with high Priority traffic or mixed high/low priority traffic could have this functionality enabled by gNB.

Proposal 2: UE-initiated COT carrying PRACH is automatically shared with the gNB without any additional indication.

Proposal 3:  An explicit indication from UE to gNB that UE has initiated a COT

- If the UE has an UL CG transmission and if CG-UCI Channel Occupancy Time (COT) sharing information bit-field is enabled it is interpreted as the UE didn’t start its own COT.

- If the UE has an UL CG transmission and if CG-UCI Channel Occupancy Time (COT) sharing information bit-field is disabled, it is interpreted as the UE started its own COT.

Proposal 4: UE COT-initiating functionality is RRC (or dynamically) configured to the UE.

Proposal 5: UE COT initiation enabling/disabling is determined from the traffic priority.

Proposal 6: FFP parameters for UE-initiated COT could be provided by SIB-1.

Proposal 7: UE FFP periodicity determined from higher layer parameters but overridden by explicit dedicated signalling.

Proposal 8: No DCI indication for UE COT-initiation in next FFP and restrict UE COT-initiation to high priority traffic.

Proposal 9: Support Alt-a with further reduction to the transmission confining interval to take UE processing time into consideration.

Proposal 10: The gNB signals the initiating of its own COT or the sharing of a UE-initiated COT using different DMRS cyclic shifts.

Proposal 11: There is no need to support and specify a UE-initiated COT cancellation

Proposal 12: If COT cancellation is needed, a time duration t is to be introduced to process the cancellation signal and cancel the ongoing transmission

Proposal 13: If COT cancellation is needed, the UE should be configured semi-statically about the time instants when it should cancel an ongoing UE-initiated COT.

Proposal 14: If COT cancellation is needed, Cancellation should be defined as a UE capability. The UE signals its support of the cancellation of an ongoing UE-initiated COT.

Proposal 15: UE initiating a COT within a gNB-initiated COT, and gNB initiating a COT within a UE-initiated COT is supported and configurable.

Proposal 16: UE initiating a COT within a gNB-initiated COT could be allowed only if transmission overlaps with the gNB FFP idle period.

### R1-2100378	CATT	Enhancements for unlicensed band URLLC IIoT

Proposal 1: In semi-static channel access mode, UE should be able to determine whether a scheduled UL transmission should be transmitted according to shared gNB COT or UE-initiated COT by DCI indication method.

Proposal 2: In semi-static channel access mode, when a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, whether the configured UL transmission is allowed to correspond to UE-initiated COT should be based on gNB configuration.

Proposal 3: In semi-static channel access mode, when a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, gNB can inform UE a transmission pattern to indicate which COT(s) can be used for UE initialization.

Proposal 4: Option 1 “Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16” is taken as baseline for supporting UL CG for URLLC in unlicensed band.

### R1-2100543	TCL Communication Ltd.	Enhancements for unlicensed band URLLC IIoT

Observation 1: Multiple configurations help combat the random packet arrival without incurring large latency but it introduces signaling overhead.

Observation 2: The main limitation of the existing CG standardization in URLLC and NR-U is related to transport block confined within a period.

Observation 3: DL symbols in the middle of an UL transmission reduce the transmission time, which gets further reduction due to LBT requirement after the gap.

Observation 4: Dropping a transmission over semi-statically configured flexible symbols causes a QoS degradation.

The discussion and the observations have led to the following proposals in this document:

Proposal 1: CG-UCI is always transmitted even when the CG PUSCH is being transmitted over a licensed carrier.

Proposal 2: It is proposed to further investigate the scenario when DL symbols occur in the middle of an UL scheduled resource.

Proposal 3: For CG transmission, if dynamic SFI is configured but the UE cannot decode dynamic SFI, semi-static flexible symbols in the scheduled resource are used for PUSCH.

Proposal 4: The TDRA table is extended with the indication of number of repetitions. Each TB is indicated by a SLIV and number of repetitions. A SLIV only corresponds to one TB and not to PUSCH repetition of a TB.

Proposal 5: The number of entries in the new TDRA table increases based on the number of the scheduled TBs, the maximum allowed number of repetitions for each TB, the number of bits in TDRA field of DCI.

### R1-2101614	NTT DOCOMO, INC.	Discussion on enhancements for unlicensed band URLLC

Proposal 1: UE in IDLE/INACTIVE mode does not initiate COT, i.e., PRACH is not used to initiate COT in IDLE/INACTIVE mode.

Proposal 2: FFP parameters for UE-initiated COT can be provided to the UE by dedicated RRC signalling only, i.e., not provided by SIB1.

Proposal 3: Following values are supported for the period of an FFP for the UE-initiated COT:

1ms, 2ms, 2.5ms, 4ms, 5ms, 10ms

Proposal 4: FFP period for UE-initiated COT is independently provided from the FFP period for gNB-initiated COT and is independently provided among UEs

Proposal 5: Offset of FFP for UE-initiated COT can be configured with an arbitrary number with symbol level granularity subject to Offset < FFP period

Proposal 6: When a scheduled/configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE,

If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT.

Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT

When a scheduled UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE:

If the UE has already initiated the UE FFP, then UE assumes that the scheduled UL transmission corresponds to UE-initiated COT

Otherwise, if the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT.

Proposal 7: No additional specification is necessary for the indication to initiate a COT in a next FFP associated to the UE

Proposal 8: No explicit indication is necessary for UE to indicate to gNB that it has initiated a COT in an FFP

Proposal 9: Support Option 2-a: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and cg-RetransmissionTimer-r16, respectively.

Proposal 10: Configuration of cg-RetransmissionTimer is not mandated when CG is configured on unlicensed spectrum for both FBE and LBE

### R1-2100791	Spreadtrum Communications	Discussion on enhancements for unlicensed band URLLC IIoT

Proposal 1: UE in IDLE/INACTIVE mode does not use semi-static channel access mode.

Proposal 2: At least {1ms, 2ms, 2.5ms, 4ms, 5ms, 10ms} values are supported for the period of an FFP for the UE-initiated COT.

Proposal 3: Typical integer factor of period of configured UL transmission can be supported for the period of an FFP for the UE-initiated COT.

Proposal 4: Offset in FFP of UE-initiated COT is the starting point of first UE-initiated COT relative to the boundary of even indexed radio frame.

Proposal 5: A UE-initiated COT cannot cross the boundary of even indexed radio frame.

Proposal 6: UE determines the initiator of a COT based on Alt 1 or Alt 2.

- Alt 1: Introduce additional bit field in the scheduling DCI

- Alt 2: Based on ChannelAccess-CPext field in DCI

Proposal 7: When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE:

- Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT

Proposal 8: Support one option from Option 1 and Option 2-a for CG-PUSCH harmonization.

- Option 1: Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16.

- Option 2-a: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and cg-RetransmissionTimer-r16, respectively.

### R1-2101015	Panasonic Corporation	Enhancements for unlicensed band URLLC IIoT

Observation 1: Multiple starting time offset for configured grant, which is configured as the amount of CP extension, can be reused to support UE-initiated COT.

Observation 2: It should be clarified that whether the difference of CP extension is called as the change of FFP or not.

Observation 3: If DG PUSCH is used for UE-initiated COT together with CG PUSCH, to support CP extension for multiple starting time offset as in CG PUSCH for DG PUSCH could be considered.

Observation 4: If the difference of CP extension is called as the change of FFP, the start of FFP might be always CG PUSCH if DG PUSCH does not have CP extension. If DG PUSCH supports CP extension, the amount of CP extension for DG PUSCH should be same as that configured to CG PUSCH.

Proposal 1: The UE is not allowed to transmit during the idle period of any FFP associated with the serving gNB (regardless whether the serving gNB initiates a COT in that FFP).

Observation 5: The decision on whether to support RACH transmission to initiate a COT by UE in RRC IDLE/INACTIVE mode could be up to RAN2.

Observation 6: If UE-initiated COT is supported in IDLE/INACTIVE mode, FFP parameters for UE-initiated COT should be provided to the UE by SIB.

Proposal 2: No explicit indication to indicate to the gNB that it has initiated a COT in an FFP is necessary.

Proposal 3: For harmonization of CG features, “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter.

Proposal 4: When configured grant Type 1 or Type 2 are configured on unlicensed spectrum, it would be useful that at least functions related to autonomous retransmission on CG and COT sharing are separately enabled/disabled by the configuration.

### R1-2101676	WILUS Inc.	Discussion on enhancement for unlicensed URLLC IIoT

Proposal 1: For Rel-17, regarding the signaling for FBE operation when a UE operates as an initiating device, it should be supported that a gNB provides FFP parameters for UE-initiated COT to the UE by SIB-1 in addition to dedicated RRC signaling like that of a gNB initiated COT in Rel-16 NR-U.

Proposal 2: For semi-static channel access mode, it should be allowed to use the transmission of any scheduled/configured UL channel/signal to initiate a COT by a UE regardless of DL transmission burst’s reception within one channel occupancy even for the case when the UE is in IDLE/INACTIVE mode.

Proposal 3: We prefer to have an explicit or implicit signaling mechanism based on DCI of scheduled UL transmission to determine whether a scheduled UL transmission should be transmitted according to UE-initiated COT or gNB-shared COT.

Proposal 4: We propose to have Alt-a as the UE behavior on determination of gNB and UE’s COT for the configured UL transmission.

When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE,

Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT.

Proposal 5: It should be further discussed whether or not to possibly transmit configured-grant PUSCH with repetition at candidate SS/PBCH block positions for the same SS/PBCH block index after the detection of the SS/PBCH block index.

Proposal 6: It should be further discussed how to handle on LBT gap/switching gap for segmented transmission of nominal repetition by slot boundary or LBT gap between non-contiguous PUSCH type-B repetitions by DL reception (e.g., candidate SS/PBCH blocks, or others) if PUSCH repetition type B is supported in unlicensed band for URLLC/IIoT.

### R1-2100183	OPPO	Enhancements for unlicensed band URLLC IIoT

Proposal 1: FFP configuration for UE to initiate a COT should be configured via SIB1 for idle/inactive UE and via dedicate RRC parameters for connected UE.

Proposal 2: The UE’s COT end position in a UE FFP should be aligned with the gNB’s COT end position in the gNB FFP.

Proposal 3: UE should determine the initiator of a COT based on ChannelAccess-CPext field in DCI.

Proposal 4: Alt-a should be adopted for UE to determine the initiator of a COT for configured grant uplink transmission.

Proposal 5: DCI format 2_0 can be used to cancel UE-initiated COT at least for configured uplink transmission.

Proposal 6: A group-common PDCCH transmitted at the beginning of the gNB FFP can be introduced to help UE differentiate whether the UL resource is within a gNB-initiated COT or not.

Proposal 7: Harmonization for NR-U PUSCH repetition and Type-B repetition, e.g. NR-U PUSCH repetition allowing slot boundary, should be considered to ensure continuous transmission.

Proposal 8: Option 1 is preferred that CG-UCI procedure and CG-DFI procedure follow R16 NR-U mechanism. CG-UCI procedure is configured by cg-RetransmissionTimer and CG-DFI is configured by cg-minDFI-Delay under the condition that cg-RetransmissionTimer is configured.

Proposal 9:  cg-RetransmissionTimer can be configured for each configured grant independently.

### R1-2101540	Sharp	Enhancements for unlicensed band URLLC IIoT

Proposal 1: Reuse FFP-g periodicity range {1, 2, 2.5, 4, 5, 10} as the baseline for FFP-u periodicity range. Optionally, 8 ms can be added to better support CG PUSCH transmission.

Proposal 2: Clarify the definition of time offset in FFP-u configuration. At this point, our view is that the time offset should be defined as from the start of SFN 0 to the start of the first FFP-u.

Proposal 3: Whether a UE-initiated COT is initiated to transmit a dynamic scheduled PUSCH is indicated by the DCI format scheduling the PUSCH, reusing ChannelAccess-CPext/ChannelAccess-CPext-CAPC field in the DCI format.

Proposal 4: When a CG PUSCH is aligned with a UE FFP boundary, we prefer Alt-a for determining shared gNB COT or UE-initiated COT, with indicating UE’s determination to gNB. The condition that the gNB COT is initiated and the CG PUSCH transmission overlaps with the idle period of gNB FFP requires further discussion.

Proposal 5: If UE would initiate a UE COT in a UE FFP to transmit a CG PUSCH, if the CG PUSCH overlaps with a gNB idle period, the UE FFP is considered being disabled and UE does not initiate the UE COT.

Proposal 6: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter.

### R1-2100691	NEC	Enhancements for unlicensed band URLLC IIoT

Proposal 1: Predetermined rules are supported for both configured transmission and scheduled transmission.

Proposal 2: Do not support sharing of UE initiated COT from one UE to another UE via gNB.

Proposal 3: gNB may send a PDCCH to cancel a low priority UE’s transmission and release the corresponding UE initiated COT in order to support high priority URLLC transmission of another UE.

Proposal 4: Once a UE initiated COT is released by gNB, the UE may not initiate another COT for the same transmission/service until gNB reschedules its UL transmission.

Proposal 5: Support the operation based on combined URLLC and NR-U CG features without new RRC parameters.

### R1-2100054	FUTUREWEI	Further considerations on UE initiated COT for FFP

Proposal 1: In semi-static channel access mode, a UE should be able to determine whether a scheduled UL transmission should be transmitted according to shared gNB COT or UE-initiated COT.  The UE determines the initiator of a COT based on any of the following options (Alt 1, Alt 4 or Alt 5)):

DCI based (either an additional bit field in the scheduling DCI or using the existing ChannelAccess-CPext field)

RRC signalling

MAC CE based

Proposal 2: In semi-static channel access mode, when a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, the UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration (Alt c) .

Proposal 3: When a UE receives a configured grant for UL transmission that starts after the UE FFP boundary and ends after the beginning of the idle period of that UE FFP the UE shall skip this transmission if the UE has already initiated the UE FFP the UE shall discard.

Proposal 4: A device that initiated a COT for FFP shall use the FFP configuration used to initiate the COT until the end of the current FFP. The device that initiated COT cannot be a responding device in a COT initiated by another device during the current FFP.

Observation 1: The transmit authorization for the responding devices is valid only for the current COT, therefore “an authorization” cannot extend beyond the current initiating device’s COT duration. If necessary, it must be provided in each initiator device’s COT.

Observation 2: Only for a transmission a device is required to determine if it is an initiating or a responding device.

Proposal 5: A UE device that transmits as responding FFP device shall use the FFP configuration of the initiating COT gNB for the duration of the gNB FFP. The UE cannot itself initiate another COT for the duration of the current initiating device FFP unless explicitly allowed by gNB.

Proposal 6: The UE shall support capabilities signaling to inform gNB that it can initiate COTs for semi-static channel access.

### R1-2101115	Xiaomi	Enhancement for unlicensed band URLLC IIoT

Proposal 1: No need to restrict or set dependence between the FFP configurations of gNB and UE.

Proposal 2: In the case of UE-to-gNB COT sharing in semi-static channel access mode with a gap > 16us, gNB shall perform an additional CCA. Only when energy was detected with a level below the ED threshold level, gNB can start the transmission.

Proposal 3: A responding device can still transmit in the shared COT even if the shared COT collides with the idle period of FFP configured for the responding device.

Proposal 4: Further studied how to enable gNB to indicate a UE which initiates a COT to share channels to the gNB.

Observation 1: Configuring periodical UL channels, such as CG-PUSCH, at the beginning of FFP, will facilitate UE to initiate a COT successfully.

Proposal 5: To guarantee continuous channel occupation, padding signals or repetition of transmitted channels may be needed to fill the gaps between multiple UL channels in a UE initiated COT.

Proposal 6: UE transmits HARQ-ACK feedback for a PDSCH according to the shared gNB COT as long as the HARQ-ACK is within the same COT containing the PDSCH.

### R1-2101333	Charter Communications	Unlicensed spectrum operation for URLLC IIoT

Proposal 1: Support Option 3: CG-UCI based procedures are supported for unlicensed. CG-DFI based procedures are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16.

Proposal 2: Support Alt. 3: UE determines the initiator of a COT based on a predetermined rule(s).

Proposal 3: Support Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT

## List of previous agreements

### Agreements in RAN1#102-e

Agreements:

- For semi-static channel access mode,

- If sensing is needed, it is performed immediately before the configured/scheduled transmission opportunity.

- For operation with semi-static channel access, the Rel-16 random starting offsets for UL configured grants with Full BW allocation when UE initiates a COT, is not supported.

Agreements:

- For semi-static channel access mode,

  - When gNB operates as an initiating device

    - The gNB is not allowed to transmit during the idle period of any FFP associated with the gNB in which the gNB initates a COT

  - When a UE operates as an initiating device

    - The UE is not allowed to transmit during the idle period of any FFP associated with the UE in which the UE initates a COT

  - When a UE shares a COT initiated by the gNB during an FFP associated with the gNB

    - The UE is not allowed to transmit during the idle period of that FFP in which the UE shares the COT initiated by the gNB

  - When the gNB shares a COT initiated by a UE during an FFP associated with the UE

    - The gNB is not allowed to transmit during the idle period of that the FFP in which the gNB shares the COT initiated by the UE

  - FFS whether/how to support additional restrictions to the idle period

Agreements:

- For semi-static channel access mode, support using the transmission of any scheduled/configured UL channel/signal to initiate a COT by a UE in RRC_CONNECTED mode

  - FFS the case when the UE is IDLE/INACTIVE mode

Agreements:

- A UE initiates a COT in an FFP associated with the UE, if the UE transmits a UL transmission burst starting at the beginning of the FFP and ending at any symbol before the FFP’s idle period after a successful CCA of 9us immediately before the UL transmission burst.

Update on 8/26

Agreements:

- At least for FBE, configuration of (cg-RetransmissionTimer) should not be mandated when configured grant Type 1 or Type 2 are configured on unlicensed spectrum.

Conclusion:

Further study and decide how to harmonize the CG features for Rel-16 URLLC and Rel-16 NR-U. Table 1 in R1-2005376 can be used as a starting point for the corresponding discussion and decision.

Agreements:

- Conditions on the channel access procedures with respect to sensing duration and transmission gap for UE-initiated COT with UE-to-gNB COT sharing is similar as those for gNB initiated COT and gNB-to-UE COT sharing in Rel-16 by exchanging UE and gNB roles.

Agreements:

- UE-to- gNB COT sharing in semi-static channel access mode is supported.

  - The gNB determines a COT in an FFP associated to a UE, that is initiated by the UE, if the gNB detects a UL transmission from the UE starting from the beginning of the FFP and ending before the idle period of the FFP.

    - FFS details

  - When the gNB determines a UE has initiated a COT in an FFP associated to the UE, the gNB can transmit within the FFP and before the idle period corresponding to the FFP.

    - FFS whether/how UE to gNB COT sharing when the gap is >16us

Update from 8/28 GTW

Agreements:

For semi-static channel access mode,

o    Start of FFP for UE-initiated COT can be different from the start of FFP for gNB-initiated COT.

o    FFS: FFP Periodicity for UE-initiated COT can be different from the FFP periodicity for gNB-initiated COT.

Agreements:

- For semi-static channel access mode,

- FFP parameters for UE-initiated COT can be provided to the UE by at least dedicated RRC signaling.

  - FFS on to be provided by SIB-1

- FFS whether the UE FFP periodicity is explicitly configured, or implicitly determined based on other higher layer parameters

### Agreements in RAN1#103-e

Agreements:

- In semi-static channel access mode, a single FFP (periodicity and offset) is associated to an initiating device (gNB or UE) at a given time which can be used for the purpose of channel occupancy. The FFP configuration that is used for initiating channel occupancy purposes, is such that it shall not be changed for at least 200ms

Conclusion:

- For operation on unlicensed channels and irrespective of the adopted LBT mechanism (LBE or FBE), all transmissions in DL and UL are controlled by gNB similarly to licensed channels, and potential collisions or blocking are controlled/mitigated by gNB.

Agreements:

  - UE-to-gNB COT sharing in semi-static channel access mode with a gap > 16us is supported

Conclusion:

If a device X at a given time is initiating a COT, the applicable FFP for the device X is the FFP associated with X.

If a device X at a given time is sharing a COT initiated by a device Y, the applicable FFP for the device X is the FFP associated with Y.

Note 1: One of the devices X and Y is a UE and the other is its serving gNB.

Note 2: Whether or not there is additional restriction on idle period is still FFS.

Agreements:

Down-select one of the following options (target RAN1#104-e):

- Option 1: Both “CG-UCI based procedures” and “CG-DFI based procedures” are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16.

- Option 2-a: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and cg-RetransmissionTimer-r16, respectively.

- Option 2-b: “CG-UCI based procedures” and “CG-DFI based procedures” are independently enabled or disabled for unlicensed using respective RRC parameter, i.e. new parameter X and new parameter Y, respectively, where X and Y are different from cg-RetransmissionTimer-r16.

- Option 3: CG-UCI based procedures are supported for unlicensed. CG-DFI based procedures are enabled or disabled for unlicensed using one RRC parameter i.e. cg-RetransmissionTimer-r16

- Note: Procedures based on CG-UCI rely on UE including CG-UCI in CG PUSCH at least as in Rel-16 where the values of the respective fields of CG-UCI are decided by UE.

- Note: Procedures based on CG-DFI rely on automatic re-transmission on CG configuration and reception of CG downlink feedback information (DFI) in DCI for re-transmissions.

Agreements:

- The gNB configures a UE to initiate semi-static CO in an unlicensed channel(s) only if the gNB configures the UE also with the higher layer parameters of the gNB’s initiating semi-static CO in the same channel(s).

  - Note: UE initiated FBE configuration is configured per serving cell

Agreements:

In semi-static channel access mode, FFP Period for UE-initiated COT is separately provided from FFP period for gNB-initiated COT.

o    Note: Any value for the period, shall be at least 1ms and at most 10ms.

o    Note: Aim for low complexity operation to handle gNB and UE COT interactions

Agreements:

In semi-static channel access mode, a UE should be able to determine whether a scheduled UL transmission should be transmitted according to shared gNB COT or UE-initiated COT.

- UE determines the initiator of a COT based on at least one of the following alternatives:

  - Alt 1: Introduce additional bit field in the scheduling DCI

  - Alt 2: Based on ChannelAccess-CPext field in DCI

  - Alt. 3: Based on a predetermined rule(s)

  - Alt. 4: Based on RRC signalling

  - Alt. 5: Based on MAC CE

  - FFS other alternatives

- FFS on overriding possibility and/or the assumption

- Note: A scheduled UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT.

Agreements:

In semi-static channel access mode:

- When a configured UL transmission is aligned with a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE, down-select one of the following:

  - Alt-a: If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and the UE has already determined that gNB is initiated that gNB FFP, UE assumes that the configured UL transmission corresponds to gNB-initiated COT. Otherwise, UE assumes that the configured UL transmission corresponds to UE-initiated COT

  - Alt-b: The UE assumes that the configured UL transmission corresponds to UE-initiated COT.

  - Alt-c: The UE assumption on whether the configured UL transmission is allowed to correspond to UE-initiated COT is based on gNB configuration.

- When a configured UL transmission starts after a UE FFP boundary and ends before the idle period of that UE FFP associated to the UE:

  - If the UE has already initiated the UE FFP, then UE assumes that the configured UL transmission corresponds to UE-initiated COT

  - Otherwise, If the transmission is confined within a gNB FFP before the idle period of that gNB FFP, and if the UE has already determined that gNB has initiated that gNB FFP, then UE assumes that the configured UL transmission corresponds to gNB-initiated COT.

- FFS on other conditions for determining the corresponding UE or gNB initiated COT

- Note: A configured UL transmission cannot be transmitted according to both shared gNB COT and UE-initiated COT.