3GPP TSG RAN WG1 #106bis-e		                                   					       												                 R1-2109917

e-Meeting, October 11th – 19th, 2021

Agenda Item:	8.17.13

Source:	Moderator (AT&T)

Title:	Summary of UE features for DSS

Document for:	Discussion/Decision

# Introduction

This document presents the summary of email discussion/approval 106bis-e-R17-UE-features-DSS-01] during RAN1 #106bis-e. According to the Chairman’s Notes:

106bis-e-R17-UE-features-DSS-01] Email discussion UE features for DSS – Ralf (AT&T) 1st check point: October 14 Final check point: October 19

The following was discussed and/or agreed during RAN1 #106bis-e within the scope of 106bis-e-R17-UE-features-DSS-01]. All proposals are based on the latest RAN1 UE features list for Rel-17 NR in [1].

# Summary of Contributions Submitted to RAN1 #106bis-e

The following is the moderator’s summary of contributions submitted to RAN1 #106bis-e in this agenda item.

| 34. NR_DSS | 34-1 | Cross-carrier scheduling from SCell to PCell/PSCell (Type B) | Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ | 6-5 | Yes |  |  | Per BC | N | N |  | sSCell can only be configured in FR1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Summary |
| --- | --- |
| ZTE [2] | 34. NR_DSS 34-1 Cross-carrier scheduling from SCell to PCell/PSCell (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell CIF configured on [sSCell/P(S)Cell] for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling |
| Vivo [3] | Regarding '1)CIF configured on sSCell for CCS from sSCell to PCell/PSCell' in the preliminary feature group, it should be corrected to 'CIF configured on PCell/PSCell is used for CCS from sSCell to PCell/PSCell' since the CIF is configured in the CrossCarrierSchedulingConfig of the scheduled cell(i.e., Pcell/PScell). In addition to the configuration of associated parameters for BD handling, UE also needs to report its capability to gNB so that gNB can provide a proper configuration. It is suggested to adding ‘UE reporting of associated parameters’. The capabilities of CCS with the same SCS and different SCS between scheduling cell and scheduled cell are defined separately in R15, mainly because CCS with different SCS is more complex than the case with same SCS. It is natural to define sScell scheduling Pcell with the same SCS and with different SCS as two capabilities, where the basic capability is sScell scheduling Pcell with the same SCS. 6-10 Cross carrier scheduling for the same numerology 1) Cross carrier scheduling for the same numerology with CIF where numerologies for scheduling cell and scheduled cell are same 6-10a Cross carrier scheduling for different numerologies 1) Cross carrier scheduling for the different numerologies with CIF where numerologies for scheduling cell and scheduled cell are different Since the WID is for FR1 CA and sScell can only be located in FR1, there is a difference between FR1 and FR2 for this feature, it is suggested adding 'Applicable to FR1 only' to the column 'Need of FR1/FR2 differentiation'. Proposal: For the UE feature on DSS, the following with the following changes should be considered Change '1)CIF configured on sSCell for CCS from sSCell to PCell/PSCell' to 'CIF configured on PCell/PSCell is used for CCS from sSCell to PCell/PSCell' Add UE reporting of associated parameters for BD handling CCS from sScell to Pcell for the same numerology and CCS from sScell to Pcell for different numerologies are defined as separate feature groups Add 'Applicable to FR1 only' to column 'Need of FR1/FR2 differentiation' 34. NR_DSS 34-1 Cross-carrier scheduling from SCell to PCell/PSCell for the same numerology (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell where numerologies for sSCell and PCell/PSCel are same CIF configured on Pcell/PScell is used on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ Applicable to FR1 only 34. NR_DSS 34-1a Cross-carrier scheduling from SCell to PCell/PSCell for different numerologies (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell where numerologies for sSCell and PCell/PSCel are different CIF configured on Pcell/PScell is used for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ Applicable to FR1 only |
| Huawei/HiSilicon [4] | Regarding the column of “Mandatory/Optional”, it is suggested to be “Optional with capability signalling” |
| Samsung [5] | For cross-carrier scheduling, NR has specified couple of UE capabilities in Rel-15/16 - Rel-15: FG 6-10, Cross carrier scheduling for the same numerology - Rel-16: FG 18-5, DL cross-carrier scheduling with different SCS - Rel-16: FG 18-5b, UL cross-carrier scheduling with different SCS In light of reusing existing capability as much as possible, combining above Rel-15/16 capabilities, the resulting Rel-17 UE feature would become as Table 1 below which includes: - The component description is simplified. - The description of Type A UE can be clarified further once RAN1 agrees. - CIF is covered by legacy capabilities and the prerequisite is updated accordingly. - FFSs are removed. Index Feature group Components Prerequisite feature groups 34-1 Cross-carrier scheduling from SCell to PCell/PSCell (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell (Type B) CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ 6-5, 6-10, 18-5, 18-5b |
| MediaTek Inc. [6] | In the Rel-17 DSS WID (RP-211345), it is noted that: This work item is limited to FR1, and includes the following objectives for NR Dynamic Spectrum Sharing (DSS): PDCCH enhancements for cross-carrier scheduling including [RAN1, RAN2] PDCCH of SCell scheduling PDSCH or PUSCH on P(S)Cell Note: The total PDCCH blind decoding budget should not be changed as a result of this work Note: These enhancements are not specific to DSS and are generally applicable to cross-carrier scheduling in carrier aggregation Since the feature of “SCell scheduling PDSCH or PUSCH on P(S)Cell” is not specific to DSS and is generally applicable to cross-carrier scheduling in carrier aggregation, we propose to divide the feature into 3 subfeatures: same numerology between sSCell and P(S)Cell lower-numerology sSCell scheduling higher-numerology P(S)Cell higher-numerology sSCell scheduling lower-numerology P(S)Cell In RAN1 #104-bis-e, RAN1 agrees the agreement below for Rel-17 DSS: Agreement PDCCH overbooking on sSCell USS set(s) is not allowed and we think this should be captured in the UE feature table. All Rel-17 UE features should be optional 34. NR_DSS 34-1a Cross-carrier scheduling from SCell to PCell/PSCell (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Same numerology between sSCell and P(S)Cell Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling 34. NR_DSS 34-1b Cross-carrier scheduling from SCell to PCell/PSCell (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Lower-numerology sSCell scheduling higher-numerology P(S)Cell 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling 34. NR_DSS 34-1c Cross-carrier scheduling from SCell to PCell/PSCell (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Higher-numerology sSCell scheduling lower-numerology P(S)Cell 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling |
| Intel Corporation [7] | The first bullet is regarding the CIF configuration. Since the CIF value is configured to PCell/PSCell using the CrossCarrierSchedulingConfig IE in the PCell/PSCell configuration, it is better to make it clear that the CIF is configured to PCell/PSCell. For the second bullet, it is helpful to explicitly capture sSCell USS set(s) means DCI format 0_1, 1_1, 0_2, 1_2 (if supported). The note only captures that ‘sSCell can only be configured in FR1’. Since DSS is currently a feature for FR1, it is more accurate to capture that ‘both PCell/PSCell and sSCell can only be configured in FR1’. 34-1 Cross-carrier scheduling from SCell to PCell/PSCell (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell CIF configured on sSCellto PCell/PSCell for CCS from sSCell to PCell/PSCell USS set(s) for DCI format 0_1,1_1,0_2,1_2 (if supported) configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ 6-5 PCell/PSCell and sSCell can only be configured in FR1 |
| Apple [8] |  |
| Ericsson [9] | We propose the above updates to the initial UE frature description capturing our view on #unicast DCI limits for the SCell to P(S)Cell cross-carrier scheduling. 34. NR_DSS 34-1 Cross-carrier scheduling from SCell to PCell/PSCell (Type B) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters #unicast DCI limits for PCell/PSCell scheduling When PCell/PSCell SCS ≤ sSCell SCS, processing of N1 unicast DCI(s) scheduling DL for P(S)Cell from sSCell and P(S)Cell, and N2 unicast DCI(s) scheduling UL for P(S)Cell from sSCell and P(S)Cell in slot(s) overlapping with one P(S)Cell slot (N1, N2) = ([1],[1]), ([2],[2]) for FDD P(S)Cell (N1, N2) = ([1],[2]), ([2],[4]) for TDD P(S)Cell FFS: limits for PCell/PSCell SCS > sSCell SCS case Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ 6-5 Yes Per BC N N sSCell can only be configured in FR1 |
| Qualcomm Incorporated [10] | The FG should NOT be per UE due to the difficulty of UE testing for all the frequency bands including licensed, unlicensed, and NTN bands. We consider that FG34-1 can be a basic capability to indicate the support of cross-carrier scheduling from a sSCell to PCell/PSCell. This includes minimum set of components, including Type-A monitoring, PCell/PSCell slot-level monitoring, narrowband precoding for a CORESET, etc. A UE should be able to indicate on which pair(s) of frequency band(s) the UE can support the combination(s) of {PCell/PSCell, sSCell}. For the PCell/PSCell, the SCS is only 15kHz. The frequency band(s) that can be configured as the PCell/PSCell is/are the band(s) where the UE reports support of FG5-28 (Rate-matching around LTE-CRS). 34. NR_DSS 34-1 Cross-carrier scheduling from SCell to PCell/PSCell (Type B) for DL and UL with search space restrictions (Type A) Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell with search space restrictions (Type A) CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured so such that the UE monitors does not monitor them in overlapping same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters (to be discussed in the Rel-17 WI) FFS: #unicast DCI limits for PCell/PSCell scheduling Processing one unicast DCI scheduling DL on PCell/PSCell per PCell/PSCell slot and its aligned N consecutive sSCell slot(s) Processing one unicast DCI scheduling UL on PCell/PSCell per PCell/PSCell slot and its aligned N consecutive sSCell slot(s) N={1, 2, 4} for {15kHz, 30kHz, 60kHz} SCS for sSCell Candidate pair(s) of frequency band(s) for {PCell/PSCell, sSCell} SCS of PCell/PSCell is 15kHz SCS of sSCell is {15kHz, 30kHz, 60kHz} The frequency band(s) that can be configured as the PCell/PSCell is/are the band(s) where the UE supports FG5-28 For CSS set(s) and USS set(s) on the PCell/PSCell and USS set(s) on the sSCell (for CCS from sSCell to PCell/PSCell), the monitoring occasion is within the first 3 OFDM symbols of a PCell/PSCell slot One CORESET configuration per BWP on sSCell for PCell/PSCell scheduling Total number of CORESET configuration(s) on PCell/PSCell and on sSCell for PCell/PSCell scheduling on the active BWPs is per FG3-1/FG3-3 Up to 3 search space sets per BWP on sSCell for PCell/PSCell scheduling Total number of search space sets on PCell/PSCell and on sSCell for PCell/PSCell scheduling on the active BWPs is up to 10 Precoder-granularity of REG bundle size FG3-7 is not applied to PCell/PSCell and sSCell if the UE is configured with cross-carrier scheduling from the sSCell to the PCell/PSCell PCell/PSCell and sSCell are frame boundary aligned Rel-15 PDCCH monitoring capability for PCell/PSCell and sSCell for PCell/PSCell scheduling A-CSI-RS on PCell/PSCell triggered by a DCI format received on sSCell {yes, no} Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with UE capability signalling |
| Nokia/Nokia Shanghai Bell [11] |  |

| 34. NR_DSS | 34-2 | Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) | Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling | 6-5 | Yes |  |  | Per BC | N | N |  | sSCell can only be configured in FR1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Summary |
| --- | --- |
| ZTE [2] | 34. NR_DSS 34-2 Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on [sSCell/P(S)Cell] for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling |
| Vivo [3] | The introduction of Type A UE was to reduce the PDCCH BD complexity by introducing restrictions on the simultaneous monitoring of DCIs from sScell and Pcell/PScell. The BD complexity of Type A UE also depends heavily on the BD processing options employed in addition to the simultaneous DCI monitoring restrictions. For Type A UE, if simultaneous monitoring of DCI from Pcell/PScell and sScell on the same instance is allowed, and BD/CCE processing option is the same as Type B UE, then the implementation complexity of Type A UE is the same as Type B UE and there is no need to define FG 34-2(Type A UE). If no simultaneous DCI monitoring is allowed and the BD/CCE processing option is different from Type B UE, we can support the introduction of FG 34-2 for Type A UE. Therefore, we propose to add a bracket to FG34-2 until further details of the Type A UE are finalized. Regarding '1)CIF configured on sSCell for CCS from sSCell to PCell/PSCell' in the preliminary feature group, it should be corrected to 'CIF configured on PCell/PSCell is used for CCS from sSCell to PCell/PSCell' since the CIF is configured in the CrossCarrierSchedulingConfig of the scheduled cell(i.e., Pcell/PScell). In addition to the configuration of associated parameters for BD handling, UE also needs to report its capability to gNB so that gNB can provide a proper configuration. It is suggested to adding ‘UE reporting of associated parameters’. The capabilities of CCS with the same SCS and different SCS between scheduling cell and scheduled cell are defined separately in R15, mainly because CCS with different SCS is more complex than the case with same SCS. It is natural to define sScell scheduling Pcell with the same SCS and with different SCS as two capabilities, where the basic capability is sScell scheduling Pcell with the same SCS. 6-10 Cross carrier scheduling for the same numerology 1) Cross carrier scheduling for the same numerology with CIF where numerologies for scheduling cell and scheduled cell are same 6-10a Cross carrier scheduling for different numerologies 1) Cross carrier scheduling for the different numerologies with CIF where numerologies for scheduling cell and scheduled cell are different Since the WID is for FR1 CA and sScell can only be located in FR1, there is a difference between FR1 and FR2 for this feature, it is suggested adding 'Applicable to FR1 only' to the column 'Need of FR1/FR2 differentiation'. Proposal: For the UE feature on DSS, the following with the following changes should be considered Add a bracket to Type A UE Change '1)CIF configured on sSCell for CCS from sSCell to PCell/PSCell' to 'CIF configured on PCell/PSCell is used for CCS from sSCell to PCell/PSCell' Add UE reporting of associated parameters for BD handling CCS from sScell to Pcell for the same numerology and CCS from sScell to Pcell for different numerologies are defined as separate feature groups Add 'Applicable to FR1 only' to column 'Need of FR1/FR2 differentiation' 34. NR_DSS 34-2 [Cross-carrier scheduling from SCell to PCell/PSCell for the same numerology with search space restrictions (Type A)] Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions where numerologies for sSCell and PCell/PSCel are same CIF configured on Pcell/PScell is used on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Applicable to FR1 only 34. NR_DSS 34-2 [Cross-carrier scheduling from SCell to PCell/PSCell for different numerologies with search space restrictions (Type A)] Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions where numerologies for sSCell and PCell/PSCel are different CIF configured on Pcell/PScell is used for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling Applicable to FR1 only |
| Huawei/HiSilicon [4] | Regarding the column of “Mandatory/Optional”, it is suggested to be “Optional with capability signalling” |
| Samsung [5] | For cross-carrier scheduling, NR has specified couple of UE capabilities in Rel-15/16 - Rel-15: FG 6-10, Cross carrier scheduling for the same numerology - Rel-16: FG 18-5, DL cross-carrier scheduling with different SCS - Rel-16: FG 18-5b, UL cross-carrier scheduling with different SCS In light of reusing existing capability as much as possible, combining above Rel-15/16 capabilities, the resulting Rel-17 UE feature would become as Table 1 below which includes: - The component description is simplified. - The description of Type A UE can be clarified further once RAN1 agrees. - CIF is covered by legacy capabilities and the prerequisite is updated accordingly. - FFSs are removed. Index Feature group Components Prerequisite feature groups 34-2 Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions (Type A) CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling 6-5, 6-10, 18-5, 18-5b |
| MediaTek Inc. [6] | In the Rel-17 DSS WID (RP-211345), it is noted that: This work item is limited to FR1, and includes the following objectives for NR Dynamic Spectrum Sharing (DSS): PDCCH enhancements for cross-carrier scheduling including [RAN1, RAN2] PDCCH of SCell scheduling PDSCH or PUSCH on P(S)Cell Note: The total PDCCH blind decoding budget should not be changed as a result of this work Note: These enhancements are not specific to DSS and are generally applicable to cross-carrier scheduling in carrier aggregation Since the feature of “SCell scheduling PDSCH or PUSCH on P(S)Cell” is not specific to DSS and is generally applicable to cross-carrier scheduling in carrier aggregation, we propose to divide the feature into 3 subfeatures: same numerology between sSCell and P(S)Cell lower-numerology sSCell scheduling higher-numerology P(S)Cell higher-numerology sSCell scheduling lower-numerology P(S)Cell In RAN1 #104-bis-e, RAN1 agrees the agreement below for Rel-17 DSS: Agreement PDCCH overbooking on sSCell USS set(s) is not allowed and we think this should be captured in the UE feature table. All Rel-17 UE features should be optional 34. NR_DSS 34-2a Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Same numerology between sSCell and P(S)Cell 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling 34. NR_DSS 34-2b Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Lower-numerology sSCell scheduling higher-numerology P(S)Cell 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling 34. NR_DSS 34-2c Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Higher-numerology sSCell scheduling lower-numerology P(S)Cell 6-5 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling |
| Intel Corporation [7] | The first bullet is regarding the CIF configuration. Since the CIF value is configured to PCell/PSCell using the CrossCarrierSchedulingConfig IE in the PCell/PSCell configuration, it is better to make it clear that the CIF is configured to PCell/PSCell. For the second bullet, it is helpful to explicitly capture sSCell USS set(s) means DCI format 0_1, 1_1, 0_2, 1_2 (if supported). Further, for FG 34-2, one more bullet can be added to capture no restriction for the overlap between Type0/0A/1/2 CSS sets on PCell/PSCell and USS sets on sSCell. However, the overlap handling between Type0/0A/1/2 CSS sets on PCell/PSCell and USS sets on sSCell is FFS. The note only captures that ‘sSCell can only be configured in FR1’. Since DSS is currently a feature for FR1, it is more accurate to capture that ‘both PCell/PSCell and sSCell can only be configured in FR1’. 34-2 Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCellto PCell/PSCell for CCS from sSCell to PCell/PSCell USS set(s) for DCI format 0_1,1_1,0_2,1_2 (if supported) configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and Type0/0A/1/2 CSS sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell. FFS overlap handling. FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling 6-5 PCell/PSCell and sSCell can only be configured in FR1 |
| Apple [8] |  |
| Ericsson [9] | We propose the above updates to the initial UE frature description capturing our view on #unicast DCI limits for the SCell to P(S)Cell cross-carrier scheduling. 34. NR_DSS 34-2 Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters #unicast DCI limits for PCell/PSCell scheduling When PCell/PSCell SCS ≤ sSCell SCS, processing of N1 unicast DCI(s) scheduling DL for P(S)Cell from sSCell and P(S)Cell, and N2 unicast DCI(s) scheduling UL for P(S)Cell from sSCell and P(S)Cell in slot(s) overlapping with one P(S)Cell slot (N1, N2) = ([1],[1]), ([2],[2]) for FDD P(S)Cell (N1, N2) = ([1],[2]), ([2],[4]) for TDD P(S)Cell FFS: limits for PCell/PSCell SCS > sSCell SCS case 6-5 Yes Per BC N N sSCell can only be configured in FR1 |
| Qualcomm Incorporated [10] | them in [slot/symbol] of PCell/PSCell and sSCell Yes Per BC N N sSCell can only be configured in FR1 34-2 Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) for DL and UL without search space restrictions (Type B) Support of Cross-carrier scheduling from sSCell to PCell/PSCell without search space restrictions (Type B) CIF configured on sSCell for CCS from sSCell to PCell/PSCell Candidate pair(s) of frequency band(s) for {PCell/PSCell, sSCell} among the candidate pair(s) reported in FG34-1 sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured sosuch that the UE does not monitor monitors them in same overlapping [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling 6-5 34-1 Yes Per BC N N sSCell can only be configured in FR1 Optional with UE capability signalling |
| Nokia/Nokia Shanghai Bell [11] |  |

| 35. LTE_NR_DC_enh2 | 35-1 | Temporary RS based SCell activation | SCell activation with the assistance of temporary RS Temporary RS is aperiodic and triggered by MAC CE. | 6-5 | Yes | N/A |  | Per UE[/Per BC] | No | No |  |  | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Summary |
| --- | --- |
| ZTE [2] | 35. LTE_NR_DC_enh2 35-1 Temporary RS based SCell activation SCell activation with the assistance of temporary RS Temporary RS is aperiodic and triggered by MAC CE. 6-5 Yes N/A Per UE No No Optional with capability signalling |
| Vivo [3] |  |
| Huawei/HiSilicon [4] |  |
| Samsung [5] |  |
| MediaTek Inc. [6] |  |
| Intel Corporation [7] | According to RAN1 agreements, temporary RS will be based on aperiodic TRS and FFS other signals, e.g. CSI-RS for CSI measurement. It is necessary to make this design clear. It is beneficial to capture per RAN1 agreement that temporary RS is only configured within the BWP indicated by firstActiveDownlinkBWP-Id for the sSCell. Further, a RAN1 working assumption is that a SSB of the to-be-activated SCell can be indicated as a QCL source for the temporary RS in case of known SCell Proposal: • Propose to capture temporary RS is based on aperiodic TRS and FFS other signals • Propose to capture temporary RS is only configured within the BWP indicated by firstActiveDownlinkBWP-Id • Propose to capture QCL source for temporary RS 35-1 Temporary RS based SCell activation SCell activation with the assistance of temporary RS Temporary RS is aperiodic and triggered by MAC CE. Temporary RS is based on aperiodic TRS and FFS other signals Temporary RS is only configured within the BWP indicated by firstActiveDownlinkBWP-Id for the sSCell A SSB of the to-be-activated SCell can be indicated as a QCL source for the temporary RS in case of known SCell 6-5 |
| Apple [8] |  |
| Ericsson [9] | We propose the above updates to the initial UE feature description to align the description with below RAN1 #102-e agreement (Note: other than TRS, no other RS candidates have been agreed in subsequent meetings). Agreements: TRS is selected as temporary RS for Scell activation · If more functionalities are confirmed to be supported by temporary RS, other RS candidates, e.g. aperiodic CSI-RS, P/SP-CSI RS, SRS and RS based on SSS/PSS, are not precluded. · The TRS should be triggered by DCI or MAC-CE. FFS which exact triggering command. 35. LTE_NR_DC_enh2 35-1 TRS for SCell activation SCell activation with the assistance of TRS TRS is aperiodic and triggered by MAC CE. 6-5 Yes N/A Per UE[/Per BC] No No Optional with capability signalling |
| Qualcomm Incorporated [10] | FG35-1 should be per-BC and contains components that indicate max numbers of temporary RSs per CC and per UE, max number of trigger states, and max number of temporary RSs that can be associated with a trigger state. We assume that a temporary RS is constructed by multiple NZP-CSI-RS resources/resource sets and therefore, max numbers of NZP-CSI-RS resources/resource sets are subject to FG2-33. 35. LTE_NR_DC_enh2 35-1 Temporary RS based SCell activation SCell activation with the assistance of temporary RSSCell activation with the assistance of temporary RS triggered by MAC CE Temporary RS is aperiodic and triggered by MAC CE.Maximum number of temporary RS resource sets that can be configured to UE per CC {1 … 16} Maximum number of temporary RS resource sets that can be configured to UE across CCs {1 … 256} Maximum number of triggering states for temporary RS based SCell activation by a MAC-CE {1 … 64} Maximum number of temporary RS resource sets that can be associated with a triggering state {1 … 16} Note: following are reported via the legacy feature, FG2-33 Maximum number of configured NZP-CSI-RS resources per CC Maximum total number of simultaneous NZP-CSI-RS resources in active BWPs across all CCs Maximum number simultaneous NZP-CSI-RS resources per CC Maximum total number of CSI-RS ports in simultaneous NZP-CSI-RS resources in active BWPs across all CCs 6-5 Yes N/A Per UE[/Per BC] No No Optional with capability signalling |
| Nokia/Nokia Shanghai Bell [11] | o Type can be confirmed as “per UE”. o Need for FR1/FR2 differentiation should be ”yes”, since testability needs have shown that in cases like this FR differentiation has been needed. |

Other Comments

| Company | Summary |
| --- | --- |
| ZTE [2] |  |
| Vivo [3] |  |
| Huawei/HiSilicon [4] | The following agreement was made in RAN1#106: Agreement: Specification supports dormant BWP operation on sSCell for a UE is configured CCS from sSCell to P(S)Cell. It can be seen that whether dormant BWP operation is supported on sSCell for a UE is configured CCS from sCell to P(S)Cell should be specified, therefore gNB should be informed with UE capability. Proposal: UE feature regarding dormant BWP operation on sSCell for a UE is configured CCS from sSCell to P(S)Cell needs to be informed to gNB 34. NR_DSS 34-3 Dormant BWP operation on sSCell for a UE is configured CCS from sSCell to P(S)Cell. Support dormant BWP operation on sSCell for a UE is configured CCS from sSCell to P(S)Cell One of FG 34-1 and FG 34-2 Yes Per BC N N sSCell can only be configured in FR1 Optional with capability signalling |
| Samsung [5] | A Rel-16 UE can support DSS without hardware or specification impact for PDCCH monitoring if the UE is not required to monitor PDCCH on the P(S)Cell and on the sSCell in a same slot (slot is the one of smallest SCS in case of different SCS on P(S)Cell and sSCell); the only feature that the UE needs to support for DSS is scheduling the P(S)Cell from a sSCell. Such a solution can be considered a low-complexity design for DSS operation, which is the purpose for supporting Type-A UEs. Any other description for a Type-A UE that would lead to an exception for non-simultaneous / TDM’ed PDCCH monitoring on two scheduling cells, such as for non-Type-3 CSS on P(S)Cell, will not constitute a low-complexity design for supporting DSS operation: they will be simply Type-B UEs with certain (arbitrary) restrictions/features without any benefit to UE implementation. Observation: A UE can support DSS based on Rel-16 PDCCH monitoring where the UE does not monitor PDCCH for a scheduled cell from two scheduling cells in a same slot (for smallest SCS). The only requirement for a UE to support DSS is to support a scheduling SCell (sSCell) for the P(S)Cell. Proposal: For Type-A UE, the only requirement is to support a scheduling SCell (sSCell) for the P(S)Cell. Regarding whether/how to capture Type-A UEs in (RAN1) specification, there is currently no apparent reason to provide specification support for a Type-A UE. UE types may not be specified at all, and a Type-A UE can be a UE that supports DSS but does not support the requirements of a Type-B UE as they will be defined in UE features (according to corresponding specifications). For example, RAN1 specifications can refer to Type-B UEs based on potential related RRC configurations, such as RRC parameters for PDCCH monitoring allocation (0≤α≤1 and 0≤β≤1) among P(S)Cell and sSCell. In that case, RAN1 specifications can refer to Type-A UEs as ones with an sSCell configuration for P(S)Cell scheduling, but lacking configuration for Type-B-related RRC parameters. Observation: RAN1 specifications may not need to refer to DSS UE Types at all. |
| MediaTek Inc. [6] |  |
| Intel Corporation [7] | The current agreement is sSCell dormancy/deactivation can be supported, however, it is clear it is mandatory or optional. Since the feature CCS from sSCell to PCell/PSCell works without support of sSCell dormancy or deactivation, a new FG 34-A can be added with prerequisite feature groups 34-1 or 34-2. 34-A sSCell deactivation FFS maximum BD/CCE of PCell/PSCell when sSCell is deactivated FFS implicitly SSSG switching when sSCell is deactivated 34-1 or 34-2 34-B sSCell dormancy switching FFS maximum BD/CCE of PCell/PSCell when sSCell is dormant FFS implicitly SSSG switching when sSCell is dormant 34-1 or 34-2 |
| Apple [8] | • We propose to introduce a new FG or add one component to the proposed UE FG34-2 to cover another simplified Type A UE, i.e., the USS can only be configured on sSCell, but cannot be configured on SpCell. • The SCS that UE can support for sSCell. Even though we agree to support both the sSCell activation/deactivation and sSCell dormancy. Its operation is in contrary to the objective of this WID, i.e., to enable sSCell scheduling SpCell to improve DSS performance. From UE performance perspective, we would prefer to ensure reliable and good performance on the primary cell as much as possible, therefore • We propose UE feature on whether UE support sSCell deactivation/activation • We propose UE feature on whether UE support sSCell dormancy 34. NR-DSS 34-2a Further restriction to Type A Support of monitoring DCI formats 0_1,1_1,0_2,1_2 on PCell/PSCell USS set(s), 34-2 Yes N/A Per BC N N Optional with capability signalling 34. NR-DSS 34-3 Supported SCS of sSCell Support SCS of sSCell 34-1/34-2 Yes N/A Per BC N N Component 1: {15kHz, 15kHz and 30kHz, 15kHz and 30kHz and 60kHz} Optional with capability signalling 34. NR-DSS 34-4 Support of sSCell deactivation/activation Support of sSCell deactivation/activation when sSCell cross carrier scheduling to PCell/PSCell is configured 34-1/34-2 Yes N/A Per BC N N Optional with capability signalling 34. NR-DSS 34-5 Support of sSCell dormancy Support of sSCell dormancy when sSCell cross carrier scheduling to PCell/PSCell is configured 34-1/34-2 Yes N/A Per BC N N Optional with capability signalling |
| Ericsson [9] |  |
| Qualcomm Incorporated [10] | Add the following new feature groups 34-3 Additional PDCCH monitoring occasion on PCell/PSCell and sSCell for PCell/PSCell scheduling Additional PDCCH monitoring occasion(s) on PCell/PSCell and sSCell for PCell/PSCell other than the one in FG34-1 Consider to re-use the span-based PDCCH monitoring defined for FG3-5b where the UE reports (X, Y) where the SCS should be 15kHz. FFS details. The additional PDCCH monitoring occasion(s) is common for PDCCH monitored on PCell/PSCell and on sSCell for PCell/PSCell scheduling Candidate pair(s) of frequency band(s) for {PCell/PSCell, sSCell} among the candidate pair(s) reported in FG34-1 For the set of monitoring occasions which are within the same span: Processing one unicast DCI scheduling DL and one unicast DCI scheduling UL on PCell/PSCell across the set of monitoring occasions 34-1 Per BC N N Optional with UE capability signalling 34-4 More than one CORESET configuration on sSCell per BWP for PCell/PSCell scheduling More than one CORESET configuration on sSCell per BWP for PCell/PSCell scheduling Total number of CORESET configuration(s) on PCell/PSCell and on sSCell for PCell/PSCell scheduling on the active BWPs is per FG3-1/FG3-3 34-1 Per BC N N Optional with UE capability signalling 34-5 Up to 10 search space sets in a PCell/PSCell slot for scheduling PCell/PSCell Up to 10 search space sets per BWP on sSCell for PCell/PSCell scheduling Total number of search space sets on PCell/PSCell and on for PCell/PSCell scheduling on the active BWPs can be up to 10 34-1 Per BC N N Optional with UE capability signalling 34-6 Precoder-granularity of CORESET size when CCS from sSCell to PCell/PSCell is configured Precoder granularity of CORESET size can be configured {on sSCell, on PCell/PSCell, on both sSCell and PCell/PSCell} Candidate pair(s) of frequency band(s) for {PCell/PSCell, sSCell} among the candidate pair(s) reported in FG34-1 34-1 Per BC N N Optional with UE capability signalling |
| Nokia/Nokia Shanghai Bell [11] |  |

# Discussion/Approval Items during RAN1 #106bis-e

After review of contributions submitted to RAN1 #106bis-e in this agenda item, the following topics were identified by the moderator for discussion/approval during RAN1 #106bis-e. Companies submitted the following views on the moderator’s proposals.

# FG 34-1: Cross-carrier scheduling from SCell to PCell/PSCell (Type B)

The preliminary RAN1 NR UE feature list in [1] was submitted to RAN1 #106-e for information only. It is important that during RAN1 #106bis-e, we agree a formal baseline for RAN1 #107-e. The focus of this meeting is thus to agree on the number of rows/FGs whereas the details of each row/FG can be discussed at RAN1 #107-e and beyond. There seems to be consensus that this FG is needed. Regarding the FFS points, only those should be discussed during RAN1 #106bis-e whose resolution may result in the introduction of new feature groups (see proposals in Section 3.4).

Proposal: Agree the following feature group incl. any changes highlighted in red as baseline for further discussions during RAN1 #107-e

  - FFS points whose resolution may result in the introduction of new feature groups can be discussed during RAN1 #106bis-e

| 34. NR_DSS | 34-1 | Cross-carrier scheduling from SCell to PCell/PSCell (Type B) | [Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell (Type B)] FFS: CIF configured on [sSCell/P(S)Cell] [is used] for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling FFS: PDCCH overbooking on sSCell USS set(s) is not allowed FFS: Same numerology between sSCell and P(S)Cell FFS: USS set(s) for DCI format 0_1,1_1,0_2,1_2 (if supported) configured on sSCell for CCS from sSCell to PCell/PSCell Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ | 6-5[, 6-10, 18-5, 18-5b] | Yes |  |  | Per BC | No | N Applicable to FR1 only |  | sSCell can only be configured in FR1 | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | General structure We suggest to start with the basic/minimum components for cross-carrier scheduling from sSCell to PCell/PSCell for FG34-1, which we think must be Type-A and slot-based PDCCH monitoring. The other advanced features can be separate FGs with FG34-1 as prerequisite. Current proposal is structured such that FG34-1 is Type B and FG34-2 is Type A. With this, for any new FGs, we have to make FG34-1 or FG34-2 as prerequisite. It is also unclear whether the current FG34-1 and FG34-2 are mutually exclusive or not. For example, if a UE indicates support of FG34-1 but does not indicate support of FG34-2, does it mean the UE supports Type-B but not Type-A? Granularity of this capability indication Suppose a UE reports support of CA band combination that includes some 15kHz bands and some 30kHz bands. The current FG34-1 is a simple per-BC. Does this mean that the UE can indicate support of FG34-1 only if the implementations/tests for all the possible combinations of {PCell/PSCell, sSCell} carriers in the BC being completed? We think this is unrealistic. At least the UE should be able to indicate following two as part of this per-BC capability: (1) subcarrier spacing for sSCell, (2) frequency band pair(s) for {PCell/PSCell, sSCell}. We consider this is a fundamental aspect and hence should be considered to begin with. |
| Apple | We are fine to have a general FG34-1 as place holder to discuss the potential components for Type B UE |
| Nokia, NSB | We are ok with the basic structure to start with, but more discussion will be needed. OK to keep the list of FFS points there as reminders, but there is little point in working on them further until the WI has progressed on them. It does make sense to have a way to indicate same SCS, low-to-high, high-to-low in the end of the day, but that can be a component out of the FFS point 6) rather than splitting this to multiple FGs, unless we end up with some other components being a function of this one (the BD ones might), but that’s something that can be resolved in/after November Regarding Qualcomm’s comment above, we think the granularity of the signaling should be per BC, as proposed. Having said that we are OK to consider limitations due to subcarrier spacing on sSCell, as indicated by Qualcomm above. It should be noted that 6-9 and 6-9a already allows to differentiate the SCS of PCells and SCells, and it is not clear if anything beyond that is truly necessary. In any case, if needed a similar framework could be pursued instead of frequency band pair indication. |
| Huawei, HiSilicon | Generally OK to start with. Also prefer to per BC – the consideration raised by QC is something that was also discussed in R16. We understand the intention, however such approach would cause much more signaling that is truly needed from implementation point of view. |
| Samsung | With respect to the number of rows/FGs, we are fine with FG 34-1 for Type B UE. On the details of FG 34-1 (though it is not the main focus as per FL guidance), we have the following suggestions: Item 1) can be rephrased as “Cross-carrier scheduling from sSCell to P(S)Cell with CIF” for clarity. Item 5) is already RAN1 agreement, i.e., without FFS. However, it seems not essential to define the feature group for Type B UE. Prefer to remove it. For Item 6), since DSS scenario is FR1 only and 15kHz SCS for PCell, the SCS combination of {PCell, sSCell} would be either {15kHz, 15kHz} or {15kHz, 30kHz}. In terms of maximizing the use case and avoiding fragmentation, we suggest to keep both same and different numerology between sSCell and P(S)Cell for this FG 34-1. Referring to Rel-16 UE capability of crossCarrierSchedulingDL-DiffSCS-r16 ENUMERATED {low-to-high, high-to-low, both}, the possible value of SCS combination for DSS would be {15khzAnd15khz, 15khzAnd30khz, both}. For Item 7), we don’t see the need to include item 7) as part of FG 34-1 definition. Agree to include as 6-10, 18-5, 18-5b additional pre-requisites. |
| vivo | Support to have a separate FG for type B UE, but type B UE is an advanced feature compared with type A UE, so the FG No. should be changed to 34-2. The details of the capability indication shall be considered. If only BC information is indicated (e.g., band A+band B is indicated by UE capability), then it means that the UE is mandated to support all potential combinations of Pcell+sScell on the bands belonging to the BC, e.g., Pcell on band A+sScell on band B, and sScell on band A+ Pcell on band B. However, this unnecessarily complicates UE implementation. UE should further indicate other details, e.g., which band of the BC it can support for Pcell or sScell when sScell to schedule Pcell is configured. The details can be included as components of the type A/type B UE, or they can be indicated separately. FFS details of the capability indication, e.g., which band is supported as Pcell/PScell, and which band is supported as sScell Regarding the Prerequisite feature groups, it is preferred not to couple sScell scheduling Pcell with legacy CCS FG(i.e., 6-10, 18-5, 18-5b) for simplicity, so we suggest that only 6-5 can be kept. 6-5[, 6-10, 18-5, 18-5b] |
| Intel | We are fine to define FG 34-1 for Type B UE. In the current RAN1 discussion, there is no clue that a Type B UE must support operation of Type A UE. We are open for discussion on this point. Regarding item 6), we prefer to allow same SCS, sSCell with lower SCS and sSCell with higher SCS. Though the current WI is for DSS, the feature itself applies in general. This is similar to extend UE features for unlicensed to licensed operation. We are fine with 6-10, 18-5, 18-5b as additional pre-requisites |
| MTK | Support to have a separate FG for type B UE, but type B UE is an advanced feature compared with type A UE, so the FG No. should be changed to 34-2. The possible value of SCS combination can be {15khzSpCellAnd15khzSCell, 15khzSpCellAnd30khzSCell, both} The granularity of the signaling should be per BC as suggested by QC We prefer to keep item 5) without FFS to capture RAN1 agreement vivo’s comment on potential combinations of Pcell+sScell on the bands belonging to the BC is valid. Support to add the FFS: FFS details of the capability indication, e.g., which band is supported as Pcell/PScell, and which band is supported as sScell With “6-5[, 6-10, 18-5, 18-5b]” captured in prerequisite feature groups, does this mean the SCS combinations reported by UE for “6-5[, 6-10, 18-5, 18-5b]” are also supported by this feature? |
| ZTE | We are supportive to have FG34-1 as a placeholder for type B UE for sSCell scheduling PCell. The details of components can be further discussed when more agreements are mature. |
| Ericsson1 | OK to have 34-1 for Type B UE Prerequisites Only DL CA [6-5] is prerequisite. Other FGs are related features and not prerequisites and should not be added (i.e., a UE supporting this FG may also support other cross-carrier scheduling related FGs but no reason to mandate UE support of those other CCS combinations). If companies prefer to discuss other FGs as prerequisites, OK to mark those as FFS but they should not be added as “baseline for further discussion” FR1/FR2 differentiation Column should be empty until it is clear how to capture the aspect of restricting sSCell to FR1 only. “sSCell can only be configured in FR1“ can be added as a comment in red (i.e., baseline for further discussion) as that is common understanding. Components 1) Agree with Samsung proposed rephrasing as “Cross-carrier scheduling from sSCell to P(S)Cell with CIF” for clarity. That may remove the need to have FFS, red text etc. 6) Agreements so far have been for “at least P(S)Cell SCS less than or equal to sSCell SCS”. So, that text can be used as baseline for further discussion. Or the component can be removed for now. We are open to indicate the supported SCS combinations as suggested by other companies and this can be discussed further 7)Should be deleted. It does not apply to Type B UE. The “if supported” is only for Type A UE per agreements. |

# FG 34-2: Cross-carrier scheduling from SCell to Pcell/PSCell [with search space restrictions] (Type A)

The preliminary RAN1 NR UE feature list in [1] was submitted to RAN1 #106-e for information only. It is important that during RAN1 #106bis-e, we agree a formal baseline for RAN1 #107-e. The focus of this meeting is thus to agree on the number of rows/FGs whereas the details of each row/FG can be discussed at RAN1 #107-e and beyond. There seems to be consensus that this FG is needed. Regarding the FFS points, only those should be discussed during RAN1 #106bis-e whose resolution may result in the introduction of new feature groups (see proposals in Section 3.4).

Proposal: Agree the following feature group incl. any changes highlighted in red as baseline for further discussions during RAN1 #107-e

  - FFS points whose resolution may result in the introduction of new feature groups can be discussed during RAN1 #106bis-e

| 34. NR_DSS | 34-2 | Cross-carrier scheduling from SCell to Pcell/PSCell [with search space restrictions] (Type A) | Support of Cross-carrier scheduling from sSCell to Pcell/PSCell [with search space restrictions] (Type A) FFS: CIF configured on [sSCell/P(S)Cell] [is used] for CCS from sSCell to Pcell/PSCell FFS: sSCell USS set(s) (for CCS from sSCell to Pcell/PSCell) and at least following search space sets on Pcell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of Pcell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for Pcell/PSCell scheduling FFS: PDCCH overbooking on sSCell USS set(s) is not allowed FFS: Same numerology between sSCell and P(S)Cell FFS: USS set(s) for DCI format 0_1,1_1,0_2,1_2 (if supported) configured on sSCell for CCS from sSCell to Pcell/PSCell FFS: sSCell USS set(s) (for CCS from sSCell to Pcell/PSCell) and Type0/0A/1/2 CSS sets on Pcell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of Pcell/PSCell and sSCell. FFS overlap handling | 6-5[, 6-10, 18-5, 18-5b] | Yes |  |  | Per BC | No | No Applicable to FR1 only |  | sSCell can only be configured in FR1 | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | General structure As we have commented to FG34-1, it is unclear why Type-B is the first FG and Type-A is the second FG. Does this mean a UE is allowed to report FG34-1 only? |
| Apple | We are fine to have a general FG34-2 as place holder to discuss the potential components for Type A UE |
| Nokia, NSB | We are OK with the FG as starting point, but more discussion will be needed. |
| Huawei, HiSilicon | Generally OK to start with. |
| Samsung | With respect to the number of rows/FGs, we are fine with FG 34-2 for Type A UE. On the details of FG 34-2 (though it is not the main focus as per FL guidance), we have the following suggestions: Title of this FG “[with search space restrictions]” may need to be revised depending on ongoing RAN1 discussions. Item 1) can be rephrased as “Cross-carrier scheduling from sSCell to P(S)Cell with CIF” for clarity. (same comment above) Item 2) and 8) need to be revised based on ongoing RAN1 discussions. Current formulation of Type-A as in item 2) and 8) are not acceptable. Item 5) is already RAN1 agreement, i.e., without FFS. However, it seems not essential to define the feature group for Type A UE. Prefer to remove it. (same comment above) For Item 6), since DSS scenario is FR1 only and 15kHz SCS for PCell, the SCS combination of {PCell, sSCell} would be either {15kHz, 15kHz} or {15kHz, 30kHz}. In terms of maximizing the use case and avoiding fragmentation, we suggest to keep both same and different numerology between sSCell and P(S)Cell for this FG 34-2. Referring to Rel-16 UE capability of crossCarrierSchedulingDL-DiffSCS-r16 ENUMERATED {low-to-high, high-to-low, both}, the possible value of SCS combination for DSS would be {15khzAnd15khz, 15khzAnd30khz, both}. (same comment above) For Item 7), we don’t see the need to include item 7) as part of FG 34-2 definition. (same comment above) Agree to include as 6-10, 18-5, 18-5b additional pre-requisites. (same comment above) |
| vivo | Support to have a separate FG for type A UE if SS restrictions and a simple BD handling scheme (e.g., option B) is considered, but type A UE for the same Pcell/sScell numerology case should be the basic feature while type A UE for different numerologies and type B UE are advanced feature on top of it. Thus, the feature group number of type A with the same Pcell/sScell numerology should be 34-1, and a separate feature group 34-1a of type A UE with different Pcell/sScell numerologies should be introduced. The details of the capability indication shall be included in the FFS details of the capability indication, e.g., which band is supported as Pcell/PScell, and which band is supported as sScell And regarding the Prerequisite feature groups, as we commented to type B UE, only 6-5 can be kept. 6-5[, 6-10, 18-5, 18-5b] |
| Intel | OK to have this feature |
| MTK | Support to have a separate FG for type A UE, but type A UE is an basic feature compared with type B UE, so the FG No. should be changed to 34-1. The possible value of SCS combination can be {15khzSpCellAnd15khzSCell, 15khzSpCellAnd30khzSCell, both} The granularity of the signaling should be per BC as suggested by QC We prefer to keep item 5) without FFS to capture RAN1 agreement vivo’s comment on potential combinations of Pcell+sScell on the bands belonging to the BC is valid. Support to add the FFS: FFS details of the capability indication, e.g., which band is supported as Pcell/PScell, and which band is supported as sScell With “6-5[, 6-10, 18-5, 18-5b]” captured in prerequisite feature groups, does this mean the SCS combinations reported by UE for “6-5[, 6-10, 18-5, 18-5b]” are also supported by this feature? |
| ZTE | We are ok to have a placeholder for type A UE. However, most of the functionalities of type A UE have not finalized yet, it is difficult to discuss the details at this stage. |
| Ericsson1 | OK to have 34-2 for Type A UE Prerequisites Only DL CA [6-5] is prerequisite. Other FGs are related features and not prerequisites and should not be added (i.e., a UE supporting this FG may also support other cross-carrier scheduling related FGs but no reason to mandate UE support of those other CCS combinations). If companies prefer to discuss other FGs as prerequisites, OK to mark those as FFS but they should not be added as “baseline for further discussion” FR1/FR2 differentiation Column should be empty until it is clear how to capture the aspect of restricting sSCell to FR1 only. “sSCell can only be configured in FR1“ can be added as a comment in red (i.e., baseline for further discussion) as that is common understanding. Components 1) Agree with Samsung proposed rephrasing as “Cross-carrier scheduling from sSCell to P(S)Cell with CIF” for clarity. That may remove the need to have FFS, red text etc. 6) Agreements so far have been for “at least P(S)Cell SCS less than or equal to sSCell SCS”. So, that text can be used as baseline for further discussion. Or the component can be removed for now. We are open to indicate the supported SCS combinations as suggested by other companies and this can be discussed further |

# FG 35-1: Temporary RS SCell activation

The preliminary RAN1 NR UE feature list in [1] was submitted to RAN1 #106-e for information only. It is important that during RAN1 #106bis-e, we agree a formal baseline for RAN1 #107-e. The focus of this meeting is thus to agree on the number of rows/FGs whereas the details of each row/FG can be discussed at RAN1 #107-e and beyond. There seems to be consensus that this FG is needed. Regarding the FFS points, only those should be discussed during RAN1 #106bis-e whose resolution may result in the introduction of new feature groups (see proposals in Section 3.4).

Proposal: Agree the following feature group incl. any changes highlighted in red as baseline for further discussions during RAN1 #107-e

  - FFS points whose resolution may result in the introduction of new feature groups can be discussed during RAN1 #106bis-e

| 35. LTE_NR_DC_enh2 | 35-1 | [TRS\Temporary] RS [based/for] SCell activation | [SCell activation with the assistance of temporary RS/TRS] [TRS\Temporary RS] is aperiodic and triggered by MAC CE. FFS: Temporary RS is based on aperiodic TRS and FFS other signals FFS: Temporary RS is only configured within the BWP indicated by firstActiveDownlinkBWP-Id for the sSCell FFS: A SSB of the to-be-activated SCell can be indicated as a QCL source for the temporary RS in case of known SCell FFS: Maximum number of temporary RS resource sets that can be configured to UE per CC {1 … 16} FFS: Maximum number of temporary RS resource sets that can be configured to UE across CCs {1 … 256} FFS: Maximum number of triggering states for temporary RS based SCell activation by a MAC-CE {1 … 64} FFS: Maximum number of temporary RS resource sets that can be associated with a triggering state {1 … 16} [Note: following are reported via the legacy feature, FG2-33 Maximum number of configured NZP-CSI-RS resources per CC Maximum total number of simultaneous NZP-CSI-RS resources in active BWPs across all CCs Maximum number simultaneous NZP-CSI-RS resources per CC Maximum total number of CSI-RS ports in simultaneous NZP-CSI-RS resources in active BWPs across all CCs] | 6-5 | Yes | N/A |  | [Per UE[/Per BC] | No | [No/Yes] |  |  | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | We are OK with having the row. We do not think per-UE makes sense, considering the UE testing differentiation among licensed, unlicensed, and NTN band. |
| Nokia, NSB | We are OK with the row. We don’t see the motivation for FFS points 4) – 8) though, but this anyway needs to wait for the decisions in the WI before finetuning the components. Per UE is the right granularity, with FR1/FR2 differentiation. The issue of differentiation between licensed and unlicensed has been resolved already in Rel-16, and same solution applies to Rel-17 features as well, with extension to NTN if needed. |
| vivo | Fine with the row in principle, but we think this FG should be per band or per BC. We are not sure why the following rows are needed FFS: Temporary RS is based on aperiodic TRS and FFS other signals FFS: Temporary RS is only configured within the BWP indicated by firstActiveDownlinkBWP-Id for the sSCell FFS: A SSB of the to-be-activated SCell can be indicated as a QCL source for the temporary RS in case of known SCell Further, the motivation and use case of FR1/FR2 differentiation should be clarified. |
| Intel | We are OK to start with this FG. |
| MTK | Fine with the row in principle, support per BC. Some of the FFS (as mentioned by vivo) are already RAN1 agreements so the “FFS” can be removed. |
| Huawei, HiSilicon | OK with the row. Share similar view with Nokia that Per UE is sufficient and the Rel-16 solution to differentiate licensed and unlicensed bands can be reused. |
| ZTE | Ok with the row to start with. |
| Ericsson1 | OK with having a row for 35-1 Prefer to use [TRS/Temporary RS] in all components. |

# Additional feature groups in the 34-x family of DSS features

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34. NR_DSS | 34-1a | Cross-carrier scheduling from SCell to Pcell/PSCell for different numerologies (Type B) | Support of Cross-carrier scheduling (CCS) from sSCell to Pcell/PSCell where numerologies for sSCell and Pcell/PSCel are different CIF configured on Pcell/Pscell is used for CCS from sSCell to Pcell/PSCell sSCell USS set(s) (for CCS from sSCell to Pcell/PSCell) and search space sets on Pcell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of Pcell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for Pcell/PSCell scheduling Note: The SCell configured with Cross-carrier scheduling to Pcell/PSCell is referred to as ‘sSCell’ |  |  |  |  |  |  | Applicable to FR1 only |  |  | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | As we have indicated for FG34-1, it is important to allow a UE to be able to report its support of sSCell numerology. If we specify a new row, the UE should be able to indicate which SCS can be configured for sSCell. |
| Apple | We think it is important for UE to indicate the supported SCS of sSCell even thought the detailed FG can be up for FFS |
| Nokia, NSB | As commented above, it would be preferrable to make them components rather than separate capabilities |
| Samsung | No need for FG 34-1a. As commented above, FG 34-1 can include both same and different numerology between sSCell and P(S)Cell. |
| vivo | Support to have a FG for mixed numerologies case |
| Intel | We don’t think differentiation of numerology needed, since RAN1 is currently designing common solution for P(S)Cell/sSCell with same or different numerology |
| MTK | We are fine to either introduce this new FG group or introduce the SCS combination as components of FG 34-1/34-2. |
| Ericsson1 | We do not see need for this FG. Can be part of 34-1 |

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34. NR_DSS | 34-1b | Cross-carrier scheduling from SCell to Pcell/PSCell (Type B) | Support of Cross-carrier scheduling (CCS) from sSCell to Pcell/PSCell CIF configured on sSCell for CCS from sSCell to Pcell/PSCell sSCell USS set(s) (for CCS from sSCell to Pcell/PSCell) and search space sets on Pcell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of Pcell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for Pcell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Lower-numerology sSCell scheduling higher-numerology P(S)Cell | 6-5 | Yes |  |  | Per BC | N | N |  | sSCell can only be configured in FR1 | Optional with capability signaling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34. NR_DSS | 34-1c | Cross-carrier scheduling from SCell to Pcell/PSCell (Type B) | Support of Cross-carrier scheduling (CCS) from sSCell to Pcell/PSCell CIF configured on sSCell for CCS from sSCell to Pcell/PSCell sSCell USS set(s) (for CCS from sSCell to Pcell/PSCell) and search space sets on Pcell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of Pcell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters FFS: #unicast DCI limits for Pcell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Higher-numerology sSCell scheduling lower-numerology P(S)Cell | 6-5 | Yes |  |  | Per BC | N | N |  | sSCell can only be configured in FR1 | Optional with capability signalling |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | We think Pcell/PSCell for this scenario is a carrier with SCS 15kHz and hence the proposed 34-1b is NOT necessary. |
| Apple | We think the P(S)Cell can only have 15KHz. So the oonly issue we need to discuss is higher SCS sSCell to schedule P(S)Cell This is another proposal to indicate the supported SCS of sSCell which we are supported in general |
| Nokia, NSB | As commented above, it would be preferrable to make them components rather than separate capabilities |
| Samsung | No need for FG 34-1b/1c. As commented above, FG 34-1 can include both same and different numerology between sSCell and P(S)Cell. |
| vivo | We think there is no need to consider the case where sScell SCS is lower than Pcell SCS. |
| Intel | We prefer to indicate the combination of numerologies in FG 34-1 since common design applies to all combinations of SCSs. |
| MTK | We are fine to either introduce these new FG groups or introduce the SCS combination as components of FG 34-1/34-2. |
| Ericsson1 | We do not see need for these rows. Can be part of 34-1 |

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34. NR_DSS | 34-2 | [Cross-carrier scheduling from SCell to Pcell/PSCell for different numerologies with search space restrictions (Type A)] | Support of Cross-carrier scheduling from sSCell to Pcell/PSCell with search space restrictions where numerologies for sSCell and Pcell/PSCel are different CIF configured on Pcell/Pscell is used for CCS from sSCell to Pcell/PSCell sSCell USS set(s) (for CCS from sSCell to Pcell/PSCell) and at least following search space sets on Pcell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of Pcell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for Pcell/PSCell scheduling |  |  |  |  |  |  | Applicable to FR1 only |  |  | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | Same comment as above. |
| Apple | This is just another variance of indicating the supported SCS of sSCell |
| Nokia, NSB | As commented above, it would be preferrable to make them components rather than separate capabilities |
| Samsung | No need for above clarification on FG 34-2. As commented above, FG 34-2 can include both same and different numerology between sSCell and P(S)Cell. |
| vivo | Support. FG of R15/R16 CCS for same numerology case and CCS for different numerologies cases are defined in two FGs. Similarly, sScell scheduling Pcell with same/mixed numerologies can be defined as different FGs. |
| Intel | Not needed. Same comments above. |
| MTK | We are fine to either introduce this new FG group or introduce the SCS combination as components of FG 34-1/34-2. |
| Ericsson1 | We do not see need for this row. Can be part of 34-2. |

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34. NR_DSS | 34-2b | Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) | Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Lower-numerology sSCell scheduling higher-numerology P(S)Cell | 6-5 | Yes |  |  | Per BC | N | N |  | sSCell can only be configured in FR1 | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34. NR_DSS | 34-2c | Cross-carrier scheduling from SCell to PCell/PSCell with search space restrictions (Type A) | Support of Cross-carrier scheduling from sSCell to PCell/PSCell with search space restrictions CIF configured on sSCell for CCS from sSCell to PCell/PSCell sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling PDCCH overbooking on sSCell USS set(s) is not allowed Higher-numerology sSCell scheduling lower-numerology P(S)Cell | 6-5 | Yes |  |  | Per BC | N | N |  | sSCell can only be configured in FR1 | Optional with capability signalling |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | Same comment as above. |
| Apple | Same comments as above |
| Nokia, NSB | As commented above, it would be preferrable to make them components rather than separate capabilities |
| Samsung | No need for above clarification on FG 34-2b/2c. As commented above, FG 34-2 can include both same and different numerology between sSCell and P(S)Cell. |
| vivo | Please see our comments above |
| Intel | Not needed. Same comments above. |
| MTK | We are fine to either introduce this new FG group or introduce the SCS combination as components of FG 34-1/34-2. |
| Ericsson1 | We do not see need for this row. Can be part of 34-2. |

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34. NR_DSS | 34-3 | Dormant BWP operation on sSCell for a UE is configured CCS from sSCell to P(S)Cell. | Support dormant BWP operation on sSCell for a UE is configured CCS from sSCell to P(S)Cell | One of FG 34-1 and FG 34-2 | Yes |  |  | Per BC | N | N |  | sSCell can only be configured in FR1 | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | OK to have this FG. |
| Apple | We are supportive |
| Nokia, NSB | There is no need for new capability here unless some new functionality is also defined. Dormant BWP support for SCell is a Rel-16 capability, and if that SCell happens to be an sSCell, it is still the same thing unless new functionality is defined. This discussion is still pending in the WI, and the same applies also for RRC_INACTIVE case. |
| Huawei, HiSilicon | Ok as placeholder - may need to monitor the progress of whether new function is introduced. |
| Samsung | We share the view from Nokia. |
| vivo | OK |
| Intel | Fine to have this FG, since sSCell dormancy is kind of additional functionality to basic CCS from sSCell to PCell |
| MTK | We may need this new feature since how to handle sSCell dormancy is still under discussion in the WI and new functionality (Ex. auto SpCell search space activation upon SCell dormancy) may be introduced. |
| Ericsson1 | Do not see need for this row. OK to discuss further if any specific issue is identified that needs separate capability. |

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34. NR_DSS | 34-A | sSCell deactivation | FFS maximum BD/CCE of PCell/PSCell when sSCell is deactivated FFS implicitly SSSG switching when sSCell is deactivated | 34-1 or 34-2 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34. NR_DSS | 34-B | sSCell dormancy switching | FFS maximum BD/CCE of PCell/PSCell when sSCell is dormant FFS implicitly SSSG switching when sSCell is dormant | 34-1 or 34-2 |  |  |  |  |  |  |  |  |  |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | On FG34-A, we would like to confirm the intention – for example, is it correct understanding that if the UE does not indicate FG34-A, the UE does not support sSCell deactivation? On FG34-B, we do not think we have agreed “dormancy switching”. Clarification is necessary. |
| Apple | In principle, we support UE capability reporting on the support the sSCell deactivation and dormancy. The detailed components can be FFS |
| Nokia, NSB | Same comment as in 34-3, too early to agree on such FGs now. |
| Huawei, HiSilicon | 34-A is not preferred to be separate. 34-B needs some clarification – seems can be included with 34-3. It is preferred that there is minimized additional function introduced for dormancy for DSS enh. |
| Samsung | For 34-A, isn’t deactivation is a default behavior? Agreement (RAN1#104-e) • When CCS from sSCell to PCell/PSCell is configured, CA activation/deactivation operation for the sSCell is supported 34-B needs clarification |
| vivo | We would like to ask for clarification on the difference between 34-B in this table and 34-3 in the previous table. |
| Intel | We prefer to have feature group of sSCell deactivation and sSCell dormancy, since both are additional functionalities to basic CCS from sSCell to PCell. We think 34-3 and 34-B can be merged. The items in 34-A/B are just reflecting proposals from RAN1 contributions. We prefer to keep such FFS items. The final adoption/revision/removal of the item can be up to further discussion. |
| MTK | For 34-A, We may need this new feature since how to handle sSCell deactivation is still under discussion in the WI and new functionality (Ex. auto SpCell search space activation upon SCell deactivation) may be introduced. For 34-B, it seems to be the same as 34-3 and can be removed. |
| Ericsson1 | Do not see need for these rows. Same comment as Nokia. |

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34. NR-DSS | 34-2a | Further restriction to Type A | Support of monitoring DCI formats 0_1,1_1,0_2,1_2 on Pcell/PSCell USS set(s), | 34-2 | Yes | N/A |  | Per BC | N | N |  |  | Optional with capability signalling |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34. NR-DSS | 34-3 | Supported SCS of sSCell | Support SCS of sSCell | 34-1/34-2 | Yes | N/A |  | Per BC | N | N |  | Component 1: {15kHz, 15kHz and 30kHz, 15kHz and 30kHz and 60kHz} | Optional with capability signalling |
| 34. NR-DSS | 34-4 | Support of sSCell deactivation/activation | Support of sSCell deactivation/activation when sSCell cross carrier scheduling to Pcell/PSCell is configured | 34-1/34-2 | Yes | N/A |  | Per BC | N | N |  |  | Optional with capability signalling |
| 34. NR-DSS | 34-5 | Support of sSCell dormancy | Support of sSCell dormancy when sSCell cross carrier scheduling to Pcell/PSCell is configured | 34-1/34-2 | Yes | N/A |  | Per BC | N | N |  |  | Optional with capability signalling |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | We are OK with 34-2a. For 34-3, we are open with this approach or our proposed approach. In either case, we consider that a UE should be able to indicate the supported sSCell SCS and the band pair(s) for {Pcell/PSCell, sSCell} in the BC. For 34-4 and 34-5, same comments as above. |
| Apple | We support all four proposed FGs |
| Nokia, NSB | Same comment as in 34-3, too early to agree on such FGs now. |
| Samsung | For 34-2a, we don’t see the need, as commented for 34-2. This can be decided in RAN1. For 34-3, we don’t see the need. It can be incorporated in 34-1/34-2. For 34-4 and 34-5, same comments as above. |
| vivo | For 34-2a and 34-3, we think 34-a and 34-3 can be included as components of FG of type A/type B UE For 34-4 and 34-5, same comments as above. |
| Intel | 34-2a: we don’t see a benefit to define such restriction. Does it rule out fallback DCI formats in USS on PCell/PSCell? However, fallback DCI is anyway monitored in CSS. 34-3: there is not need for separate FG for SCS combinatons 34-4/34-5: we are in general fine with such FG. |
| MTK | For 34-2a, the description is not quite clear to us. For 34-3, we think it can be incorporated in 34-1/34-2. For 34-4 and 34-5, they can be merged with previous features discussed related to SCell dormancy/deactivation. |
| Ericsson1 | Do not see need for these rows (note some seem to be overlapping with other proposals above). Same comment as Nokia. |

The following new feature group in the 34-x family of DSS features was proposed by one or more companies during RAN1 #106bis-e. Please indicate in the table below whether you agree with the introduction of such a new row/FG.

At this point, it is not important whether you agree with the exact details of the proposed new FG. Rather you should indicate whether you see the need for introducing such a feature group in principle (e.g., in relation to the FFS points in Sections 3.1 and 3.2).

| 34-3 | Additional PDCCH monitoring occasion on PCell/PSCell and sSCell for Pcell/PSCell scheduling | Additional PDCCH monitoring occasion(s) on Pcell/PSCell and sSCell for Pcell/PSCell other than the one in FG34-1 Consider to re-use the span-based PDCCH monitoring defined for FG3-5b where the UE reports (X, Y) where the SCS should be 15kHz. FFS details. The additional PDCCH monitoring occasion(s) is common for PDCCH monitored on Pcell/PSCell and on sSCell for Pcell/PSCell scheduling Candidate pair(s) of frequency band(s) for {Pcell/PSCell, sSCell} among the candidate pair(s) reported in FG34-1 For the set of monitoring occasions which are within the same span: Processing one unicast DCI scheduling DL and one unicast DCI scheduling UL on Pcell/PSCell across the set of monitoring occasions | 34-1 |  |  |  | Per BC | N | N |  |  | Optional with UE capability signalling | 34-3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34-4 | More than one CORESET configuration on sSCell per BWP for Pcell/PSCell scheduling | More than one CORESET configuration on sSCell per BWP for Pcell/PSCell scheduling Total number of CORESET configuration(s) on Pcell/PSCell and on sSCell for Pcell/PSCell scheduling on the active BWPs is per FG3-1/FG3-3 | 34-1 |  |  |  | Per BC | N | N |  |  | Optional with UE capability signalling | 34-4 |
| 34-5 | Up to 10 search space sets in a Pcell/PSCell slot for scheduling Pcell/PSCell | Up to 10 search space sets per BWP on sSCell for Pcell/PSCell scheduling Total number of search space sets on Pcell/PSCell and on for Pcell/PSCell scheduling on the active BWPs can be up to 10 | 34-1 |  |  |  | Per BC | N | N |  |  | Optional with UE capability signalling | 34-5 |
| 34-6 | Precoder-granularity of CORESET size when CCS from sSCell to Pcell/PSCell is configured | Precoder granularity of CORESET size can be configured {on sSCell, on Pcell/PSCell, on both sSCell and Pcell/PSCell} Candidate pair(s) of frequency band(s) for {Pcell/PSCell, sSCell} among the candidate pair(s) reported in FG34-1 | 34-1 |  |  |  | Per BC | N | N |  |  | Optional with UE capability signalling | 34-6 |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| Qualcomm | We think they are necessary considering the implementability and testability of cross-carrier scheduling from sSCell to Pcell/PSCell. Regarding the above 34-3, we think the basic capability should be slot-based PDCCH monitoring and hence separate UE capability is necessary for span-based PDCCH monitoring. Regarding the above 34-4 and 34-5, we think these are necessary same as for Rel-15. Regarding the above 34-6, current wideband RS CORESET is per-UE capability and hence should not be applied to cross-carrier scheduling from sSCell to Pcell/PSCell, in which case a UE is required to monitor PDCCH on two scheduling cells for a given scheduled cell. Note that if we have FG34-1 for Type-B and FG34-2 for Type-A, the prerequisite features for the above FGs are “34-1 or 34-2” |
| Apple | We are open to those UE FGs. |
| Nokia, NSB | It is not clear if all these FGs are needed when one takes into account the existing Rel-15 FGs. It is also not clear why those are not listed as prerequisites, that would help in understanding the relationship between them. |
| Huawei, HiSilicon | As Nokia commented. |
| Samsung | These FGs seem to be similar to legacy ones (e.g., FG 3-5b, 3-3, 3-8, 3-7, respectively). First, we need to discuss whether this separate FGs are needed for Rel-17 DSS. |
| Vivo | 34-3: we are open to discuss when span-based monitoring is supported for DSS and the details on how to support 34-4, 34-5, 34-6: OK |
| Intel | We are open for the FGs. On the other hand, it seems better to postpone them until there is a related discussion in AI 8.13.1 |
| MTK | We support 34-3 and 34-6. For 34-4 and 34-5, we tend to think the existing Rel-15 FGs (FG3-3, 3-8) can be reused to also indicate the capability for DSS case. |
| Ericsson1 | 34-3 is not aligned with current 34-1 description. So better to remove now. We are ok to discuss further once a consistent formulation is available. 34-4,5,6 do not see why separate signaling is needed given Rel15 capability indication is available. OK to discuss further but rows should be deleted as it is too early to introduce separate rows at this point. |

# Proposed Baseline for RAN1 #107-e and outcome of RAN1 #106bis-e

Based on the inputs in Section 3, the following is proposed as baseline for RAN1 #107-e and outcome of RAN1 #106bis-e for NR_DSS.

Proposed Agreement: Agree the following table, incl. the changes highlighted in red and the yellow highlighting, as baseline for further discussions during RAN1 #107-e

| Features | Index | Feature group | Components | Prerequisite feature groups | Need for the gNB to know if the feature is supported | Applicable to the capability signalling exchange between UEs (Sidelink WI only)”. | Consequence if the feature is not supported by the UE | Type (the ‘type’ definition from UE features should be based on the granularity of 1) Per UE or 2) Per Band or 3) Per BC or 4) Per FS or 5) Per FSPC) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Capability interpretation for mixture of FDD/TDD and/or FR1/FR2 | Note | Mandatory/Optional |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34. NR_DSS | 34-12 | Cross-carrier scheduling from SCell to PCell/PSCell (Type B) | [Support of Cross-carrier scheduling (CCS) from sSCell to PCell/PSCell (Type B)] CIF configured on sSCell for CCS Cross-carrier scheduling from sSCell to PCell/PSCell with CIF sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and search space sets on PCell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of PCell/PSCell and sSCell FFS: BD limit handling between [Option A/C] or [Option C] and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling FFS: PDCCH overbooking on sSCell USS set(s) is not allowed FFS: Same numerology between sSCell and P(S)Cell FFS: USS set(s) for DCI format 0_1,1_1,0_2,1_2 (if supported) configured on sSCell for CCS from sSCell to PCell/PSCell Note: The SCell configured with Cross-carrier scheduling to PCell/PSCell is referred to as ‘sSCell’ | 6-5[, 6-10, 18-5, 18-5b, 34-1] | Yes |  |  | Per BC FFS | No | N Applicable to FR1 only |  | sSCell can only be configured in FR1 FFS: UE should be able to indicate following two as part of this per-BC capability: (1) subcarrier spacing for sSCell, (2) frequency band pair(s) for {PCell/PSCell, sSCell} | Optional with capability signalling |
| 34. NR_DSS | 34-21 | Cross-carrier scheduling from SCell to PCell/PSCell [with search space restrictions] (Type A) | Support of Cross-carrier scheduling from sSCell to PCell/PSCell [with search space restrictions] (Type A) CIF configured on sSCell for CCS Cross-carrier scheduling from sSCell to PCell/PSCell with CIF FFS: sSCell USS set(s) (for CCS from sSCell to PCell/PSCell) and at least following search space sets on PCell/PSCell can only be configured such that UE does not monitor them in same [slot/symbol] of PCell/PSCell and sSCell USS sets for DCI formats 0_1,1_1,0_2,1_2 (if supported) USS sets for DCI formats 0_0,1_0 Type3-CSS set(s) for DCI formats 1_0/0_0 with C-RNTI/CS-RNTI/MCS-C-RNTI FFS: BD limit handling and any configuration of associated parameters and UE reporting of any associated parameters FFS: #unicast DCI limits for PCell/PSCell scheduling FFS: PDCCH overbooking on sSCell USS set(s) is not allowed FFS: Same numerology between sSCell and P(S)Cell FFS: USS set(s) for DCI format 0_1,1_1,0_2,1_2 (if supported) configured on sSCell for CCS from sSCell to Pcell/PSCell FFS: sSCell USS set(s) (for CCS from sSCell to Pcell/PSCell) and Type0/0A/1/2 CSS sets on Pcell/PSCell can be configured so that the UE monitors them in overlapping [slot/symbol] of Pcell/PSCell and sSCell. FFS overlap handling | 6-5[, 6-10, 18-5, 18-5b] | Yes |  |  | Per BC FFS | No | No Applicable to FR1 only |  | sSCell can only be configured in FR1 FFS: UE should be able to indicate following two as part of this per-BC capability: (1) subcarrier spacing for sSCell, (2) frequency band pair(s) for {PCell/PSCell, sSCell} | Optional with capability signalling |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| vivo | For item 6) in 34-1/2, considering some companies’ comments that sScell scheduling Pcell for mixed numerologies case can be component of FG 34-1/34-2, we suggest refining the wording to make it crystal clear. FFS: Same numerology or different numerologies between sSCell and P(S)Cell For prerequisite feature groups: We are still not convinced that [6-10, 18-5, 18-5b] can be part of the prerequisites, it does not make sense to mandate UE with sScell scheduling Pcell to support all components such as {low-to-high} and all SCS combination specified in these CCS feature groups. [, 6-10, 18-5, 18-5b] For FFS: UE should be able to indicate following two as part of this per-BC capability: (1) subcarrier spacing for sSCell, (2) frequency band pair(s) for {PCell/PSCell, sSCell}, so far we have not reached a formal conclusion/agreement that Pcell SCS can only be 15kHz, and we hope that this feature can be generally applied to any Pcell with limited PDCCH capacity at FR1, it is suggested to keep open at this stage that the Pcell SCS other than 15kHz can be allowed (of course, it needs to be no larger than the sScell SCS), so Pcell's SCS may need to be indicated as well. FFS: UE should be able to indicate following two as part of this per-BC capability: (1) subcarrier spacing for sSCell and/or subcarrier spacing for Pcell, (2) frequency band pair(s) for {PCell/PSCell, sSCell} |
| Apple | Comment 1 For FG34-1 on the Type A UE, we also need to add the following component for further discussion to honor the working assumption we agreed in the past meeting quoted below. Unless WA is reverted with consensus and strong technical issue, WA should be respected. The proposed TP is as following (to be added to FG34-1) FFS: Support of monitoring DCI formats 0_1,1_1,0_2,1_2 on PCell/PSCell USS set(s) Working Assumption When CCS from sSCell to PCell/PSCell is configured, UE can be configured to monitor DCI formats 0_1/1_1/0_2/1_2 that schedule PDSCH/PUSCH on PCell/PSCell on PCell/PSCell USS set(s), and/or on sSCell USS set(s) The WA to be confirmed after agreements are made on PDCCH BD/CCE handling and PDCCH overbooking handling for CCS from sSCell to PCell/PSCell Specs also allow UEs supporting functionality of only Alt-1. Capability signaling details, if any, can be handled during the UE capability discussion for Rel17 FFS: Whether the UE can monitor PDCCH from both cells in the same slot. Comment 2 We also need to discuss the UE capability on whether UE supports SCell deactivation or dormancy on sSCell. There is no reason why we design a feature to shift the PDCCH monitoring to sSCell because operators are concerned about the PDCCH scheduling flexibility of SpCell, then we deactivate or dormant the sSCell and potentially with some artificial design to shift the PDCCH monitoring back to SpCell. We would want to minimize the negative impact of this unreasonable design to the actual UE implementation and UE performance We can add the following two components to FG34-1/34-2, or we prefer to introduce new UE FG. FFS: Support of sSCell deactivation/activation when sSCell cross carrier scheduling to PCell/PSCell is configured FFS: Support of sSCell dormancy when sSCell cross carrier scheduling to PCell/PSCell is configured |
| Nokia, NSB | We are OK with the FL proposal. |
| Qualcomm | Comment 1: We believe at least following FFSs must be added in the FG34-1 and FG34-2. For them, we would like to discuss what should be the components of basic features and what should be separate advanced capabilities. FFS: PDCCH monitoring occasion(s) is within the first 3 OFDM symbols of a PCell/PSCell slot We are open to discuss advanced capability enabling subslot-based PDCCH monitoring, but as for the basic FGs, PDCCH monitoring should be “slot-based”. FFS: Numbers of CORESET configurations and search space sets on sSCell (for PCell/PSCell cross-carrier scheduling) Note: Maximum numbers of CORESET configurations and search space sets for a given scheduled cell shall be unchanged. FFS: frame boundary alignment between PCell/PSCell and sSCell Support of FG18-7 for the BC should not mean the UE supports unaligned operation between PCell/PSCell and sSCell. FFS: Precoder granularity of CORESET size when CCS from sSCell to PCell/PSCell is configured FG3-7 is per-UE capability. For a UE monitoring CORESETs on different scheduling cells for a given scheduled cell, a separate FG should be prepared. Comment 2: We disagree with vivo that the WI scopes PCell/PSCell other than 15kHz. The FGs should be limited to the PCell/PSCell with 15kHz. We support to capture “FFS: UE should be able to indicate following two as part of this per-BC capability: (1) subcarrier spacing for sSCell, (2) frequency band pair(s) for {PCell/PSCell, sSCell}” in FG34-1 and FG34-2. However we are not sure why it is in ‘Note’ column. We believe it should replace the current component 6). Comment 3: We are OK to have the FFSs proposed by Apple. Comment 4: We agree with vivo; we do not think 6-10, 18-5, 18-5b should be prerequisite. CCS from sSCell to PCell/PSCell mostly reuses RAN1 spec of the general cross-carrier scheduling. However, it does not mean the UE has to support general CCS in order to declare support of CCS from sSCell to PCell/PSCell. Our initial proposal was that Type-B should be an additional feature on top of Type-A. However, in the main session, companies propose BD/CCE handling for Type-A that is different from the one for Type-B. If this is the case, we do not think Type-A should be prerequisite for Type-B. This highly depends on the discussion in the main session. |
| Samsung | We agree to have FGs 34-1 and 34-2 as baseline. Keeping FFS would give outline for next discussion. However, from the discussion above, it tends to mix the RAN1 agreed FFS and individual company’s FFS which lead the discussion diverge. Once RAN1 agrees Type A/B UE behavior in AI 8.13.1 (in this and next RAN1 meetings), we can address most FFSs for FG 34-1 and 34-2 (items 3) – 7) for FG 34-2, items 2) – 8) for FG 34-1).Therefore, we are also OK to remove current FFSs for now. Furthermore, we believe that RAN1 is not targeting to dump all RAN1 agreements into UE feature. |
| MTK | The following two comments are same as vivo: For item 6) in 34-1/2, considering some companies’ comments that sScell scheduling Pcell for mixed numerologies case can be component of FG 34-1/34-2, we suggest refining the wording to make it crystal clear. FFS: Same numerology or different numerologies between sSCell and P(S)Cell For prerequisite feature groups: We are still not convinced that [6-10, 18-5, 18-5b] can be part of the prerequisites, it does not make sense to mandate UE with sScell scheduling Pcell to support all components such as {low-to-high} and all SCS combination specified in these CCS feature groups. [, 6-10, 18-5, 18-5b] Besides, since it seems whether the SCS of PCell/PSCell is limited to 15kHz is not decided yet, we suggest to add the following FFS: FFS: Whether the PCell/PSCell SCS other than 15kHz can be allowed |
| Huawei, HiSi | We agree with Samsung that most of the FFS may be resolved in main session but ok to keep those as highlights. One thing related to the main session discussion is the pre-requisite FG. We’d like to highlight 6-5 as well for both 34-1 and 34-2. Our view is that the DSS enh. is not limited to 15 kHz SCS. |

Based on the inputs in Section 3, the following is proposed as baseline for RAN1 #107-e and outcome of RAN1 #106bis-e for LTE_NR_DC_enh2.

Proposed Agreement: Agree the following table, incl. the changes highlighted in red and the yellow highlighting, as baseline for further discussions during RAN1 #107-e

| Features | Index | Feature group | Components | Prerequisite feature groups | Need for the gNB to know if the feature is supported | Applicable to the capability signalling exchange between Ues (Sidelink WI only)”. | Consequence if the feature is not supported by the UE | Type (the ‘type’ definition from UE features should be based on the granularity of 1) Per UE or 2) Per Band or 3) Per BC or 4) Per FS or 5) Per FSPC) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | Capability interpretation for mixture of FDD/TDD and/or FR1/FR2 | Note | Mandatory/Optional |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 35. LTE_NR_DC_enh2 | 35-1 | [TRS\Temporary] RS [based/for] Scell activation | [Scell activation with the assistance of temporary RS/TRS] [TRS\Temporary RS] is aperiodic and triggered by MAC CE FFS: Temporary RS is based on aperiodic TRS and FFS other signals FFS: Temporary RS is only configured within the BWP indicated by firstActiveDownlinkBWP-Id for the sSCell FFS: A SSB of the to-be-activated Scell can be indicated as a QCL source for the temporary RS in case of known Scell FFS: Maximum number of temporary RS resource sets that can be configured to UE per CC {1 … 16} FFS: Maximum number of temporary RS resource sets that can be configured to UE across CCs {1 … 256} FFS: Maximum number of triggering states for temporary RS based Scell activation by a MAC-CE {1 … 64} FFS: Maximum number of temporary RS resource sets that can be associated with a triggering state {1 … 16} [Note: following are reported via the legacy feature, FG2-33 Maximum number of configured NZP-CSI-RS resources per CC Maximum total number of simultaneous NZP-CSI-RS resources in active BWPs across all CCs Maximum number simultaneous NZP-CSI-RS resources per CC Maximum total number of CSI-RS ports in simultaneous NZP-CSI-RS resources in active BWPs across all CCs] | 6-5 | Yes | N/A |  | [Per UE[/Per BC/per band] | No | [No/Yes] |  |  | Optional with capability signalling |

| Company | Comments/Questions/Suggestions |
| --- | --- |
| vivo | Ok |
| Nokia, NSB | We are OK with the FL proposal. |
| Qualcomm | OK with the FL proposal for further discussion. Note that we think FR1/FR2 differentiation is necessary even if the FG35-1 is per-BC. Implementation/test for TRS/temporary RS based Scell activation should not be common for FR1 and FR2. We need to discuss this. |
| Futurewei | Generally ok. We are not sure that this FG does not need TDD/FDD differentiation. The slot position n+k, the minimum requirements, etc., may be different for TDD/FDD. We’d like to hear from other companies. |
| MTK | We are fine with current FL proposal |

# Conclusion

After further discussion on the RAN1 email reflector the following was agreed as part of this email discussion:

# References

- R1-2108679, Preliminary RAN1 UE features list for Rel-17 NR, Moderators (AT&T, NTT DOCOMO, INC.)

- R1-2108861, Discussion on Rel-17 UE features for DSS, ZTE

- R1-2109023, Discussion on UE features for DSS, vivo

- R1-2109155, Rel-17 UE features for DSS, Huawei/HiSilicon

- R1-2109535, UE features for DSS, Samsung

- R1-2109554, On UE features for DSS, MediaTek Inc.

- R1-2109653, UE features for DSS, Intel Corporation

- R1-2110072, Views on Rel-17 eDSS UE features, Apple

- R1-2110146, UE features for DSS and CA Enhancements, Ericsson

- R1-2110231, UE features for DSS and LTE_NR_DC_enh2, Qualcomm Incorporated

- R1-2110275, On UE features for DSS and LTE NR DC enhancements, Nokia/Nokia Shanghai Bell