## Slide 1: Way forward on PDSCH HARQ timing on Scell in TDD CA
Samsung, Ericsson, ST-Ericsson, InterDigital Communications, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Panasonic
3GPP TSG RAN WG1 #68bis R1-121841
Jeju, Korea, 26 – 30 March 2012 Agenda item: 7.2.1.5

## Slide 2: Agreement in RAN1#68
The PDSCH HARQ timing on SCell shall
  follow the PCell SIB1 configuration if the set of DL subframes indicated by the SCell SIB1 configuration is a subset of the DL subframes indicated by the PCell SIB1 configuration
  FFS if the set of DL subframes indicated by the SCell SIB1 configuration is NOT a subset of the DL subframes indicated by the PCell SIB1 configuration

## Slide 3: Proposal (Case B)
If the set of DL subframes indicated by the SCell SIB1 configuration is a superset of the DL subframes indicated by the PCell SIB1 configuration, the PDSCH HARQ timing on SCell shall
  follow the PCell SIB1 configuration in case of cross carrier scheduling
  follow the SCell SIB1 configuration in case of self scheduling

## Slide 4: Proposal (Case C)
If the set of DL subframes indicated by the SCell SIB1 configuration is neither a superset nor a subset of the DL subframes indicated by the PCell SIB1 configuration, the PDSCH HARQ timing on SCell shall
  follow the PCell SIB1 configuration in case of cross carrier scheduling
  follow a PDSCH HARQ timing reference configuration in case of self scheduling (Table 1 in R1-121014, see next slide)

## Slide 5
UL-DL configuration for PDSCH HARQ |  | PCell SIB1 UL-DL configuration |  |  |  |  |  | 
timing reference |  | 0 | 1 | 2 | 3 | 4 | 5 | 6
SCell SIB1 UL-DL configuration | 0 | - | 1 | 2 | 3 | 4 | 5 | 6
 | 1 | 1 | - | 2 | 4 | 4 | 5 | 1
 | 2 | 2 | 2 | - | 5 | 5 | 5 | 2
 | 3 | 3 | 4 | 5 | - | 4 | 5 | 3
 | 4 | 4 | 4 | 5 | 4 | - | 5 | 4
 | 5 | 5 | 5 | 5 | 5 | 5 | - | 5
 | 6 | 6 | 1 | 2 | 3 | 4 | 5 | -
Meaning of the colors |  | Case A | Case B | Case C |  |  |  |