## Slide 1: WF on PUCCH Format 1a/1b resource allocation for ePDCCH based HARQ-ACKs
Sharp, NSN, Nokia, Pantech, Samsung
TSG-RAN WG1 Meeting #69
Prague, Czech, 21-25 May 2012
Agenda Item: 7.6.5
Document for: Discussion and Decision
R1-123013

## Slide 2: Proposals
The PUCCH Format 1a/1b resource for HARQ-ACK transmission in response to ePDCCH-scheduled PDSCH is at least partly determined implicitly from the index of the respective first eCCE
Specification support for avoiding collisions of PUCCH format 1a/1b resources corresponding to ePDCCH and PDCCH is provided in order to avoid scheduler restrictions, increased blocking probability and throughput loss

## Slide 3: Possible Alternatives
Alt.1
  Fully orthogonal resources for HARQ-ACK due to PDCCH and ePDCCH (PUCCH Format 1a/1b resources due to ePDCCH follow the ones due to PDCCH)
    UE determines legacy PUCCH Format 1a/1b resources either by decoding PCFICH or by assuming the maximum number of legacy PDCCH OFDM symbols (similar to determining starting PDSCH symbol in Rel-10)

## Slide 4: Possible Alternatives
Alt.2a
  The starting PUCCH Format 1a/1b resource for ePDCCH based HARQ-ACKs can be configured separately from N(1)_PUCCH
    FFS whether the configuration of the starting PUCCH resource for ePDCCH is cell-specific or UE-specific
  DCI formats scheduling PDSCH by ePDCCH can be configured to include a PUCCH Resource Indicator (ARI)
Alt.2b
  The starting PUCCH Format 1a/1b resource for ePDCCH based HARQ-ACKs can be configured separately from N(1)_PUCCH
    FFS whether the configuration of the starting PUCCH resource for ePDCCH is cell-specific or UE-specific
  FFS whether DCI formats scheduling PDSCH by ePDCCH can be configured to include a PUCCH Resource Indicator (ARI)
Alt.2c
  DCI formats scheduling PDSCH by ePDCCH can be configured to include a PUCCH Resource Indicator (ARI)
  FFS whether the starting PUCCH Format 1a/1b resource for ePDCCH based HARQ-ACKs can be configured separately from N(1)_PUCCH
    FFS whether the configuration of the starting PUCCH resource for ePDCCH is cell-specific or UE-specific