## Slide 1: Way forward on soft buffer handling
CMCC, ITRI, Panasonic, Samsung, …
3GPP TSG RAN WG1 #70bis R1-124615
San Diego, USA, October 8 – 12, 2012 Agenda item: 7.2.3

## Slide 2: Proposal
For TDD inter-band CA with different UL/DL configuration,
  The rate matching procedure in TS 36.212 is kept unchanged except the following:
    MDL_HARQ is the maximum number of DL HARQ processes defined in Table 7-1 in TS 36.213 for the DL-reference UL/DL configuration of the serving cell
  The operation of storing soft channel bits in TS 36.213 is kept unchanged except the following:
    MDL_HARQ is the maximum number of DL HARQ processes defined in Table 7-1 in TS 36.213 for the DL-reference UL/DL configuration of the serving cell
  MDL_HARQ is separately determined for self-scheduling case and cross-carrier scheduling case

## Slide 3: Annex A: Rate matching
The parameter NIR for a serving cell is
  MDL_HARQ is the maximum number of DL HARQ processes defined in Table 7-1 in TS 36.213 for the DL-reference UL/DL configuration of the serving cell
  Other parameters reuse Rel-10 definitions for the serving cell

## Slide 4: Annex B: Storing soft channel bits
For each serving cell, for at least KMIMO *min(MDL_HARQ, Mlimit) transport blocks, upon decoding failure of a code block of a transport block, the UE shall store at least nSB received soft channel bits for the code block, where
  MDL_HARQ is the maximum number of DL HARQ processes defined in Table 7-1 in TS 36.213 for the DL-reference UL/DL configuration of the serving cell
  Other parameters reuse Rel-10 definitions for the serving cell