## Slide 1: Way forward on simulation assumptions for data channel
Huawei, HiSilicon, MediaTek Inc., CATT, ZTE, Ericsson, ST-Ericsson, Qualcomm, …
3GPP TSG RAN WG1 Meeting #72
St Julian’s, Malta, 28th January – 1st February 2013 Agenda item: 7.3.4
Document for: Decision
R1-130778

## Slide 2: Background
During and after the RAN1#71 meeting some companies discussed simulation assumptions for the data channel.
Some parameters have multiple opinions.

## Slide 3: Email discussed simulation assumptions on PDSCH
Parameter | Value
System bandwidth | 1.4 MHz or 10MHz
Frame structure | FDD or TDD
Carrier frequency | 2.0 GHz for FDD/ 2.6GHz for TDD
Antenna configuration | 2x2, low correlation for FDD; 8x2, low correlation for TDD for TDD
Channel model | EPA
Doppler shift | 1Hz or 2Hz
MCS | 0
Number of DL RBs | 6 or 1
Transmission mode | TM2
Frequency error | 100Hz or 20Hz
Performance target | 10% iBLER
Channel estimation | Channel estimation needs to be clarified in the contribution

## Slide 4: Email discussed simulation assumptions on PUSCH
Parameter | Value
System bandwidth | 10MHz
Frame structure | FDD or TDD
Carrier frequency | 2.0 GHz for FDD/ 2.6GHz for TDD
Antenna configuration | 1x2, low correlation for FDD; 1x8, low correlation for TDD
Channel model | EPA
Doppler shift | 1Hz or 2Hz
MCS | 0
Number of UL RBs | 1
Transmission mode | TM1
Frequency error | 100Hz or 20Hz
Performance target | 10% iBLER
Channel estimation | Channel estimation needs to be clarified in the contribution

## Slide 5: Proposed simulation assumptions on PDSCH
Parameter | Value
System bandwidth | 10MHz
Frame structure | FDD or TDD
UL-DL configuration | [0]
Carrier frequency | 2.0 GHz for FDD/ 2.6GHz for TDD
Antenna configuration | 2x2, low correlation for FDD; 8x2, low correlation for TDD for TDD
Channel model | EPA
Doppler spread | 1Hz
TBS | [20bits]
Number of DL RBs | [2]
Transmission mode | TM2
Frequency tracking error | 100Hz or 20Hz
Performance target | 10% iBLER
Channel estimation | Realistic multiple subframes channel estimation & ideal channel estimation, filter length should be indicated
The minimum required SINR | [-19.3]dB for FDD; FFS for TDD
Output | The amount of repetitions to achieve performance target at the minimum required SINR

## Slide 6: Proposed simulation assumptions on PUSCH
Parameter | Value
System bandwidth | 10MHz
Frame structure | FDD or TDD
UL-DL configuration | [0]
Carrier frequency | 2.0 GHz for FDD/ 2.6GHz for TDD
Antenna configuration | 1x2, low correlation for FDD; 1x8, low correlation for TDD
Channel model | EPA
Doppler shift | 1Hz
TBS | [20bits]
Number of UL RBs | [2]
Transmission mode | TM1
Frequency tracking error | 100Hz or 20Hz
Performance target | 10% iBLER
Channel estimation | Realistic multiple subframes channel estimation & ideal channel estimation, filter length should be indicated.
The minimum required SINR | [-24.3]dB for FDD; FFS for TDD
Output | The amount of repetitions to achieve performance target at the minimum required SINR