## Slide 1: Way Forward for NAICS scenarios
Orange, Telecom Italia, Deutsche Telekom, T-Mobile USA, China Unicom, KDDI, Docomo, Vodafone

## Slide 2: NAICS scenario #1
Homogeneous network, only macro-cell, ISD = 500m
Non-ideal backhaul between sites
Inter-cell coordination assumptions
  Intra-site coordination is possible
  Inter-site coordination is limited due to backhaul constraints
  NB: This scenario is similar to CoMP scenario 1 in TR36.819

## Slide 3: NAICS scenario #2
Small cells are deployed within the macro-cell coverage
Co-channel deployment
Sparse deployment of small cells
Small cells are deployed outdoors
Backhaul assumptions
  Between macro-cell and small cells within its coverage: Non-ideal
  Among macro cells: Non-ideal
Inter-cell coordination assumptions
  According to the backhaul assumptions, every inter-cell coordination is limited, except the intra-site coordination
  NB: This scenario is similar to CoMP scenario #3 in TR36.819, but with imperfect backhaul

## Slide 4: NAICS scenario #3
Small cells are deployed within the macrocell coverage
Co-channel deployment
Sparse deployment of small cells
Small cells are deployed outdoors
Backhaul assumptions
  Between macro-cell and small cells within its coverage: Quasi-ideal backhaul
  Among macro cells: Non-ideal
Inter-cell coordination assumptions
  According to the backhaul assumptions, the coordination is possible in the following cases:
    Intra-site macro cells coordination
    Coordination between a macro-cell and a small cell within its coverage
    Coordination among small cells within the coverage of the same macro cell
  According to the backhaul assumptions, the coordination is limited in the following cases:
    Inter-site coordination between macro-cells
    Coordination between a macro-cell and a small cell outside its coverage
    Coordination among small cells within the coverage of different macro cells
  NB: This scenario is similar to CoMP scenario #3 in TR36.819

## Slide 5: General considerations
Synchronization error: Different levels of synchronization error between the cells are considered. Asynchronous network is not precluded.
Inter-cell coordination mechanisms:
  No CoMP, no (f)eICIC
  The only possible scheduling coordination mechanisms relate to network-assistance for advanced receivers (example: PRBs alignment, constraints on interferer’s MCS)