## Slide 1: WF on UCI feedback mechanisms for TDD-FDD CA
NTT DOCOMO, Panasonic, SONY, KCME, IIR, Kyocera
R1-134869
3GPP TSG RAN WG1 #74bis
Guanzhou, China, 7th – 11th August 2013
Agenda iterm 7.2.3.1

## Slide 2: Background
SCell PUCCH is a necessary feature for TDD-FDD CA as well as for dual connectivity
This is because “PUCCH on PCell-only” cannot work well in the scenario where: “many small cells are deployed in a macro cell”
TDD-FDD CA is operated for UEs using macro cell and each of small cells
Macro
Small
Freq.
Small
Freq.
F1
F2

## Slide 3: PUCCH issue
In this scenario, PUCCH is still transmitted on macro
  DL traffic can be offloaded to small cells but UCI cannot
  TDD-FDD CA UEs still transmit PUCCH on macro cell
    This is more problematic in case of TDD-macro PCell
FDD
TDD
Freq.
UL
DL
UL/DL
UL/DL
UL/DL
PUCCH on PCell only !!
FDD, PCell
TDD, SCell

## Slide 4: Analysis of PUCCH overhead
Assumption for CA | Num. of Small cells | Num. of RBs for PUCCH |  |  | PUCCH overhead
 |  | A/N | CQI | SR | 
No SCell (Non-CA) | 0 | 2.3 | 4 | 1.3 | 15.2%
1 x small cell is SCell | 1 | 3.2 | 8 | 1.3 | 24.9%
2 x small cells are SCells | 2 | 4.0 | 8 | 1.3 | 26.7%
4 x small cells are SCells | 4 | 5.8 | 8 | 1.3 | 30.3%
8 x small cells are SCells | 8 | 9.4 | 8 | 1.3 | 37.4%
16 x small cells are SCells | 16 | 16.5 | 8 | 1.3 | 51.6%
16 x small cells are SCells + 16 x small cells are SCells # 2 Small Cell carriers, 2 DL CA | 32 | 30.7 | 8 | 1.3 | 80.1%
16 x small cells are SCells + 16 x small cells are SCells # 2 Small Cell carriers, 3 DL CA | 32 | 51.2 | 12 | 1.3 | More than 100%
10MHz macro cell is PCell for all cases
MIMO in SCell : 2 x 2
18 ACK/NACK resources/RB, 6 CQI resources/RB, 18 SR resources/RB
CQI/SR periodicity: 20msec
Number of non-DRX UEs : 480
Scalable increase of PUCCH overhead is unavoidable

## Slide 5: Proposals
PUCCH transmission is supported on SCell for TDD-FDD CA for both TDD-PCell and FDD-PCell cases
  Each of DL HARQ mechanisms is in principle the same as non-CA TDD/FDD single-cell cases
FFS until RAN1#75:
  Option 1: Semi-statically configured
  Option 2: Dynamically switched
  Option 3: Simultaneous transmission is supported