## Slide 1: WF on Timing Synchronisation of D2D Outside of Network Coverage
NEC, SAMSUNG
R1-13xxxx
3GPP TSG RAN WG1 Meeting #74bis
Guangzhou, China, 7th – 11th October 2013 Agenda item: 7.2.8.1.1
Document for: Decision

## Slide 2: Background
To handle resource allocation and interference avoidance in broadcast communication, it is nice to synchronize multiple transmitter UEs in the transmission range of receiver UE(s).

## Slide 3: Background
Technically, there are two basic approaches for timing synchronisation:
  Centralised approach: in this approach, one D2D UE will take charge of cluster head role to provide timing reference for other D2D UE(s) in the cluster or within its transmission range to synchronize to:
    In this case, there is a heavy dependency on the cluster head for providing timing reference. If the cluster head is removed or move away from the cluster, there is a need for a re-selection of cluster head.
    This approach is not scalable due to the limited transmission range. It can be extended to hierarchical approach with increasing management overheads.
  Distributed approach: In this approach, a D2D UE initiates a reference timer for other D2D UEs within its transmission range to adopt and each and every D2D UE(s) that has adopted the nominated reference timer will participate to providing and maintaining timing reference within their transmission range.
    This approach is scalable for the sake of some convergence time.

## Slide 4: Proposal
Network-wide Synchronization for timing synchronization of D2D outside of network coverage shall be supported:
Network wide synchronisation is achieved through beacon(sync.) signal.
  Consider both centralised and distributed approach for timing synchronisation of D2D outside of network coverage: Detailed design is FFS.
  Beacon signal used in both centralised and distributed approach should be self-contained, so that it should be possible for a D2D UE receiver to decode it without assistance of additional signalling or reference signal or synchronisation signal.