## Slide 1: Way Forward on FDD-TDD switching enhancement in FDD-TDD joint operation
CMCC, Huawei, HiSilicon, MediaTek, CATR, ZTE, KDDI, CHTTL, ITRI, Deutsche Telekom, CATT
3GPP TSG-RAN WG1 Meeting #74bis Guangzhou, China, 7 - 11 Oct, 2013
Agenda Item: 7.2.3.2
R1-134967

## Slide 2: Use case
FDD and TDD networks can be deployed to provide different services with different QoS requirements, possibly due to
  Different coverage characteristics due to different frequency bands
  Different backhaul latency affecting time-sensitive services
  Limited capability of small cell network, i.e. no voice service
Switching between FDD and TDD networks is needed based on services in this case

## Slide 3: Possible switching approaches
Possible switching approaches are (but not limited to):
  Inter-frequency Handover:
    If the source eNB can prepare the target eNB
    But not always practical between eNBs from multi-vendors
  RRC release with redirection
    When the source eNB is not able to prepare the target eNB
    Performance not satisfactory (up to several seconds in latency observed from field measurements)
  Dual-connectivity (if supported in Rel-12)
    Current baseline UE requirement is 2Tx2Rx
    Network requirements may include
      Large backhaul capacity between FDD and TDD eNB, depending on user plane architecture (e.g., SeNB connects to Service Gateway through MeNB)
      RRC coordination between SeNB and MeNB (which can be difficulty due to large backhaul latency)
      TDD and FDD networks may not be connected or may be connected at a higher node than the dual connectivity split

## Slide 4: Proposal
Performance of the previously mentioned switching approaches may be inadequate for the identified use case
Enhancements on switching between TDD/FDD mode need to be considered
  Should support a minimum UE requirement of 1 UL, 1 DL (i.e., same as the current dual mode UEs)
  Switching should be fast enough to meet time-sensitive service requirements
Capture the use case and the above observations in TR36.847