## Slide 1: WF on D2D Discovery Transmit Timing
Samsung, Qualcomm, ETRI
TSG-RAN WG1 Meeting #75
San Francisco, USA, 11th – 15th November 2013
R1-135937

## Slide 2: Backgrounds
In last RAN1#74bis meeting, transmit timing of type 1 discovery was discussed
At least for discovery:
  Any UEs that do not have an active timing advance value (including RRC_Idle UEs in coverage if transmission of discovery signal is supported for such UEs, and out of coverage UEs that do not have an active timing advance value) use T2 = 0.
  FFS for UEs with an active timing advance value.

## Slide 3: Proposal
For type 1 discovery
  In FDD
    RRC_Connected D2D UEs inside network coverage transmit discovery signal based on DL reference timing (T2 = 0).
  In TDD
    T2 is FFS.