## Slide 1: Way Forward on PRACH for MTC enhanced coverage
Vodafone
3GPP TSG RAN WG1 #75 R1-135944
San Francisco, USA, 11 – 15 November 2013
Agenda item: 6.2.2.2.2

## Slide 2: PRACH architecture aspects
WA on usage of existing PRACH formats from RAN1#74bis is confirmed.
Enhanced coverage UEs and legacy UE may share the same time/frequency resource. In this case, enhanced coverage UEs will use CDM to multiplex with legacy UEs.
In addition define time-frequency resource region separate for “enhanced coverage” UEs.
  Within new region, CDM is allowed.
  Specification of FDM in this region is FFS.
  Specification of Frequency Hopping within this region is FFS.
NOTE: RACH resource mapping for the “low complexity UE not requiring enhanced coverage” is FFS.

## Slide 3: PRACH repetition levels and associated behaviour
Specified maximum numbers of levels: Working assumption of 3 (this does not include “zero coverage extension”). More evidence needed if we were to extend this.
eNB-configurable number of levels (1, 2, 3) up to specified max level.
Number of repetitions per level:
  working assumption: configurable value.
  FFS ranges of this value per level – come back later in week.
1 attempt = configured number of repetitions.
If UE does not receive a RAR after 1 attempt, it moves to next highest level (e.g. 5 to 10, and 10 to 15).
At highest level, FFS on how many attempts are allowed, and the overall procedure (e.g. Backoff etc).
Starting level:
  Start at the lowest level as baseline in initial IDLE mode access case. We could allow optimisations so UE can instead decide the starting level (e.g. based on defined measurements or other means), but FFS on the way of detecting and specifying that (more analysis invited for next meeting).
  In RRC connected mode could be configured by eNB (dedicated RRC signalling).
NOTE: Pmissed-detection relaxation only impacts the max number of possible repetitions overall we need to specify.

## Slide 4: Other aspects
Observation: Need to evaluate max RACH latency with 15dB coverage extension for RAN2.