## Slide 1: Way Forward on Discovery and Measurement Enhancement(s)
NTT DOCOMO, ZTE, ETRI, Panasonic, Samsung
R1-135957
3GPP TSG RAN WG1 #75
San Francisco, USA, 11th – 15th November 2013
Agenda item 6.2.6.2

## Slide 2: Background
Conclusion:
To support an enhanced transition time reduction, discovery procedure/signal(s) is needed
Cells operating a cell on/off may transmit discovery signal(s) supporting at least for cell identification, coarse time/frequency synchronization, intra-/inter- frequency RRM measurement of cells and QCL
  Note that QCL is not always necessary or possible depending on the procedure
  Note that all QCL features might not needed
  Need of RLM is FFS
Possible conclusion and observation:
If new discovery signal(s)/procedure(s) are defined, they may be used in cells not operating a cell on/off
Discovery and measurement enhancement(s) in Rel. 12 should enable UE to reliably detect and measure at least the three strongest small cells subject to meeting the side conditions (e.g., for RSRP)

## Slide 3: Proposal
Conclusion:
If new discovery signal(s)/procedure(s) are defined for small cell on/off, they may be considered in cells not operating a cell on/off
  The new discovery signal(s)/procedure(s) do not replace existing Rel-8/11 discovery signal(s)/procedure(s).
Observation:
Discovery and measurement enhancement(s) in Rel. 12 should enable UE to reliably detect and measure at least the three strongest cells subject to meeting the side conditions (e.g., for RSRP)