## Slide 1: Some Remaining Details for 3D channel modeling
Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Samsung, LG Electronics, Huawei, Hisilicon, NSN, Nokia
3GPP TSG RAN WG1 #75 R1-136026
San Francisco, USA, 11th – 15th November 2013
Agenda item: 6.2.7.1

## Slide 2: Proposal
Reuse ESA values from WINNER+ as following:
 |  | UMi/UMaO2I | UMi outdoor |  | UMa outdoor | 
 |  | LOS/NLOS | LOS | NLOS | LOS | NLOS
EoA spread (ESA) log10([°]) | μ | 1.01 | 0.60 | 0.88 | 0.95 | 1.26
 | σ | 0.43 | 0.16 | 0.16 | 0.16 | 0.16

## Slide 3: Proposal
Reuse cluster ESA values from WINNER+ as following:
 | UMi/UMa O2I | UMi outdoor |  | UMa outdoor | 
 | LOS/NLOS | LOS | NLOS | LOS | NLOS
Cluster ESA ([°]) | 3 | 7 | 7 | 7 | 7

## Slide 4: Proposal
 | UMi/UMa O2I | UMi outdoor |  | UMa outdoor | 
 | LOS/NLOS | LOS | NLOS | LOS | NLOS
ESD ([°]) | 25 | 12 | 10 | 15 | 50
ESA([°]) | 25 | 12 | 10 | 15 | 50
Reuse autocorrelation distance values from WINNER+ as following:
Horizontal Autocorrelation Distance:
For simplicity of channel modeling, all large scale parameters are assumed to have a vertical autocorrelation distance less than floor height, e.g. 3 meters
Vertical Autocorrelation Distance:

## Slide 5: Proposal
Limiting ZoD and ZoA
  Assuming that generated ZoD and ZoA in Step 7 have been bounded with [0, 360], then following restriction should be applied