## Slide 1: Proposal on New UE Category
Huawei, HiSilicon
3GPP TSG RAN WG1 #76
Prague, Czech Republic, 10th – 14th February 2014
Agenda item 7.1
R1-140856

## Slide 2: Transport Block Sizes (1/2)
Send LS to RAN2 stating RAN1 agreed to
  Introduce new categories: Category 9 and 10
  Backward compatibility
    Cat. 9 indicates cat. 6
    Cat. 10 indicates cat. 7
  New transport block sizes and soft buffer sizes (Table 4.1-1 36.306)
UE Category | Maximum number of DL-SCH transport block bits received within a TTI (Note) | Maximum number of bits of a DL-SCH transport block received within a TTI | Total number of soft channel bits | Maximum number of supported layers for spatial multiplexing in DL
Category 9 | 452256 | 149776 (4 layers) 75376 (2 layers) | 5481216 | 2 or 4
Category 10 | 452256 | 149776 (4 layers) 75376 (2 layers) | 5481216 | 2 or 4

## Slide 3: Transport Block Sizes (2/2)
Table 4.1-2 of 36.306 (UL)
UE Category | Maximum number of UL-SCH transport block bits transmitted within a TTI | Maximum number of bits of an UL-SCH transport block transmitted within a TTI | Support for 64QAM in UL
Category 9 | 51024 | 51024 | No
Category 10 | 102048 | 51024 | No
Table 4.1-4 of 36.306 (MCS bits)
  75376 bits for both categories 9 and 10

## Slide 4: Rate Matching (1/2)
Use the following values for limited buffer rate matching (LBRM) in 36.212 section 5.1.4.1.2
If Nsoft = 35982720,
KC= 5,
elseif Nsoft = 5481216
if the UE is capable of supporting no more than a maximum of two spatial layers for the DL cell,
KC = 3
else
KC = 3/2
elseif Nsoft = 3654144 and the UE is capable of supporting no more than a maximum of two spatial layers for the DL cell,
KC = 2
else
KC = 1
End if.

## Slide 5: Rate Matching and Soft Buffering
Before finalizing the CRs for 36.212 and 36.213, determine first
  Will UE category to use at the eNB be signaled to UE?
  How will multiple UE categories be interpreted if a UE signals both ue-Category-v1020 and ue-Category-v11xy
  And hence how
    The value of Nsoft is selected according to UE category in 36.212 section 5.1.4.1.2
    The value of Nsoft is selected according to UE category in 36.213 section 7.1.8