## Slide 1: Way Forward on PUCCH resource allocation for HARQ-ACK with eIMTA ([76-06])
NSN
R1-141064
RAN1 #76
Prague, Czech Republic
February 10-14, 2014

## Slide 2: Subframe indexing principles
Subframes are indexed according to the principle
  First type: fixed subframes having the same HARQ timing for both eIMTA and non-eIMTA UEs
  Second type: fixed subframes having different HARQ timing for eIMTA and non-eIMTA UEs
  Third type: flexible subframes
No further separation between the second and the third group of subframes, i.e. block interleaving is applied for second and third group of subframes together

## Slide 3: Resource allocation formulas for PDCCH
For the first type of subframes the exact equation is the same as in 36.213 but M refers to the Table on Slide #4
For 2nd and 3rd type of subframes, PUCCH resource for antenna port p0 is given by:
For 2nd and 3rd type of subframes, PUCCH resource for antenna port p1 is given by:
In the above equations, M1 refers to the Table on slide #5
is RRC configured

## Slide 4: Subframe indexing tables (1/2)
The following tables are adopted
  FFS whether implicit resource allocation is supported for DL HARQ reference configuration #5 (depending on the outcome of [76-07])
  Note: whether or not to capture Table 1 into the specs is up to the editor
  Note: some of the entries in Table 1 are in brackets, such as (6). This represents a case when there exist subframe indexes in the DL association set corresponding to SIB-1 UL-DL configuration, which are not present in DL association set corresponding to the DL reference UL-DL configuration. In this case, an eIMTA UE needs to reserve the PUCCH resources according to the subframe indicated in the brackets, but must not map any HARQ-ACK onto those resources to avoid resource collisions.
DL HARQ reference configuration | UL-DL Configuration given by SIB-1 | Subframe n |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 | 0 | - | - | 6 | - | - | - | - | 6 | - | -
 | 1 | - | - | 7,6 | - | - | - | - | 7,6 | - | -
 | 2 | - | - | 8,7,4,6 | - | - | - | - | 8,7,4,6 | - | -
 | 3 | Invalid |  |  |  |  |  |  |  |  | 
 | 4 | Invalid |  |  |  |  |  |  |  |  | 
 | 5 | Invalid |  |  |  |  |  |  |  |  | 
 | 6 | - | - | 7 | - | - | - | - | 7 | - | -
4 | 0 | - | - | - | - | - | - | - | - | - | -
 | 1 | - | - | 7, (6) | 4 | - | - | - | - | - | -
 | 2 | Invalid |  |  |  |  |  |  |  |  | 
 | 3 | - | - | 7, (6), 11 | 6,5 | - | - | - | - | - | -
 | 4 | - | - | 12, 8, 7, 11 | 6, 5, 4, 7 | - | - | - | - | - | -
 | 5 | Invalid |  |  |  |  |  |  |  |  | 
 | 6 | - | - | 7 | 7 | - | - | - | - | - | -
5 | 0 | - | - | 6 | - | - | - | - | - | - | -
 | 1 | - | - | 7, 6 | - | - | - | - | - | - | -
 | 2 | - | - | 8, 7, 4, 6 | - | - | - | - | - | - | -
 | 3 | - | - | 7, 6, 11 | - | - | - | - | - | - | -
 | 4 | - | - | 12, 8, 7, 11 | - | - | - | - | - | - | -
 | 5 | - | - | 13, 12, 9, 8, 7, 5, 4, 11, 6 | - | - | - | - | - | - | -
 | 6 | - | - | 7 | - | - | - | - | - | - | -
Table 1: Subframe indexing for subframes for which eIMTA and non-eIMTA UEs have the same timing (first type of subframes)

## Slide 5: Subframe indexing tables (2/2)
DL HARQ reference configuration | UL-DL Configuration given by SIB-1 | Subframe n |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 | 0 | - | - | 7, 8, 4 | - | - | - | - | 7, 8, 4 | - | -
 | 1 | - | - | 8, 4 | - | - | - | - | 8, 4 | - | -
 | 2 | - | - | - | - | - | - | - | - | - | -
 | 3 | Invalid |  |  |  |  |  |  |  |  | 
 | 4 | Invalid |  |  |  |  |  |  |  |  | 
 | 5 | Invalid |  |  |  |  |  |  |  |  | 
 | 6 | - | - | 6, 8, 4 | - | - | - | - | 8, 6, 4 | - | -
4 | 0 | - | - | 12, 7, 11, 8 | 7, 4, 5, 6 | - | - | - | - | - | -
 | 1 | - | - | 12, 8, 11 | 7, 5, 6 | - | - | - | - | - | -
 | 2 | Invalid |  |  |  |  |  |  |  |  | 
 | 3 | - | - | 12, 8 | 4,7 | - | - | - | - | - | -
 | 4 | - | - | - | - | - | - | - | - | - | -
 | 5 | Invalid |  |  |  |  |  |  |  |  | 
 | 6 | - | - | 12, 11, 8 | 4, 5, 6 | - | - | - | - | - | -
5 | 0 | - | - | 12, 7, 11, 13, 8, 4, 9, 5 | - | - | - | - | - | - | -
 | 1 | - | - | 13, 12, 8, 11, 4, 9, 5 | - | - | - | - | - | - | -
 | 2 | - | - | 13, 12, 9, 11,5 | - | - | - | - | - | - | -
 | 3 | - | - | 13, 12, 5, 4, 8, 9 | - | - | - | - | - | - | -
 | 4 | - | - | 13, 5, 4, 6, 9 | - | - | - | - | - | - | -
 | 5 | - | - | - | - | - | - | - | - | - | -
 | 6 | - | - | 13, 12, 11, 6, 8, 4, 9, 5 | - | - | - | - | - | - | -
Table 2: Subframe indexing for subframes for which eIMTA and non-eIMTA UEs have the different timing (second and third type of subframes)

## Slide 6: For information: Example of subframe indexing according to the proposal
RRC Configurable

## Slide 7: HARQ-ACK resource allocation with EPDCCH
For EPDCCH, same subframe indexing is used as for PDCCH
  This subframe indexing is also used in the ARO calculation
RRC configured offset between Type 1 and Type 2 & 3 subframes is not introduced for EPDCCH

## Slide 8: Ordering of the HARQ-ACK bits
For PUCCH format 3, the currently specified principle is used
FFS: For PUCCH format 1b with channel selection