## Slide 1: WF on Small Cell Discovery Reference Signals
Intel, NSN, Nokia, MediaTek, ETRI, NVIDIA, NEC, InterDigital, Fujitsu, BlackBerry, Qualcomm, CATT, Broadcom
3GPP TSG RAN WG1 Meeting #76bis
Shenzhen, China, 31st March – 4th April, 2014
Agenda item: 7.2.4.2.2
Document for: Decision
R1-141870

## Slide 2: Backgrounds
Agreements in RAN1#76
  In the enhanced cell discovery procedure, UE can assume multiple signals are transmitted
    UE can assume transmission of PSS (identical to the Rel-8 waveform) at least for coarse time synchronization
    Which other signal(s) the UE can assume are transmitted is FFS
      Possible candidates are one or more instances of SSS, CRS, CSI-RS, and PRS
      Which signals are useful for which purpose is FFS
  In addition to purposes given by the WID, cell multiplexing capability, UE power efficiency, and impact to legacy UE’s measurement can be considered when discussing candidate solutions

## Slide 3: Backgrounds
It is pointed out that, from the multiple contributions, SSS needs to be transmitted together with PSS not only for efficient cell ID detection but also for easy/robust frequency offset estimation.
It has been shown that multiple instances with a DRS occasion can help to enhance DRS detection performances by time/frequency reuse, muting, multiple transmissions, etc.

## Slide 4: Proposals
A DRS occasion comprises N instances.
  Both PSS and SSS are transmitted within the DRS occasion.
    FFS for the additional reference signals within the DRS occasion among no RS, CRS, CSI-RS, and/or PRS
  The N instances may contain different RS types.
  FFS for the definition of ‘instance’ (e.g. OFDM symbol (s), subframe (s), etc)
  FFS whether the instances are consecutive or not
  FFS for the exact value of N
  FFS on the details within the DRS occasion
A UE assumes the DRS occasion is periodically transmitted.