## Slide 1: WF on Power control for Dual-Connectivity
LG Electronics, NTT DOCOMO, Panasonic
R1-142675
3GPP TSG RAN WG1 #77
Seoul, Korea, May 19 - 23, 2014
Agenda item 6.2.4

## Slide 2: Proposal
In both synchronous and asynchronous cases, at least for PUCCH/PUSCH
  Minimum guaranteed power allocation P_SeNB and/or P_MeNB can be configured
    P_SeNB >=0, P_MeNB >=0, P_SeNB+P_MeNB <= PCmax
  The total power allocation per CG Palloc_xeNB can be determined by
    (1) Power allocation up to P_SeNB and P_MeNB (i.e. Ppre_SeNB and Ppre_MeNB)
      At first, UE needs to allocate power per each eNB up to P_SeNB or P_MeNB (if configured) respectively regardless of priority rule if transmission is scheduled
        Ppre_xeNB = min {power based on actual grant/assignment and TPC commands, P_xeNB}
    (2) Plus allocation of remaining power

## Slide 3: Proposal
In both synchronous and asynchronous cases:
  If look-ahead is supported or in synchronous case
    All the remaining power can be used
    For the remaining power, priority is determined based on UCI type across CG for channels not satisfied by P_SeNB or P_MeNB
      FFS on details
      Giving higher priority to a CG is not precluded
  If look-ahead is not assumed:
    Reserve P_SeNB and/or P_MeNB towards each eNB if there is potential uplink transmission
      If the UE knows it does not have transmission in the other CG in overlapped subframes based on at least semi-static information, UE does not reserve the power for that CG
    For the remaining power, earlier transmission is higher priority
  Confirm WA with clarification:
    Power control changes are not allowed one carrier in the middle of subframe in asynchronous case in dual connectivity (i.e., Power of on-going transmission is not adjusted)
  Within a CG, for the total power allocation, reuse Rel-11 relative priority and power scaling of different channel types

## Slide 4: Proposal
PRACH to PCell has the highest priority;
SRS (both towards MeNB and SeNB) have the lowest priority;
RAN1 perspective, differentiation between PUSCH with SRB and PUSCH without SRB is not assumed

## Slide 5: Appendix

## Slide 6
In async case
Allocated power of a eNB takes into account both overlapping subframes of other eNB
Palloc_xeNB = min (Palloc_xeNB_early, Palloc_xeNB_late)
Palloc_xeNB_early is the allocated power if only overlapping subframe starting earlier would be present
  The power of the overlapping subframe starting earlier cannot be changed
Palloc_xeNB is the allocated power if only overlapping subframe starting later would be present
  If actual required power of other CG in overlapping subframe starting later can be known ("look-ahead")
    Palloc_xeNB _late is calculated using the actual required power of the other eNB
  If actual required power of other CG in overlapping subframe starting later can not be known (no "look-ahead")
    Palloc_xeNB _late is calculated assuming that Ppre_xeNB of the other eNB is equal to its P_xeNB

## Slide 7
PCMAX
PMeNB
PSeNB
SF i
SF i+1
SF k
SF k+1
For Channel 4 > Channel 3 > Channel 2 > Channel 1 in priority,
Channel 1
Channel 2
Channel 3
Channel 4
Scheduled power
Allocated power (P_pre_xeNB)
Look-ahead supporting case at SF i+1 on MeNB
Ppre_MeNB
Ppre_MeNB
Ppre_SeNB
Ppre_SeNB
Palloc_MeNB_early
Palloc_MeNB_late
Remaining Power(k, i+1)
Remaining Power(k+1, i+1)

## Slide 8
PCMAX
PMeNB
PSeNB
SF i
SF i+1
SF k
SF k+1
For Channel 4 > Channel 3 > Channel 2 > Channel 1 in priority,
Channel 1
Channel 2
Channel 3
Channel 4
Allocated power
Non Look-ahead supporting case at SF i+1 on MeNB
Scheduled power
Ppre_MeNB
Ppre_MeNB
Ppre_SeNB
Ppre_SeNB
Palloc_MeNB_early
Palloc_MeNB_late
Remaining Power(k, i+1)

## Slide 9
PCMAX
PMeNB
PSeNB
SF i
SF i+1
SF k
SF k+1
For Channel 4 > Channel 3 > Channel 2 > Channel 1 in priority,
Channel 1
Channel 2
Channel 3
Downlink
Allocated power
Look-ahead supporting case at SF i+1 on MeNB
Scheduled power
Ppre_MeNB
Ppre_SeNB
Remaining Power(k, i+1)
Remaining Power(k+1, i+1)
Palloc_MeNB_late
Palloc_MeNB_early

## Slide 10
PCMAX
PMeNB
PSeNB
SF i
SF i+1
SF k
SF k+1
For Channel 4 > Channel 3 > Channel 2 > Channel 1 in priority,
Channel 1
Channel 2
Channel 3
Downlink
Allocated power
Non Look-ahead supporting case with earlier Tx prioritization at SF i+1 on MeNB
Scheduled power
Ppre_MeNB
Ppre_SeNB
Palloc_MeNB
Palloc_MeNB_late
Palloc_SeNB_late
Ppre_MeNB
Remaining Power(k, i+1)
Remaining Power(k+1, i+1)
Palloc_MeNB_early