## Slide 1: WF on TBS design for 256QAM
CMCC, Huawei, Hisilicon, CHTTL, ZTE
R1-142640

## Slide 2: Background
In RAN1#76 and 76bis meeting, the following progresses are achieved on TBS table design for 256QAM.
  Define overhead assumption(s) (REs/PRB) for PDSCH
    Use 120 REs per PRB for all 256QAM spectral efficiencies except for the highest spectral efficiency
    Use 136 REs per PRB for the highest spectral efficiency
  Reuse as many as possible of current TBS entries with up to around [2%] average padding
  Limit the number of new TBS values as much as possible
  The new transport block sizes introduced in the specification should follow the Rel-8 principle of QPP size alignment

## Slide 3: (backup)
Define overhead assumption(s) (REs/PRB) for PDSCH
  Use 120 REs per PRB for all 256QAM spectral efficiencies except for the highest spectral efficiency
  Use [136] REs per PRB for the highest spectral efficiency
    Use 136 REs per PRB for the highest spectral efficiency of TBS_L1 design
    Use 132 REs per PRB for the highest spectral efficiency of TBS_L2, TBS_L3, TBS_L4 design

## Slide 4: Proposal
TBS_L1 design principle
  for all 256QAM spectral efficiencies except for the highest spectral efficiency, TBS(ITBS,NPRB) is designed according to the following steps
    Calculate X as NPRB*120*SE(ITBS), where to SE(ITBS) is target spectral efficiency of ITBS;
    Select TBS(ITBS,NPRB) from Rel-10 TBS entries which is closest to X after adding CRC bits
  For the highest spectral efficiency, TBS(ITBS,NPRB) is designed according to the following steps
    Calculate X as NPRB*136*SE(ITBS), where to SE(ITBS) is target spectral efficiency of ITBS;
    Select TBS’(ITBS,NPRB) from Rel-10 TBS entries which is closest to X after adding CRC bits;
      If TBS’(ITBS,NPRB) results a code rate exceed 0.93 when transport blocks map to one-layer or two-layer spatial multiplexing using 136 REs per PRB ,
      then select TBS(ITBS,NPRB ) as the largest Rel-10 TBS which is smaller than TBS’(ITBS,NPRB) and does not exceed 0.93 code rate when transport blocks map to one-layer or two-layer spatial multiplexing using 136 REs per PRB ;
      Else TBS(ITBS,NPRB ) = TBS’(ITBS,NPRB )

## Slide 5: Proposal
TBS_Lm design principle for m=2,3,4
  for all TBS_Lm except for the highest TBS_Lm , TBS_Lm (TBS_L1) is designed according to the following steps, where TBS_L1 is larger than 75376
    Calculate Y as m* TBS_L1
    Select TBS_Lm from TBS candidate entries which is closest to Y
  for the highest TBS_Lm , TBS_Lm (TBS_L1) is designed according to the following steps
    Calculate Y as m* TBS_L1
    Select TBS_Lm’ from TBS candidate entries which is closest to Y
      If TBS_Lm’ results a code rate exceed 0.93 when transport blocks map to m-layer spatial multiplexing using 132 * REs per PRB ,
      then select TBS_Lm as the largest candidate TBS which is smaller than TBS_Lm’ and does not exceed 0.93 code rate when transport blocks map to m-layer spatial multiplexing using 132 * REs per PRB ;
      Else TBS_Lm = TBS_Lm’
* Note: 132REs for optimize 4-port DMRS transmission

## Slide 6: Example
TBS candidate entries include
  Rel-10 TBS entries (229) and
  [191720; 284608; ]*
  [302776; 305976; 308832; 312096; 314888; 318216; 320944; 324336; 327000; 330456; 333056; 336576; 339112; 342696; 345168; 348816; 351224; 354936; 357280; 361056; 363336; 367176; 369392; 373296; 375448; 379416; 381504; 385536; 387560; 391656; 393616; 397776; 399672; 403896;]
  *Note: [191720; 284608; ] is optimize 4-port DMRS transmission as discussed in R1-142506

## Slide 7: Example of TBS table
FFS
  According to the outcome of MCS design.