## Slide 1: WF on the remaining TBS table design for 256QAM
CMCC, Huawei, Hisilicon, CHTTL, ZTE, CATT, CATR, MediaTek, CATR, Potevio, III, coolpad
R1-143465

## Slide 2: Background
During RAN1#77, offline discussion has agreed on the TBS table for 256QAM in R1-142735
The remaining issue of 256QAM TBS is for the FFS value for Table 7.1.7.2.2-1, Table 7.1.7.2.4-1 and Table 7.1.7.2.5-1 in TS36.213 as follows:
TBS_L1 | TBS_L2 | TBS_L3 | TBS_L4
76208 | 152976 | 230104 | 305976
78704 | 157432 | 236160 | 314888
81176 | 161760 | 245648 | 324336
84760 | 169544 | 254328 | 339112
87936 | 175600 | 266440 | 351224
90816 | 181656 | 275376 | 363336
93800 | 187712 | 284608 | 375448
97896 | Alt 1: 193768 | Alt 1: 290664 | Alt 1: 387560
 | Alt 2: 195816 | Alt 2: 293736 | Alt 2: 391656
FFS

## Slide 3: Background
The differences between Alt 1 and Alt2 is that:
Table 1. Peak data rate (20MHz)*
 | Alt 1 [Mbps], 132RE | Alt 2 [Mbps], 136RE | Gain of Alt 2 over Alt 1
2Layer (2 port CRS) | 195.792 Mbps | 195.792 | 0%
4Layer (4 port CRS) | 387.536 | 391.632 | 1.05%
4Layer (4 port DMRS)** | 368.157 | 339.088 | -8.57%
8Layer (8 port DMRS)*** | 736.362 | 678.224 | -8.57%
*Note 1: This example is for FDD. But the same calculation and results applied for TDD.
**Note 2: Assuming 2 port CRS + 4 port DMRS for 4 Non-MBSFN, 4 port DMRS for 6 MBSFN
***Note 3: Assuming 2 port CRS + 8 port DMRS for 4 Non-MBSFN, 8 port DMRS for 6 MBSFN
Loss in terms of peak 8.5%

## Slide 4: Proposal
Alt 1 is chosen for Table 7.1.7.2.2-1, Table 7.1.7.2.4-1 and Table 7.1.7.2.5-1 in TS36.213.