## Slide 1: WF on Conditions for Synchronization Sources in Out-of-coverage
Samsung, Nokia Corp., Nokia Networks
3GPP TSG RAN WG1 #79 R1-145310
San Francisco, CA, 17th – 21nd November 2014
Agenda item: 6.2.1.1.3
Document for decision

## Slide 2: Background
In last RAN1 78bis meeting, the following conditions are incorporated in synchronization procedure for in-coverage UEs
  Only a UE transmitting SA or D2D data shall transmit D2DSS if;
    …
    the UE is RRC_Connected and the eNB has instructed it (by dedicated signalling) to start D2DSS transmission AND/OR
    FFS other condition(s) are satisfied if the UE is not transmitting SA or D2D data within the SA/data period in which the subframe falls OR
    all of the following conditions are satisfied:
      an RSRP threshold for communication D2DSS transmission is configured, AND
      the RSRP value of the UE is less than the threshold, AND
      the eNB has not instructed the UE (by dedicated signalling) to stop D2DSS transmission.

## Slide 3: Background
Range mismatch between D2DSS and D2D data/SA in out-of-coverage network

## Slide 4: Proposal
For out-of-coverage UEs,
  A UE transmitting SA or D2D data shall transmit D2DSS if;
    Received signal strength of all received D2DSS(s) by the UE are below the syncSourceThres.
  A UE not transmitting SA or D2D data can transmit D2DSS only if;
    Received signal strength of an out-of-sync D2DSS is above the syncSourceThres, AND
    The UE transmitting the out-of-sync D2DSS has lower priority than the UE’s reference sync source.