## Slide 1: Way Forward on LAA Evaluation Assumptions – Antenna Configuration, MCS, Wi-Fi Detailed Assumptions and Duplexing
Ericsson, Samsung, Qualcomm, Huawei, HiSilicon, Intel
3GPP TSG RAN WG1 #79
San Francisco, USA, 17th – 21st November 2014
Agenda item 6.3.2.1
R1-145330

## Slide 2: Proposal – Wi-Fi Detailed Assumptions
Parameter |  | value
MCS |  | 802.11ac MCS table without 256 QAM Optional: include 256QAM (should be the same as for LAA)
Antenna configuration |  | 2Tx2Rx in DL, Cross-polarized Optional: 1Tx2Rx in DL. UL: 1Tx2Rx Baseline: open loop Company should state assumptions if assumed otherwise
Channel coding |  | BCC Optional: LDPC code
Frame aggregation |  | A-MPDU
MPDU size |  | Up to each company
Max PPDU duration |  | Baseline:< 4 ms (Asynchronous to LTE timing) Company should state assumptions if assumed otherwise
MAC | Coordination | DCF If VoIP users are included, EDCA can be used
 | SIFS, DIFS | SIFS, DIFS
 | Detection | Energy detection & preamble detection
 | RTS/CTS | Optional
 | Contention window | Per DCF If VoIP users are included, per EDCA can be used
CCA-CS |  | -82dBm and preamble decoding (Note preamble occupies the 20MHz system bandwidth with rate 1/2 coding and BPSK modulation)
CCA-ED |  | -62dBm
ACK Modeled (successful reception, resources utilized) |  | Yes
DL/UL Duplexing |  | DL only for DL-only LAA coexistence evaluation DL & UL for DL & UL LAA coexistence evaluation
Rate control |  | Up to each company; should state assumption when reporting results
Channel selection |  | Up to each company; should state assumption when reporting results
Table 3 Wi-Fi system evaluation assumptions

## Slide 3: Proposal –LAA Detailed Assumptions
Table 4: LAA system assumptions
Parameters | Value
PCI planning for each NW | Planned
Antenna configuration | 2Tx2Rx in DL, Cross-polarized. 1Tx2Rx in UL
Transmission schemes | Based on TM4 or TM10, QPSK/16QAM/64QAM Optional: include 256QAM (should be the same as for Wi-Fi)
Turbo code block interleaving depth | Per LTE specs (1-14 LTE OFDM symbols dependent on MCS and PRB allocation)
Scheduling | Proportional fair
Link adaptation | Realistic
CCA-ED | Up to each company; should state assumption when reporting results
Channel selection | Up to each company; should state assumption when reporting results