## Slide 1: R1-150573
Discussion on Enhanced Indoor Positioning Technologies
NextNav, LLC

## Slide 2: Introduction
FCC has just approved new rules for indoor location
  Notice For Proposed Rule Making (NPRM) released in February 2014
  Report & Order approved January 29, 2015
New rules call for both high precision 2D positioning and vertical
  50m – 40% of all calls in top 50 markets in 2 years; 50m - 80% in 6 years
  Uncompensated barometric pressure for all calls from handsets with pressures sensor capability in 3 years. Dispatchable or vertical solution in top 25 markets within 6 years.
Several technologies including RFPM, hybrid A-GPS + A-FLT and Terrestrial Beacons were tested in CSRIC III in the Indoor Test Bed (2012-2013)
  http://transition.fcc.gov/bureaus/pshs/advisory/csric3/CSRIC_III_WG3_Report_March_%202013_ILTestBedReport.pdf
  Follow-up independent testing of NextNav Rev. 2 TBS system: http://apps.fcc.gov/ecfs/document/view?id=7520937523
Standardization is designed to ensure the following objectives:
  Ensures interoperability of solution
  Competitiveness in market place

## Slide 3: NextNav Overview
NextNav is a network services provider deploying a nationwide system to provide reliable, high-precision positioning information in urban and indoor environments
Spectrum licenses throughout the US and wide-area architecture provide consistent store level / floor level precision across entire metropolitan areas
Experienced team has a long and successful history in network deployment, and is backed by New Enterprise Associates (NEA) and Oak Investment Partners, Columbia Capital, Telcom Ventures and Goldman Sachs

## Slide 4: Positioning Enhancements SI Details
Study Item will evaluate positioning technology enhancements and specification impacts related to Indoor Positioning, such as:
  Enhancements to OTDOA, RFPM, UTDOA
  Inclusion of Terrestrial Beacon Systems (TBS)
  Pressure Sensor and hybrid positioning support
Broadly classified as Radio Access Technology (RAT) Dependent and RAT Independent
  Example of RAT Dependent Technologies: OTDOA, AFLT, UTDOA, etc
  Example of RAT Independent Technologies: Sensor-based, Pseudo-GNSS, TBS, etc
Multiple technologies are expected to co-exist and compliment each other to help operators meet the FCC requirements for indoor positioning.

## Slide 5: Terrestrial Beacon Systems (TBS)
Wide-area positioning systems utilizing ground-based beacons to complement GNSS solutions by extending location accuracy indoors and in urban canyons, including in the vertical dimension.
  (Reference: ILA System Architecture White Paper version 1.0)
TBS is a general term that could include all of the following:
  NextNav’s Metropolitan Beacon System (MBS)
  Indoor MEssaging System (IMES), based on QZSS (Quasi Zenith Satellite System)
  Pseudolites (PLs), work ongoing in ETSI
  Other terrestrial beacon systems

## Slide 6: Key TBS Technology Principles
Beacon
Beacon
Beacon
Cell phone
In urban canyon

GPS Satellite
Blocked!
Location Network Element (SUPL, PDE, MPC)
Cell phone
Indoors
Performance Advantage
Accurate location in urban and indoor environments
Precise vertical position (1-3m)
Fast time to first fix
Dependable performance on a wide-area basis
Deployed Broadcast Beacons
Highly synchronized
Broad coverage from minimal sites
Operate on licensed spectrum, and/or
existing GNSS spectrum
Receivers
Firmware upgrade to typical GPS baseband
Minimal handset integration
On-device computation of location
Reduced power consumption
Core Network
Utilizes existing PDE, SUPL elements
Modifications to support new IEs but leverage existing messaging framework

## Slide 7: Key MBS Technology Principles
Network architecture effectively results in a terrestrial positioning “constellation” featuring significant commonality with GPS
  MBS signals shared e.g. similar to a GNSS, network operators need not deploy their own TBSs
  Timing-based system, using highly synchronized terrestrial transmitters for positioning
  Wide-area network architecture, providing consistent indoor service across coverage area
System designed for minimally-disruptive adoption in mobile handsets
  Re-use of GPS digital baseband
  Licensed spectrum adjacent to cellular bands allows for radio re-use
In line with other GNSSs, MBS ICD has been published and made available for download
    http://www.npstc.org/download.jsp?tableId=37&column=217&id=3219&file=NextNav_MBS_ICD_vG1_0_11_11_2014.pdf
Timing solutions result in 5 ns rms synchronization across network, minimizing timing-based errors
Air interface-agnostic system – allows for evolution of location technology independent of air interface
Unique height system results in 1 – 3m vertical precision by encoding real-time environmental reference information in positioning data payload

## Slide 8: Communications Safety, Reliability and Interoperability Council Trials (“CSRIC”)
In 4Q12 the FCC’s CSRIC advisory group held a comprehensive, independent trial of location technologies for indoor E911 in the San Francisco / Silicon Valley area.
Joint effort by Public Safety, technology vendors and national wireless carriers; results released March 2013 and NextNav “Rev 2” technology tested in identical scenarios in Summer 2013
Urban
San Francisco
Financial District
Suburban
Santa Clara County
Rural
San Benito County

## Slide 9: CSRIC Review
CSRIC Working Group 3 was chartered by the FCC with, among other things, creating an information base from which indoor location accuracy standards for E911 could be established
  WG3 consisted of technology vendors, public safety representatives and the four major U.S. wireless carriers
  7 technologies assessed, 4 participated in test bed program and 3 permitted results to be disclosed
  Results published in March, 2013 completing CSRIC3, WG3’s missions
Test program was performed by a 3rd party (TechnoCom), and was completely blind to participants
  Over 13,000 test calls for each participating vendor taken across 75 test points, with a strong test bias towards urban locations (70% of test points)
NextNav engaged TechnoCom to repeat the CSRIC test protocol for dense urban, urban and suburban morphologies utilizing NextNav’s Rev 2 technology (submitted to the FCC in August)
Rev 2 technology demonstrated yield improvement, vertical accuracy improvement and horizontal accuracy gains across all morphologies

## Slide 10: POP-Weighted Performance Metrics
The following chart depicts the CSRIC Rev 1 and Rev 2 performance data, weighted by US population density in urban and suburban areas1
The U.S. Census describes 30% of the population living in urban areas, 50% in suburban areas and 20% in rural areas. Data excludes testing in rural areas, where GPS functions adequately.
Probability of Position Accuracy | Rev 1 | Rev 2
50% | 28m | 18m
68% | 41m | 28m
80% | 55m | 39m
90% | 72m | 54m

## Slide 11: Floor-Level Height Accuracy
NextNav was the only company to have tested the vertical in indoor environments. Median height error was <1.5m and 90% error was <4m.
Vertical Height Error (in m)
Vertical CDF (Rev 2 test Results)
Internal Test at Intercontinental Hotel

## Slide 12: TBS 3GPP support requirements
LPP (LTE Positioning Protocol) TS 36.355 specification impacts. High-level changes required to support MBS in LPP consist primarily of information elements for Terrestrial Beacon Systems to support:
  UE/Location Server capabilities negotiation
  Assistance Data specific to TBS-based positioning
  Identify which technology was used in UE position fix and TBS measurements
Performance specifications in RAN4
  Equivalent of TS 36.171 needed for TBS

## Slide 13: Why should 3GPP support TBS?
TBS, and specifically NextNav’s MBS implementation, has indoor location performance that has been tested and validated by an independent third party.
TBS deployments are optimized for positioning only, which is not in the case for RAT dependent positioning methods.
Operators are on the hook to meet the FCC indoor location requirements.
Operators will be best served by having a variety of technologies available to them. TBS will put one more option in the operators tool box
NextNav’s deployment will be cost effective because the same infrastructure investment that can be shared by multiple operators and other users of the service
Because location is NextNav’s only business, it is worth it for us to make the investments in precision timing that may not be economically practical for individual operators in their mobile networks that don’t requires ns synchronization precision.

## Slide 14: Summary & Recommendations
The viability and performance of TBS has been proven via 3rd party testing over the last few years
3GPP will play a key role in the adoption of these technologies that addresses the needs of public safety and emergency services
RAN1 should evaluate TBS as a candidate technology for indoor location