## Slide 1: MIB contents offline discussion
Panasonic, Nokia Networks,
Nokia Corporation
3GPP TSG RAN WG1 Meeting #80 R1-150865
Athens, Greece, 9th – 13th February 2015
Agenda item 7.2.1.2.1
Information

## Slide 2: MIB contents possibility
Currently 10 bits are available as reserved.
Possible usage for reserved bits.
  Support of CE 1 bit
  Support of Rel13 MTC UE 1 bit
  Time frequency position of MTC-SIB1 2-3 bits
    FFS: Whether repetition level of MTC-SIB1 is included or not
  TBS of MTC-SIB1 2 bits
  CFI (lower priority) 2 bits
  Sufficient number of spare bits should be reserved for future use, e.g. 4-5 bits.