## Slide 1: WF on PRACH CE Procedure
Huawei, HiSilicon, ALU, ASB, Ericsson, Intel, InterDigital, Panasonic
R1-150877
3GPP TSG RAN WG1 #80
Athens, Greece, February 9-13, 2015
Agenda item 7.2.1.2.3

## Slide 2: Rel-13 progress
The following agreements from Rel-12 were confirmed in RAN1#79:
RAN1 confirms that following PRACH related agreements in Rel-12 LC-MTC are applied for Rel-13 low-complexity UE
  For PRACH multiplexing scheme, CDM, and/or TDM and/or FDM are supported
  After the initial random access procedure, for a physical channel using repetition, the repetition level is up to network
  Multiple PRACH repetition levels are supported
  Repeating the existing preamble formats for PRACH enhancement
  In addition, define additional time/freq. resource region(s) separate for “enhanced coverage” UEs.
    Within new region, at least CDM is allowed.
  Specified maximum numbers of levels: Working assumption of 3 (this does not include “zero coverage extension”). More evidence needed if we were to extend this.
  eNB-configurable number of levels (1, 2, 3) up to specified max level.
1 attempt = configured number of repetitions.

## Slide 3: Rel-12 background
The following Rel-12 agreements are yet to be confirmed after RAN1#79:
Multiple PRACH repetition levels are supported (already in Rel-13)
  FFS: For initial random access, there is one to one mapping between PRACH repetition level and PRACH resource set. UE selects a PRACH repetition level and transmits the PRACH preamble using the PRACH resource set according to the selected PRACH repetition level
  FFS: details of PRACH resource set, repetition levels
  FFS: details of random access procedure including initial selection for repetition level
Number of repetitions per level:
  FFS for configurable value.
  FFS ranges of this value per level – come back later in week.
FFS: Power ramping is supported
If UE does not receive a RAR after 1 attempt, it moves to next highest level (e.g. 5 to 10, and 10 to 15).
At highest level, FFS on how many attempts are allowed, and the overall procedure (e.g. Backoff etc).
Possible agreements from Rel-12 yet to be considered after RAN1#79:
Starting level for contention based random access procedure:
  Case 1: FFS between starting at the lowest level or defining it based on measurement or based on other ways
  Case 2: working assumption: In RRC connected mode could be configured by eNB (dedicated RRC signalling).

## Slide 4: Proposals
For coverage enh of PRACH , for initial random access
  There is one to one mapping between PRACH repetition level and PRACH resource set
  WA: UE selects a starting PRACH repetition level based on DL measurement(s) if the DL measurement is reliable
    FFS details of the DL measurement(s)
    FFS which level is selected if the DL measurement(s) is/are unreliable
    WA subject to RAN4 feedback on measurement reliability and time
The eNB can configure how many attempts are allowed for each PRACH repetition level
FFS: Power ramping or always max power used within each repetition level
If UE does not receive a RAR after the allowed number of attempts, it moves to the next higher repetition level
FFS UE behavior when UE receives RAR, but fails contention resolution