## Slide 1: WF on discontinuous transmission for LAA
Samsung, NTT DOCOMO, Kyocera
3GPP TSG RAN WG1 #80 R1-150928
Athens, Greece
9th – 13th February 2015
Agenda item: 7.2.3.3
Document for decision

## Slide 2: Proposal
Capture the following content in the section on discontinuous transmission in the TR 36.889:
  One or more signals can be transmitted from the beginning of a downlink transmission that can provide support for the following functionalities
    AGC setting
    Channel reservation
  One or more signals can be transmitted in a downlink transmission that can provide support for the following functionalities
    Detection of the LAA transmission from the eNodeB
    Cell identification
    Time & frequency synchronization for receiving data and/or control or for measurement
    Other information if necessary
  Candidate physical signals designs can include (but not limit to):
    Existing or modified discovery signal
    Existing or modified PSS/SSS
    Existing or modified CRS
    Initial signal (definition is FFS)
    Combination of above
  Note: It is not precluded that some functionalities above may be supported by other methods