## Slide 1: WF on VoIP Traffic Model for LAA evaluation
Intel, Ericsson
R1-150815
3GPP TSG-RAN WG1 Meeting #80
Athens, Greece, 9th-13th February 2015
Document for: Decision
AI 7.2.3.3

## Slide 2: Proposal for VoIP Traffic Model (1/2)
Additional assumptions to the DL only traffic case:
  When the mixed traffic (i.e., FTP + VoIP) is evaluated in the case of both DL and UL traffic:
    The voice activity of the VoIP users is 50% for both DL and UL.
    For each VoIP user, On and Off periods of length X (e.g., X = 5) second alternates with each other in such a way that both DL and UL are not active at the same time.
      An example for X = 5 is given in the figure below.

## Slide 3: Proposal for VoIP Traffic Model (2/2)
  Performance metric
    In the case of both DL and UL traffic, 98%ile latency is measured independently for DL and UL.
    If 98%ile latency of DL is greater than 50ms, the user is declared to be in outage for DL.
      The percentage of outage VoIP users for DL should be reported.
    If 98%ile latency of UL is greater than 50ms, the user is declared to be in outage for UL.
      The percentage of outage VoIP users for UL should be reported.
    If max(98%ile latency of DL, 98%ile latency of UL) is greater than 50ms, the user is declared to be in outage.
      The percentage of outage VoIP users should be reported.