## Slide 1: WF on PBCH options
Huawei, HiSilicon
R1-150892
3GPP TSG RAN WG1 #80
Athens, Greece, February 9-13, 2015
Agenda item 7.2.1.2.3

## Slide 2: Agreements in RAN1#80
Agreements:
Narrow down the options for PBCH coverage enh as follows:
  Agree that we only select ONE of the following options that define the repetition burst within the 40ms PBCH cycle:
    Option 1: Repetition in SF#0
    Option 2: Repetition in SF#0 + repetition in SF#5 in odd frames.
    Option 3: Repetition in SF#0 + repetition in 1 other sub-frame in all frames
    Option 4: Repetition in SF#0 + repetition in 3 other sub-frames in all frames
    FFS until RAN1#80bis which REs should be excluded for PBCH repetition
  Agree that “user data and MIB repetition are assumed not to be sent in the same PRBs.”
  Agree that we shall only select ONE of the options below for configuration of transmission across 40ms cycles:
    Option A: Always send repetition in every 40ms cycle.
    Option B: Dynamic on/off of repetitions on a per 40x ms cycle basis.
    Option C: Repetition based on pattern(s) across a given number of cycles.
  Choose among Option 1-A or 2-A or 3-B or 3-C or 4-B or 4-C in RAN1#80bis

## Slide 3: Observations
Opt C can be like Opt B if Opt C is a repetition pattern across an infinite number of cycles .
Opt C can be like Opt A if Opt C is a repetition pattern across a given number of cycles and the “given number of cycles” is 1.
Opt B can be like Opt C if the transmissions of the network pattern may be turned off by the network, for example in mild coverage enhancement conditions.

## Slide 4: Examples
    Option 1A:
      eNB transmits the PBCH repetition burst in every 40ms PBCH cycle
      UE assumes the PBCH repetition burst is transmitted in every 40ms PBCH cycle
      Repetitions within a 40ms that include PBCH repetition use Option 1
    Option 4C with PBCH repetitions every 4 PBCH cycles:
      eNB transmits the PBCH repetition burst every four 40ms PBCH cycles
      UE knows from specification the pattern (SFN and number of cycles)
      Repetitions within a 40ms that include PBCH repetitions use Option 4
    Option 3B’ with PBCH repetitions possibly every 6 PBCH cycles
      eNB transmits the PBCH repetition burst possibly every six 40ms PBCH cycles
      UE knows from specification the pattern (SFN and number of cycles)
      Repetitions within a 40ms that include PBCH repetitions use Option 3

## Slide 5: Proposals
  When evaluating options, companies should clearly define the configuration of transmission across 40ms cycles and the network and UE behaviors.
  Power consumption should be considered and latency can be considered.
  Configurability of the coverage enhancement amount of the PBCH can be considered at a per cell level.