## Slide 1: WF on DL-only LAA SCell HARQ timing
Ericsson, Nokia Networks, CATT, Sharp, Samsung, NVIDIA, Kyocera, ETRI, ITL, ALU, ASB, LG Electronics, Intel, KT, III, Interdigital, CATR, Motorola
R1-152280
3GPP TSG RAN WG1 Meeting #80bis
Belgrade, Serbia, 20th – 24th April, 2015 Agenda item: 7.2.4.2
Document for: Decision

## Slide 2: Proposal
At least for DL-only LAA SCell
  The timing between the subframe (w.r.t. Pcell subframe timing) in which a LAA PDSCH transmission ends and the subframe in which the corresponding HARQ-ACK feedback is transmitted follows the DL HARQ-ACK timing based on existing FDD-FDD and TDD-FDD CA spec assuming that the LAA SCell is an FDD Scell
  * Note that this does not exclude the further discussion on the HARQ timing for multi-subframe/cross-subframe scheduling if multi-subframe/cross-subframe scheduling is to be considered.