## Slide 1
Way forward on eIMTA signaling to support up to 32 component carriers
Huawei, HiSilicon, Potevio, Qualcomm,Nokia Networks,Panasonic,CATR, Ericsson…
R1-152308
3GPP TSG RAN WG1 Meeting #80bis
Belgrade, Serbia, 20th – 24th April, 2015 Agenda item: 7.2.2.2.1
Document for: Decision

## Slide 2
Background
At RAN1#80, the issue of DL control signaling has been discussed and observation was noted that there may be need for RAN1 to study potential limitation of eIMTA signaling for supporting up to 32 CCs in Rel 13:
  The following potential issues applicable to DL control could be studied for the 36.300 CA deployment scenarios:
    Potential limitations of the eIMTA signaling

## Slide 3
Proposal
  More than 5 indexes used to indicate UL/DL reconfiguration for eIMTA operation in Rel-13 CA are not needed
    Enhancement of DCI format 1C with eIMTA RNTI is not needed
    No additional DCI format is introduced to indicate UL/DL reconfiguration for eIMTA operation