## Slide 1: WF on Further Random Access Coverage Enhancement Details
Huawei, HiSilicon, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Ericsson, CATT, IDC, Intel, NEC, Nokia, Panasonic, Sierra Wireless
R1-152347
3GPP TSG RAN WG1 #80bis
Belgrade, Serbia, April 20-24, 2015
Agenda item 7.2.1.7

## Slide 2: Progress at RAN1#80
Some FFS points were identified in RAN1#80:
For coverage enh. of PRACH, for initial random access
  There is one to one mapping between PRACH repetition level and PRACH resource set
  Multiple attempts are allowed for each PRACH repetition level
  There is a configurable number of attempts
    FFS: Whether the configuration of the number of attempts is common or separate per repetition level
  Number of attempts per PRACH repetition level can be different
  If UE does not receive a RAR after the allowed number of attempts, it moves to the next higher repetition level
  Specified maximum numbers of levels is 3 (this does not include “zero coverage extension”)
  FFS: Power ramping or always max power used within each repetition level
  FFS UE behavior when UE receives RAR, but fails contention resolution

## Slide 3: Rel-13 progress
The following agreements from Rel-12 were confirmed in RAN1#79:
RAN1 confirms that following PRACH related agreements in Rel-12 LC-MTC are applied for Rel-13 low-complexity UE
  For PRACH multiplexing scheme, CDM, and/or TDM and/or FDM are supported
  After the initial random access procedure, for a physical channel using repetition, the repetition level is up to network
  Multiple PRACH repetition levels are supported
  Repeating the existing preamble formats for PRACH enhancement
  In addition, define additional time/freq. resource region(s) separate for “enhanced coverage” UEs.
    Within new region, at least CDM is allowed.
  Specified maximum numbers of levels: Working assumption of 3 (this does not include “zero coverage extension”). More evidence needed if we were to extend this.
  eNB-configurable number of levels (1, 2, 3) up to specified max level.
1 attempt = configured number of repetitions.
RAN1#79 also agreed:
Rel-13 low complexity UE can be identified by PRACH.
    FFS for detailed indication method, e.g., Preamble and/or resource allocation

## Slide 4: Proposals on procedure
For coverage enh. of PRACH:
  The configuration of the number of attempts can be separate per level
    Note: There may be default configurations defined (up to RAN2)
  The configuration of the number of repetitions can be separate per level
    Note: There may be default configurations defined (up to RAN2)
  When UE receives RAR but fails contention resolution
    The UE uses its current repetition level until it reaches the maximum number of attempts for that level