## Slide 1: WF on Transmission Modes for LAA
Ericsson, Qualcomm
R1-152387
AI. 7.2.4.2

## Slide 2: Background
CRS was designed for systems where continuous transmission is possible
Discontinuous transmission is essential to LAA
  DM-RS based TMs support discontinuous transmission
    DM-RS is present only when data is present.
  With discontinuous transmission, legacy CRS cannot be transmitted
    CRS transmissions cannot be guaranteed to occur at least once every fifth subframes in LAA, i.e. as in TDD conf. #0
    CRS acts like DM-RS
      Cannot rely on interpolation of CRS across subframes
If CRS based TMs is supported for LAA, performance for CRS based TMs needs to be re-evaluated and changed in RAN4
      If DMRS based TMs is supported for LAA, performance for DM-RS based TMs needs can be reused in RAN4

## Slide 3: Proposal
Support only TM10 like TM for LAA on the DL
  As a starting point the following transmission scheme of PDSCH is assumed when scheduling with
    FFS: DCI format 1A
    DCI format 2D
      Up to 8 layer transmission, ports 7-14 or single-antenna port, port 7 or 8