## Slide 1
Source: Samsung
Observation for CSI-RS and feedback enhancement
for EBF/FD-MIMO
Agenda Item: 6.2.5.2.1, Document for: Discussion and Decision
R1-152885
3GPP TSG RAN1 Meeting #81
Fukuoka, Japan, 25th - 29th May 2015

## Slide 2: Introduction
This contribution provides overall summary on the evaluation results for FD-MIMO with the following considerations:
  Overall observations are provided based on the results of RU level (low 20%, mid 50%, high 70%)
  Relative mean of arrival rate, UPT and 5% UPT performance gain for all CSI enhancement schemes (including both beamformed and non-precoded) and baseline Cat.2
  Results with same antenna configuration with 16, 32 TXRUs (M,N,P,Q)=(8,4,2,16/32) under UMi CF=2GHz scenario and UMa 500m have been collected
Additional details on the evaluations results can be found in
  R1-152888 Summary of results on beamformed CSI-RS based enhancement schemes
  R1-152895 Summary of results on non-precoded CSI-RS based enhancement schemes

## Slide 3: UMi Scenario (2GHz)
Average of relative gain over baseline cat2 (8,4,2,16)
  Enhancement scheme includes both beamformed and non-precoded results
UMi scenario,
  With same TXRU configuration (8, 4, 2, 16), enhancement schemes provide gain over baseline scheme over all RU range
  With same antenna configuration (8, 4, 2), increasing TXRU (16 32) provides
    Mean UPT: 7% gain in high RU
    5% UPT: 25% gain in high RU
Mean UPT
5% UPT
Chart: 
| Low RU | Mid RU | High RU
Enhancement scheme (8,4,2,16) gain over baseline (8,4,2,16) | 0.12991 | 0.23723 | 0.28944
Enhancement scheme (8,4,2,32) gain over baseline (8,4,2,16) | 0.23 | 0.4115 | 0.553
Chart: 
| Low RU | Mid RU | High RU
Enhancement scheme (8,4,2,16) gain over baseline (8,4,2,16) | 0.050489 | 0.070832 | 0.087511
Enhancement scheme (8,4,2,32) gain over baseline (8,4,2,16) | 0.06455 | 0.12731 | 0.16542

## Slide 4: UMa 500m ISD Scenario (2GHz)
Average of relative gain over baseline cat2 (8,4,2,16)
  Enhancement scheme includes both beamformed and non-precoded results
UMa scenario with 500m ISD,
  With same TXRU configuration (8, 4, 2, 16), enhancement schemes provide gain over baseline scheme over all RU range
  With same antenna configuration (8, 4, 2), increasing TXRU (16 32) provide
    Mean UPT: 3% gain in high RU
    5% UPT: 10% gain in high RU
Mean UPT
5% UPT
Chart: 
| Low RU | Mid RU | High RU
Enhancement scheme (8,4,2,16) gain over baseline (8,4,2,16) | 0.04509 | 0.097619 | 0.12652
Enhancement scheme (8,4,2,32) gain over baseline (8,4,2,16) | 0.0395 | 0.1 | 0.1526
Chart: 
| Low RU | Mid RU | High RU
Enhancement scheme (8,4,2,16) gain over baseline (8,4,2,16) | 0.10175 | 0.16128 | 0.19673
Enhancement scheme (8,4,2,32) gain over baseline (8,4,2,16) | 0.144 | 0.2064 | 0.308

## Slide 5: Conclusions
CSI-RS and feedback enhancements offer the following general observations:
  With the same antenna configuration (M,N,P)=(8, 4, 2), increasing the number of TXRUs from 16 to 32 gives benefits
    UMi 2GHz CF: 2~7% gain in mean UPT and 10~25% gain in 5% UPT
    UMa 500m ISD: -1~3% gain in mean UPT and 4~10% gain in 5% UPT
  Enhancement schemes provide larger gain over baseline schemes with (8, 4, 2, 16) configuration