## Slide 1
Source: Samsung
Summary of DMRS Enhancements for E-BF/FD-MIMO
Agenda Item: 6.2.5.3, Document for: Discussion and Decision
R1-152901
3GPP TSG RAN1 Meeting #81
Fukuoka, Japan, 25th - 29th May 2015

## Slide 2: Introduction
DMRS enhancement for high order multi-user spatial multiplexing is one of the possible specification enhancements for FD-MIMO
This contribution provides a summary of the evaluation results on DMRS enhancement submitted to RAN1 in RAN1#80b and RAN1#81
In the RAN1#80 meeting, the following alternatives for DMRS enhancement were identified for further RAN1 evaluations:
  Alt-1: 12 DM-RS REs with OCC = 4 for up to total 4 layers per scrambling sequence
  Alt-2: 24 DM-RS REs with OCC = 2 for up to total 4 layers per scrambling sequence
  Alt-3: 24 DM-RS REs with OCC = 4 for up to total 8 layers per scrambling sequence
  Alt-4: DM-RS estimation accuracy improvement by advanced receiver assuming interference channel estimation
  Alt-5: Larger PRG size
The gains shown in the following slides are obtained for the above 5 alternatives with the MU-MIMO performance based on Rel-12 DMRS as baseline

## Slide 3: Scatter Plots for 16 TXRUs, FTP [UMi, (8,4,2,16)]
Observations
  Alt-1: Mean UPT gain has range of 0.5 ~ 17.0% and 5% UPT gain has range of 4.3 ~ 22%
  Alt-5: Mean UPT gain has range of 13.8 ~ 17.2% and 5% UPT gain has range of 8.4 ~ 18.3%
HW
Intel
LGE
HW
Intel
LGE

## Slide 4: Scatter Plots for 64 TXRUs, FTP [UMi, (8,4,2,64)]
Observations
  Alt-1: Mean UPT gain has range of -1.0 ~ 31.63% and 5% UPT gain has range of 0 ~ 89.8%
  Alt-2: Mean UPT gain has range of -3.2 ~ 1.9% and 5% UPT gain has range of -4.1 ~ 2.4%
  Alt-3: Mean UPT gain has range of 0.0 ~ 9.2% and 5% UPT gain has range of 0.0 ~ 68.7%
  Alt-4: Mean UPT gain and 5% UPT gain is 0.7% and 11.4%, respectively
CATT
QCOM
DOCOMO
CMCC
ZTE
CATT
QCOM
DOCOMO
CMCC
ZTE

## Slide 5: Scatter Plot for 16 TXRUs, Full Buffer [UMi, (8,4,2,16)]
Observations
  Alt-1: Cell average throughput gain has range of 2.5 ~ 48.0% and 5% user throughput gain has range of 0.0 ~ 23.0%
  Alt-2: Cell average throughput gain has range of -5.8 ~ 22.0% and 5% user throughput gain has range of -4.7 ~ 16.0%
  Alt-4: Cell average throughput gain has range of 4.0 ~ 10.8% and 5% user throughput gain has range of 3.4 ~ 6.7%
QCOM (4Rx)
QCOM
LGE
Samsung
HW

## Slide 6: Scatter Plot for 64 TXRUs, Full Buffer [UMi, (8,4,2,64)]
Observations
  Alt-1: Cell average throughput gain has range of 0.0 ~ 57.7% and 5% user throughput gain has range of 1.0 ~ 29.1%
  Alt-2: Cell average throughput gain has range of -6.0 ~ 11.8% and 5% user throughput gain has range of -3.6 ~ 29%
  Alt-3: Cell average throughput gain has range of 0.3 ~ 40.2% and 5% user throughput gain has range of -9.0 ~ 21.6%
  Alt-4: Cell average throughput gain has range of 3.7 ~ 10.0% and 5% user throughput gain has range of 2.2 ~ 5.6%
QCOM (4Rx)
QCOM
CATT
CMCC
ZTE

## Slide 7: Conclusions
DMRS enhancements offer the following throughout gain:
  In case of non-full buffer traffic and (M,N,P,Q)=(8,4,2,16) under UMi scenario
    Alt-1: Mean UPT gain has range of 0.5 ~ 17.0% and 5% UPT gain has range of 4.3 ~ 22%.
    Alt-5: Mean UPT gain has range of 13.8 ~ 17.2% and 5% UPT gain has range of 8.4 ~ 18.3%.
  In case of non-full buffer traffic (M,N,P,Q)=(8,4,2,64) under UMi scenario
    Alt-1: Mean UPT gain has range of -1.0 ~ 31.63% and 5% UPT gain has range of 0 ~ 89.8%.
    Alt-2: Mean UPT gain has range of -3.2 ~ 1.9% and 5% UPT gain has range of -4.1 ~ 2.4%.
    Alt-3: Mean UPT gain has range of 0.0 ~ 9.2% and 5% UPT gain has range of 0.0 ~ 68.7%.
    Alt-4: Mean UPT gain and 5% UPT gain is 0.7% and 11.4%, respectively.
  In case of full buffer traffic and (M,N,P,Q)=(8,4,2,16) under UMi scenario
    Alt-1: Cell average throughput gain has range of 2.5 ~ 48.0% and 5% user throughput gain has range of 0.0 ~ 23.0%
    Alt-2: Cell average throughput gain has range of -5.8 ~ 22.0% and 5% user throughput gain has range of -4.7 ~ 16.0%
    Alt-4: Cell average throughput gain has range of 4.0 ~ 10.8% and 5% user throughput gain has range of 3.4 ~ 6.67%
  In case of full buffer traffic (M,N,P,Q)=(8,4,2,64) under UMi scenario
    Alt-1: Cell average throughput gain has range of 0.0 ~ 57.7% and 5% user throughput gain has range of 1.0 ~ 29.1%
    Alt-2: Cell average throughput gain has range of -6.0 ~ 11.8% and 5% user throughput gain has range of -3.6 ~ 29%
    Alt-3: Cell average throughput gain has range of 0.3 ~ 40.2% and 5% user throughput gain has range of -9.0 ~ 21.6%
    Alt-4: Cell average throughput gain has range of 3.7 ~ 10.0% and 5% user throughput gain has range of 2.2 ~ 5.6%
Excel file capturing all results on DMRS enhancements: